## Slide 1
CHIMERA, FARCOS, NARCOS DAQ : DAQ coupling at LNS and GSI E. De Filippo - INFN-CT
Vetar2: 125 MHz 64 bit White Rabbit (WR) VME timing receiver/sender
GET
VME
WHITE RABBIT Switch
Power
Supply
DAQ Server with Caen A3818/A4818 PCI card
Vetar2
V2718
bridge
µTCA
CAEN V2718 + CAEN V977 IO/Reg.
MCH network switch
COBO(s) DAQ
Mutant Trigger
Beast Synchro
µTCA main modules
LNS test point for DAQ
V1495
V1495 with FPGA compatible with GANIL CENTRUM and GET. It receives 100 MHz 48 bits TS from GET.
VME
CAEN codifiers, scalers, etc

## Slide 2
The CHIFAR experiment: exploring dynamics in the low energy regime at 20 MeV/A
CHIMERA + 10 FARCOS telescopes arranged in a Ring-like structure between 16 and 30 deg. polar angle
Using a combination of neutron poor and neutron rich beams and targets:
Beams: 124Sn, 112Sn, 124Xe Targets: 64Ni, 64Zn, 58Ni
GET digital DAQ for FARCOS and «CHIMERA CsI» and the front-end electronics for FARCOS based on custom designed ASICs

## Slide 3
GET + CHIMERA DAQ COUPLING (a brief overview)
We use «NARVAL» as supervisor for both CHIMERA and GET data acquisitions (Ubuntu, CentOS)
developed at IPN-Orsay by X. Grave (maintained at GANIL, no source code available)
based on the concept of generic Actors
written in OO language ADA (core) with C++ interface
Data flow: TCP/IP
Run Control Core and GUI interface based on Java (GANIL) VME DAQ, VME-GET Coupling, Data Analysis software for CoBo(s) and VME and general MERGER developed and mainteined at INFN Catania
Silicon FEE
GET
CsI GET
µTCA BUS
VME BUS
ELECTRONIC CONTROL CORE
ELECTRONIC CONTROL CORE
Acquisition node servers
DATA CATCHING & FILTERING
STORAGE
Eth.
Eth.
OFF-LINE MERGER
FARCOS
CHIMERA

## Slide 4: CHIMERA CSI / FARCOS to GET
CPA to Dual-Gain modules
Chimera CsI:
8 ASAD  (~2k signals)
Currently adding the whole CsI forward part (ring 4-9) to GET
Farcos (20 modules):
15 ASAD  (~4k signals)
8 CoBo (max)
1 µTCA crate
1 Mutant (three levels trigger)
1 Beast (syncro from Mutant to VME)
Computer farm + Storage (disk server) + 10Gb data / 1Gb switch slow control
AGET
VHDCI cable to CoBo
ADC
AsAD board
FPGA
Network to server(s)
CoBo(s) read and reduce data from the the AsAd front-end up to 4 AsAd(s), 1024 channels
A Farcos telescope
Signal Inputs (4x64)

## Slide 5: DUAL GAIN
G. Saccà et al. IWM-EC 2024 ,
Il Nuovo Cimento C48, 74 (2025)

## Slide 6
MuTanT (The Multiplicity Trigger and Time) provides a 3 level trigger system: L0 (external trigger), L1 (multiplicity trigger) and L2 (user defined trigger) and clock alignment with the CoBos.
VME
Mutant
Busy
Accepted Trigger to L0
Dead time
Gates generations for analog VME
common trigger + shared dead-time + event-number + Timestamp
TRIGGERING WITH CHIMERA-DAQ and Mutant
Chimera coupling with VME DAQ is done by using a Common Trigger synchro: Event Counter (EC) and/or Timestamp (TS)
VME
L1 Mutant
Busy
Accepted Trigger to L0
Gates generations for analog VME
L0L1 mode or L1 mode: GET master
L1 timing >1 µs to take decision
L0 mode: Chimera silicon detectors triggering
MuTanT
Internal Multiplicity threshold
MAIN TRIGGER FOR CHIMERA/FARCOS slave
TRIGGER FARCOS master

## Slide 7
The KaliMera C++ readout library
GET + CHIMERA DAQ COUPLING (readout software)
Current version: 0.50 (2025)
Based on the library for CHIMERA VME readout first defined in 2009 up to now. It has “survived” to the MBS coupling, GET coupling and to the R3B DAQ coupling

## Slide 8
Desktop and VME digitizers for NARCOS
MFM header+ data
Standalone Readout task for Caen digitizers (gen1)
TCP
or
UDP
Data analysis client and unpackers
Eth.
Eth.
GetMFMlib
NARCOS
We are working on gen2 VME 32 channels 500 MHz, 14 bit digitizer:
To do :
standalone daq
Registering it in the VME KaliMera library
In common with Chimera/GET tools/libraries
CrossTest experiment CN@LNL
VX2730
Waveforms Storage
AmBe test (2025) LNS
1 GHz, 16 ch, 12bit
DT5742

## Slide 9
Chimera DAQ at S122 (ASYEOS-II) GSI/FAIR coupled to R3B DAQ (analog VME only)
CAVE C GSI
CAVE C GSI
CHIMERA
KRAB
R3B main DAQ rack
NEULAND

## Slide 10: S122: ASY-EOS II data taking in cave C
Titre

## Slide 11
DAQ for AsyEos-II S122: software readout + data unpacking
Kalimera C++ library (v45-> v. 050)
VME readout
DRASI
DAQ:
LMD + chimera event white-rabbit WR timestamp)
CHIMERA (drasi)
KRAB
https://github.com/R3BRootGroup/R3BRoot
In R3B DAQ chimera is a data-client sending LMD data blocks to the main time-sorter server
We gave dead-time signal to the main DAQ, and we received a common trigger from the DAQ (VULOM)
TimeStamp (TS) is derived from the WR source (10 ns accuracy). Time-order (TO) orders data based on TS
https://fy.chalmers.se/~f96hajo/drasi/doc/

## Slide 12
DAQ for AsyEos R3B : VETAR2 inside the kaliMera C++ library and DAQ readout scheme
OK-event
Accepted trigger
Vetar2: 125 MHz 64 bit White Rabbit VME timing receiver
Optical fiber to WR switch
White Rabbit TS Data Format
INIT hardware and DAQ
DRASI READER
void Read_event()
Readout loop
pop
push
INIT AND START
LMD header
To UCESB/MainDAQ (TCP/pipe)
R3B DAQ data flow
Shared queue
FIFO
Readout thread
BUFFER:
Timestamp +
MFM header +
Chimera DATA
KaliMera library

## Slide 13
Variable width trigger for Sync-check in CHIMERA-R3B (s122)
T1
T3
T1 = main R3B trigger
event
SYNCHRO on-line check

## Slide 14
Data flow and ordering (s122)
The R3B DAQ TREE describes and checks the data flow
Time-orderer TO orders each data stream based on the timestamp associated with it
Timestamp is taken fron WR source
The EventBuilder sends the data to TO
The data from TO are “stitched” i.e. put together within a time window (<4 μs). Stitched data are the raw data on which we can perform off-line data analysis
CHIMERA

## Slide 15
Unpacking data with UCESB at R3B DAQ
R3B flow for data unpacking and data analysis
UCESB stands for Unpack and Check Every Single Bit, It can read several forms of raw data formats, in particular LMD, from file or network. It writes files, both raw data in LMD or unpacked and mapped into Root, and can start a server with protocols to distribute data over network. UCESB is a program that generates unpackers to parse the acquired data.
run192 Au 600 AMeV + Au 2% KRAB_multi>=4
RPCHI (deg)
RPKRAB (deg)
multCHI
multKRAB
RPCHI -RPKRAB (deg)
Yield (arb. units)

## Slide 16
For discussion: (SYMEOS + SYSTERSE)
NARCOS: Readout with custom boards for SiPM. DAQ development with CAEN digitizers. Expected resolvable problems for coupling NARCOS prototype at FRIB. . . .
FARCOS: GET electronics, Narval supervisor, custom TimeStamp, synchronization problems with foreign DAQ. But at MSU should be past experience with GET for SπRIT TPC . . . . .
CHIMERA rings ? . . . Problems with FEE and analog electronics (too old QDCs/TDCs). New FEE, DAQ, Triggering, etc ? . . . . .

## Slide 19: Selectable-Gain CMOS Charge Preamplifier for Pulse Shape Analysis in Double Sided Silicon Microstrip Detectors for FARCOS
single design for both thicknesses and of both polarities
strip capacitance about 65 pF (300 µm) and 35 pF (1500 µm)
strip leakage current ~5 nA (300 µm) and ~25 nA (1500 µm)
target dynamic ranges: 90 MeV, 200, 350, 500 and 2000 MeV.
static power consumption ~10 mW/channel
Digitally Selectable gain
16-ch ASIC layout 0.35 μm C35B4C3 AMS tech
16-ch CPA for DSSSD
2-ch CPA for CsI(Tl) + PD readout
on-chip pulser
channel-by-channel test signal injection
temperature monitor
A Kapton cable connects each face of each DSSSC to a custom PCB motherboard housing the front-end ASIC (2x(16+1) channels.
G | FSR (MeV) | Sensitivity (mV/MeV) | Sensitivity (mV/pC) | Feedback cap. (pF)
0 | 90 | 11.11 | 250 | 4
1 | 200 | 4.44 | 100 | 10
2 | 350 | 2.78 | 62.50 | 16
3 | 500 | 2.02 | 45.45 | 22
4 | 2000 | 0.49 | 11.11 | 90
A. Castoldi, C. Guazzoni, T. Parsani: Politecnico di Milano and INFN sezione di Milano

## Slide 20
design
Main characteristics:
5 rings of 4x4 mm2 segments of fast scintillating fibers (BCF-10)
read out by 3×3 mm2 SiPMs (SensL MicroFJ-30035)
high resolution 3D printed mechanical structure
ASICs used for signal processing (32 ch CITIROC 1A)
assure compactness of the electronics and wiring
compact A7585D SiPM power modules
broad coverage from 30o to 165o
high geometrical efficiency ~87% (within covered angles)
~5% multihit probability (for 1 AGeV Au+Au reaction)
it will be sufficiently large for radioactive beams
and sufficiently small and lightweight not to disturb neutrons
max radius - 12 cm
length ~43 cm (size of a ~24” monitor)
4×160 segments in forward rings
96 segments in backward ring, 736 channels
He sleeve to suppress the δ-electron background
KRAB: multiplicity trigger, reaction plane and centrality detector for the ASYEOS II experiment at GSI/FAIR
UrQMD simulations

## Slide 21
6Li
8Li
7Li
9Be
7Be
B
He (p.t.)
4He
3He
H
320 CsI(Tl) 12 cm thick, assembled in 8 rings,
covering polar angles between 4.6 and 16 deg
CHIMERA final goal: reaction plane determination
Ring 6 (all) and Ring 5 (partial) preliminary data analysis (particle identification and calibration procedures). Work in progress . . .