## Slide 1: Gran Sasso Hands-on 2023 - PhD autumn school on experimental astroparticle physics Hands-on activity: LUNA experiment 05.10.2023 Calibration of LUNA MV accelerator Testing Ta2O5 targets and resonance strength determination at the LUNA-400 Accelerator Anup Yadav (HZDR) & Verena Aures (TUM)

## Slide 2: Stellar nucleosynthesis
Scientific motivation
The ³He(α,γ)⁷Be reaction affects both, the stellar hydrogen burning as well as the Big Bang Nucleosynthesis (BBN).
In the latter it influences the production of ⁷Li and in the former the neutrino flux in the p-p II and p-p III chain in the sun.
A recent theory study by Zhang et al. [2] proposes a correlation between the S-factor S(0) at low energies and the angular distribution of the emitted γ-rays. Measurements of this angular distribution at higher energies therefore gives the possibility to get a better estimation for a low energy data point and additionaly improves the extrapolation of the data and all analysis based on it.
The plot below shows the existing data, the solar fusion II fit and
highlights the relevant energy ranges for the sun and the BBN.
BBN produced light elements, mainly H and 4He. Other elements are synthetized inside stars with an associated energy production.
Charged-particle induced reactions
LUNA - Direct corss section measurements @ Gamow window

## Slide 3: Cross section values at stellar energies
Scientific motivation
The ³He(α,γ)⁷Be reaction affects both, the stellar hydrogen burning as well as the Big Bang Nucleosynthesis (BBN).
In the latter it influences the production of ⁷Li and in the former the neutrino flux in the p-p II and p-p III chain in the sun.
A recent theory study by Zhang et al. [2] proposes a correlation between the S-factor S(0) at low energies and the angular distribution of the emitted γ-rays. Measurements of this angular distribution at higher energies therefore gives the possibility to get a better estimation for a low energy data point and additionaly improves the extrapolation of the data and all analysis based on it.
The plot below shows the existing data, the solar fusion II fit and
highlights the relevant energy ranges for the sun and the BBN.
Example: our Sun:
kT = 1 keV
EC ≈ 0.5-2 MeV
E0 ≈ 5-30 keV
for reactions of H burning
kT but also E0 << EC !!
Exponential decrease of the cross section with decreasing energyCross sections in the range of pb-fb at stellar energies

## Slide 4: Reaction rate at stellar energies
Scientific motivation
The ³He(α,γ)⁷Be reaction affects both, the stellar hydrogen burning as well as the Big Bang Nucleosynthesis (BBN).
In the latter it influences the production of ⁷Li and in the former the neutrino flux in the p-p II and p-p III chain in the sun.
A recent theory study by Zhang et al. [2] proposes a correlation between the S-factor S(0) at low energies and the angular distribution of the emitted γ-rays. Measurements of this angular distribution at higher energies therefore gives the possibility to get a better estimation for a low energy data point and additionaly improves the extrapolation of the data and all analysis based on it.
The plot below shows the existing data, the solar fusion II fit and
highlights the relevant energy ranges for the sun and the BBN.
Laboratory:
Rlab= Np Nt e
Np = number of projectile ions ≈ 1014 pps (100 mA q=1+)
Nt = number of target atoms ≈ 1018 at/cm2
= cross section = 10-36 cm2 (often even smaller)
e= efficiency ≈1-5% for gamma rays
Rlab ≈ 1-5 10-6 counts/s ≈ 4 10-3-2 10-2 counts/h

## Slide 5: Measuring Fusion Reactions in Laboratory
Scientific motivation
The ³He(α,γ)⁷Be reaction affects both, the stellar hydrogen burning as well as the Big Bang Nucleosynthesis (BBN).
In the latter it influences the production of ⁷Li and in the former the neutrino flux in the p-p II and p-p III chain in the sun.
A recent theory study by Zhang et al. [2] proposes a correlation between the S-factor S(0) at low energies and the angular distribution of the emitted γ-rays. Measurements of this angular distribution at higher energies therefore gives the possibility to get a better estimation for a low energy data point and additionaly improves the extrapolation of the data and all analysis based on it.
The plot below shows the existing data, the solar fusion II fit and
highlights the relevant energy ranges for the sun and the BBN.
ACCELERATOR
TARGET
REACTION PRODUCTS
, p, n, , ...
DETECTOR
(to be chosen considering the particular case)
Solid or gas

## Slide 6: What can we do?
Scientific motivation
The ³He(α,γ)⁷Be reaction affects both, the stellar hydrogen burning as well as the Big Bang Nucleosynthesis (BBN).
In the latter it influences the production of ⁷Li and in the former the neutrino flux in the p-p II and p-p III chain in the sun.
A recent theory study by Zhang et al. [2] proposes a correlation between the S-factor S(0) at low energies and the angular distribution of the emitted γ-rays. Measurements of this angular distribution at higher energies therefore gives the possibility to get a better estimation for a low energy data point and additionaly improves the extrapolation of the data and all analysis based on it.
The plot below shows the existing data, the solar fusion II fit and
highlights the relevant energy ranges for the sun and the BBN.
Improve signal
  Increase beam intensity, increase target enrichment, …
Reduce background
  Active / passive shielding, background rejection via PSA, …
Novel detection techniques
  Improve efficiency as much as possible
Measure at higher energies and extrapolate

## Slide 7: Laboratory for Underground Nuclear Astrophysics (LUNA)
Scientific motivation
The ³He(α,γ)⁷Be reaction affects both, the stellar hydrogen burning as well as the Big Bang Nucleosynthesis (BBN).
In the latter it influences the production of ⁷Li and in the former the neutrino flux in the p-p II and p-p III chain in the sun.
A recent theory study by Zhang et al. [2] proposes a correlation between the S-factor S(0) at low energies and the angular distribution of the emitted γ-rays. Measurements of this angular distribution at higher energies therefore gives the possibility to get a better estimation for a low energy data point and additionaly improves the extrapolation of the data and all analysis based on it.
The plot below shows the existing data, the solar fusion II fit and
highlights the relevant energy ranges for the sun and the BBN.
LUNA 1
(1992-2001)
50 kV
LUNA 2
(2000…)
400 kV
Laboratory for Underground NuclearAstrophysics
Radiation | LNGS/surface
Muons Neutrons | 10-6 10-3
LUNA MV
(2022...)
LNGS (1400 m rock shielding  4000 m w.e.)

## Slide 8: Week 1: The future LUNA MV accelerator
Scientific motivation
The ³He(α,γ)⁷Be reaction affects both, the stellar hydrogen burning as well as the Big Bang Nucleosynthesis (BBN).
In the latter it influences the production of ⁷Li and in the former the neutrino flux in the p-p II and p-p III chain in the sun.
A recent theory study by Zhang et al. [2] proposes a correlation between the S-factor S(0) at low energies and the angular distribution of the emitted γ-rays. Measurements of this angular distribution at higher energies therefore gives the possibility to get a better estimation for a low energy data point and additionaly improves the extrapolation of the data and all analysis based on it.
The plot below shows the existing data, the solar fusion II fit and
highlights the relevant energy ranges for the sun and the BBN.
Inline Cockcroft Walton accelerator
Terminal voltage : 0.2 – 3.5 MV
Beam energy reproducibility: 0.01% TV or 50V
Beam energy stability: 0.001% TV / h
Beam current stability: < 5% / h
H+ beam: 500 - 1000 eµA
He+ beam: 300 - 500 eµA
C+ beam: 100 - 150 eµA
C++ beam: 100 eµA
80 cm-thick concrete shielding around accelerator room. This will reduce the neutron flux just outside the shielding to a value about one order of magnitude lower than the neutron flux at LNGS

## Slide 9: Experimental setup : LUNA-MV
27Al target
HPGe detector

## Slide 10: Calibration of the HPGe Detectors

## Slide 11: Calibration of the HPGe Detectors

## Slide 12: Resonance scan of 27Al(p, g)28Si reaction
Resonance scan of a well-known reaction for the accelerator energy calibration
In addition, study of beam stability for a long period

## Slide 13: LUNA 400 KV – Week 2
E beam  50 – 400 keV
I max  500 A protons I max  250 A alphas
Energy spread  70 eV Long term stability  5eV/h

## Slide 14: Target Production and Analysis (LUNA 400 kV)
Scientific motivation
The ³He(α,γ)⁷Be reaction affects both, the stellar hydrogen burning as well as the Big Bang Nucleosynthesis (BBN).
In the latter it influences the production of ⁷Li and in the former the neutrino flux in the p-p II and p-p III chain in the sun.
A recent theory study by Zhang et al. [2] proposes a correlation between the S-factor S(0) at low energies and the angular distribution of the emitted γ-rays. Measurements of this angular distribution at higher energies therefore gives the possibility to get a better estimation for a low energy data point and additionaly improves the extrapolation of the data and all analysis based on it.
The plot below shows the existing data, the solar fusion II fit and
highlights the relevant energy ranges for the sun and the BBN.
LUNA-400:
Study of resonances and cross sections in gas and solid targets below 400 keV
What we did:
Solid target production (via anodic oxidation)
Analysis of data from similar targets using BGO detectors
Characterization of the extended gas target

## Slide 15: Production of Ta2O5 Targets
Scientific motivation
The ³He(α,γ)⁷Be reaction affects both, the stellar hydrogen burning as well as the Big Bang Nucleosynthesis (BBN).
In the latter it influences the production of ⁷Li and in the former the neutrino flux in the p-p II and p-p III chain in the sun.
A recent theory study by Zhang et al. [2] proposes a correlation between the S-factor S(0) at low energies and the angular distribution of the emitted γ-rays. Measurements of this angular distribution at higher energies therefore gives the possibility to get a better estimation for a low energy data point and additionaly improves the extrapolation of the data and all analysis based on it.
The plot below shows the existing data, the solar fusion II fit and
highlights the relevant energy ranges for the sun and the BBN.
Solid target production via anodic oxidation on tantalum backings (Ta2O5)
Homogeneous targets
Well known relation between voltage and target thickness:
d = 1.9225 x (V + 1.4) nm

## Slide 16: Production of Ta2O5 Targets
Scientific motivation
The ³He(α,γ)⁷Be reaction affects both, the stellar hydrogen burning as well as the Big Bang Nucleosynthesis (BBN).
In the latter it influences the production of ⁷Li and in the former the neutrino flux in the p-p II and p-p III chain in the sun.
A recent theory study by Zhang et al. [2] proposes a correlation between the S-factor S(0) at low energies and the angular distribution of the emitted γ-rays. Measurements of this angular distribution at higher energies therefore gives the possibility to get a better estimation for a low energy data point and additionaly improves the extrapolation of the data and all analysis based on it.
The plot below shows the existing data, the solar fusion II fit and
highlights the relevant energy ranges for the sun and the BBN.
18O (99 %) @ 78 V
Different thicknesses appear in different colors:
18O (99 %) @ 48 V (but power supply failure)
2 ml UPW + 0.1 ml 18O (89 %) @ 30 V

## Slide 17: Characterization of Solid Targets: Aims and Techniques
Scientific motivation
The ³He(α,γ)⁷Be reaction affects both, the stellar hydrogen burning as well as the Big Bang Nucleosynthesis (BBN).
In the latter it influences the production of ⁷Li and in the former the neutrino flux in the p-p II and p-p III chain in the sun.
A recent theory study by Zhang et al. [2] proposes a correlation between the S-factor S(0) at low energies and the angular distribution of the emitted γ-rays. Measurements of this angular distribution at higher energies therefore gives the possibility to get a better estimation for a low energy data point and additionaly improves the extrapolation of the data and all analysis based on it.
The plot below shows the existing data, the solar fusion II fit and
highlights the relevant energy ranges for the sun and the BBN.
Target thickness
  Use thickness from formula in nm to obtain ΔE with SRIM
  Compare theoretical result with measurement data (fit)
with resonance strength and wavelength
Stopping power
  Obtain maximal yield Ymax via data fitting
  Get stopping power from relation
Composition
Nuclear Resonant Reaction Analysis (NRRA)

## Slide 18: Characterization of Targets with NRRA (BGO Detectors)
Scientific motivation
The ³He(α,γ)⁷Be reaction affects both, the stellar hydrogen burning as well as the Big Bang Nucleosynthesis (BBN).
In the latter it influences the production of ⁷Li and in the former the neutrino flux in the p-p II and p-p III chain in the sun.
A recent theory study by Zhang et al. [2] proposes a correlation between the S-factor S(0) at low energies and the angular distribution of the emitted γ-rays. Measurements of this angular distribution at higher energies therefore gives the possibility to get a better estimation for a low energy data point and additionaly improves the extrapolation of the data and all analysis based on it.
The plot below shows the existing data, the solar fusion II fit and
highlights the relevant energy ranges for the sun and the BBN.
BGO scintillator crystal detector
Worse energy resolution than HPGe but high efficiency
Detector covers entire solid angle and detects sum of photon energies
Peak of 151 keV resonance of 18O(p, γ)19F reaction at 8137.7 keV

## Slide 19: Characterization of the Ta2O5 Targets with NRRA
Scientific motivation
The ³He(α,γ)⁷Be reaction affects both, the stellar hydrogen burning as well as the Big Bang Nucleosynthesis (BBN).
In the latter it influences the production of ⁷Li and in the former the neutrino flux in the p-p II and p-p III chain in the sun.
A recent theory study by Zhang et al. [2] proposes a correlation between the S-factor S(0) at low energies and the angular distribution of the emitted γ-rays. Measurements of this angular distribution at higher energies therefore gives the possibility to get a better estimation for a low energy data point and additionaly improves the extrapolation of the data and all analysis based on it.
The plot below shows the existing data, the solar fusion II fit and
highlights the relevant energy ranges for the sun and the BBN.
Scan of sample (several proton energies)
Spreaded peak around 8137.7 keV
Determine area of peak with subtracted background
Do this for every measurement point (proton energy)
Calculate yield = counts/charge

## Slide 20: Characterization of the Ta2O5 Target (78 V)
Scientific motivation
The ³He(α,γ)⁷Be reaction affects both, the stellar hydrogen burning as well as the Big Bang Nucleosynthesis (BBN).
In the latter it influences the production of ⁷Li and in the former the neutrino flux in the p-p II and p-p III chain in the sun.
A recent theory study by Zhang et al. [2] proposes a correlation between the S-factor S(0) at low energies and the angular distribution of the emitted γ-rays. Measurements of this angular distribution at higher energies therefore gives the possibility to get a better estimation for a low energy data point and additionaly improves the extrapolation of the data and all analysis based on it.
The plot below shows the existing data, the solar fusion II fit and
highlights the relevant energy ranges for the sun and the BBN.
99 % of Oxygen-18
Ymax via fit: 2.942 c/uC
ΔE via fit: 19.572 keV
ΔE via formula and SRIM: 17.370 keV
= 3.223 x 10-14 eV/g/cm2

## Slide 21: Characterization of the Ta2O5 Target (30 V)
Scientific motivation
The ³He(α,γ)⁷Be reaction affects both, the stellar hydrogen burning as well as the Big Bang Nucleosynthesis (BBN).
In the latter it influences the production of ⁷Li and in the former the neutrino flux in the p-p II and p-p III chain in the sun.
A recent theory study by Zhang et al. [2] proposes a correlation between the S-factor S(0) at low energies and the angular distribution of the emitted γ-rays. Measurements of this angular distribution at higher energies therefore gives the possibility to get a better estimation for a low energy data point and additionaly improves the extrapolation of the data and all analysis based on it.
The plot below shows the existing data, the solar fusion II fit and
highlights the relevant energy ranges for the sun and the BBN.
Ymax via fit: 0.273 c/uC
ΔE via fit: 7.776 keV
Ratio of Ymax: 0.09
9 % of Oxygen-18

## Slide 22: Characterization of Gas Target Density
Scientific motivation
The ³He(α,γ)⁷Be reaction affects both, the stellar hydrogen burning as well as the Big Bang Nucleosynthesis (BBN).
In the latter it influences the production of ⁷Li and in the former the neutrino flux in the p-p II and p-p III chain in the sun.
A recent theory study by Zhang et al. [2] proposes a correlation between the S-factor S(0) at low energies and the angular distribution of the emitted γ-rays. Measurements of this angular distribution at higher energies therefore gives the possibility to get a better estimation for a low energy data point and additionaly improves the extrapolation of the data and all analysis based on it.
The plot below shows the existing data, the solar fusion II fit and
highlights the relevant energy ranges for the sun and the BBN.
Monitor gas target density
Measure pressure and temperatures at different positions
Obtain density via ideal gas law
Include results in data analysis

## Slide 23: Characterization of Gas Target Density
Scientific motivation
The ³He(α,γ)⁷Be reaction affects both, the stellar hydrogen burning as well as the Big Bang Nucleosynthesis (BBN).
In the latter it influences the production of ⁷Li and in the former the neutrino flux in the p-p II and p-p III chain in the sun.
A recent theory study by Zhang et al. [2] proposes a correlation between the S-factor S(0) at low energies and the angular distribution of the emitted γ-rays. Measurements of this angular distribution at higher energies therefore gives the possibility to get a better estimation for a low energy data point and additionaly improves the extrapolation of the data and all analysis based on it.
The plot below shows the existing data, the solar fusion II fit and
highlights the relevant energy ranges for the sun and the BBN.
Calorimeter heats up gas (lower density)
Constant high density in target chamber
Density drops with increasing distance from target chamber (collimator and pumps)
Collimator
Calorimeter
Target Chamber

## Slide 24: Summary
Scientific motivation
The ³He(α,γ)⁷Be reaction affects both, the stellar hydrogen burning as well as the Big Bang Nucleosynthesis (BBN).
In the latter it influences the production of ⁷Li and in the former the neutrino flux in the p-p II and p-p III chain in the sun.
A recent theory study by Zhang et al. [2] proposes a correlation between the S-factor S(0) at low energies and the angular distribution of the emitted γ-rays. Measurements of this angular distribution at higher energies therefore gives the possibility to get a better estimation for a low energy data point and additionaly improves the extrapolation of the data and all analysis based on it.
The plot below shows the existing data, the solar fusion II fit and
highlights the relevant energy ranges for the sun and the BBN.
First week – Energy calibration of HPGe detectors and the LUNA MV accelerator
Second week – Target production and characterization of solid target using the LUNA 400 kV accelerator
Determination of extended gas target density profile
Thanks to our supervisors Denise and Federico!