## Slide 1: LAr Purity Monitoring
Keyu Shang, Ginevra De Lauretis, Michael Lewis
Tutors: Valentina Biancacci (GSSI), Riccardo Biondi (GSSI), Natalia Di Marco (GSSI) Gosia Haranczyk (LNGS), Michele Morella (LNGS)

## Slide 2: Introduction – LAr Detectors
Liquid Argon (LAr) detectors are used widely in particle, astro-particle, and applied physics applications:
Dark Matter (Darkside, Deap)
Neutrino Physics (ICARUS, DUNE, LEGEND)
PET Scanners
LAr is highly sought after due to its appropriate properties:
Noble gas is inert and scalable
Cheaper than other gases (Xenon)
High light output with singlet + triplet decay
Long electron lifetimes

## Slide 3: Introduction – LAr Purity and Scintillation
LAr scintillation properties include:
High light yield (40 photons per keV)
Emission wavelength: 128 nm (VUV)
Excimer lifetimes:
    Singlet  τs = ~5 ns
    Triplet  τt = 1.6 μs
Impurities (O2 + N2) can affect decay times:
Quenching mostly the triplet lifetime

## Slide 4: Our Goals – LEGENDArYno for Future LAr Detector
The current search for 0νββ from 76Ge isotopes using HPGe:
Currently running LEGEND-200
The future project is LEGEND-1000
Goals:
To test and characterize light detectors for future upgrade to LEGEND experiment, LEGEND-1000.
Must determine the optical properties of the LAr in LEGEND-1000.
The activity:
Characterize and understand common properties of the light detectors and estimate LAr purity from real data.
HPGe Detectors under UV
LEGEND-1000 Prototype

## Slide 5: Experimental Setup - Electronics
Oscilloscope
High-Voltage
Controller
Dark Box
Cover for
Dark Box
LED Pulse Generator

## Slide 6: Experimental Setup - PMT
PMT
Blue LED
PMT Window
Dynodes
H-V connection
Signal Output
Top view of PMT in dark box
Side view of PMT in dark box
D = 10cm

## Slide 7: Results – PMT Characterization with no LED
To understand the characteristics of the PMT under high voltage (HV), we can evaluate the single photoelectron peak to understand:
Gain
Dark count rate (DCR)
Baseline RMS
Mean +/- standard of area
From this, we can choose the optimal HV for PMT operation
LED source was used to imitate the light flashes from LAr and see how the signal is affected
Three different PMTs were characterized under only HV:
PMT-Michael (2-inch)
PMT-Keyu (2-inch)
PMT-Ginevra (3-inch)

## Slide 8: Results – PMT-Michael with no LED (1400V)

## Slide 9: Results – DCR vs. HV

## Slide 10: Results – Gain vs. HV
We test the response from the LED using PMT-Michael at HV = 1400V

## Slide 11: Results – PMT-Michael with LED
Triggered on PMT signal and with coincidence

## Slide 12: Results – PMT-Michael with LED
Multi-Photon peaks
Coincidence peak
Noise+DCR peaks, mixed with SPE peak

## Slide 13: Results – Estimating purity from real LAr data
Single Waveform from the light pulse in LAr
Shorter lifetime pulse
longer lifetime pulse
The Lar data was taken from the setup on the right:
60L metal sealed dewar, CF – 160 top flange
Scintillation from LAr viewed from two 2-inch TPB-coated PMTS
PMT readout with linear amplifiers
HV power supply
Temperature sensors to monitor the LAr
Multiple components from singlet, triplet, and intermediate effects:
We are interested in the long triplet lifetimes.

## Slide 14: Results – Estimating purity from real LAr data
Lifetime (τ) μs | [O2] ppm | [N2] ppm
1.37 | 0.19 | 0.95
0.94 | 0.81 | 3.98
0.57 | 2.09 | 10.3

## Slide 15: Results – Estimating purity from real LAr data
Lifetime (τ) μs | [O2] ppm | [N2] ppm
1.37 | 0.19 | 0.95
0.94 | 0.81 | 3.98
0.57 | 2.09 | 10.3
From our calculated concentration of O2 and N2, we can estimate the level of purity of Argon received from the supplier:
E.g., for τ = 0.94 μs, the concentrations correspond to an Argon rating of 5.0 (>99.999%)
This method is appropriate to measure the purity in LAr detectors (LEGENDArYno)

## Slide 16
Thanks for Listening!!!!