## Slide 1
The FIREX program at the Institute of Laser Engineering and future upgrades
Alessio Morace.
Institute of Laser Engineering, Osaka University.
PALS laboratory, FZU, IPP, Czech Academy of Sciences

## Slide 2
NIF ignition and introduction to ILE’s FIREX
Brief summary of FIREX-I results, Fast electron and Ion Fast Ignition
Necessity for change in approach: Increase intensity for PW pulse.
FIREX-NEO and upgrades
Summary of the TALK
Outline of the talk

## Slide 3
In the indirect approach the laser energy is converted into a thermal bath of soft x-rays with quasi-plankian distribution at 300 eV.
The soft x-rays ablate the outer surface of the capusule and drive the compression.
Heating of the DT gas is obtained by PdV work.
At peak density the temperature of the DT gas reaches 4.5-6 keV.
With ignition and burn into the “cold” fuel DT temperature goes well above 10 keV.
NIF Ignition was achieved by indirect drive
Notes: Mention CHS in icf description for slide 7

## Slide 4: By 2021, experiments had produced ~70% of the input energy – we were close!
Increased Coupling (HybridE / I-Raum)
Higher velocity & lower coast-time
Higher velocity
“Burning Plasma”
Regime
IGNITION
Recent experiments have produced ~150% of the input energy – IGNITION!!
Notes: AND SO WITH THESE ENCOURAGING, RECENT RESULTS, I'M GOING TO TURN THE PRESENTATION OVER TO MY COLLEAGUE DEREK MARISCAL TO TALK TO YOU ABOU THE SIMULATION, AND IN PARTICULAR THE MACHINE LEARNING, THAT HELP GUIDE THE DESIGN AND OPTIMIZATION OF THE NUCLEAR FUSION RESEEARCH ON THE NIF

## Slide 5
Improve the laser technology:
NIF is Flash lamp pumped laser. Over 90% of the energy is lost during the pump process. Diode pumped laser would drastically improve the efficiency ~ 10x.
Now on NIF about 1/2 of the laser energy produced goes into the holhraum.
The indirect-drive CHS approach is also intrinsically inefficient as the vast majority of the laser energy goes into heating the holhraum itself, and part of if escapes through the entrances in the form of x-rays.
NIF Ignition was achieved by indirect drive
Notes: Rename the title

## Slide 6
Alternative ICF approaches: Fast Ignition
The difficulty and extreme sensitivity to symmetry and instabilities in CHS igntion led to the conception of alternative approaches, the most popular of which is Fast Ignition.
In fast ignition the stages of compression and heating are separated, with the heating produced by a ultra-high intensity laser pulse, which will produce energetic particle beams (electrons or protons/ions) that will deliver their energy in the compressed core. Creating a lateral hot spot triggering ignition and burn.

## Slide 7
Diesel engine
Compression
Self-
Ignition
Burn
Gasoline engine
Spark Plug
Ignite with spark plug
→ Downsizing
Compression
Ignition
Burn
External
Ignition
Central
Ignition
Scheme
Fast
Ignition
Scheme
PdV work by implosion produces the spark in the central ignition scheme.
External energy injection produces the spark in the fast ignition scheme.

## Slide 8
The FIREX project at ILE, The University of Osaka
The FIREX-I project aimed at demonstrating the heating up to 5 keV of a compressed plasma with rR ~0.1g/cm2. Two main approaches adopted were Fast Electron and Ion Fast Ignition
Utilizes the fast electron beam generated by the UHI laser to directly heat up the compressed core.
Utilizes the protons/ions, generated as secondary source from a thin foil, to heat up the compressed core.

## Slide 9
GXII-LFEX system
GXII beamlines
12 beams
3.5 kJ at 2w
1.2-10 ns
LFEX beamline
4 beamlets
10 kJ , 2.5 kJ/beamlet
1.5 kJ for 1.5 ps operation

## Slide 10
GXII-LFEX system
This is the T1 chamber at ILE.
It receives LFEX laser and the GXII beams in spherical symmetry (4 kJ at 2w)
It allows for scaled down FI experiments

## Slide 11
GXII-LFEX system
LFEX
This is the T1 chamber at ILE.
It receives LFEX laser and the GXII beams in spherical symmetry (3.5 kJ at 2w)
It allows for scaled down FI experiments

## Slide 12
GXII-LFEX system
LFEX
GXII
GXII
GXII
This is the T1 chamber at ILE.
It receives LFEX laser and the GXII beams in spherical symmetry (4 kJ at 2w)
It allows for scaled down FI experiments

## Slide 13
NIF ignition and introduction to ILE’s FIREX
Brief summary of FIREX-I results, Fast electron and Ion Fast Ignition
Necessity for change in approach: Increase intensity for PW pulse.
FIREX-NEO and upgrades
Summary of the TALK
Outline of the talk

## Slide 14
Fast Electron Fast Ignition (S. Fujioka group)
Resistive
Heating
Drag
Heating
Diffusive
Heating
Three major mechanisms of isochoric heating with REB*
Fast electron
Bulk electron
Resistive
Heating
Diffusive
Heating
Drag
Heating
Drag heating:
Energy transfer from relativistic electrons to bulk electrons via binary collisions.
Resistive heating:
Ohmic heating via a return current that is driven by the forward REB for sustaining the current neutrality.
Diffusive heating:
Heat transport from a heated plasma to a cold plasma via nonlocal-diffusive fashion.
*REB: Relativistic Electron Beam

## Slide 15
Conventional thin shell fuel
Advanced solid ball fuel
Solid ball fuel has been chosen over shell (S. Fujioka group)
Ragarding the compressed fuel, solid ball have been selected, being hydrodynamically stable and mass producible

## Slide 16
Fast Electron Fast Ignition, ILE approach
1mm
B ~ kT
Current ~ several MA
GEKKO-XII
Capacitor-coil
for REB collimation
S. Fujioka+, Sci. Rep. 2013.
Plasma mirror
for cooling REB
Y. Arikawa+, Appl. Opt. 2016.
A. Morace+. Nuclear Fusion 2017
Guiding cone
for laser-absorption
R. Kodama+, Nature 2004.
Solid ball
for stable fuel compression
S. Fujioka+, Phys. Rev. E, 2015.

## Slide 17
Experimental set-up
GEKKO-XII (2w)
for implosion
Cu-Ka imaging
Flat crystal
Cu-Ka spectroscopy
Spherical crystal
GEKKO-XII (1w)
for B-field
Current
Cu-doped CH solid ball
(250 mmf)
Gold cone
(45 deg. full angle)
Plasma mirror
LFEX
Interaction point
Fast Electron Fast Ignition, ILE approach

## Slide 18
Significant heating > 1 keV was measured in the compressed Cu-oleate plasma
#43780
Temperature
Current
Cu-doped CH solid ball
(250 mmf)
Gold cone
(45 deg. full angle)
X-ray image
Heated area
Drag Heating Efficiency

## Slide 19
”Classic” proton fast ignition concept at ILE
The concept is similar to Fast Electron Fast Ignition. However the current density is lower, but the coupling efficiency is higher. The key parameters to be investigated and enhanced are:
Conversion efficiency
Focusing
Heating efficiency (coupling)
2D PIC simulation
2D Hydrodynamic simulation
Courtesy Prof. Fujioka

## Slide 20
FIREX -1 activity on Proton Fast Ignition.
Investigated the LPI for multiple beamlet kJ-class laser and demonstrated that temporally and spatially overlapped beamlets lead to more than 200% increment in conversion efficiency via interference.
A. Morace et al. Nature Communications 10, 2995 (2019)
Studied the proton beam dynamics in focusing plasma devices and demonstrated that the dynamics is dominated by super-strong B-fields.
A. Morace et al. Scientific Reports 12, 6876 (2022)
225 eV
205 eV
200 eV
Investigated the ion induced heating in mid-Z material through x-ray spectroscopy .
Martynenko, Morace et al. PPCF 65 (2023)

## Slide 21
Towards a fully integrated PFI experiment in early 2026
In this experiment we use cone targets attached to a cu-oleate ball 200 um in diameter + 30 um PVVA coating
Oleate ball
PFI cone
hemishell
PFI cone
Hemi-shell
300 um
300 um
Despite this, it appears clear that the PFI approch alone may be insufficient the heat up the plasma to ignition temperature

## Slide 22
Rationale for looking to new approaches to FI
These “classic” approaches to Ignition have some severe limitations.
In particular for Fast electron FI we have:
Complexity of the setup, unrealistic in high-repetition rate scenario.
Limitation of the heating provided by hot electrons
For Ion/proton FI:
Integrated experiments absent, the two attempted so far failed miserably.
Severe limitations in conversion efficiency, especially in presence of large imposion plasmas and cone structure.
Limited contribution provided by the protons, while Carbon stopping occurs at too low densities, not suitable for a lateral hot spot generation.
We searched for different mechanisms

## Slide 23
NIF ignition and introduction to ILE’s FIREX
Brief summary of FIREX-I results, Fast electron and Ion Fast Ignition
NEW FI approach: Direct heating of a compressed, solid DT ball .
GXII and LFEX upgrades
Summary of the TALK
Outline of the talk

## Slide 24
Direct heating of a compressed, solid DT ball (Y. Sentoku)
A new Fast Ignition approach is proposed, involving implosion and direct heating of a solid DT ball by an extreme intensity, PetaWatt, picosecond laser.
Al 0.1µm
DT 250um liquid
(current: CD 100um)
Spike pulse
Foot pulse
1
2
3
4
5
E=6kJ, λ=351nm,
1D-hydro simulation
ρ=100g/cm3
rR=0.219 g/cm2
The maximum achievable density is proportional to the foot/spike ratio
High dynamic range pulse tayloring is required.
6kJ of GXII energy at 3w can compress a 250 um radius solid DT ball to 0.22g/cm2 with foot/spike ratio > 1000

## Slide 25
nc
100nc
10000nc
Implosion of a sold ball by 6kJ/3w
1D-hydro simulation density profile
2D-PICLS simulation
Full PIC:
kinetic physics
Reduced PIC:
collisional
energy
transport
Core plasma:
highly collisional
Corona plasma:
not so collisional
Heat transport
Laser plasma interaction
Plasma profile inserted in the PICLS simulation (Y. Sentoku, N. Iwata, H. Nagatomo)

## Slide 26
Direct heating of a compressed, solid DT ball (Y. Sentoku, N. Iwata )
100 g/cc
Collisional 2D PIC simulation by PICLS
Heating laser: 1 PW, Energy 2.3 kJ, pulse width 2.4 ps, spot diameter 10 um (→ I = 1.23 x 1021 W/cm2, a0 = 30)
Target: DT solid ball imploded by a 6 kJ laser. Initial density profile calculated by a radiation hydro simulation ILESTA-1D.
8000x8000 grids, 5 particles per cell for each ion species, Bremsstrahlung radiation colling included.
ne / nc
40000
0.4
Electron density
Magnetic field Bz
D+ energy density
[GG]
3
-3
x [mm]
200
100
0
y [mm]
200
100
0
100
0
y [mm]
x [mm]
x [mm]
200
100
0
100
0
-100
y [mm]

## Slide 27
The heatwave propagates and heats the compressed core (Y. Sentoku, N. Iwata)
Electron pressure
D+ pressure
alpha yield
Electron heat wave ~ 0.06c
Average ion energy
Te
Density r
The dominant component that determines core heating is the propagation of the heatwave from the LPI region

## Slide 28
Quasi-2D collisional PIC simulation of plasma interface evolution (Y. Sentoku, N. Iwata)
DT plasma
106
105
104
103
102
10
1
0.1
Fully resolve up to 104 nc
120
0
40
80
x [mm]
Laser
a0 = 30,
1 PW
250 fs
2 ps
Electron energy spectrum observed in x > 40 mm
Temporal evolution of plasma density
1 ps
0.5 ps
3.5 ps
Maxwellian fitting
Tp = 15 MeV
250 fs
2 ps
ne / nc
Initial plasma profile
104
103
102
10
1
0.1
0.01
0
20
40
30
x [mm]
102
101
100
10-1
10-2
Electron energy [MeV]
dN/d(log E) (= E dN/dE)
Over 2 ps we observe hole-boring and density profile steepening till it reaches the limit (plasma pressure counteracts the radiation pressure )
Laser light pushes the plasma surface up to the limit density at t ~ 2 ps.
After reaching to the limit density, copious electrons with energies lower than the ponderomotive energy appear.

## Slide 29
LFEX injection
Simulation time limit
Time (ps)
Energy (normalized by LFEX)
Fusion energy output
Fusion yield keeps rising exponentially even after LFEX pulse terminates (Y. Sentoku, N. Iwata)
It appears that we can approach fusion gain of 1 with 2.5 kJ LFEX energy, with intensity > 1x1021W/cm2 and a 6 kJ, 3w compression laser

## Slide 30
NIF ignition and introduction to ILE’s FIREX
Brief summary of FIREX-I results, Fast electron and Ion Fast Ignition
NEW FI approach: Direct heating of a compressed, solid DT ball .
GXII and LFEX upgrades
Summary of the TALK
Outline of the talk

## Slide 31
Upgrades for GXII and LFEX have been funded
Operation system
Oscillator, pre-amplifier
Optics damage repairing
Pulse post compressor
Interaction chamber
Capacitor bank, pulse power switch
Controlling system
Flash lamps
Laser diagnostics
Precision pulse shaping,
smoothed beam profile
Tritium target capability
Precision target positioner
Increase shot rate
Laser energy improvement

## Slide 32
New oscillators with SSD beam smoothing for GXII (Y. Arikawa and GXII team)
t
Arbitral Wave form Oscillator
(MODBOX)
Fiber Spectrum modulator
G1
G2
G3
Spike pulse oscillator
Foot pulse oscillator
10%T
Amp
14.25GHz
4.9GHz
8.4 GHz
I
Arbitral Wave form Oscillator
(MODBOX)
Fiber Spectrum modulator
CW seed laser
SSD-1D
Fiber laser system
SSD-3D
Free space system
Regen Amp
3rd harmonics
t
I
5000
1
200
1
90%R
It will allow for foot/spike ratio of 5000 with 3 direction SSD beam profile smoothing

## Slide 33
SSD-3D + phase plate
Focus beam pattern with random phase plate
Smoothing by spectrum
dispersion SSD
1st direction
2nd direction
3rd direction
Hexagonal shape
Gekko 12 beams
match to the hexagonal focal pattern
N. Miyanaga, G.Miyaji, 2002
3 directional SSD beam smoothing

## Slide 34
Precision Monitors
Focusing
improved focal spot
Current focal spot
Current Near field
pattern monitor
Capacitor bank: Automated gas gap switch system
At OPCPA-AMP: precision excitation laser system improving energy control, uniform intensity distribution, and pulse contrast.
Main AMP : Repolish damaged optics, enabling x3 energy ( 4 kJ @ compressor)
Compressor: Precision on-shot beam monitor,
At target chamber: post compressor
Project leader: S. Fujioka
LFEX upgrades

## Slide 35
Post-compressor for extreme intensity LFEX (A. Morace, Y. Arikawa)
In order to achieve extreme intensities on LFEX, it is required to increase the energy of LFEX to ~ 4kJ, pre-compress the LFEX pulse from 2 ns to 100 ps with the LFEX compressor, and finally compress from 100 ps to 1 ps with a post compressor installed directly in the target chamber.
Compressor
Target
Chamber
OAP
Post-compressor concept
100 ps LFEX @ 4 kJ
1 ps LFEX
Compressor : 2 ns to 1.5 ps, 1kJ in 4 beams focused by a single parabola

## Slide 36
Post compressor concept
The post-compressor is a partially sacrificial system composed by only 4 optics.
We work at damage threshold on the M1, concave parabola, I ~ 6 x1011 W/cm2
We are above damage threshold on the gratings G1 and G2 which will be replaced after every shot
We will work on the final OAP as plasma mirror with intensity ~ 6x 1013 W/cm2
Expected intensity on target ~ 1-5x1021 W/cm2
TCC
40.5 cm
12 cm
40 cm
M1
G1
G2
M2

## Slide 37
A second design being considered allows for co-axial focusing
Reflection from M1 at 90 deg from LFEX, compressor dimensioning remains the same.
M2 will be a f/1 parabola
M1
G1
G2
M2

## Slide 38: Japan–US Collaborative Technical Discussion with Lawrence Livermore National Laboratory
LLNL visit (February 2025)
Discussion with LLNL laser group, Optics group,
Pulse power groups,
Coating on KDP crystals
Precision fiber oscillator
Plasma-electrode
pockels cell (PEPC)
Pulse power switches
Thanks to the great helps by LLNL,
our development are progressed!

## Slide 39
ILE’s strategy: We are refurbishing GEKKO-XII & LFEX lasers. Our facility will demonstrate the heatwave fast ignition with gain ~ 1
Current
2026年
2029年
Refinement
Proof of Principle： NIF
High-efficiency demonstration
FIREX
PRL2020
GEKKO-XII
6kJ
Tailored pulses
II. Achieve high-density implosion
for solid ball explosion
core density 10g/cc → >100g/cc
GEKKO-XII
6kJ
Tailored pulses
PW Laser
3kJ/3ps
Advanced DT Target Development Research
Measurement and improvement of DT mixing ratio
Development of high-quality DT target
I. Demonstrate heatwave heating
& hole boring over critical
density
High rep laser
development
Senju-Lite (10J/100Hz)
III. Integrated Experiment
solid ball implosion + LFEX heating
core density >100g/cc
Demonstration of efficient heating
Ion temperature ~ 10keV + neutron diagnostics
GEKKO-XII
6kJ/3w
pulse shaping
LFEX（4 beam）
3kJ/1.5-6ps
deformable
Gain ~ 1
Design a compact laser fusion with about 100kJ laser energy and with gain > 100.
J-EPoCH
Senju (100J/100Hz)

## Slide 40
Summary
In summary, ILE future strategy for ICF will be focused on the direct heating of compressed, solid DT ball.
This scheme promised to reach gain of 1 using less than 10kJ total laser energy on target.
Upgrades for both GXII and LFEX system will be implemented to achieve the condtions required to access gain 1
We hope to provide you with exciting results in a few years, Thank you!