## Slide 1: Fusion energy research with high power lasers in Europe: from ELI to HiPER+
Leonida Antonio GIZZI
ILIL, INO, Consiglio Nazionale delle Ricerche, Pisa, Italy
also @ ELI-ERIC
2nd INFN School and Workshop on “High Power Lasers for Fundamental Science and Applications” (HPLA2025)

## Slide 2: Inertial fusion energy: where we stand
Foto NASA
Nuclear fusion is the “challenge of challenges” in the energy field.
Laser Fusion is a very promising approach:
  use powerful laser pulses to compress and heat a small fuel capsule until fusion reactions are ignited.
In recent years, we have witnessed extraordinary progress
  the first experiment in the world to achieve net energy gain at the National Ignition Facility (NIF).
This is the beginning of a complex journey.

## Slide 3: Founding principle: fusion reactions
  Among the many possible fusion reactions, only some have practical uses based on their efficiency and the abundance of the "reactants" in nature.
(Temperatura (11600 x °K/keV)
Prop Probabilità

## Slide 4: From fusion reactions to electricity
A fusion reactor converts into electricity the kinetic energy of particles from fusion reactions
D + T → n (14.07 MeV) + 4He (3.52 MeV)

## Slide 5: How laser fusion works
The laser rapidly heats the outer surface → the material explodes outward.
By reaction, fuel is compressed to extreme densities and temperatures and ignites;
This entire process occurs within billionths of a second (inertial confinement).
Indirect drive (ID) uses a cavity to convert laser light into X-rays to ease the compression phase
In direct drive (DD) Laser Fusion many laser beams are focused onto a millimeter-scale capsule containing deuterium and tritium.

## Slide 6: Indirect drive: breakthrough
In December 2022, experiments performed at the National Ignition Facility (NIF) in the U.S. have demonstrated a “net energy gain” from an inertial confinement fusion (ICF) experiment with ID
Gain = 3.15MJ (fusion yield) / 2.05 MJ (laser input energy) = 1.54
Ignition shots
Most recent result: 8.6 MJ

## Slide 7: Experimental evidence of direct drive
Direct drive experiments at omega: 30 kJ
V. Gopalaswamy et al. Nature 2019
V. Goncharov EUROfusion seminar, 2022
Experiments at OMEGA (LLE, Rochester University, US) show a steady progress in the DIRECT DRIVE experiments: recenty, increase of neutron yield by 10 times and energy coupling to the hot spot by 6 times (recent experiments used a deep learning approach to optimize implosions).
Laser direct drive experiments couple 3-6 times more energy to the hot spot compared to the NIF indirect drive experiments
Direct Drive is more subject than DD to the growth and the impact of hydro instabilities which distort the target during implosion, making ignition hard to achieve
Omega Laser
Laboratory for Laser Energetics
University of Rochester

## Slide 8: Challenge: spherical compression
Compression symmetry - The capsule must be compressed in a perfectly uniform way. Even a small asymmetry can prevent ignition.
Hydrodynamic instabilities - Phenomena such as Rayleigh–Taylor instability amplify microscopic imperfections, reducing compression efficiency.
Materials and extreme physics - During the process, matter reaches high-density plasma conditions that are difficult to model and to measure. New theoretical models and advanced diagnostics (e.g. X-ray FEL) are required.
Understanding ignition and burn - Predicting when the plasma “turns on” and how the burn front propagates remains one of the greatest uncertainties in the field.
Compression symmetry and uniformity is a major challenge

## Slide 9: Mitigation strategies
How to mitigate the impact of hydro instabilities in Direct Drive?
Separation of the compression phase and the ignition phase.
Options:
Fast Ignition exotic and non-scalable physics
requires laser
Shock Ignition compatible with present-day laser technology 

## Slide 10: Challenge: laser-plasma interaction
Stimulated scattering instabilities can siphon energy away from the main process and degrade the quality of the implosion;
To mitigate them, an emerging strategy is the use of broadband laser systems
The reduced coherence inhibits these instabilities , improving both symmetry and stability of the compression.
Many physical processes occur in the interaction between laser light and the plasma surrounding the pellet
DOI 10.1088/1741-4326/aab21a

## Slide 11: Parametric instabilities
SRS and TPD generate fast electrons, that can preheat the fuel and/or affect the shock pressure
Laser-Plasma Interaction of ignition pulse (1015-1016 W/cm2) is dominated by parametric instabilities including Stimulated Brillouin Scattering (SBS), Stimulated Raman Scattering (SRS) and Two Plasmon Decay (TPD) – and filamentation.
energy is backscattered by SRS/TPD and SBS (up to ~40-50%) - can increase laser energy requirements
(Laser coherence manipulation, Broadband laser, comb diode lasers…)
Froula et al., Plasma Phys. Control. Fusion 54 (2012) 124016
Is it possible to turn off or limit the growth of LPI ?

## Slide 12: Challenge: laser
IFE requires laser sources with extremely high power, but also high repetition rates (10–15 shots per second), far beyond today’s experimental capabilities.
Broadband laser for suppression of instabilities
Electrical-to-optical wall-plug efficiency above 10%
Diode pumped solid-state lasers or gas lasers under development.
IFE relies on a new generation of high power lasers

## Slide 13: Challenge: reactor
Low-cost fuel capsules - Fuel capsules must be manufactured by the millions per year, with perfect quality - a challenge reminiscent of semiconductor industry scaling.
Reaction chambers and resistant materials - Each shot generates neutrons, X-rays, and debris; materials must withstand extreme conditions for years.
Measurement and control - Systems must operate at the picosecond and micrometer level, to control each experiment in real time.
IFE reactor concept needs new materials and components

## Slide 14: Europe-wide initiatives
2005-2014 European Project “HIPER” (High Power Laser Energy Research Facility)
HiPER, conceived as a large-scale laser system designed to demonstrate significant energy production form ICF, was listed on the ESFRI large scale facility roadmap and awarded preparatory phase funding (2 M€) by the EU with additional funding from STFC, UK, and the Ministry of Education, Czech Republic, and work in-kind from many other partners
The project was based on the assumption that NIF would ignite during the National ignition Campaign (2009-2012)
www.hiper-laser.org

## Slide 15: The EU IFE community
COST Action MP1208 «Developing the Physics and the Scientific Community for Inertial Fusion at the time of NIF ignition» 2013-2017
Laserlab Europe AISBL supports 3 ICF-related groups:
Expert group in ICF/IFE
Expert group in micro-structured materials
Expert group in laser-generated EMP
EUROFusion within Enabling Research projects EUROFusion supports projects related to direct-drive and shock ignition at the level of /year (2017-2024)
24 groups and more than 100 researchers involved throughout Europe

## Slide 16: HiPER+ Research Infrastructure
HiPER+ Consortium
Conceptual Design
To address scientific and technological challenges including: modelling, laser, LPI, facility engeneering etc …
A large scale infrastructure to demonstrate ignition (DD)

## Slide 17: EXPERIMENTAL ROADMAP TOWARDS SHOCK IGNITION IFE
How to approach the final goal of “Performing shock ignition demonstration experiments” ?
Geometry
Spherical
Cylindrical
Planar
Laser Energy
Omega
SG-II
Orion
LULI,
PALS Phelix
ELI
NIF
SG-III
LMJ/PETAL
Gekko
HiPER+RF

## Slide 18
EXTREME LIGHT INFRASTRUCTURE
ELI-Beamlines facility, Prague, Czech Republic
ELI Attosecond Light Pulse Source (ELI-ALPS) in Szeged, Hungary
ELI Nuclear Physics (ELI-NP), Magurele, Romania
(Approx 1 Bln € investment)
A joint effort of the whole laser and plasma community

## Slide 19
19
ELI Facilities
Excellence across three facilities.
ELI Beamlines
High-Energy Beam facility, develops and applies ultra-short pulses of ultra-intense radiation to explore extreme conditions or produce high-energy particles and radiation.
ELI Attosecond Light Pulse Source (ALPS)
Attosecond Light Pulse Source, offers unique time-resolved investigation possibilities for both nonrelativistic and relativistic interaction of light with all the four states of matter.
ELI Nuclear Physics (NP)
Nuclear Physics facility with ultra-intense lasers and brilliant gamma beams (up to 19 MeV) to produce and explore new nuclear states or generate neutron beams.
Dolní Břežany, Czech Republic
Szeged, hungary
Măgurele, romania

## Slide 20
ELI as a medium-scale facility: why it is important for IFE
Fundamental physics studies of IFE:
  EoS, opacities
  Instabilities
  Laser absorption
  Shocks
Training of young scientist
Testbed for diagnostics, targetry, emp, debris etc.
What is HEDP: > 1Mbar or > 1011 J/m3 = 100 J/mm3
Extreme state of matters are of extreme relevancee
for ICF/IFE, astrophysics, geophysics etc.

## Slide 21
L4 ATON laser system at ELI Beamlines
high-energy (1.5 kJ), high-peak power (10 PW)
Mixed Nd:glass (>15nm spectral bandwidth @1w)
Pulse compressor
MLD gratings 1136 l/mm, off plane-of-incidence (3.25°) Littrow geometry
Beam size 620 x 620 mm, fluence 0.4 J/cm2
Gratings 850 x 700 mm made by LLNL
Mirrors phased to gratings G2 and G3
Compressor chamber: 18 m length, 4.2 m height
G1
G3
G2
G4
South tower
North tower
L4-ATON: 1.5kJ/150fs (10PW) @1shot/min target performance (demonstrated – 786J/154fs  5.1 PW)
South Tower
North Tower
Gratings Alignment
L4 Compressor Optics
Full beam size 60x60 cm
Compressor input 30x30 cm
Compressor output
Energy at the compressor input on Oct 1, 2025
Demonstration of 5 PW (Oct 2025): multi-PW laser with the highest energy worldwide!

## Slide 22
Beam profile (31x31 cm)
“Hot state” beam (1shot/min) wavefront error <λ/10 rms
Strehl ratio ≈ 0.7
Grid structure is a diagnostic artefact
FWHM =2.4 ns
71%
of pulse energy
29% of pulse energy
Pedestal length ≈ 7.3 ns
2 ns pulse with pedestal at two different energies
FWHM = 2.4 ns
FWHM ≈ 2.3 ns
89%
84%
77%
of pulse
energy
21%
15%
9%
of pulse
energy
5 ns gap
Double 2.5 ns pulse with various contrast ratio
Example of a sequence of pulses of different energies and lengths requested by users
Examples of pulse temporal profiles requested by users
Close to diffraction limit FWHM ~35 µm, diffr. limit 32 µm
L4n (ns pulse) ATON laser system @ ELI Beamlines
high-energy (1.5 kJ), high-rep,-rate (1shot/min), nanosecond pulses
L4 long pulse in operation – 1.5kJ (0.6kJ @2w)/2-10ns/1shot/2min)

## Slide 23
P3 Plasma Physics Platform (E3) @ ELI Beamlines
1-10PW (L3+L4) & kJ-ns class lasers
L4n-P3: exp platform for HEDP, including ICF/IFE and shock physics
High rep. rate capability at kJ level (up to 1shot/min)
L4n pulse width tuneability (2-10 ns), temporal shaping (~100ps res), and narrow-band vs broadband (~7nm @527nm) options
time-resolved diagnostics for LPI (Raman, Brillouin, TPD), shock physics (VISAR/SOP), and X-ray and particle diagnostics
Targetry: solid, gas, multi-layer, foam, cryogenics, etc.
L4 + L3 as PW backligther in LFL/SFL setup (e.g. Betatron source)
P3 interaction chamber

## Slide 24
Major diagnostic systems for IFE-relevant research @ ELI Beamlines
In front of target: time-resolved
Backscattered radiation (SRS, SBS, TPD)
Around the target: time-resolved
Side-scatter radiation
Behind the target: VISAR/SOP
for EoS studies
Betatron radiation at 90o for shock propagation
& imaging of deuterated targets using X-rays, THz, electrons

## Slide 25: ELI IFE Mission-based Call Proposals: Distribution by Research Topics and Requested ELI Systems
Target and Plasma Interaction Studies
• ELI ALPS: HF PW laser + UFO station
• ELI Beamlines: L4n + L3 lasers + P3 platform
• ELI Beamlines: L4n laser + E3 exp. area, optionally L3 laser
• ELI Beamlines: L4n laser + E3 exp. Area
• ELI-NP: HPLS 1PW+E5, 1PW + E6
Diagnostics & Platform Development
• ELI Beamlines: L3 (L4p) laser + Gammatron beamline + P3 platform
• ELI-NP: HPLS 10PW laser + E6 exp. area
Laser-Driven Fusion Concepts
• ELI ALPS: Sylos3 laser + LEIA-n beamline; HF PW laser + UFO station
• ELI Beamlines: Lasers L4, L3 + Betatron source; Lasers L3 and L4 Sync + P3 platform
Ion and Particle Transport
• ELI ALPS: Sylos3 laser + LEIA-n beamline; HF PW laser + UFO station
• ELI Beamlines: L3 laser + ELIMAIA beamline
• ELI ALPS: Sylos3 laser + LEIA-n beamline
Outcome of the selection expected soon

## Slide 26: Summary
Recent historical progress shows that it is achievable.
Transforming it into a reliable energy source will require a convergence of physics, engineering, advanced materials, and new laser technologies.
Inertial Fusion Energy is an endeavor at the very edge of contemporary technology.
It is a challenge—but also an extraordinary opportunity for a EU-wide collaboration for a staged approach from DD ignition demonstration to the reactor.