## Slide 1
CH4rLiE Annual Meeting
CH4rLiE (PRIN PNRR 2022 -P2022FTF7L)
Updates on barn measurements
Biagini D.1,2, Dinuccio E.1,2
1 DISAFA, Università di Torino
2 INFN Sezione di Torino
Pavia, 28 Gennaio 2025

## Slide 2
Concluded
UNITO Unit
Role in the Project
CH4rLiE (PRIN PNRR 2022 -P2022FTF7L)

## Slide 3
EVALUATION OF CATTLE EMISSIONS IN DIFFERENT BARN CONDITIONS
automatic delta scrapers
DONALISIO - FARM (Volvera, TO)
Reared cows: 310 heads
Naturally-ventilated dairy barn
Slurry removal frequencies: 4 times/day
4 measuring compaigns over the course of a year, covering season variability
4 measuring compaigns over the course of a year, covering season variability

## Slide 4
METHODOLOGY
Measurement of GHG and NH3 emission rates
Ventilation rate
(mᶟ h⁻¹)
Gas emission
(g h⁻¹)
QEPAS + Multipoint sampler
Gas concentration (ppm)
CO2 mass balance method
VR
CIGR, 2002
EMISSION MEASUREMENTS ANIMAL’S BUILDING
CH4rLiE (PRIN PNRR 2022 -P2022FTF7L)

## Slide 5
Measurement of GHG and NH3 emission rates
VR (m3 h-1 animal-1)= Cprod /(CO2 inside – CO2 outside)*10-6
Cprod = 0.185 * ϕtot /1000
0.185 is the amount of CO2 produced by one dairy cow for 1000 W of produced heat
Φtot is the total heat production for one dairy cow, function of:
Daily milk production
Days of pregnancy
Live weight
Average temperature
METHODOLOGY
EMISSION MEASUREMENTS ANIMAL’S BUILDING

## Slide 6
METHODOLOGY
GHG | NH3
CO2 mass balance + QEPAS | 
5 internal sampler point every 10 m equipped with dust filter
2D anemometer to detect the approching wind direction
Quarts-enhanced photoacoustic spectroscopy (QePAS) analyser (A) coupled with a multipoint sampler (B)
A
B
Animal building
Temperature and humidity sensors (Hobo)
1 external sampling point (according to the prevailing WD)
6 mm Ø PTFE tubes
EMISSION MEASUREMENTS ANIMAL’S BUILDING
Equipment

## Slide 7
Quarts-enhanced photoacoustic spectroscopy (QePAS) analyser
measure the vibrational relaxation rate of gas species, employing quartz tuning forks (QTFs) as sound detectors

## Slide 8: Results: temporal and spatial variations in methane concentrations within the barn
CH4 concentration (ppm)
Av. 8.40 ppm
Av. 8.04 ppm
Av. 6.94 ppm
Av. 14.5 ppm

## Slide 9: Results: season variability in average methane concentrations
CH4 concentration (ppm)

## Slide 10: Results: Daily trend in methane concentrations
CH4 concentration (ppm)
16/07/2024 (Summer conditions)

## Slide 11: Some Considerationions
Seasonal Variability:
CH4 concentrations show significant seasonal differences, with the highest levels observed during summer, likely due to increased microbial activity, ration variations, and higher temperatures
Daily Fluctuations:
Diurnal trends influenced by animal activity, with peaks typically occurring after feeding times