## Slide 1
ACCELERATOR TECHNOLOGIES
Challenges for high intensity accelerators
Chris Rogers (STFC Rutherford Appleton Laboratory)
With thanks to many colleagues for valuable suggestions and contributions

## Slide 2: High Intensity Concepts
Many particle physics applications need high intensity accelerated particle beams
  Neutrino oscillation physics
  Meson physics (muons, kaons, pions)
  Baryon physics
  Many more…
  Mostly generated from hadronic interactions → high intensity proton accelerators
Addressing intensity limitations important for current & next generation facilities
  Non-Collider physics @ CERN
  Swiss muon source @ PSI
  Non-European facilities e.g. JPARC, Fermilab
  Other European facilities – FAIR, ESS, ISIS
For many applications, seek highest possible intensities
  Where are the limits?
2

## Slide 3: Limits to High Intensity Operation
Two classes of limit – losses during acceleration and load on beam intersecting devices
Losses during acceleration
  As intensity increases, beam-destructive forces increase i.e. harder to control the beam
  Meanwhile as intensity increases, fractional loss must decrease to maintain 1 W/m
Beam Intersecting Devices
  Must withstand huge energy
  Energy of a speeding truck hitting device every second
  E.g. charge exchange injection & target
3
H-
p
p
Charge exchange
injection
Acceleration loss
& collimation
Target
π, μ, K, ++
p
p
Extraction
Ion source

## Slide 4: Injection Foil
Most proton accelerators do ring injection using charge exchange injection
Accelerate H- in a linac
  Get energy above space charge limit
Strip excess electrons using a foil
  Allows accumulation of proton beam
  Can combine long H- pulse
Limited by heat deposition on foil
  Advanced foil materials
  E.g. nanocrystalline Carbon foils
N. Evans, Operational Experience with Nano-crystalline Injection Foils at SNS, HB2021, 2021
Circulating
protons
Injected H-
Thin foil
Dipoles
4

## Slide 5: Laser Stripping
J-PARC scheme:
  Strip H- → H0 using first laser
  Excite H0 → H0* using second laser
  Strip H0 → p using third laser
  Enhance laser power using resonant laser cavity
SNS scheme:
  Relativistically boosted B-field strips H- → H0
  Further magnet excites H0 → H0*
  Laser finally strips remaining electron H0* → p
P.K. Saha et al, Status of the Laser Manipulations of H- Beam at J-PARC, IPAC2023
V. Danilov et al, Three Step H- Charge Exchange Injection with a narrow-band laser, PRSTAB 6 (2003)
5

## Slide 6: Target
Production of secondary particles by firing protons onto target
  Fixed targets currently in use at neutrino facilities
  Rotating wheels at PSI
Rapid temperature cycling
  Active cooling e.g. forced flow Helium
Extreme radiation damage
  Swelling
  Structural degradation
Horn or solenoid focusing
  Must withstand intense secondary hadronic flux
C. Densham et al, Design of the T2K Target for a 0.75-MW
Proton Beam, HB2010
Credit: PSI
6

## Slide 7: Target – Advanced Concepts
Roland Garoby et al, The European Spallation Source Design, Phys. Scr. 93 014001, 2018
11 m
7
Advanced concepts to move target material away from beam
  Rotating disks
  Conveyors
  Fluidised powders
  Flowing liquid metal targets
T. Davenne et al, Observed proton beam induced disruption of a tungsten powder target, PRAB 21, 2018

## Slide 8: High Intensity Limitations during Acceleration
Space charge
  Particles repulse each other from intrinsic charge
  Causes a defocusing force that is stronger at low energy
  Destroys high intensity beams
Wakefields
  Particles induce EM waves in the beam pipe
  Dependent on properties of beam & beam pipe
  Destroys high intensity beams
Mitigations
  Precise beam shaping
  Detailed analysis of hardware EM properties
  Careful lattice design e.g. to high order multipoles
8
A. Romanov, The IOTA/FAST Facility: Status, Performance, Upgrades, IOTA/Fast Collaboration Meeting 2024

## Slide 9: Simulation Codes
Many important codes
  PyOrbit, Impact, OPAL, Warp, G4Beamline, Zgoubi and many more…
CERN-led Xsuite initiative
  Integration of many different accelerator packages
  Share common code tools
  Bespoke packages for simulating different physics problems
    Accelerator lattice development
    Beam-matter interactions
    Error analysis & correction
    Collective effects
    Many others
https://xsuite.readthedocs.io/en/latest/
9

## Slide 10: Addressing the Challenges at existing facilities
Increase beam power:
  Suppression of space charge
  Increase number of pulses per second (rep rate)
LHC Injectors Upgrade completed 2021
  Upgrade initial linac to 160 MeV H-
  Continuing R&D to high energy complex supporting CERN fixed-target programmes
PSI Cyclotron upgrade ongoing
  Improved RF systems to suppress halo formation
  Enables clean extraction
PIP2 linac at Fermilab under construction
Increased rep rate at JPARC
10
M. Schneider et al, Upgrade of the PSI Injector 2 Cyclotron, Cyclotrons2019

## Slide 11: New facilities under construction
European Spallation Source
  Long pulse proton linac for neutron production
  2 MW, 800 MeV beam in first phase
Facility for Anti-proton and Ion Research
  29 GeV protons
  Multi-GeV/u ions (depending on species)
  Fast ramping superconducting dipoles
  Target stations and storage/cooling rings
11
Credit: ESS
Credit: FAIR

## Slide 12: Advanced Muon Beams
PSI
  Improved solenoids for muon beam transport
  Transverse muon cooling using modified Wien filter
  Longitudinal frictional muon cooling
  Under construction
Fermilab advanced muon facility (proposed)
  High acceptance storage ring
  Time-Energy phase rotation
  At planning stage
A. Antognini et al, Phase space compression of a positive muon beam in two spatial dimensions, https://arxiv.org/abs/2410.21162
12
D. Hitlin, The Advanced Muon Facility, CLFV23

## Slide 13: Muon Collider source
Muon collider proton driver high power proton source
  2 MW proton source comparable to state of the art
  Short proton pulse
  Proposed to host high intensity experimental programme
13
D. Schulte et al, The Muon Collider, 2025

## Slide 14: Advanced Neutrino Beam Facilities
Two new accelerator facilities proposed for neutrino production
ESSnuSB
  Add H- capability & Accumulator ring to ESS
  Short baseline experiments
  Long baseline oscillation experiment
nuSTORM
  Store O(GeV) muons
  Create high intensity & well-characterised neutrino beam for cross-section measurement
14
M. Drakos et al, ESSnuSB input to 2026 ESPPU
J.B. Lagrange et al, Racetrack FFAG muon decay ring for nuSTORM with triplet focusing JINST 13 no 9, 2018

## Slide 15: Synergy with other programmes
Many shared technologies with colliders
  Many linac upgrades benefit from linear collider cavity R&D
  Low energy muon beam cooling may be beneficial for muon collider
  Linac4 supports HL-LHC operation
  FCCee collimators for Beamstrahlung
Proton accelerators are important facilities for chemistry, material, nuclear and life science
  J-PARC multiphysics facility – Materials and Life Science experimental facility
  PSI μSR beamlines and neutron spallation source
  Other non-HEP facilities
    ISIS (UK), ESS (Sweden), SNS (US), CSNS (China) & many others
D. Schulte et al, The Muon Collider, 2025 (Abridged)
S. Aritome et al, Acceleration of cooled positive muons by a Radio-frequency cavity, PRL 134, 2025
15

## Slide 16: Conclusion
High intensity facilities important for delivering secondary particle sources
  Neutrinos, pions, muons, kaons, neutrons …
High intensity facilities major outcome of the 20th century HEP programme
  This is your technology
Vibrant community dedicated to delivering beams at the highest intensities
  Huge challenges
  Overcome by brilliant teams
Essential to support ongoing R&D to maintain delivery of higher and higher fluxes
  CERN
  Other European facilities
  Facilities outside Europe
16

## Slide 17: Further Information
24th June 2025
Open Symposium on the European Strategy for Particle Physics

## Slide 18: Synergy with other Sciences
Accelerator technology major outcome of HEP programme in C20th
Proton accelerators are important facilities for chemisty, material, nuclear and life science
  J-PARC multiphysics facility – Materials and Life Science experimental facility
  PSI μSR beamlines and neutron spallation source
  Other non-HEP facilities
    ISIS (UK), ESS (Sweden), SNS (US), CSNS (China) & many others
High intensity essential to improve resolutions
  Very active R&D ongoing between major labs
Credit: ICRU
18

## Slide 19: Strategic Considerations
Intensity frontier has important synergies with other programmes
  Return on investment & impact important for any facility
In the event of a future e+e- collider, should Europe support intensity frontier?
  At CERN?
  At other European facilities? Noting heavy oversubscription
  At other facilities outside Europe
19

## Slide 20: Synergy with Collider programme
Important synergy between high intensity non-collider and collider facilities
Many shared technologies
  Many linac upgrades benefit from linear collider cavity R&D
  Low energy muon beam cooling may be beneficial for muon collider
  Linac4 supports HL-LHC operation
  FCCee collimators for Beamstrahlung
D. Schulte et al, The Muon Collider, 2025 (Abridged)
S. Aritome et al, Acceleration of cooled positive muons by a Radio-frequency cavity, PRL 134, 2025
20
S Candido, presentation at FCC week, 2025

## Slide 21: Synergy with other Sciences
Accelerator technology major outcome of HEP programme in C20th
Proton accelerators are important facilities for chemisty, material, nuclear and life science
  J-PARC multiphysics facility – Materials and Life Science experimental facility
  PSI μSR beamlines and neutron spallation source
  Other non-HEP facilities
    ISIS (UK), ESS (Sweden), SNS (US), CSNS (China) & many others
High intensity essential to improve resolutions
  Very active R&D ongoing between major labs
Credit: ICRU
21

## Slide 22: Mitigations
Mitigation of wake-field driven losses requires great care
  Suppress wakefield build-up by controlling EM properties of beam pipe
  E.g. careful design of accelerator equipment
Precise beam shaping
  Beam painting techniques during injection
  Second (and higher) harmonic RF cavities
Careful choices in lattice design can reduce impact of space charge
  Controlling field up to high order multipoles
  Damping of resonance effects
  E.g. IOTA/FAST test facility
A. Romanov, The IOTA/FAST Facility: Status, Performance, Upgrades, IOTA/Fast Collaboration Meeting 2024
22
M R Harold, A possible upgrade for ISIS, PAC97

## Slide 23: PSI High Intensity Muon Beamline
Improved muon beam transport
  Solenoid focused transport channel
Muon beam cooling
  Compression of horizontal and vertical beam by modified Wien filter
  Compression of longitudinal beam by frictional cooling
A. Antognini et al, Phase space compression of a positive muon beam in two spatial dimensions, https://arxiv.org/abs/2410.21162
A. Antognini et al, Phase space compression of a positive muon beam in two spatial dimensions, https://arxiv.org/abs/2410.21162
23

## Slide 24: Advanced Muon Facility
Fermilab proposes advanced muon facility
  High acceptance storage ring and energy-time phase rotation
    Make bunch longer but with smaller energy spread
  Strongly reduced energy spread of muon beam
D. Hitlin, The Advanced Muon Facility, CLFV23
24

## Slide 25: Addressing the Challenges at existing facilities
LHC Injectors Upgrade
  Upgrade initial linac to 160 MeV
    Bring energy above space charge limit
  Upgrade to charge exchange injection
  Upgrades to acceleration chain to support higher power
Serves both high energy and high intensity programme
Completed 2021
25

## Slide 26: Fermilab Synchrotron
PIP-II Upgrade: New linear accelerator to 800 MeV
  Get above space charge limit
  Adjustments to boosters to manage new energy/current
  Deliver 1.2 MW beam power on target
Studying options to go beyond 2 MW
  Accelerator Complex Evolution
M. Ball et al, The PIP-II CDR, 2017
26

## Slide 27: JPARC Synchrotron
Steady increase in achieved beam current
  Detailed modelling of the accelerator
  Understanding of loss-generating processes
  Improved injection systems
More than double pulse frequency (rep rate)
Further improvement in beam performance
Credit: J-PARC
Credit: J-PARC
27

## Slide 28: PSI Cyclotron
Direct extraction of accelerated bunches needs good bunch separation
  Space charge causes halo formation
  Beam hits the extraction septum
Stronger accelerating RF
  Blocks the space charge smearing
  Accelerates faster than space charge smearing
  Injector upgrade complete 2026
  Main ring upgrade in design phase
M. Schneider et al, Upgrade of the PSI Injector 2 Cyclotron, Cyclotrons2019
C. Baumgarten et al, PSI Injector and the 72 MeV Transfer Line: MinT-Simulations vs Measurements, Cyclotrons2019
28