## Slide 1
PLENARY / Large-scale accelerator projects at CERN, part I
FCC-hh
Frank Zimmermann (CERN)
Warm thanks to the FCC Collaboration, and in particular, to Bernhard Auchmann, Amalia Ballarino, Michael Benedikt, Jean-Paul Burnet, Massimo Giovannozzi, Mike Koratzinos, Elliot Lipeles, Michelangelo Mangano, Thys Risselada, Gustavo Perez Segurana, Florian Sonnemann, and Ezio Todesco !

## Slide 2
hadron collider peak luminosity versus centre-of-mass energy
past & present hadron colliders
HL-LHC collider
under construction
the proposed FCC-hh

## Slide 3
future circular hadron collider FCC-hh
Main parameters FSR 2025
FCC-hh functional layout
parameter | FCC-hh | FCC-hh CDR | HL-LHC
collision energy cms [TeV] | 85 | 100 | 14
dipole field [T] | 14 | 16 | 8.33
circumference [km] | 90.7 | 97.8 | 26.7
beam current [A] | 0.5 | 0.5 | 1.1
synchr. rad. per ring [kW] | 1200 | 2400 | 7.3
peak luminos. [1034 cm-2s-1] | 30 | 30 | 5 (lev.)
events/bunch crossing | 1000 | 1000 | 132
stored energy/beam [GJ] | 6.5 | 8.3 | 0.7
integr. luminosity / IP [fb-1] | 20000 | 20000 | 3000
Parameter optimization to lower electricity consumption (~max. consumption of FCC-ee)
Magnetic field considered realistic with today’s technologies (Nb3Sn, ~14T, 1.9 K)

## Slide 4
FCC-hh beam optics perfectionated for highest energy !
M. Giovannozzi, G. Perez Segurana, T. Risselada, E. Todesco
~275m
 | CDR cell 12-dipole | 12-dipole | 16-dipole
# dipoles | 4668 | 4288 | 4464
Cell length [m] | 213.030 | 213.030 | 275.792
Circumference [km] | 97.75 | 90.657 | 90.657
CM energy @14T [TeV] | 88.477 | 81.275 | 84.611
Short Straight Section
regular arc cell

## Slide 5
Combined-function main magnets
Separate-function main magnets
# MB/half-cell
Flat top energy
optimisation of main magnet length
M. Giovannozzi, G. Perez Segurana, E. Todesco
energy reach and aperture clearance for different injection energies

## Slide 6
FCC-hh injector options
superconducting machine in the SPS tunnel (scSPS)
modified faster-ramping LHC
new 4 T machine in the LHC tunnel
2 T superferric machine in the LHC tunnel (1.75 TeV, not shown in the table), resulting energy swing x14, similar to LHC (~15)
 | unit | scSPS | modif. LHC | 4 T LHC
circumference | km | 6.8 | 26.7 | 26.7
#apertures |  | 1 | 2 | 1
injection energy | GeV | 26 | 450 | 450
extraction energy | TeV | 1.3 | 3.3 | 3.3
injection field | T | 0.12 | 0.6 | 0.6
maximum field | T | 6 | 6 | 6
energy/field swing |  | 50 | 7 | 7
#dipoles |  | 372 | 1232 | 1232
#bunches |  | 640 | 2600 | 2600
stored energy | MJ | 15 | 167 | 167
collider filling time | min | 37 | 46 | 39

## Slide 7
FCC-hh instantaneous & ideal integrated luminosity over 24 h
initial luminosity ; peak luminosity , initial event pile up ; peak pile up , optimum physics run time ; ideal luminosity / day ; luminosity / year with, conservatively, 160 days of operation / yr & 70% machine availability [instead, with 185 days of physics beam operation and 80% availability the annual integrated luminosity of FCC-hh would be ~30% higher].

## Slide 8
FCC-hh – SR power leveling !?!
=5 MW
2 MW
=73 TeV
=85 TeV
=5 MW
2 MW
=73 TeV
=85 TeV
over one day: ~8.5 fb-1 at 73 TeV and 3.5 fb-1 at 85 TeV
Leveling synchrotron radiation (SR) power: start with higher current and highest luminosity – up to maximum pile up – at lower energy and ramp up energy when current has decreased – either in discrete steps (below) or continually
Strategic Joint Meeting of the HFCC, Stony Brook University, , 8–9 Nov 2024
E. Lipeles
ramp
12 → 14 T
turnaround

## Slide 9
technical readiness and R&D requirements for FCC-hh
Component /Subsystem | TRL | Main parameter to be improved | Improvement factor | R&D effort (CERN contributions) |  | 
 |  |  |  | Personnel [FTEy] | Material [MCHF] | Timescale [years]
Nb3Sn conductora | 7 | Cost & industrialisation (more manufacturers) | 3 | 10 | 30 | 7
Nb3Sn magnet short model | 6 | max. fieldb | 20% | 100 | 20 | 5
Nb3Sn scaling to 5 m | 5 | length | 3 | 100 | 40 | 10
Nb3Sn scaling to 15 m | 4 | length | 3 | 100 | 100 | 15
HTS magnet short model 20 T | 3 | fieldc & all accelerator magnet features | 5-10 | 100 | 50 | 10
HTS long magnet 20 T | 1 | length | 15 | 100 | 150 | 25
aThis includes only contracts to lower the price and to have more manufacturers.
bTarget of 15 T, for operation at 14 T.
c2 to 4 T already achieved, but not with all requirements.
E. Todesco, B. Auchmann

## Slide 10
E. Todesco, B. Auchmann
14 T Nb3Sn “accelerated” roadmap: short models & scaling in length
Ongoing
12 T and 14 T short models
Short model program on two selected designs
(>5 each type)
`25
`26
`27
`28
`29
`30
`31
`32
`33
`34
`35
`36
`37
`38
`39
`40
`41
RunIII
HL-LHC RunIV
HL-LHC RunV
Selection of final design
to start long magnets
5-m-long prototypes
(>5 each type)
15 m long prototypes (>5)
`42
`43
`44
`45
`46
`47
`48
`49
`50
`51
Industrialization (pre-series magnets)
Production and test
Installation and commissioning
`52
`53
`54
Tender
for the series
First selection
of design
Feedback
HL-LHC operation
Select the design by 2028/29 (first indications from HFM tests in 2026-2027)
Short model program to verify reproducibility and optimize manufacturing processes: in 2029-2031
Scaling in length in two steps: TRL 7 achieved between 2032 and 2040
Industrialization for final magnets, with pre-series
9 years of production, installation and commissioning in parallel
2055 as possible date for FCC-hh start as a standalone project

## Slide 11
Ongoing
12 T and 14 T short models
(7 designs, 1 or 2 of each type)
Short model program on two selected designs
(>5 each type)
Selection of final design
to start long magnets
`25
`26
`27
`28
`29
`30
`31
`32
`33
`34
`35
`36
`37
`38
`39
`40
`41
RunIII
HL-LHC RunIV
HL-LHC RunV
5-m-long prototypes
(>5 each type)
15 m long prototypes (>5 each type)
`42
`43
`44
`45
`46
`47
`48
`49
`50
`51
Industrialization (pre-series magnets)
Production and test
Installation and commissioning
`52
`53
`54
Tender
for the series
First selection
of design
14 T Nb3Sn further “accelerated” roadmap w. early industry involvement & parallelisation
this roadmap indicates 2051 as possible date for FCC-hh start as a standalone project
E. Todesco

## Slide 12
Demonstrators: magnets not having all features of a short model, but proving a part of the technology
  RMM, based on block design, 50 mm aperture, but without flared ends, very large coil (not affordable for FCC)
  reached 17T and 15.7 T in stable operation; it proves that technology can go there !
  launched by FCC in the CDR phase (well before HFM)
Work launched by D. Tommasini, WP Leader J.-C. Perez
what has been achieved
D. Tommasini, E. Todesco, B. Auchmann

## Slide 13
FCC-hh High-Field Magnet Nb3Sn and HTS R&D ongoing
Nb3Sn:
12- and 14-T short demonstrators
different coil geometries
tests scheduled for 2026
HTS R&D in various domains:
REBCO and IBS Conductor R&D
racetrack coil developments
E. Todesco, B. Auchmann

## Slide 14
A. Ballarina
ReBCO – Why ?
ReBCO
performance refers to conductor recently procured by CERN in unit lengths > 200 m.
Cost (E/m) reduced by a factor ~3 in the last two years

## Slide 15
ReBCO production plan in China – Shanghai Superconductor
Amalia Ballarino, Bai Song
>5x rest of the world

## Slide 16
 |  | Energy c.o.m. | Field | Current density | Ampere turns per meter of magnet | Magnet lenght | Number of magnets | Total
 |  | (TeV) | (T) |  | (A) | (m) | (adim) | (TA m)
LHC | Nb-Ti | 7.0 | 8.3 | 380/480 | 3800 | 14.3 | 1232 | 0.067
FCC-hh | Nb3Sn | 90 | 14 | 360 | ~8000 | 14.3 | ~4500 | ~0.5
FCC-hh | HTS | 125 | 20 | 400 | ~14000 | 14.3 | ~4500 | ~0.9
SPPC | HTS | 125 | 20 | ~400 | ~14000 | 14.3 | ~4500 | ~0.9
Order of 0.5 to 1 TA m: half to one million of km of cable carrying 1 kA
  Equivalent to 1 kA superconducting cable/wire connecting 1.5 to 3 times the distance of the Earth to the Moon
How much ReBCO might we need to build an FCC-hh ?
E. Todesco
Applied Superconductivity Conference, SLC, 4 Sept. 2024

## Slide 17
PRE-SERIES
CANAVASSING
Demonstrators to select cable
and design
SCOPING
Short model ≥14 T
Selection of cable and
insulation technology
`25
`26
`27
`28
`29
`30
`31
`32
`33
`34
`35
`36
`37
`38
`39
`40
`41
RunIII
HL-LHC RunIV
HL-LHC RunV
FEASIBILITY
Reproducibility and first scaling in length
`42
`43
`44
`45
`46
`47
`48
`49
`50
`51
PROTOTYPING
INDUSTRIALIZATION
`52
`53
`54
Proof of short model
with all requirements
Proof of reproducibility
and first long magnets
HTS roadmap
Target: by 2035 a proof of a short model dipole with all features for FCC
  Aperture, field ≥14T, field quality, protection, …
Target: TRL 7 in 2040-2045
This timeline gives FCC-hh operation in 2070
B. Auchmann, E. Todesco

## Slide 18
resource requirements – capital cost and operation
Domain | FCC-hh Cost [MCHF]
FCC-ee dismantling | 200
Collider* | 13400
Injectors and transfer linear | 1000
Civil Engineering | 520
Technical infrastructures | 3960
Experiments | N/A
Total | 19080
Cost summary table in 2024 MCHF for the construction of FCC-hh.
The annual cost of operation has not been determined.
The cost of electricity is of order 150–200 MCHF p.a.
The human resources required for FCC-hh have not been estimated.
*target price of 2.0 MCHF per 14.3 m long magnet with 1.0 MCHF of conductor, 0.5 MCHF for assembly, and 0.5 MCHF for components
A. Unnervik, F. Sonnemann, et al.

## Slide 19
FCC-hh power demand by technical systems at 85 TeV beam centre-of-mass energy
FCC-hh power demand during different operational periods for operation at collision energy of 85 TeV, with cryo eco-mode
Environmental impact (peak & integrated energy consumption)
system | power [MW]
radiofrequency | 17
cryogenics | 207
cooling & ventilation | 40
magnet powering | 33
experiments | 24
data centre | 8
general services | 26
total | 355
period | days / year | power [MW]
shutdown | 120 | 122
technical stop | 10 | 122
downtime | 37 (=185*0.2) | 122
commissioning | 30 | 324
machine development | 20 | 324
beam operation | 148 (=185x0.8) | 355
J.-P. Burnet et al.

## Slide 20
FCC-hh total annual energy consumption:
<2.5 TWh for 1.9 K Nb3Sn
<2.0 TWh for Nb3Sn magnets at 4.5 K
Cryogenic parameters – 1.9 and 4.5 K options
Parameter | 1.9 K | 4.5 K
Circumference [km] | 90.7 | 90.7
Dipole field [T] | 14 | 14
Centre of mass energy [TeV] | 85 | 84
Sync. Rad. for 2 beams [MW] | 2.4 | 2.4
Magnet temperature [K] Beam screen temperatures [K] | 1.9 [40 – 60] | 4.5 [40 – 60]
Helium Cryogenic Capacity @ 4.5 K equivalent [kW] | 1040 | 698
Number of cryo islands [-] | 8 | 8
Number of cryoplants in total [-] | 16 | 16
Arc cooling length [km] | 16 x 4.9 = 78.4 km | 16 x 4.9 = 78.4 km
Electrical power [MW] | 206 | 139
Helium inventory [tons] | 820 | 390
P. Borges de Sousa

## Slide 21
CO2 equivalent cost of construction and operation
domain / activity | GHG [kt CO2]
CE underground | 50
CE surface sites | 10
Accelerator hardware | 1500a
Electricity consumption during operation pear year | 28-42 (22-32 for 4.5 K)
Number of years of operation | 25
Total | 2100-2600
Average/yr for 35 year lifecycle | 60-75
GHG emissions for FCC-hh following FCC-ee
a1234 kt CO2(eq) for 366 kt of raw material used for the arc dipoles and quadrupoles (cold masses and cryostats) based on EPDs of raw materials available today on the market.
G. Arduini, J. Gutleber, R. Losito, et al.

## Slide 22
timeline
FCC-hh timeline as a second phase after FCC-ee.
Fastest possible FCC-hh timeline as a stand-alone project.
Milestone | Date
Conceptual design study | 2014-18
Definition of placement scenario | 2022
Feasibility Report ready | 2025
Main technologies R&D completion | 2054
Technical Design Report ready | 2054
Latest Project Approval | 2054
Environmental evaluation & project authorization processes | 2054-2058
Industrialisation & magnet production | 2054-2069
Civil engineering – collider | 2060-2068
FCC-ee dismantling | 2063-2064
TI installation – collider | 2065-2069
Accelerator installation – collider | 2068-2072
HW commissioning – collider | 2071-2073
Beam commissioning – collider | 2073
Physics operation start | 2074
Milestone | Date
Conceptual design study | 2014-18
Definition of placement scenario | 2022
Feasibility Report ready | 2025
Latest Project Approval | 2033
Environmental evaluation & project authorization processes | 2026-35
Main technologies R&D completion | 2037
Technical Design Report ready | 2037
Industrialisation & magnet production | 2038-2053
Civil engineering – collider | 2037-2046
TI installation – collider | 2043-2050
Accelerator installation – collider | 2046-2052
HW commissioning – collider | 2049-2053
Beam commissioning – collider | 2054
Physics operation start | 2055

## Slide 23
timeline in graphical form
FCC-hh timeline as a second phase after FCC-ee.
Fastest possible FCC-hh timeline as a standalone project.

## Slide 24
a few take-home messages
FCC-hh as FCC’s 2nd stage, possibly based on HTS, could start operation in ~2074; it will be a formidable machine, SR leveling etc.
FCC-hh based on 14 T Nb3Sn magnets could start operation in ~2055, centre-of-mass energy ~85 TeV, as a standalone project
Higher magnet temperature of 4.5 K, or even 10 K (HTS), reduces the electrical power required; important for societal acceptance
Worldwide HTS conductor development driven by other fields & applications is expected to lower the cost of future HTS magnets

## Slide 25
spare slides

## Slide 26
A 14 T magnet for FCC must reliably deliver 15-15.5 T on the test bench. (Similarly, 16 T magnets would have to deliver 17-17.5 T - difficult given the decrease of Nb3Sn Ic at high fields.)
The 16 T target considered in the FCC CDR (2018/19) as attainable on paper only with parameters that go beyond what has been found to be good engineering in HL-LHC. The CDR designs for 16 T had
  up to 200 MPa coil stress (risky, given HL-LHC experience!),
  a relatively small margin of 14% to critical field/current (as compared to 22% in HL-LHC; 14% margin in the LHC comes with a larger enthalpy margin due to the presence of superfluid helium inside the coil; Nb3Sn coils have to be impregnated and cannot benefit from helium heat capacity),
  and the designs used a conductor with aspirational properties (1500 A/mm2 at 16 T, 4.2 K) that have not been demonstrated yet in a multi-filamentary wire, much less in industrial production (SotA is 1200 A/mm2 at 16 T, 4.2 K).
The updated 14 T target allows to
  increase operational margins from 14 to 20%
  reduce coil stresses to about 150 MPa, deemed reasonable based on HL-LHC experience
  use industrially available conductor (we continue to work on improved performance wires, but now with the goal of building more compact and thus cheaper coils)
  reach 85 TeV c.o.m energy with an improved filling factor, and potentially 90 TeV if we can improve more (e.g., stronger HTS sextupoles, etc.)
  reduce the synchrotron radiation by 50% for 15% lower c.o.m. energy, which helps to reach the accelerator-wide sustainability goals
  substitute a sizable part (up to 50%) of the coils' conductor with the much cheaper Nb-Ti, thus reducing dramatically the conductor cost. (The same is not possible for 16 T magnets; this was studied in EuroCirCol)
  In short, the updated parameters and the 14 T field targe are based on experience gathered after the CDR (2019).
why 14 T dipoles ?
E. Todesco, B. Auchmann

## Slide 27
physics coverage: 85 TeV vs 100 TeV
M. Mangano
Going from 85 to 100 TeV extends by 20% the possible discovery reach at the highest masses and increases by similar amounts the production rates for Higgs bosons or other SM objects. The critical targets that defined the 100 TeV goal could be fulfilled with improved detector performance at 85 TeV to compensate for the slight rate loss. This includes:
the precision targets of Higgs measurements (which are by and large dominated anyway by experimental systematics), including the Higgs self-coupling measurement
the exploration of the full theoretically-allowed mass range for WIMP DM candidates
the exploration of BSM models with a strong first-order phase-transition
Where 100 TeV gave us an extra edge and safety buffer (e.g. for the detection of the higgsino WIMP DM candidate, where the theoretical upper limit is around 1.1 TeV and 100 TeV gives sensitivity up to 1.3 TeV), 85 TeV can still make it, although counting on improved detector sensitivity (eg at 85 TeV we just make it to 1.1 TeV for the higgsino). If 85 TeV give more operational margin for the operation of Nb3Sn dipoles, 100 TeV give more operational margin in terms of exploration and measurement precision.
The example above of the higgsino indicates that further reducing further the energy below 80-85 TeV starts getting us in a region where the complete coverage of interesting regions of BSM parameter space cannot be guaranteed. As we go down below 80 TeV we could in principle increase the luminosity, since synchrotron radiation is reduced and the luminosity could double wrt the 85/100 TeV luminosity. This allows to partially compensate for the lower energy, but ability to cope with the challenge of operating with a pileup of 2000 is well beyond what we can assess today.
What is certainly lost at 85 TeV, which cannot be regained, is sensitivity to resonances in the 40-45 TeV mass range… However, we have no compelling model today that points to this specific mass range as a mandatory target. Incidentally, if a 40 TeV Z' existed, 85 TeV would at least show a few sigma evidence, even though it could not make it to the full 5 s discovery that is possible with 100 TeV.

## Slide 28
FCC-hh integration – it fits into the 5.5 m tunnel !
F. Valchkova

## Slide 29
Chao Yao and Yanwei Ma,
Superconducting materials: Challenges and opportunities for large-scale applications,
iScience 24, 102541, June 25, 2021
Main applications of superconducting power and magnetic technologies

## Slide 30
illustration & conductor forms for practical superconducting materials
Chao Yao and Yanwei Ma, iScience 24, 102541, 2021