## Slide 1: High-Gradient Wakefield Accelerators
M. Turner on behalf of the Wakefield Accelerator Community
1

## Slide 2: High-Gradient Wakefield Accelerators
Includes all concepts that can achieve an acceleration gradient > 1 GeV/m
  High gradients → Compact accelerators → Potentially lower cost & environmental footprint*
Wakefields in Plasma
Wakefields in Dielectric Structures
Laser Driven
Beam Driven
Laser Driven
Beam Driven
Center of the HEP effort: wakefields in plasma  > GeV/m gradients demonstrated
  Dielectric structures may have advantages for certain functions
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025
* than a linear accelerator based on RF acceleration technology, at the same energy
2 / 15
Also see talk by M. Titov, C. Bloise
Notes: 2

## Slide 3: Wakefield Accelerator Pillars
Light sources, e.g. FELs
Medical
National security
Radiation generation
Higgs factory*
Energy frontier linear collider (e.g. 10 TeV)
Fixed target experiments
Injector for a synchrotron/collider
Collider component
Test beams
Applications
Wakefields for PP/HEP
Colliders Based on Wakefield Technology
Near-Term
Mid-Term
Long-Term
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025
3 / 15
* if still relevant
Also see talk by J. List
Notes: 3

## Slide 4: Outline
Summary & Conclusions
Timeline & Plans
Progress since the last ESPP
Possible HEP Contributions
23.06.2025
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
Applications & Collider
Design Studies

## Slide 5: Outline
Summary & Conclusions
Timeline & Plans
Progress since the last ESPP
Possible HEP Contributions
23.06.2025
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
3 Highlights
Applications & Collider
Design Studies

## Slide 6
1. Collider Relevant Beams Can Now Be Simulated with Open-Source Codes
4 / 15
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025
8 hrs on 256 GPUs Perlmutter (NERSC)
3D, full-PIC
Modelling of 50 multi-GeV stages
  Idealized transport
  Low witness bunch charge
Fedeli L, Huebl A, et al. SC22: 2022. DOI:10.1109/SC41404.2022.00008
Open source https://github.com/Angel/FP/Wake-T moving soon to https://github.com/Wake-T/Wake-T
Ferran Pousa et al., in preparation
Numerical convergence: 7 min on a CPU core
2D cylindrical, quasistatic
Beams with nm-scale emittance including ion motion, on a laptop
E.g. using:
J-L Vay et al., WarpX MS FY23.1 and FY23.2 (2023);
2022 Gordon Bell Prize: one of the most prestigious awards in high-performance computing.
Numerical convergence: 9 hrs on a NVIDIA 100 GPU
Notes: 6

## Slide 7: Progress in Simulation Tools Enables Collider Physics Studies
4 / 15
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025
Collider Parameter Optimization
 and parameter tuning using, e.g., machine learning
Bayesian optimisation of machine parameters
Enables transverse tolerances studies
Chen et al, TUPS012, ABEL: the Adaptable Beginning-to-End LINAC Simulation Framework, Proceedings of IPAC (2025)
Adli et al, TUPS011, Transverse Tolerance in the Plasma-Wakefield Acceleration Blowout Regime, Proceedings of IPAC (2025)
Notes: Add logos, add also desy result,
7

## Slide 8: 2. Progress in Plasma Source Development
1-10 m long scalable plasma sources demonstrated
1 m long Helicon Plasma
2x107 discharges
10-150 Hz operation
ceramic
Low voltage solid-state discharge system
 MHz repetition rate
Plasma parameters, e.g.:
Length
Repetition rate
Shape
High repetition rate (up to MHz) sources demonstrated
HOFI (Hydrodynamic Optical Field Ionized) plasma channels
A. Picksley et al., Phys. Rev. Lett. 133, 255001 (2024).
J. E. Shrock et al., ,” Phys. Rev. Lett. 133, 045002 (2024).
R. J. Shalloo et al.,,” Phys. Rev. E 97, 053203 (2018).
A. Picksley et al.,,” Phys. Rev. E 102, 053201 (2020).
A. Alejo et al., Phys. Rev. Accel. Beams 25, 011301 (2022)
1 m long helicon plasma source
10 m long discharge plasma source
Destruction-free guiding structures enable 10 GeV electron energies in laser-driven plasma wakefield accelerators.
5 / 15
D’Arcy, R., et al. Recovery time of a plasma-wakefield accelerator. Nature 603, 58–62 (2022).

## Slide 9: 3. Progress in Experiments Highlights from Single Stage Experiments  Laser-Driven
6 / 15
Energy
Beam Quality
Efficiency
Winkler, P. et al. Active energy compression of a laser-plasma electron beam. Nature 640, 907–910 (2025).
Energy spread and jitter below permille level by employing active stabilization
 Laser to electron conversion efficiency of at least ∼30%
 Multi-GeV energy gain
E. Rockafellow et a;., High charge laser acceleration of electrons to 10 GeV
NIM A, Volume 1077, August 2025, 170586
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025
Matched Guiding and Controlled Injection in Dark-Current-Free, 10-GeV-Class, Channel-Guided Laser-Plasma Accelerators
A. Picksley et al., Phys. Rev. Lett. 133, 255001 (2024)
 ~10 GeV energy gain over 10 cm
 Multiple acceleration regimes that may be difficult to control
 ~9.2 GeV energy gain over 30 cm
 Laser-created ‘free-standing’ plasma channels that can be recreated at the repetition rate of the laser
 Multiple independent results
C. Aniculaesei et al., The acceleration of a high-charge electron bunch to 10 GeV in a 10-cm nanoparticle-assisted wakefield accelerator. Matter Radiat. Extremes 2024; 9 (1): 014001
Notes: Add logos, add also desy result,
9

## Slide 10: 3. Progress in Experiments Highlights from Single Stage Experiments  Beam-Driven
6 / 15
Energy
Beam Quality
Efficiency
Winkler, P. et al. Active energy compression of a laser-plasma electron beam. Nature 640, 907–910 (2025).
Energy spread and jitter below permille level by employing active stabilization
 Laser to electron conversion efficiency of at least ∼30%
 Multi-GeV energy gain
E. Rockafellow et a;., High charge laser acceleration of electrons to 10 GeV
NIM A, Volume 1077, August 2025, 170586
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025
Matched Guiding and Controlled Injection in Dark-Current-Free, 10-GeV-Class, Channel-Guided Laser-Plasma Accelerators
A. Picksley et al., Phys. Rev. Lett. 133, 255001 (2024)
 ~10 GeV energy gain over 10 cm
 Multiple acceleration regimes that may be difficult to control
 ~9.2 GeV energy gain over 30 cm
 Laser-created ‘free-standing’ plasma channels that can be recreated at the repetition rate of the laser
 Multiple independent results
C. Aniculaesei et al., The acceleration of a high-charge electron bunch to 10 GeV in a 10-cm nanoparticle-assisted wakefield accelerator. Matter Radiat. Extremes 2024; 9 (1): 014001
 Emittance preservation at micron level for 40 MeV energy gain (on top of 1 GeV)
 ~60% driver depletion
C Zhang et al 2024 Plasma Phys. Control. Fusion 66 025013
 42% local energy transfer efficiency
C. A. Lindstrøm et al., Phys. Rev. Lett. 126, 014801 (2021)
Lindstrøm, C.A. et al. Emittance preservation in a plasma-wakefield accelerator. Nat Commun 15, 6097 (2024)
Notes: Add logos, add also desy result,
10

## Slide 11: 3. Progress in Experiments Highlights from Single Stage Experiments
6 / 15
Energy
Beam Quality
Efficiency
Matched Guiding and Controlled Injection in Dark-Current-Free, 10-GeV-Class, Channel-Guided Laser-Plasma Accelerators
A. Picksley et al., Phys. Rev. Lett. 133, 255001 (2024)
 ~10 GeV energy gain over 10 cm
 Multiple acceleration regimes that may be difficult to control
 ~9.2 GeV energy gain over 30 cm
 Laser-created ‘free-standing’ plasma channels that can be recreated at the repetition rate of the laser
 Multiple independent results
C. Aniculaesei et al., The acceleration of a high-charge electron bunch to 10 GeV in a 10-cm nanoparticle-assisted wakefield accelerator. Matter Radiat. Extremes 2024; 9 (1): 014001
Winkler, P. et al. Active energy compression of a laser-plasma electron beam. Nature 640, 907–910 (2025).
Energy spread below the permille level
Employing active stabilization
Lindstrøm, C.A., Beinortaitė, J., Björklund Svensson, J. et al. Emittance preservation in a plasma-wakefield accelerator. Nat Commun 15, 6097 (2024)
 Emittance preservation at micron level for 40 MeV energy gain (on top of 1 GeV)
 ~60% driver depletion
C Zhang et al 2024 Plasma Phys. Control. Fusion 66 025013
 Laser to electron conversion efficiency of at least ∼30%
 Multi-GeV energy gain
E. Rockafellow et a;., High charge laser acceleration of electrons to 10 GeV
NIM A, Volume 1077, August 2025, 170586
 42% local energy transfer efficiency
C. A. Lindstrøm et al., Phys. Rev. Lett. 126, 014801 (2021)
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025
Notes: Add logos, add also desy result,
11

## Slide 12: Outline
Summary & Conclusions
Timeline & Plans
Progress since the last ESPP
Applications & Collider
Design Studies
Possible HEP Contributions
23.06.2025
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025

## Slide 13: Summary of Applications Laser-Driven
23.06.2025
7 / 15
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
Laser-Driven Plasma Wakefield Injector for PETRA IV injector complex :
  Final Goal: 6 GeV injector, to decrease the spatial footprint and power requirements
PIP4 CDR A. Martinez de la Ossa et al. doi:10.3204/PUBDB-2024-06078
Notes: Add logos of labs
13

## Slide 14: Summary of Progress on Applications Beam-Driven
23.06.2025
7 / 15
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
Laser-Driven Plasma Wakefield Injector for PETRA IV injector complex :
  Final Goal: 6 GeV injector, to decrease the spatial footprint and power requirements
(Proton-driven plasma wakefield experiment at CERN) Run 2c and d approved  First fixed-target applications after LS4
 Towards a demonstrator facility for multistage plasma acceleration, that could be implemented at any major laboratory
PIP4 CDR A. Martinez de la Ossa et al. doi:10.3204/PUBDB-2024-06078
ESPP Input #172: AWAKE - Input to the European Strategy for Particle Physics Update on behalf of the AWAKE Collaboration (link), #235: Summary Report of the Physics Beyond Colliders Study at CERN (link)
Notes: Add logos of labs
14

## Slide 15: Summary of Progress on Applications Laser and Beam-Driven
23.06.2025
7 / 15
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
Laser-Driven Plasma Wakefield Injector for PETRA IV injector complex :
  Final Goal: 6 GeV injector, to decrease the spatial footprint and power requirements
(Proton-driven plasma wakefield experiment at CERN) Run 2c and d approved  First fixed-target applications after LS4
 Towards a Demonstrator facility for multistage plasma acceleration, that could be implemented at any major laboratory
(Particle accelerator research infrastructure based on novel plasma acceleration)
 FEL user facility by 2031
  FEL lasing achieved by 4 groups!
    Enabled by improved beam-quality and stability
PIP4 CDR A. Martinez de la Ossa et al. doi:10.3204/PUBDB-2024-06078
1
2
3
4
ESPP Input #172: AWAKE - Input to the European Strategy for Particle Physics Update on behalf of the AWAKE Collaboration (link), #235: Summary Report of the Physics Beyond Colliders Study at CERN (link)
Notes: Add logos of labs
15

## Slide 16: Outline
Summary & Conclusions
Timeline & Plans
Progress since the last ESPP
Possible HEP Contributions
23.06.2025
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
Applications & Collider
Design Studies

## Slide 17
To Be a Collider Technology, Wakefield Accelerators Must Offer a Path To…
High
Energy
High
Efficiency
High
Luminosity
100’s of GeV
Multi-TeV
>1034 cm-2 s-1
> 10% wall-plug to beam
8 / 15

## Slide 18: To Achieve This…
8 / 15
Repetition rate
and
Charge per bunch
and
Emittance
Staging
or
Energetic drivers
Wall-plug to Drivers
x
Driver to Wake
x
Wake to Witness
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025

## Slide 19: Collider Design Studies
9 / 15
HALHF Hybrid, Asymmetric, Linear Higgs Factory
e- acceleration in e- beam–driven plasma wakefields
e+ acceleration in radiofrequency cavities (C3 technology)
To make most effective use of space  collision of polarised 375 GeV e- with 42 GeV e+
Advantages:
+ most advanced wakefield collider concept  avoids e+ acceleration in plasma
+ compact footprint, ~5 km
Since 2023
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025

## Slide 20: Collider Design Studies - Challenges
9 / 15
HALHF Hybrid, Asymmetric, Linear Higgs Factory
e- acceleration in e- beam–driven plasma wakefields
e+ acceleration in radiofrequency cavities
To make most effective use of space  collision of 375 GeV e- with 42 GeV e+
Advantages:
+ most advanced wakefield collider concept  avoids e+ acceleration
+ compact footprint, ~5 km
Since 2023
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025
Challenges:
High repetition rate plasma operation and cooling, Staging, Production and acceleration of polarized beams, BDS design,…
10-15 years of R&D
ESPP Input #57: HALHF: a hybrid, asymmetric, linear Higgs factory using plasma- and RF-based acceleration (link)

## Slide 21: Collider Design Studies
9 / 15
HALHF Hybrid, Asymmetric, Linear Higgs Factory
ALiVE
A Linear accelerator for Very high Energies
e- acceleration in e- beam–driven plasma wakefields
e+ acceleration in radiofrequency cavities (C3 technology)
To make most effective use of space  collision of polarised 375 GeV e- with 42 GeV e+
e- and e+ acceleration in single stage p+ beam-driven plasma wakefields
  Enabled by the energetic and short p+ drivers
  p+ drivers: high-rep.-rate 500 GeV synchrotron
Advantages:
+ most advanced wakefield collider concept  avoids e+ acceleration in plasma
+ compact footprint, ~5 km
Advantages:
+ avoids staging
+ compact footprint
+ scaling to higher energies (10 TeV)
Since 2023
Since 2024
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025

## Slide 22: Collider Design Studies - Challenges
9 / 15
HALHF Hybrid, Asymmetric, Linear Higgs Factory
ALiVE
A Linear accelerator for Very high Energies
e- acceleration in e- beam–driven plasma wakefields
e+ acceleration in radiofrequency cavities
To make most effective use of space  collision of 375 GeV e- with 42 GeV e+
e- and e+ acceleration in p+ beam-driven plasma wakefields
Single plasma stage per arm!
  Enabled by the energetic and short p+ drivers
  p+ drivers supplied by high-rep.-rate synchrotron
Advantages:
+ most advanced wakefield collider concept  avoids e+ acceleration
+ compact footprint, ~5 km
Advantages:
+ avoids staging
+ compact footprint
Since 2023
Since 2024
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025
Challenges:
High repetition rate plasma operation and cooling, Staging, Production and acceleration of polarized beams, BDS design,…
10-15 years of R&D
ESPP Input #57: HALHF: a hybrid, asymmetric, linear Higgs factory using plasma- and RF-based acceleration (link)
Challenges:
High power synchrotron, Proton Bunch Compression, Plasma Source Development, Positron Acceleration, Energy Transfer Efficiency, Beam Quality Preservation,…
ESPP Input #210: Proton-Driven Plasma Wakefield Acceleration for Future HEP Colliders (link)

## Slide 23: Collider Design Studies
9 / 15
HALHF Hybrid, Asymmetric, Linear Higgs Factory
ALiVE
A Linear accelerator for Very high Energies
10 TeV Design Initiative for a 10 TeV pCM Wakefield Collider
Technology candidates:
Laser-Driven Plasma Wakefields
Beam-Driven Plasma Wakefields
Structure Wakefields
Collider type:
e+e-
e-e-
γγ
e- acceleration in e- beam–driven plasma wakefields
e+ acceleration in radiofrequency cavities (C3 technology)
To make most effective use of space  collision of polarised 375 GeV e- with 42 GeV e+
e- and e+ acceleration in single stage p+ beam-driven plasma wakefields
  Enabled by the energetic and short p+ drivers
  p+ drivers: high-rep.-rate 500 GeV synchrotron
Advantages:
+ most advanced wakefield collider concept  avoids e+ acceleration in plasma
+ compact footprint, ~5 km
Goals include delivery of:
+ end-to-end design study report in 2028
+ roadmaps and resource estimates
Advantages:
+ avoids staging
+ compact footprint
+ scaling to higher energies (10 TeV)
Since 2023
Since 2024
Since 2025
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025

## Slide 24: Collider Design Studies - Challenges
9 / 15
HALHF Hybrid, Asymmetric, Linear Higgs Factory
ALiVE
A Linear accelerator for Very high Energies
10 TeV Design Initiative for a 10 TeV pCM Wakefield Collider
Technology candidates:
Laser-Driven Plasma Wakefields
Beam-Driven Plasma Wakefields
Structure Wakefields
Collider type:
e+e-
e-e-
γγ
e- acceleration in e- beam–driven plasma wakefields
e+ acceleration in radiofrequency cavities
To make most effective use of space  collision of 375 GeV e- with 42 GeV e+
e- and e+ acceleration in p+ beam-driven plasma wakefields
Single plasma stage per arm!
  Enabled by the energetic and short p+ drivers
  p+ drivers supplied by high-rep.-rate synchrotron
Advantages:
+ most advanced wakefield collider concept  avoids e+ acceleration
+ compact footprint, ~5 km
Goals include delivery of:
+ end-to-end design study report in 2028
+ roadmaps and resource estimates
Advantages:
+ avoids staging
+ compact footprint
Since 2023
Since 2024
Since 2025
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025
Challenges:
High repetition rate plasma operation and cooling, Staging, Production and acceleration of polarized beams, BDS design,…
10-15 years of R&D
ESPP Input #57: HALHF: a hybrid, asymmetric, linear Higgs factory using plasma- and RF-based acceleration (link)
Challenges:
High power synchrotron, Proton Bunch Compression, Plasma Source Development, Positron Acceleration, Energy Transfer Efficiency, Beam Quality Preservation,…
ESPP Input #210: Proton-Driven Plasma Wakefield Acceleration for Future HEP Colliders (link)
Chosen design constraints:
Ez,avg > 500 MeV/m
ℒ/Ptot > 1032 cm-2s-1 MW-1
ESPP Input #98: Design Initiative for a 10 TeV pCM Wakefield Collider (link)

## Slide 25: Preliminary Plasma Collider Parameters
10 / 15
HALHF:
e-: 48 stages x 7.8 GeV = 375 GeV
e+: RF Linac 40 MV/m x 1.05 km= 42 GeV
ALIVE:
e-: 1 x 125 GeV
e+: 1 x 125 GeV
HALHF:
Avg. rep. rate: 16 kHz
Charge per bunch: 1.6 nC (e-) / 4.8 nC (e+)
Emittance (H/V): (90/0.32) mm mrad (e-) / (10/0.035) mm mrad (e+)
Luminosity: 1.2x1034 cm-2s-1 *  two IPs
* (0.76x1034 cm-2s-1 ) in top 1%
ALIVE:
Avg. rep. rate: 7.2 kHz
Charge per bunch: 3.2 nC (e-) / 3.2 nC (e+)
Emittance (H/V): (0.1/0.1) µm mrad (e-) / (0.4/0.4) µm mrad (e+)
Luminosity: 7x1034 cm-2s-1 **
** (0.25x1034 cm-2s-1 ) in top 1%
HALHF (PWFA Linac):
Wallplug-to-driver: 55%
Driver-to-wake efficiency: 80 %
Wake-to-beam efficiency: 50 %
Driver-to-beam efficiency: 40%
Wallplug-to-witness efficiency: 22%
ALIVE:
Wallplug-to-driver: 46 % (assumed)
Driver-to-wake efficiency: 12 % *
Wake-to-beam efficiency: 50 %
Driver-to-beam efficiency: 6 %
Wallplug-to-witness efficiency: 3 %
Luminosity
Energy
Efficiency
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025
ESPP Input #159: Contribution of ALEGRO to the Update of the European Strategy on Particle Physics (link)
* there are avenues to improve

## Slide 26: Since the Last ESPP…
Thanks to recent progress in beam quality, plasma-based accelerators are approaching the performance levels required for applications
  e.g. FELs, injectors, and fixed-target experiments…
For the first time, there are concrete collider parameter sets
  Not final  many discussions and design efforts are advancing
  Community is actively engaging with the high-energy physics (HEP) community (accelerator experts, detector experts, particle physicists, etc…) to gather diverse and critical input.
    Goal: provide a strong physics case and a credible machine development plan
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025
Challenges remain:
e.g., staging, positron acceleration, overall efficiency, high-rep rate modules (plasma, laser, linac), polarized beams,…
11 / 15

## Slide 27: Outline
Summary & Conclusions
Timeline & Plans
Progress since the last ESPP
Possible HEP Contributions
23.06.2025
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
Applications & Collider
Design Studies

## Slide 28: Timeline
First user facilities
Low-Energy
Injector
Particle physics applications
Higgs factories **
10+ TeV
collider **
O (~GeV)
O (~10s GeV)
250 GeV
10 TeV
AWAKE
 Exploratory studies
Injector for PETRA IV
~5 years*
US: P5
HALHF
ALiVE
10 TeV Design Study
~10 years*
* Realistic timescale with current funding commitment
Collider building block**
EuPRAXIA
** Funding uncertain
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025
12 / 15
Notes: Parallel ed
28

## Slide 29: Recent Review of the LDG R&D Efforts
13 / 15
February 2025
ESPP Input #154: European Accelerator R&D Platform Review for the Laboratory Directors Group (link)
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025
Recommendations (link):
#1: Ensure the timely completion of HALHF pre-CDR study and plan for an independent review
#2: Develop a plan to construct a demonstrator for multi-stage plasma acceleration capable of producing collider-grade beams
Technology Readiness:
Key technologies for plasma-based colliders are not yet ready.
Current Technology Readiness Levels (TRLs) have been established.
Progress vs. 2022 R&D Roadmap:
Progress and current R&D status are appropriate and sufficient.
Significant advancements achieved, e.g., high-quality beam generation via plasma acceleration.
Plans for 2025–2026:
R&D plans for 2025–26 are adequate.
Priority set on the HALHF collider design study.
link
Reduced scope: focus on plasma wakefield acceleration and HALHF

## Slide 30: Outline
Summary & Conclusions
Timeline & Plans
Progress since the last ESPP
Possible HEP Contributions
23.06.2025
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
Applications & Collider
Design Studies

## Slide 31: Possible Wakefield Accelerator Contributions to PP/HEP
14 / 15
Wakefield accelerators are a possibility for an energy upgrade
using:
“wakefield acceleration, either only for the electron beam à la HALHF or for both beams. For the longer future, it may make possible e+e– or γγ colliders with energies of 10 TeV and above.”
Wakefield technology could be an upgrade to parts of a collider, e.g.:
  Plasma Based Injector
For linear colliders
Wakefield accelerators could provide beams, e.g. for
  SF-QED experiments
  Dark Matter Search Experiments
Support for colliders based on other technologies:
  Test beam generation (for detector and instrumentation R&D)
  IP-physics studies incl. simulation tools development
  Spin off: Laser-based beam collimation
ESPP Input #140: A Linear Collider Vision for the Future of Particle Physics (link)
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
Beyond colliders
ESPP Input #191: Input to the European Strategy for Particle Physics: Strong-Field Quantum Electrodynamics (link), ESPP Input #235: Summary Report of the Physics Beyond Colliders Study at CERN (link)
Also see talk by J. List
23.06.2025
Notes: Put Logos
A and B
Meesaging up down
31

## Slide 32: Outline
Summary & Conclusions
Timeline & TRL & Plans
Progress since the last ESPP
Possible HEP Contributions
23.06.2025
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
Applications & Collider
Design Studies

## Slide 33: Summary & Conclusions
Plasma-based accelerators are approaching the performance levels required for applications
  First applications are expected to come online within the next 5-10 years
Significant progress has been made on collider concepts, including the development of concrete parameter sets
  There are remaining challenges that will require R&D
  HALHF– and AliVE pre-CDRs will be prepared
  No showstopper has been found, and the field is very active across theory, simulations, and experiments
Support for High-Gradient Wakefield Accelerator R&D is essential!
  Such investment will enable this community to contribute meaningfully to future PP and HEP programs at many levels—and potentially shape the very long-term future of the field
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025
15 / 15

## Slide 34
Thank you for your attention!
Summary of relevant ESPP submission documents:
#57: HALHF: a hybrid, asymmetric, linear Higgs factory using plasma- and RF-based acceleration (link)
#98: Design Initiative for a 10 TeV pCM Wakefield Collider (link)
#140: A Linear Collider Vision for the Future of Particle Physics (link)
#154: European Accelerator R&D Platform Review for the Laboratory Directors Group (link)
#159: Contribution of ALEGRO to the Update of the European Strategy on Particle Physics (link)
#172: AWAKE - Input to the European Strategy for Particle Physics Update on behalf of the AWAKE Collaboration (link)
#191: Input to the European Strategy for Particle Physics: Strong-Field Quantum Electrodynamics (link)
#210: Proton-Driven Plasma Wakefield Acceleration for Future HEP Colliders (link)
#235: Summary Report of the Physics Beyond Colliders Study at CERN (link)
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025

## Slide 35: Backup

## Slide 36: Impact of Accelerator R&D for Physics Beyond Colliders
For all advanced acceleration schemes:
  The potential delivery of high energy electron beams with narrow energy spread for beam dump, fixed target, high-field QED, …, experiments.
  Test beam generation (for detector R&D or instrumentation development)
  Simulation tool development, e.g. implementation of SF-QED effects
ESPP submission: Summary Report of the Physics Beyond Colliders Study at CERN (link)
Search for Dark Photon | SF-QED
Electrons delivered at 50 GeV in bunches with 5 × 109 particles and a total running time of, e.g., 3 months giving 1016 Electrons on Target. | Experiments could be performed with 50 GeV electrons, as in the E144 experiment, but with increased laser power
Possible withing the Run 2 experimental facility
For certain applications (LDMX experiment), DLAs may be ideal!
+ add EPAC
ESPP ID #191: Input to the European Strategy for Particle Physics: Strong-Field Quantum Electrodynamics (link)
Current Status and Future Prospects for the Light Dark Matter eXperiment, LDMX collaboration, arXiv:2203.08192 (2022)
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025

## Slide 37: ALEGRO
ALEGRO: Advanced LinEar collider study GROup : An international study group to promote Advanced and Novel Accelerators for High Energy Physics applications.
  Foster and trigger advanced linear collider related activities
  Provide a framework to amplify international coordination, broaden the community, involving accelerator laboratories/institutes
  Identify topics requiring intensive R&D and needed facilities
 Driven by the ICFA-Advanced and Novel Accelerators (ANA) Panel
Main activities:
Organize workshops dedicated to applications of ANAs to particle and high-energy physics.
ESPP Input #159: Contribution of ALEGRO to the Update of the European Strategy on Particle Physics (link)
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025

## Slide 38: TRL Levels HALHF
ESPP Input #154: European Accelerator R&D Platform Review for the Laboratory Directors Group (link)

## Slide 39: Advances in Simulation Tools Enables Studies of Collider Relevant Beams
39
Acceleration of Flat Beams
S. Diederichs et al., Resonant Emittance Mixing of Flat Beams in Plasma Accelerators, Phys. Rev. Lett. 133, 265003 (2024)
Acceleration of flat beams requires special consideration, e.g. flat beam drivers
Stable Positron Acceleration in Thin, Warm, Hollow Plasma Channels
T. Silva et al., Phys. Rev. Lett. 127, 104801 (2021)
Positron Acceleration
Thin, warm hollow channels for high-quality positron acceleration with high gradients
Positron acceleration remains a challenge:
 Recent review paper
Positron acceleration in plasma wakefields
G. J. Cao et al., Phys. Rev. Accel. Beams 27, 034801(2024)
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025
Notes: Add logos, add also desy result,
39

## Slide 40
20.06.2025
Presenter | Presentation Title
40
Accelerating for e-
Decelerating for e-
Focusing for e-
Defocusing for e-
Drive
bunch
e-
Periodicity: λpe

## Slide 41: Collider-Quality Beams can Now be Simulated with Open-Source Codes
41
3D quasistatic
Ion motion, ionisation, spin tracking included
Mesh refinement makes simulations in 3D (very) affordable.
S. Diederichs et al., Comput. Phys. Comm. 276 108421 (2022) Open-source: https://github.com/Hi-PACE/hipace
3D full-PIC
modelling of 50 multi-GeV stages
  idealized transport
  low witness bunch charge
J-L Vay et al., WarpX MS FY23.1 and FY23.2 (2023);
256 GPUs for 8h on Perlmutter (NERSC)
Open source https://github.com/Angel/FP/Wake-T moving soon to https://github.com/Wake-T/Wake-T
Ferran Pousa et al., in preparation
WakeT
HiPACE++
WarpX
2D cylindrical, quasistatic
adaptive grid method  fully converged simulations of beams with nm-scale emittance including ion motion, on a laptop
Numerical convergence: 7min on a CPU core
Numerical convergence: few hrs on few GPU’s
Fedeli L, Huebl A, et al. SC22: 2022. DOI:10.1109/SC41404.2022.00008
+ collaborators
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025
Notes: Add logos, add also desy result,
41

## Slide 42: Progress on the Collider Components Highlights
42
Efficient Laser Drivers
Plasma Sources
LPA Guiding channels
Development of scalable plasma sources at CERN
10 m long Discharge Plasma
1 m long Helicon Plasma
Use of HOFI (Hydrodynamic Optical Field Ionized) Plasma Channels enables record electron energies
KALDERA  based on Ti:Sa technology, started commissioning
kBELLA  efficient coherent combination of fiber lasers 10’s mJ at kHz, 100+ mJ in progress scheduled for next year
Development of Joule-class kHz laser systems:
Multiple technologies being investigated, e.g. Ti:Sa, fiber lasers, TmYLF, Tm-doped ceramics
A. Picksley et al., Phys. Rev. Lett. 133, 255001 (2024).
J. E. Shrock et al., ,” Phys. Rev. Lett. 133, 045002 (2024).
R. J. Shalloo et al.,,” Phys. Rev. E 97, 053203 (2018).
A. Picksley et al.,,” Phys. Rev. E 102, 053201 (2020).
A. Alejo et al., Phys. Rev. Accel. Beams 25, 011301 (2022)
free standing structures  no damage
work at high repetition rate
2x107 discharges
10-150 Hz operation
ceramic
low voltage solid-state discharge system
 MHz repetition rate
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025
Notes: Add logos, add also desy result,
42

## Slide 43: Collider Design Studies (1/3)
43
HALHF Hybrid, Asymmetric, Linear Higgs Factory
e- acceleration in e- beam–driven plasma wakefields
e+ acceleration in radiofrequency cavities
Advantages:
+ most advanced wakefield collider concept  avoids e+ acceleration
+ compact footprint (~5 km)
Since 2023
ESPP Input #57: HALHF: a hybrid, asymmetric, linear Higgs factory using plasma- and RF-based acceleration (link)
    Asymmetric collisions: 375 GeV polarized e- with 41.7 GeV polarized e+ (boost: γ=1.67), Centre-of-mass energy: 250 GeV.
      Using higher e- energy is a cost-effective solution given the large acceleration gradients in plasma wakefields (48 stages with ~1 GV/m peak gradient).
      e+ accelerated in Cryo-Cooled Copper (C3) linac at ~40 MeV/m.
    Other collider components based on scaled designs from ILC and CLIC.
HALHF implementation @CERN investigated
Estimated luminosity: 1.2x1034 cm-2s-1  two IPs
Estimated total power usage: 106 MW
Estimated cost: 3.8 BCHF (2024 Swiss francs)
Estimated R&D time (technically limited): 10-15 years
Foster et al., Phys. Open 23, 100261 (2025)
for details, see ESPP Input #57
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025
Notes: Proposed parameter set
Feedback from the community
Updated parameter set
43

## Slide 44: Collider Design Studies (2/3)
44
ESPP Input #210: Proton-Driven Plasma Wakefield Acceleration for Future HEP Colliders (link)
ALIVE
A LInear accelerator for Very high Energies
e- and e+ acceleration in p+ beam-driven plasma wakefields
Single plasma stage per arm!
  Enabled by the energetic and short p+ drivers
  p+ drivers supplied by high-rep.-rate synchrotron
Advantages:
+ avoids staging of plasmas
+ compact footprint
Since 2024
Major technical challenges and propose strategies to overcome them:
Proton Bunch Compression, Plasma Source Development, Positron Acceleration, Energy Transfer Efficiency, Beam Quality Preservation…
Collider Parameters:
Centre-of-mass energy (CoM): 250 GeV. Estimated luminosity: 1.7x1034 cm-2s-1
Footprint: ~4 x 2 km.
7 km circumference
high rep. rate: 14.4 kHz
500 GeV p+ synchrotron
Plasma acceleration stage accelerating witness beams (e- and e+ ) using the wakefields generated by short (mm scale) proton bunches
Preliminary investigation of a Higgs factory based on proton-driven plasma wakefield acceleration J. Farmer et al., 2024 New J. Phys. 26 113011
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025

## Slide 45: Collider Design Studies (3/3)
45
ESPP Input #98: Design Initiative for a 10 TeV pCM Wakefield Collider (link)
Since 2024
10 TeV Design Initiative for a 10 TeV pCM Wakefield Collider
Technology candidates:
Laser-Driven Plasma Wakefields
Beam-Driven Plasma Wakefields
Structure Wakefields
Collider type:
e+e-
e-e-
γγ
Goals include delivery of:
+ end-to-end design study report in 2028
+ roadmaps and resource estimates
The Design Study aims to produce a unified, self-consistent concept for a 10 TeV parton-center-of-mass (pCM) collider based on wakefield accelerator (WFA) technology.
The Study is Initiated by the 2023 US P5 Report, but it is a global undertaking.
Assume for now that is an upgrade of an ILC-type facility.
Chosen design constraints:
Ez,avg > 500 MeV/m
ℒ/Ptot > 1032 cm-2s-1 MW-1
Broad participation: detector physicists, particle physicists, etc…
https://indico.slac.stanford.edu/category/138/
209 Endorsers!
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025

## Slide 46: Roadmap based on LDG report findings
LDG
Defined in 2023
Recommendation #1 (link):
Ensure the timely completion of HALHF pre-CDR study and plan for an independent review
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025
Notes: Make this in paralle
46

## Slide 47: Plasma Wakefield Linac
Driver 1
Witness
Driver 2
Plasma 1
Plasma 2
Refocus
Witness
Driver
Plasma
Witness
Driver
Witness
Driver loses energy
Witness gains energy
  Energy gain per stage depends on the drive, witness and plasma parameters
One plasma stage may be sufficient
If the single stage energy gain is not sufficient
 Staging until the desired energy is reached
Unit cell
Interstage: conventional magnetic optics and/or plasma lenses
from (link)
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025
Notes: If we look more closely at a plasma wakefield acceleration stage, we have the driver, which excites a plasma wakefield, and the witness which gains energy from the wakefields. When the driver is a laser pulse, one sometimes adds a guiding channel
47

## Slide 48: FEL Lasing Achieved by Four Groups  Enabled by Improved Beam-Quality and Stability
20.06.2025
9
Wang, et al. Free-electron lasing at 27 nanometres based on a laser wakefield accelerator. Nature 595, 516–520 (2021).
188 MeV, ~6.3% energy spread, ~100 pC
Labat, M., et al. Seeded free-electron laser driven by a compact laser plasma accelerator. Nat. Photon. 17, 150–156 (2023).
Pompili, R., et al. Free-electron lasing with compact beam-driven plasma wakefield accelerator. Nature 605, 659–662 (2022).
Seeded free-electron laser
SASE gain >1000, some gain on >90% events
~100 MeV, 2% energy spread, ~90 pC
S. K. Barber et al., Greater than 1000-fold gain in a free-electron laser driven by a laser plasma
accelerator with high reliability, under review
Beam-driven
5.8 MeV energy gain, 0.3% energy spread, 20 pC
Lasing at 27 nm
490 MeV, ~0.5% energy spread, 30 pC
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
Notes: Add logos of labs
48

## Slide 49: Progress Towards First Applications
10
Run 2c and d approved
Separate Self-Modulation from acceleration to accelerate bunches with quality at few GeV energies
Experiments starting in 2029
First applications after LS4
Proton-driven plasma wakefield experiment at CERN
Toward a demonstrator facility for multistage plasma acceleration
Developing:
nonlinear plasma lenses
self-correction mechanisms
 multistage demonstrator facility e.g., with 50 GeV for strong-field QED, to be implemented in a major accelerator lab.
Particle accelerator research infrastructure based on novel plasma acceleration
C. A. Lindstrøm et al., Proceedings of IPAC 2025
ESPP Input #172: AWAKE - Input to the European Strategy for Particle Physics Update on behalf of the AWAKE Collaboration (link)
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025
AWAKE is the first to go
into LS3!
High repetition rate plasma sources
Technology R&D and critical experimental facilities
LPA demonstrator stages (low average power, near collider emittances)
PWFA staging (including low-energy design at EuPRAXIA@SPARC_LAB)
Positron beam test capabilities
FEL user facility starting in 2029

## Slide 50: Laser-Driven Plasma Wakefield Injector for PETRA IV
PIP4 CDR A. Martinez de la Ossa et al. doi:10.3204/PUBDB-2024-06078
Goal:  6 GeV injector, which could notably decrease the spatial footprint and the power requirements of the PETRA IV injector complex
High-Gradient Wakefield Accelerators, ESPP Symposium Venice 2025
23.06.2025
KALDERA  based on Ti:Sa technology, started commissioning
Development of Joule-class kHz laser systems:
Multiple technologies being investigated, e.g. Ti:Sa, fiber lasers, TmYLF, Tm-doped ceramics
kBELLA  efficient coherent combination of fiber lasers
Currently: 10’s mJ at kHz, 100+ mJ in progress scheduled for next year
11

## Slide 51
T. Grismayer | Conference | 2025
Particle-in-cell method can couple plasma kinetic scales and QED
1) Classical Radiation recoil
M. Vranic et al., CPC 204 (2016), J. L. Martins et al., PPCF 58 (2016)
2a) Non-linear Compton and Non-linear Breit-Wheeler
T. Grismayer et al., POP 23 (2016), T. Grismayer et al., PRE 95 (2017)
2b) Particle merging algorithm
M. Vranic et al., CPC 191 (2015)
3) Linear Compton scattering
F. Del Gaudio et al., JPP 86(5) (2020), F. Del Gaudio et al., PRL 125 (2020)
4) Bremstrahlung and Bethe-Heitler
O. Amaro et al, et al, submitted (2024)
5) Euler-Heisenberg solver (quantum vacuum polarisation)
T. Grismayer et al., NJP 9 095005 (2021), Z. Zhang et al., Comm. Phys. 8, 1-11 (2025)
6) Heuristic photon emission and pair production for astro setups
F. Cruz et al., ApJL, 919 L4 (2021) and F. Cruz et al., ApJ, 908 (2021)
Integration of equations of motion: moving particles
Integration of field equations: updating fields
Deposition: calculating current on grid
Interpolation: evaluating force on particles
QED processes coupled to PIC
Tools to model plasma accelerators up to the interaction point are ready.
OSIRIS is now open source.
Notes: In conclusion, I presented here ab initio simulations of QED cascades at pulsar polar caps.
In 1D, simulations with realistic parameters show the periodic formation of high multiplicity plasma fronts that are advected to the magnetosphere, with the vacuum gap extending over a distance well described with an available analytical model.
I have then presented a new way to scale the QED parameters such that, with more modest numerical parameters, one can get qualitatively equivalent results. Scaling the QED parameters, however, allows for multidimensional simulations. For the particular case presented here, where the gap size is comparable to the polar cap radius, we observe highly tilted pair fronts developing, breaking the polar cap into smaller, drifting gaps. Lastly, we believe that this may be used to extract observables such as radially resolved surface energy deposition.

## Slide 52
Beam-beam interaction in various regimes of disruption and SF-QED effects
Regime: and
Regime: and
V. Yakimenko et al., PRL 122, 190404 (2019)
Photon spectrum and pair yields
High brightness photon source
Probing the non-perturbative SF-QED
with extreme short beams
F. Del Gaudio et al., PRAB 22, 023402 (2019)
Photon beam density
Regime: and
Pair yield
front of the beam expanding
tail of the beam pinching
Anomalous pinch in
Electron-electron collision
W. Zhang et al.., arXiv:2412.09398 (2024)
T. Grismayer et al.