## Slide 1: Longitudinal beam coupling impedance mitigation studies for CERN PS accelerator complex
Ph.D. in Accelerator Physics – XXXVII cycle
Michela Neroni*
Advisors
Prof. Andrea Mostacci (Sapienza, University of Rome)
Dr. Christine Vollinger (CERN)
Final Defence - 30th of January 2025
*michela.neroni@uniroma1.it

## Slide 2: Outline
Introduction and motivations
Longitudinal beam coupling impedance of:
      Extraction kickers
      Septa magnets
      Pumping manifolds
Conclusions
Introduction and motivations
Longitudinal beam coupling impedance of:
      Extraction kickers
      Septa magnets
      Pumping manifolds
Conclusions

## Slide 3: Beam intensity upgrades in the CERN injector complex
Parasitic mechanisms leading to beam instabilities and losses must be limited in the Proton Synchrotron (PS).
PSB
PS
SPS
LHC
AD
n-TOF
East Area
North Area
AWAKE
From LINAC 3 and LEIR
From LINAC 4
Proton Synchrotron (PS) accelerates ions and protons beams towards experimental areas and Super Proton Synchrotron (SPS).
Oldest CERN synchrotron  it was designed for working with lower intensities.
Constant need for higher intensity and brightness beams (High Luminosity LHC, Physics Beyond Colliders projects)  high quality beam from the injectors complex is crucial.

## Slide 4: Longitudinal beam coupling impedance
Bunch of charged particles facing:
Cross section variations of beam chamber
Finite resistivity of the walls
Effect of wake field produced by a moving leading particle, , on a point charge , at a fixed distance in the longitudinal direction can be quantified through the longitudinal wake function:
Wake field
It can affect one or more following bunches  Beam quality degradation and beam instabilities
Fourier transform
Longitudinal beam coupling impedance
Lorentz force
CST Studio Suite®
x
y

## Slide 5: Longitudinal beam coupling impedance evaluation
  Log-formula, related to distributed impedances:
      ,
      with characteristic impedance of the device including coaxial wire.
 Device Under Test
Single stretched wire measurements*
Stretched thin wire
Electromagnetic simulations
Wake potential:
Charge distribution function
Longitudinal wake impedance
z
s
E.g. Wakefield simulation
Particle beam
Modern software allows the analysis of complex geometries with high accuracy.
CST Studio Suite®
*H. Hahn and F. Pedersen, “On Coaxial Wire Measurements of the Longitudinal Coupling Impedance,” Tech. Rep. BNL-50870, Brookhaven National Laboratory, 1978.

## Slide 6: Proton Synchrotron longitudinal impedance model
*A. Lasheen. PS Longitudinal Impedance Model. Zenodo, 2020. doi:10.5281/zenodo.4722835.
Kickers
RF cavities
Vacuum equipment
Total Longitudinal PS Impedance Model*
Accelerator impedance model
Impedance of each accelerator component (e.g. kickers, septa, beam diagnostics,..)
Ʃ
Input for beam dynamics simulation
Latest update of PS longitudinal impedance model was in 2020. LHC Injectors Upgrade (LIU) requirements have been achieved in the PS ( p/b, with bunches).
Tackling critical impedance sources and adding missing contributors (e.g. septa magnets) will provide additional margin.
Impedance model must be kept up-to-date, to ensure the use of the most recent geometrical model of each component.

## Slide 7: Impedance model and beam spectrum in the CERN Proton Synchrotron
PS beam spectrum and impedance at flat top for LHC proton beam
The impedance sources have different effects depending on their wavelength-to-bunch length ratio, , with frequency of the impedance peak and bunch length.
Low frequency range includes sources up to 40 MHz  Longitudinal coupled-bunch instabilities expected in this frequency range.
High frequency sources are expected to drive microwave instability, leading to uncontrolled emittance blow-up.

## Slide 8: Observations of longitudinal instabilities at CERN Proton Synchrotron
Large variety of beams produced in the PS results in different beam stability regimes  important to tackle specific impedance source causing instability.
Example of recent observation of microwave instability at transition crossing for LHC ions beam:
Among the beams in the PS, some were observed to be at the longitudinal stability limit:
  Coupled bunch instabilities observed in LHC and fixed target protons beams, characterized by train of bunches.
      Narrowband and high shunt impedance sources acting in the same frequency range of action of RF system (low frequency range)¹ extraction kickers suspected contributors with some peaks at low frequency.
  Microwave instabilities observed at transition crossing in AWAKE beam and LHC ions beam.
      Measurements of high frequency modulation with RF off in long bunch regime², showed beam modulation at 1.2 GHz, compatible with pumping manifold impedance (vacuum equipment).
A. Lasheen et al., “Identification of impedance sources responsible for longitudinal beam instabilities in the CERN PS,” in CERN Yellow Reports: Conference Proceedings, vol. 9, pp. 323–323, 2020.
E. Vinten and A. Lasheen, “Longitudinal microwave instability with long bunches in the CERN Proton Synchrotron,” in Proc. IPAC’23, Venice, Italy, pp. 2661–2664, 2023.
200
600
1000
1400
240
245
250
255
Time (ns)
0
Frame number

## Slide 9: Methodology overview
Identification of impedance source
Analytical evaluation
(applicable just in simpler cases)
Electromagnetic simulations
Radio frequency measurements
Wakefield simulations
(Particle beam source)
Frequency domain
(S-parameters)
Useful for direct comparison with bench measurements
Is there agreement?
Benchmark of simulation model
Full understanding of impedance contribution
If yes
Update of existing impedance model
Impedance mitigation strategy
Complementary tools, to be used in conjunction
CST Studio Suite®
To be equally proven with simulations and measurements
Eigenmode simulations
(resonator structures)
Objective:
Upgrade of existing accelerator for working with higher intensities

## Slide 10
Introduction and motivations
Longitudinal beam coupling impedance of:
      Extraction kickers
      Septa magnets
      Pumping manifolds
Conclusions
Introduction and motivations
Longitudinal beam coupling impedance of:
      Extraction kickers
      Septa magnets
      Pumping manifolds
Conclusions
Outline

## Slide 11: Fast extraction process: kickers and septa magnets
Fast rise/fall time ( ns) for magnetic field pulse
  Ferrite material
Fast deflection brings the beam from the circular orbit to the extraction channel.
Kicker magnet
Septum magnet
Circulating beam
Extracted beam
Magnetic septum
Kicker magnet
It gives the final deflection to the extracted beam.
M. J. Barnes, “Kicker Systems,” in CERN Accelerator School: Beam Injection, Extraction and Transfer, vol. 5, p. 229, CERN Yellow Reports: School Proceedings, 2017.

## Slide 12: Proton Synchrotron extraction kickers
Two kickers and one septum magnet involved in the main extraction from PS towards SPS and experimental areas.
KFA71
KFA79
SMH16
IV
Kickers first installed in the 1970s.
Twelve magnet modules foreseen for extraction, split in two different devices.
2.45 m
Impedance study of the 3-modules kicker can be extended on the 9-modules kicker.

## Slide 13
Model geometry and materials
3D models built starting from technical drawings and existing models.
Ferrite dispersive behaviour  experimental values* of relative magnetic permeability of Ferrite 8C11.
Optimization of simulation settings is also required to properly handle large complexity
Accurate geometry and material definition in electromagnetic simulation is of paramount importance:
*M. Giovannozzi et al., The CERN PS multi-turn extraction based on beam splitting in stable islands of transverse phase space: Design Report. CERN Yellow Reports: Monographs, Geneva, Switzerland: CERN, 2006.
n-cells transmission line magnet
Beam
Characteristic impedance of each module is 15 Ω
Beam

## Slide 14: Analytical and simulated longitudinal impedance
3-modules kicker
Ferrite drives the broadband behaviour as described by analytical model*.
Narrowband resonances in the low frequency range problematic for coupled bunch instabilities.
* H. Tsutsui, “Some simplified models of ferrite kicker magnet for calculation of longitudinal coupling impedance”, Tech. Rep. CERN-SL-2000-004-AP, CERN, 2000
Analytical model geometry*
Impedance per unit length can be derived  Effective magnet length used in this case

## Slide 15: Spare and current kicker module geometry
Spare 3-modules kicker (KFA79) available for impedance measurements equipped with a new module unit whose laminations and frame are differently shaped.
Impedance validation and mitigation carried out on the spare kicker geometry.
Beam
Current
Spare
Beam spectrum

## Slide 16
Adding cable terminations
Spare 3-modules kicker
Input connector  cables terminated on open circuit when the main switch in off-state, i.e. when not extracting from the PS
Output connector 
Connecting cables terminated on 15 Ω
Circuit schematic of a magnet module unit*
* L. Sermeus et al., “The kicker systems for the PS Multi-turn Extraction”, No. CERN-ATS-2010-140, 2010
Previous simulations were considering kicker in stand-alone... Each magnet module is connected to the power circuit by means of long transmission line cables  impedance model of the component must include the kicker as it is in the actual configuration in the accelerator.
Frequency domain simulation reproducing wire measurements setup (wire simulation)
output connector terminated with 15 Ω resistor (actual kicker configuration).
Beam axis

## Slide 17: Stretched wire measurements of the spare 3-modules kicker
Output power connectors terminated on a 15 Ω resistor and input connectors left undefined open
Excellent agreement of simulations and measurements  3D model benchmarked.
Beam axis

## Slide 18: Wakefield simulations of the 9-modules kicker
Impedance amplitude driven by number of ferrite elements.
High shunt impedance resonances at low frequency. Shunt impedance comparable to the one of an RF cavity.
Full understanding of kickers impedance allows starting with a mitigation strategy to address the low frequency resonances
Beam spectrum
Beam

## Slide 19: Location of the low frequency resonances
E-field monitor at 35.7 MHz
9-modules kicker – Top view
3-modules kicker – Side view: E-field monitor at 19.7 MHz, 32.2 MHz and 45.5 MHz.
Beam axis
Beam axis

## Slide 20: Mitigation solution for Proton Synchrotron extraction kickers
How can we mitigate the unwanted contributions?
Idea: create a path for the induced currents by connecting all the ground contacts.
Leading in simulation to an impedance peak reduction of a factor five.
The same mitigation solution with equal outcome was observed in simulations of the 9-modules kicker.
3-modules spare kicker
Beam

## Slide 21: Impedance measurements with transition pieces of 3-modules kicker
Mitigation solution fully proven. Low frequency resonances completely dampened with the insertion of transition pieces.

## Slide 22: Outline
Introduction and motivations
Longitudinal beam coupling impedance of:
      Extraction kickers
      Septa magnets
      Pumping manifolds
Conclusions
Introduction and motivations
Longitudinal beam coupling impedance of:
      Extraction kickers
      Septa magnets
      Pumping manifolds
Conclusions

## Slide 23: Proton Synchrotron septa magnets
Movable magnet yoke
Beam screen
Septum blade
RF fingers: placed to bridge the gap between the impedance screen and the end covers on both sides.
Impedance evaluation addressed with stretched wire measurements.
4 septa magnets measured, one case example shown here  Extraction septum (SMH16).
Picture of an extraction septum
PS impedance model to be updated with missing septa impedance.
Mainly resistive wall impedance driven by the conductivity of beam screen material  broadband impedance contribution expected.
Extremely complex geometry and yoke laminations material properties as a function of frequency are unknown  difficult to address the impedance evaluation with simulations.
Extracted beam
Circulating beam

## Slide 24: Stretched wire measurements of the extraction septum
A spare septum was measured, impedance assessment needed to qualify for installation.
Suspicion of RF contact issues
Multiple reflections caused by the remaining mismatch between the VNA and the DUT at the flange interface.
Two sharp notches at frequencies of 965 MHz and 1.47 GHz, and additional notch above 400 MHz.
Visual inspection showed RF fingers all lifted. Rework on non-contacting fingers needed.
Port 1
Port 2
Wire stretched along beam axis

## Slide 25
Stretched wire measurements of the extraction septum
Septum magnet remeasured after repair on the contact fingers.
Large impedance peaks at frequencies of 965 MHz and 1.47 GHz, as well as resonance above 400 MHz, are now greatly attenuated.
Narrowband resonances corresponded to a gap or discontinuity along the circulating beam path.
Mainly broadband impedance contribution.
Impedance measurements proven to be essential for determining impedance contribution of septa magnets and to check the presence of any assembly defects, not discernible through simulations.
 Mitigation of unwanted impedance contribution addressed by measuring each device before installation.

## Slide 26
Introduction and motivations
Longitudinal beam coupling impedance of:
      Extraction kickers
      Septa magnets
      Pumping manifolds
Conclusions
Introduction and motivations
Longitudinal beam coupling impedance of:
      Extraction kickers
      Septa magnets
      Pumping manifolds
Conclusions
Outline

## Slide 27: Proton Synchrotron pumping manifolds impedance
There are 100 straight sections along the PS accelerator, generally 1 manifold for each section:
50 empty manifold units.
55 manifolds equipped with beam diagnostic instrumentation, or pickup.
Insertion blind flange or pickup unit
Vacuum pump connection
Inner radius mm
Empty pumping manifolds suspected to be the source of microwave instabilities.
Impedance study addressed through eigenmode, wakefield simulations, and analytical considerations.

## Slide 28: Longitudinal impedance simulations of pumping manifold
Maximum shunt impedance reduced to 1.8 kΩ
Empty manifold
Maximum shunt impedance of 75 kΩ at 1.2 GHz
Pickup already acting as a shield  empty case is the target for impedance mitigation.
Manifold with pickup
Beam
Beam

## Slide 29: Empty manifold – field monitors
1.22 GHz
1.26 GHz
1.34 GHz
1.43 GHz
First four modes of a cylindrical resonator with the same dimensions:
 Shield needed to mitigate manifold impedance contribution.
Empty manifold acts as a cylindrical resonator, with radius mm
Beam
Beam
Beam
Beam

## Slide 30: Mitigation solutions
Among the different alternatives, two solutions were giving best performance:
Dummy pickup, longer and with elliptical cross-section.
Stainless steel beam screen.
Ferrite
RF fingers
Ferrite
Beam
Beam

## Slide 31: Simulated impedance with mitigation solutions
Remembering that one empty manifold unit gives a shunt impedance of 75 kΩ at 1.2 GHz.
Impedance comparing the two mitigation solutions:
A dummy and longer pickup with an elliptical cross-section gives the best performance for impedance reduction.
Ferrite
RF fingers
Ferrite
Elliptical pickup
Beam screen
Beam
Beam

## Slide 32: Outline
Introduction and motivations
Longitudinal beam coupling impedance of:
      Extraction kickers
      Septa magnets
      Pumping manifolds
Conclusions
Introduction and motivations
Longitudinal beam coupling impedance of:
      Extraction kickers
      Septa magnets
      Pumping manifolds
Conclusions

## Slide 33: Conclusions
Excellent agreement of electromagnetic simulations and bench measurements of impedance model for the extraction kicker magnets.
  High accuracy impedance model in the low frequency range allows a better prediction of longitudinal coupled bunch instability.
  Effective mitigation solutions including transition pieces were proposed and installed in the spare 3-modules kicker for future replacement of the kicker in the PS.
Impedance evaluation of septa magnets highlighted the importance of radio frequency measurements to detect assembly defects and to address the impedance problem when simulations become complex.
For empty pumping manifolds impedance mitigation was needed to limit the impact on microwave instabilities. Effective mitigation solutions showed a huge reduction of the empty manifold impedance.
The study allows to update the PS longitudinal impedance model  accurate prediction of accelerator performance.
Methodology: electromagnetic simulation and bench measurements applied to Proton Synchrotron (PS) key components.

## Slide 34
Thank you for the attention!

## Slide 35
Lists of publications
Journal Articles
M. Neroni, M. Barnes, L. Ducimetiere, et al., “Characterization of the longitudinal beam coupling impedance and mitigation strategy for the fast extraction kicker KFA79 in the CERN PS,” Journal of Physics: Conference Series, vol. 2687, no. 6, p. 062 012, Jan. 2024. doi: 10.1088/1742-6596/2687/6/062012.
M. Neroni, M. Barnes, A. Lasheen, A. Mostacci, B. Popovic, and C. Vollinger, “Beam coupling impedance of the main extraction kickers in the CERN PS,” Journal of Instrumentation, vol. 19, no. 08, T08001, Aug. 2024. doi: 10.1088/1748-0221/19/08/T08001.
S. Singh, M. Neroni, P. Benoit, et al., “Development and Implementation of a RC Snubber to Suppress Breaker Arcing Present in High-Stored-Energy Superconducting Magnet Systems,” IEEE Transactions on Applied Superconductivity, vol. 33, no. 5, pp. 1–4, 2023. doi: 10.1109/TASC.2023.3238294.
S. Singh, W. Głuchowska, M. Neroni, B. Cure, A. Dudarev, and M. Mentink, “CERN North Area Multi-Purpose Superconducting Magnet Facility,” IEEE Transactions on Applied Superconductivity, vol. 32, no. 6, pp. 1–5, 2022. doi: 10.1109/TASC.2022.3146809.
Conference Proceedings
M. Neroni, S. Albright, H. Damerau, et al., “Recent updates in the impedance characterization of the CERN PS Booster Finemet RF system,” English, in Proc. IPAC’24, (Nashville, TN), ser. IPAC’24 - 15th International Particle Accelerator Conference, JACoW Publishing, Geneva, Switzerland, May 2024, pp. 3120–3123, ISBN: 978-3-95450-247-9. doi: 10.18429/JACoW-IPAC2024-THPC52.
C. Vollinger, M. Sullivan, and M. Neroni, “Mitigation of beam coupling impedance for the wire scanners in the CERN Super Proton Synchrotron,” English, in Proc. IPAC’24, (Nashville, TN), ser. IPAC’24 - 15th International Particle Accelerator Conference, JACoW Publishing, Geneva, Switzerland, May 2024, pp. 3116–3119, ISBN: 978-3-95450-247-9. doi: 10.18429/JACoW-IPAC2024-THPC51.
P. Krkotic, S. Calatroni, M. Neroni, et al., “Impedance analysis of deformable RF contact bridges for high luminosity LHC,” English, in Proc. IPAC’23, (Venice, Italy), ser. IPAC’23 - 14th International Particle Accelerator Conference, JACoW Publishing, Geneva, Switzerland, May 2023, pp. 3470–3473, ISBN:978-3-95450-231-8. doi: 10.18429/JACoW-IPAC2023-WEPL153.
Talks in international conferences
Contributed oral: M. Neroni et al., ”Beam coupling impedance of the main extraction kickers in the CERN PS”, in Proc. 68th ICFA Advanced beam dynamics workshop on High-Intensity and High-Brightness Hadron beams (HB2023), CERN, Geneva, Switzerland, Oct. 2023.
Internal notes and presentations given at internal meetings
M. Neroni, ”Impedance measurements and simulation on the KFA79”, Presentation at Impedance Working Group meeting, CERN, Geneva, Switzerland, July 2022. https://indico.cern.ch/event/1181518
M. Neroni, ”Longitudinal impedance studies of KFA79”, Presentation at Accelerator Beam Transfer Forum meeting, CERN, Geneva, Switzerland, Oct. 2022. https://indico.cern.ch/event/1208317
M. Valente Dos Santos, M. Neroni and C. Vollinger, ”Measurement of the SMH16.3 Magnetic Septa”, No. CERN-ACC-NOTE-2023-0013, CERN, Geneva, Switzerland, Sept. 2023. http://cds.cern.ch/record/2870131
M. Neroni, ”Beam coupling impedance of the main extraction kickers in the CERN PS”, Presentation at PS Coordination Meeting #111, CERN, Geneva, Switzerland, Oct. 2023. https://indico.cern.ch/event/1340543/
M. Neroni, ”Longitudinal beam coupling impedance mitigation studies for CERN PS accelerator complex”, Presentation at SY-RF Seminars, CERN, Geneva, Switzerland, Nov. 2023. https://indico.cern.ch/event/1280060/

## Slide 36
Spare slides

## Slide 37: The CERN Proton Synchrotron
Parameter | LHC (protons) | LHC (ions) | AWAKE | n-TOF | East Area | AD | SFTPRO
Total intensity [] | 1870 | 10 | 30 | 850 | 60 | 2000 | 2400-3000
Intensity per bunch [ ppb or cpb] | 2.6 | 2.5 | 3 | 85 | 6 | 40 | 240-300
Long. Emittance [eVs] | 1.2 | 10 | 0.3 | 3 | 3 | 3 | 2
Long. instability type | Coupled bunch | Microwave | Microwave | Not limited by long. instability |  |  | Coupled bunch
Parameter | LHC (protons) | LHC (ions) | AWAKE | n-TOF | East Area | AD | SFTPRO
 | 1870 | 10 | 30 | 850 | 60 | 2000 | 2400-3000
 | 2.6 | 2.5 | 3 | 85 | 6 | 40 | 240-300
Long. Emittance [eVs] | 1.2 | 10 | 0.3 | 3 | 3 | 3 | 2
Long. instability type | Coupled bunch | Microwave | Microwave | Not limited by long. instability |  |  | Coupled bunch
PS beam parameters for LHC injection and fixed target experiments.

## Slide 38: Beam instabilities and mitigation strategy
Depending on the decay time of the wake field, we can distinguish two types of impedances:
Narrow-band impedances , impedance bandwidth and bunch length). Wake field lasts during the passage of many bunches
 coupled bunch instabilities.
Broad-band impedances (). Wake field produced by these impedance sources decays over one bunch length
 single bunch instabilities.
 Reducing Q factor: introduction of HOM-couplers, broadening methods like insertion of absorbers (e.g. ferrites).
 Reducing R/Q and therefore changing the overall geometry (to be decided in the design phase or mitigated with adding shields in an existing structure)
:
,
C. Vollinger et al., “Needs and solution for machine impedance reduction”, Proc. of ICFA Mini-Workshop on Impedances and Beam Instabilities in Particle Accelerators, Benevento, Italy, 2017.
E. Shaposhnikova, “Present knowledge of the longitudinal SPS impedance”, 10th Workshop on LEP - SPS Performance: Chamonix X, Chamonix, 2000.

## Slide 39
Courtesy of A. Lasheen
Shunt impedance threshold for coupled-bunch instabilities
Courtesy of Alexandre Lasheen
E. Shaposhnikova, “Longitudinal stability of the LHC beam in the SPS,” Tech.
Rep. SL-Note-2001-031-HRF, CERN, Geneva, Switzerland, 2001.
Courtesy of Jake Flowerdew
Comparison between impedance of RF cavities and extraction kickers at flat top energy in the low frequency range up to 80 MHz.

## Slide 40: PS Microwave instability with Pb Ions
No longitudinal emittance blow-up
200 MHz controlled emittance blow-up
Microwave instability occurs at PS transition.
Can be avoided with 200 MHz controlled emittance blow up.
With emittance blowup we observe uncaptured beam at handover to 80 MHz system → At stability limit.
Uncaptured beam
ppb
Growth rate:

## Slide 41
Wire simulation on 3-modules kicker
Simulated between kicker input and output port, when adding a wire along beam axis and changing output connector termination.
Cable terminations highly impacting on impedance behaviour in the low frequency range  15 Ω terminations must be considered in the measurements.

## Slide 42: Longitudinal impedance measurements on the KFA71
Output power connectors terminated on a 15 Ω resistor and input connectors left undefined open.
Satisfactory convergence could not be reached for frequency domain simulations of KFA71 due to geometrical complexity of the model  Wakefield simulations used for comparison.

## Slide 43
Module-Tank: ground conductor contact
Alternative positioning of transition pieces
Transition pieces placed closer to the beam chamber
Module-Module: HV plates contact
 Almost just broadband contribution caused by the ferrite left