## Slide 1: Neutrino mass with the PTOLEMY project PTOLEMY meeting Italia 19/02/2025

## Slide 2: Detection concept: Neutrino Capture on 𝛽 unstable nuclei
Proposal for their direct experimental detection in [AG.Cocco, G.Mangano, M.Messina JCAP 06(2007)015]
CnB Detection Requires:
energy resolution set by mn
Electron flavor expected with
m ≳50meV
from neutrino oscillations
M.G. Betti et al JCAP 07(2019)047
Beta decays
Relic capture
Requirements on energy resolution for neutrino mass measurement are weaker than relic case (50 meV)

## Slide 3: PTOLEMY first physics goal: neutrino mass
We plan to reach neutrino mass sensitivity of below 150 meV in 5 years
HOW?
  Exploiting a novel concept of a compact dynamic electromagnetic filter
  By measuring the end-point of T spectrum by using O(10 mg) of atomic T

## Slide 4
PTOLEMY detector scheme
PonTecorvo / PrinceTon Observatory for Light Early-universe Massive-neutrino Yield
p
Transverse drift filter
RF-tracker
Target
TES µCal
18.6 keV
© James Mead
Notes: Cryogenic transition edge sensor gives us the energy resolution BUT requires <100Hz rate to avoid saturation
Hence this 18.6 keV slowing potential and this EM filter BUT for this filter to be effective it needs to have a fast dynamic setting
To provide the trajectory information for the fast dynamic setting an CR-based tracking system is required between the target and the filter (NIKHEF)
Atomic tritium (to avoid smearing from molecular excitations) embedded on graphene will be the target for the prototype (this introduces its own problems)

## Slide 5
atomic H as a tool to ‘pinch’ the sp2 bonds towards a sp3 configuration while maintaining the planar nature of graphene
sp3 C-H bond
Hydrogen and Deuterium loading on graphene at Roma1 and Roma3
Betti et all, Nano Lett. 22, 2971 (2022)
UKAEA’s Active Gas Handling System (tritium for JET, EU Tokamak) for feasibility study & design requirement of a new T loading chamber
Quote received few days ago
H on Nanoporous Graphene (NPG):
T-chamber in Rome side view:
Notes: 5

## Slide 6
RF detection setup at LNGS: electron trap

## Slide 7
Electron cyclotron RF radiation studies
simulation of the pattern of RF radiation
carrier
secondary
sideband
sideband
Kr inlet
RF detection
CST simulation

## Slide 8
Candidate electron events
RF emission frequency vs time of single electron in the permanent magnet
Carrier
Secondary
P[W]

## Slide 9
Electron signature: trigger rate (data)
Source open
(RUN11)
Source closed
(RUN12)
BKG=14/1/25
RUN11-12=30/5/24
Source closed
(t=0)
Source: 85Rb → 83mKr
Lifetime Kr = 158.1 min
FreqRF=26GHz
PRF=1fW
FreqIF=550MHz
PRF=2μW
Electronic chain:
Low noise amplification +
down-conversion

## Slide 10: RF readout electronics
DAQ
LNA
DIPLEXER
Dedicated downconverter developed @ NIKHEF
DAQ with FPGA trigger under development @ NIKHEF
RTO64 used for DAQ
LNA
IF
RF
Tc

## Slide 11
Particle trajectories can be calculated/predicted analytically:
PTOLEMY filter: years of development
A design for an electromagnetic filter for precision energy measurements at the tritium endpoint
M.G.Betti et al, Prog.Part.Nucl.Phys. 106 (2019) 120-131
Implementation and optimization of the PTOLEMY transverse drift electromagnetic filter
A.Apponi et al, JINST 17 (2022) 05, P05021
From 18 keV to O(1 eV) in 50 cm
vs 70 m in the case of KATRIN
FOCUSING
with Einzel lens
Microcalorimeter

## Slide 12: Full demonstrator simulation (Princeton)

## Slide 13
Transmission Simulation Setup
1 mm radius circular area split into 50 rings (5 shown)
50 rings = 10,200 particles
Uniform distribution of pitch θ within a 10 degree window
8 fixed phi Φ emission angles
All electrons with initial KE = 18.6 keV
E.g.
  θ = 30±5, Φ = 0 (N=10,200)
  θ = 30±5, Φ = 45 (N=10,200)
  …
  θ = 30±5, Φ = 315 (N=10,200)
θ = 30±5, Φ = 0..315  N=81,600
θ = 40±5, Φ = 0..315  N=81,600
…
1mm radius
(5 rings)

## Slide 14
Methodology
2D plane monitors placed every 1 cm in z
  11x6 cm in (x,y) centered at (0,0)
Record individual particle hit information (incl. multiple hits per particle due to cyclotron motion)
At each Z coordinate:
Transmission efficiency: Extract # of unique particle hits per plane, express as percentage of N
Average KE: Take average over all hits (incl. duplicates)
Pitch angle: Calculate instantaneous pitch angle from momentum components for hits within 5mm of x=0, then take average pitch over these hits
+/-5mm
z
z
x
x
y

## Slide 15
Showing θ = 30±5 with individual Φ bin

## Slide 16
Showing θ = 20±5, 30±5, 40±5
averaged over Φ bins

## Slide 17
Showing θ = 20±5, 30±5, 40±5
averaged over Φ bins

## Slide 18
HV High precision stability (LNGS)
Vin
Vout
HV Capacitor (?)
Diode
chain
Field
Mill
Differential Amp
Precision
Multimeter
Climatic chamber - N2
E
Single board (1 kV)
σ = 0.3 mV

## Slide 19
𝝙EFWHM = 0.022 eV @ 0.8 eV
𝝙EFWHM = 0.05 eV @ 10 eV
Based on the expertise of the INRiM electron detection with TES! Key elements: high quality TES and new e-source based on nanostructures
Phys.Rev.Applied 22 (2024) 4, L041007
First measurement of electrons
@ 100 eV with a resolution ~1-1.5 eV
Calorimetry at INRiM
19

## Slide 20
Cryogenic, compact (goal O(cm^3)), switchable
Electron rate and electron energy not correlated
UV fiber
HV
TES
EGUN:
~ 1.5 cm
TES designed for HOLMES
Dynamic range: soft X-ray (E<=10 keV)
Energy resolution: 4-5 eV FWHM @6 keV
Chip with 64 TES with different geometries
Microwave multiplexing readout
Performance:
e-measurement at MiB
Electron spectrum @ dV= 100V
noise
e-signal

## Slide 21
Ew(eV) | Ep(eV) | DE (meV) | (mm) | (mm) | 
5 | 50 | 50 | 250 | 0.5 | 33
5 | 50 | 100 | 250 | 1 | 16
Ew(eV) | Ep(eV) | DE (meV) |  |  | 
5 | 50 | 50 | 250 | 0.5 | 33
5 | 50 | 100 | 250 | 1 | 16
RoI
Ew
Specs Phoibos 225
Electrostatic analyser as alternative electron detector
Magnetic field | < 5 mG
Operating temperature | T ambient
Surface stability vs time | Stable (graphite)
Max rate | 2 MHz
An example of Electron Analyser Project:
Functioning requests:
600 mm

## Slide 22
Alternative energy measurement
Electorstatic analyser
Ptolemy e.m. filter
Ep
Ep- dE
Ep + dE
MCP
Anode
Delay Line
Helmholtz – Lagrange law
preamp.
CFD
TDC
Position sensitive detector (MCP+delay line)
allows parallel acquisition
Electrostatic lenses
Electron optic basic equation
Energy resolution
(bandpass energy):
DE: energy resolution
Ep : pass energy
x: slit width
R0: mean radius
q: accepted angle
Two concentric hemispheres
for the energy selection

## Slide 23: Reference source
Source:
ρ = 0.2 mg/m2
(full loading)
1μg (50 cm2)
716 MBq
(19.3 mCi)
7 cm
7 cm
3 years
Esposure:
3 years
Efficiency:
50%
Very small
& compact
source
Total number of β emissions from tritium:
23

## Slide 24: Sensitivity as a function of tritium mass
Remarks:
- the sensitivity is weakly dependent upon the energy resolution (500 meV is already a good starting point)
- 1 μg is potentially comparable or even better than the projection of the best technology on the market
- 100 μg (0.5 m2) can potentially probe the neutrino mass down to the IO scenario
In preparation a theory paper on solid state effects on the electron spectrum & consequent theory systematics on mn extraction (A. Casale, A. Esposito G. Menichetti, V. Tozzini)
(No syst. Uncertainty included)

## Slide 25
PTOLEMY Demonstrator
aims at showing the capability of the PTOLEMY collaboration to master technologies
Integration of all sub-components to achieve full electron transport (fully budgeted)
Spectrum measurement of tritium electrons
Measurement with resolution O(1 eV)
New option for first e-measurement in low magnetic field
are under investigation: modified Skipper/CCD
Final mass sensitivity goal by using about 10 mg of tritium on graphene
25

## Slide 26
Demonstrator parts under constructions: magnet, order issued
Magnet: Key subsystem
ASG (Genova)/Suprasys(Bilbao)
26

## Slide 27
HV filter electrodes feedthrough
Vacuum
station
Antenna signal FT
top or bottom or both
Cold source
For vacuum
environment
Volume hosting G-T sample
with standard CF flanges with
possibility to make it longer and
connected to vacuum suitcase
for G-T transfer. Possible adapter to be added afterword
Vacuum gauge
Vacuum gauge
(not visible)
Cylindrical volume hosting future electron detector
(not drawn)
120 cm OD
200 mm OD
ALCA technology (Vicenza)
order issued
Demonstrator parts under constructions: vacuum chamber

## Slide 28: GANTT

## Slide 29: GANTT Tasks and Milestones

## Slide 30: To conclude: activities ongoing in 2025
Graphene hydrogenation demonstrated, to be ported to tritium - no scientific show-stopper
Plans to collaborate with UK AEA 2) Magnet ready in few months, at LNGS by fall 2025, electrodes design ongoing 3) RF radiation detection well advanced - to be integrated in the demonstrator 4) Several electron source for calibration, HV stability close to requirement 5) First detection of 100 eV electron with TES, warm detector based on
electrostatic analyser commercially available with 50 meV resolution

## Slide 31: Outlooks
First operation in 2026
Aim to physics results after 3 years
LoI/CDR in preparation for July CSN II meeting

## Slide 32: Backup

## Slide 33
Methodology
2D plane monitors placed every 1 cm in z
  11x6 cm in (x,y) centered at (0,0)
Record individual particle hit information (incl. multiple hits per particle due to cyclotron motion)
At each Z coordinate:
Transmission efficiency: Extract # of unique particle hits per plane, express as percentage of N
Average KE: Take average over all hits (incl. duplicates)
Pitch angle: Calculate instantaneous pitch angle from momentum components for hits within 5mm of x=0, then take average pitch over these hits
+/-5mm
z
z
x
x
y

## Slide 34
Magnete permanente da 1T triziato
Coils per trasporto di elettroni

## Slide 35
Impacchettamento target: scalabilità

## Slide 36
3x4
3x4
3x3
Simulazione di un array
B=0.1T

## Slide 37: solid state effects on decay (Casale, esposito, menichetti, tozzini)
Various final states of induce features in the electron spectrum
To determine the final helium binding potential is very subtle
Different ways of implementing the sudden approximation lead to different predicted rates
The paper studies this and other solid state effects. It also provides a first rough rule of thumb to determine the theory systematics on
Angelo Esposito
LNF 2025

## Slide 38: Sensitivity with Profile Likelihood
L0
median
L0
L
[Cowan et al. (2013)]
L0: Null hypothesis
Mass distortion is not simulated but is fitted
L1: Alternative hypothesis
Mass distortion is simulated and fitted
Median sensitivity (90% CL)
In 50% of cases the alternative hypothesis exceeds the 10% tail of the null hypothesis