## Slide 1: Picosecond X-ray pulses at Elettra 2.0 with “crab cavities”
Simone Di Mitri
Elettra Sincrotrone Trieste & University of Trieste

## Slide 2: Elettra Sincrotrone Trieste
ELETTRA, 2-2.4 GeV SRLS:
in operation since 1994
FERMI, 1.5 GeV FEL:
in operation since 2010
Elettra Sincrotrone Trieste is an international multidisciplinary research centre of excellence, open to the international research community, featuring a 2.0/2.4 GeV, third-generation synchrotron light source (Elettra), a free-electron laser light source (FERMI) and a variety of support laboratories.
Z. Ebrahimpour’s talk today
Shut down in July for major upgrade

## Slide 3: Elettra 2.0 – Diffraction Limit
Almost all experimental techniques gain from either a large 6-D photon density (brilliance) or a large coherent flux (degeneracy parameter):
for
Diffraction Limit
ICS
4GSR
and
More flux at the sample, for any given -range
Higher -harmonics by means of low-gap IDs
Shorter integrated time of measurement
Micro- and nano-focusing
Transverse x&y coherence up to 1 keV

## Slide 4: Science drivers of timing modes at SRLS
3GSR
4GSR
  Track non-equilibrium states (e.g. aerosol in free-flight)
  Map reversible dynamics of molecular systems
  Probe charge transfer dynamics
  Image orbital, spin, and lattice degrees of freedom
+ Improve lateral resolution
+ Improve energy resolution
+ Reduce the integrated time of measurements
Avoid sample burning or ablation
Avoid space charge shielding
Multi-MHz rep. rate
Wide & continuous -tuneability
Full polarization control
  50–100 ps:
  PES, EXAFS, imaging
  1–5 ps processes @ nm size:
  Elementary conformational protein dynamics & protein-protein interaction.
  Atomic motion in molecular vibrations.
  Chemical reaction intermediates.
New science

## Slide 5: Elettra 2.0 – Timing Mode
Parameter | Elettra 2.0 | Crab Cavities | FERMI | Units
Spectral range | 0.02 - 50 | 0.1 - 10 | 0.01 – 0.7 | keV
Rep. rate | 1 – 400 | 0.1 – 1 | 0.05 | MHz
Pulse duration, rms | 30 | 0.5 – 2 | 0.005 – 0.1 | ps
Flux at sample, ave | 106 – 1013 | 105 – 109 | 109 – 1013 | ph/sec
Spectral resolution | 10-5 – 10-4 | 10-4 | 10-4 – 10-3 (w/o mono) | 
Polarization | all | all | all | 
Coherence | Hor. ≤ 1 keV | Hor. < 0.5 keV | full | 
# Beamlines / Run | 31 | < 10 | < 2 | 

## Slide 6: “Crab cavities” working principle
Fill pattern:
200 regular bunches, 2 mA/bunch, 4 ns-time sep.
1 tilted bunch, 2 mA , 32 ns time sep., 1.157 MHz
Pulse selection:
  Temporal gating
  distorted orbit
  chopper
A. Lunin et al., Phys. Proc. 79 (2015) 54.
A. Lunin, T. Khabiboulline, V. Yakovlev , “A White Paper on Design and Fabrication of SRF Deflecting Cavities for Elettra 2.0”, FNAL note.
A. Zholents, NIM A 798 (2015) 111
See also: X. Huang, PRAB 2016, 2019, 2023

## Slide 7: Flux vs. pulse duration
0.8 MV @ 3GHz
On-the-fly control of pulse duration, flux, rep. rate (chopper), polarization (ID)
  At each beamline, without interference with neither other beamlines nor accelerator operation
1.2 MV @ 3GHz

## Slide 8: Nanospectroscopy @ 800 eV
1 x 0.9 µm2
REGULAR:
55 ps
1.3e10 ph/s
1 x 2.3 µm2
SHORT:
4 ps, drift
1.5e9 ph/s
1 x 1.3 µm2
SHORT:
4 ps, hybrid
1.8e9 ph/s
V-mono res. power: 2000 - 4500
The slit selects a sub-space of radiation emitted by the tilted e-bunch
Transverse coherence and energy resolution largely preserved
From accelerator to sample (elegant + Spectra + ShadOUI):

## Slide 9: Diffraction limit, spectral flatness
55ps, x-pol.
4ps, y-pol.
4ps, x-pol
3.7ps, x-pol
Potentially useful for on-the-fly energy scan at EXAFS, XAS…

## Slide 10: Timing modes @ SRLS
@ E2.0

## Slide 11: Summary
Picosecond duration, at several beamlines, for Eph > 100 eV
Tunable 0.1–1 (100) MHz rep. rate, 1–10 % flux relative to standard single bunch emission
Transverse coherence, energy resolution & polarization largely preserved
Standard bunches pay a doubled vertical emittance (6  12 pm rad)
Conceptual design report is being finalized. Technical design report is in progress
CCs are not in the Elettra 2.0 baseline. Still, full support from management, international committees and beamline scientists. Search for funds to prototype.

## Slide 12: Acknowledgements
A. Zholents (ANL)
X. Huang (SLAC)
R. Calaga, A. Grudiev (CERN)
The Elettra team for the Crab Cavities:
A. Bianco (retired), M. Altissimo, E. Busetto, A. Carniel, S. Cleva, I. Cudin, S. Dastan, B. Diviacco, A. Fabris, E. Karantzoulis, S. Krecic, S. Lizzit, M. Lonza, K. Manukian, C. Masciovecchio, M. Modica, E. Principi, N. Shafqat
for guidance to “Crab Cavs” simulations
Thank you for your attention
Questions are welcome!

## Slide 13: Back up slides

## Slide 14: Magnetic lattice
The present magnetic lattice will be entirely replaced by a denser and stronger one, including combined-function elements (3x dipoles, 4x quadrupoles).
45-fold smaller e-beam emittances
5-fold smaller beam sizes at IDs
x100 brilliance at the source (1-10 keV)
Reduced acquisition time
Photon-hungry techniques
Lateral resolution
CDI in keV range, ptychography, XPCS
– 12 of such cell in the existing tunnel –

## Slide 15: Improved radiation source
Dipole magnet: spectral flux density
Elettra @1.6T
Elettra 2.0 @1.6T
Elettra 2.0 @6T (superbend)
EPU: radiation 4-D volume at the source
EPU: on-axis Ang. Spectr. Flux Density of odd harmonics 3 – 11.

## Slide 16: Beamlines

## Slide 17: Deflecting voltages
Quasi-waveguide Multicell Resonator (QMiR) @ 2.815 GHz for APS (ANL).
Intrinsic low-Q SOMs and HOMs in a sparse frequency pattern.
Low gap, relatively high surface fields, nonlinear field components.
A. Lunin et al., Phys. Proc. 79 (2015) 54.
A. Lunin, T. Khabiboulline, V. Yakovlev , “A White Paper on Design and Fabrication of SRF Deflecting Cavities for Elettra 2.0”, FNAL note.
Design and optimization by N. Shafqat et al..
  Re-design of the ANL prototype for a larger beam aperture, to meet the requirements on short-range wakefields. Aperture > 8 mm-V x 12 mm-H.
  2 + 2 pure-Nb cavities @ 4,5 K (extension of the 3HC cryogenic system).
  RF source input power < 500 W per cavity

## Slide 18: Short pulse production
Deflecting voltage, vertical tune and phase advance
Small coupling
Small energy spread, small harmonic number, few ID periods
Short wavelength
The mode of short pulse selection depends on the beamline layout
The minimum pulse duration depends on deflecting voltage, beam emittances, photon energy

## Slide 19: Theoretical minimum pulse durations
Theoretical minimum FWHM pulse duration calculated for drift (orange) and hybrid optics (blue), across the beamline’s full spectral range and for beam RMS energy spread of 0.1%.
Dashed vertical lines are for the ideal case of a monochromatic electron beam.
3 ps

## Slide 20: Shortest durations at Elettra 2.0
Beamline | LOWEST photon energy |  |  |  | HIGHEST photon energy |  |  | 
Name [keV] | tFWHM (ps) |  | F/F (%) |  | tFWHM (ps) |  | F/F (%) | 
 | DR | HYB | DR | HYB | DR | HYB | DR | HYB
1.2 [0.03-1.7] | 17 | 9 | 6 | 2.5 | 3 | 1.7 | 1.5 | 2.8
2.1 [0.13-4.0] | 48.5 | 1.2 | 35 | 1.6 | 46 | 0.8 | 18 | 1.7
3.2 [0.01-0.2] | 48 | 10.5 | 20 | 1.6 | 42 | 2.1 | 5 | 1.8
4.2 [0.01-1.5] | 22 | 22 | 15 | 5 | 3.1 | 3.6 | 1 | 6.5
5.1 [4-21] | 34 | 6.4 | 12 | 2.7 | 18 | 3.0 | 5 | 2.6
5.2 [3.5-15] | 16 | 0.9 | 3 | 2 | 15 | 0.9 | 3 | 1.9
6.2 [0.34-4.0] | 3.7 | 3.7 | 0.5 | 3.6 | 1.7 | 1.9 | 0.5 | 3
7.2 [3.5-15] | 6.5 | 1 | 1 | 2 | 6.5 | 0.9 | 1.5 | 2
8.1 [0.15-1.5] | 27 | 1 | 9 | 1.4 | 9.6 | 0.8 | 1 | 1.7
8.2 [0.04-1.5] | 16 | 6 | 7 | 3 | 3.2 | 1.7 | 1 | 3.5
9.2a [0.01-0.2] | 38 | 6.7 | 15 | 1.9 | 13.5 | 1.8 | 3 | 2.0
9.2b [0.08-1.5] | 20 | 2.8 | 4 | 2 | 5.8 | 1.1 | 1 | 2.3
10.1 [0.5-7.0] | 12.5 | 0.7 | 1 | 1.3 | 8.5 | 0.7 | 2 | 1.6
10.2 [4-15] | 2.1 | 1.2 | 0.5 | 2.7 | 2.2 | 1.2 | 1 | 2.7
11.1 [3-15] | 28 | 33 | 12 | 12 | 14 | 19 | 6 | 17
11.2 [9-25] | 38 | 9 | 16 | 2 | 27 | 4.8 | 7 | 2.4
F/F(%) is relative to single bunch emission @ ID

## Slide 21: NanoSpectroscopy @ 800 eV (1/3)
Spectral flux in central cone, V/H-polarization, 2 mA/bunch – DRIFT mode
(blue) photon pulse from standard electron bunch, opening 60 µrad x 60 µrad:
55 ps, 1.9e12 ph/s/0.1%BW ; S1/S0=1 (EU, u = 10 cm, Lu = 4 m)
(green) short photon pulse from tilted electron bunch, opening 60 µrad x 10 µrad:
3.7 ps FWHM, 4.3e10 ph/s/0.1% or 1e4 ph/pulse/0.1%, S1/S0= 0.98
(orange-pink) short photon pulse from tilted electron bunch, opening 60 µrad x 24 µrad:
4 ps FWHM, 1.1e11 ph/s/0.1% or 1e5 ph/pulse/0.1%, S1/S0= 0.98/-1
Single pulse useful spectral flux: 6%
Intensity drop at higher energies, off-axis electrons motion

r
() > r
H-pol.
H-pol.
V-pol.

## Slide 22: Example @ 0.8 keV
Beamline optics | Standard | SP Drift | SP Hybrid
Photon energy [keV] | 0.8 | 0.8 | 0.8
FE slit gap (x  y) [m] | 690  690 | 690  280 | 690  690
FE angular acceptance (x  y) [rad] | 60  60 | 60  24 | 60  60
Slit gap at the monochromator entrance (y) [m] | 8 | - | 10
Slit gap at the monochromator exit (y) [m] | 6 | 12 | 10
Energy resolving power | 4500 | 2000 | 2900
Light pulse |  |  | 
Spatial size* at the FE slit, FWHM [m] | 90  42 | 90  80 | 90  99
Angular divergence* at the FE slit, FWHM [rad] | 38  32 | 38  23 | 38  59
Duration, FWHM [ps] | 55 | 4 | 4
Degree of linear polarization, S1/S0 | 1 | 0.98 | 0.98
Spectral flux at source point [1010ph/s/0.01%bw] | 19 | 1.1 | 1.7
Relative spectral flux at source point [%] | 100 | 6 | 9
Flux at sample [1010ph/s] | 1.3 | 0.15 | 0.18
Relative spectral flux at sample [%] | 100 | 12 | 14
Spatial size at sample, FWHM (x  y) [m] | 1.0  0.9 | 1.0  2.3 | 1.0  1.3
Nanospectroscopy-like soft x-ray beamline. 3% transmission efficiency.

## Slide 23: Example @ 12 keV
HBSAXS-like tender x-ray beamline. 11% transmission efficiency.
Beamline optics | Standard | SP Drift-1 | SP Drift-2
Photon energy [keV] | 12 | 12 | 12
FE slit gap (x  y) [m] | 550  550 | 550  400 | 550  200
FE angular acceptance (x  y) [rad] | 48  48 | 48  35 | 48  17
Energy resolving power | 5700 | 5700 | 5700
Light pulse |  |  | 
Spatial size* at the FE slit, FWHM [m] | 86  13 | 86  80 | 86  65
Angular divergence* at the FE slit, FWHM [rad] | 24  24 | 24  35 | 24  28
Duration, FWHM [ps] | 55 | 2.7 | 2.3
Spectral flux at source point [1010ph/s/0.01%bw] | 3.8 | 0.2 | 0.1
Relative spectral flux at source point [%] | 100 | 6 | 3
Flux at sample [1010ph/s] | 0.73 | 0.04 | 0.02
Relative spectral flux at sample [%] | 100 | 6 | 3