## Slide 2: Contents
Longitudinal Phase Space Linearization
ACC39 made by Fermilab for FLASH
AH1 made by INFN-LASA for European XFEL

## Slide 3: Contents
Longitudinal Phase Space Linearization
ACC39 made by Fermilab for FLASH
AH1 made by INFN-LASA for European XFEL

## Slide 4: TESLA Test Facility for e+e- Linear Collider

## Slide 5: From TTF1 to TTF2/FLASH
laser driven electron RF gun
photon beam diagnostics
superconducting accelerating modules
120 MeV 250 MeV
beam diagnostics
16 MeV
sc pre- accelerator
4 MeV
undulator
bunch compressor
TTF1
TTF2/FLASH

## Slide 6: SASE: Self Amplifiesd Spontaneous Emission
log (power P)
gain ~ 105
low gain
non-linear
(high-gain linear
regime)
P(z) = Po exp(z/Lgain)
log (power P)
undulator length, z
gain ~ 105
bunch interacts with undulator field
micro bunches develop
micro bunches emit coherently ~ N2 (N ≈ 106)
Key requirement:
high peak currents of > 1 kA
low emittance < λ/4pi ~ 1-2 μm
low energy spread ∆E/E < 10-3
exponential gain
P(z) = Po exp(z/Lgain)

## Slide 7: FEL asks for High Current and High Quality
GENESIS simulation of the TTF parameters
Sven Reiche (UCLA)
Modulation of the electron bunches
undulator
entrance
half-way
saturation
full saturation

## Slide 8: VUV­FEL requirements at TTF
1st lasing of VUV-FEL at long wave length l (32 nm acheived) does not require the 3.9 GHz module
Trying to lase at shorter l requires higher peak current I ≈ 2.5 kA
3.9 Ghz module required for
  driving the FEL instability
  getting radiation pulse with significant energy
from Proc. of EPAC 2002, 1798 (2002)
VUV­FEL beam requirements for lasing at 25 and 6 nm
3rd Harmonic Module mini-Review. P. Piot. 11.08.2005

## Slide 9: 3rd Harmonic System for TTF
TESLA-FEL 01-03 (2001)

## Slide 10: Origin of the non linear Energy Distribution
Electrons are gaining energy integrating the electric field while crossing the RF accelerating cavity
In each point of the cavity the field vary sinusoidally vs time
Because of the the non negligible bunch length the energy gain along the bunch is not constant and not linearly distributed
Bunch compression needed for high peak current is strongly affected
TM010 mode
Standing Wave

## Slide 11: Energy Distribution along the Bumch
V3 = V1 / 9

## Slide 12: TTF/FLASH as in 2007
initial bunch length restricted by collective effects
two stage bunch compression
off crest acceleration in ACC1 and ACC2/3
requires good rf field stability

## Slide 13: FLASH and XFEL with 3rd Harmonic

## Slide 14: 3rd Harmonic for high peak curreny
The 3rd harmonic module operating in decelerating phase in conjunction with the ACC1 module provides linearization of the rf acceleration field with time during the duration of the beam bunch.
Near crest at bunch center s = 0
V3 = V1 / 9
ϕ3.9 is ~180 deg (decelerating mode) and s = - ct. The head of the bunch is at positive s and ϕ1.3 must be positive too
Shifting ϕ3.9 by 12°, a linear chirp is obtailed for a more efficient compression

## Slide 15: The 3rd Harmonic Module from Fermilab

## Slide 16: Contents
Longitudinal Phase Space Linearization
ACC39 made by Fermilab for FLASH
AH1 made by INFN-LASA for European XFEL

## Slide 17: Beam dynamics aspects
Motivation:
  single-pass FELs demand high brightness e- beam
  small emittance and high peak currents are needed:
  user also want radiation pulse with significant energy
−1/ 2 5/
Design criteria for the x-ray FEL (VUV-FEL):
generate a long e- bunch
charge-density reduced
space charge effect mitigated
accelerate to high enough energy
(SC force 1/2)
take care of the bunch compression
1& 2 induce a non-linear distortion of the longitudinal
phase space impact on the bunch compression
3rd Harmonic Module mini-Review. P. Piot. 11.08.2005

## Slide 18: 3rd Harm. to Improve Beam Characteristics
Energy distribution in the bunch before and after bunch compressor without (left) and with (right) the 3rd harmonic cavity, calculated for TTF photoinjector.
3rd Harmonic Module mini-Review. P. Piot. 11.08.2005

## Slide 19: Case of TTF­1: nonlinear compression
NOT lasing lasing
from PRL 88, 104802 (2001)
1: longitudinal phase space
2: charge temporal distribution
Pros:
  sub-ps radiation pulses
  stable compression
  natural at TTF-1
Cons:
  throw away a lot of charges
  radiation pulse energy reduced
  beam dynamics associated to head and tail very different
  hard to tune and diagnose the e- beam
3rd Harmonic Module mini-Review. P. Piot. 11.08.2005

## Slide 20: Beam dynamics aspects
3.9 GHz System main requirements
E3.9 EBC1 i.e. E3.9
3rd Harmonic System decelerates the beam
phase spaces and
beam profiles before BCs
and
after BCs
BC1
BC2
3rd Harmonic Module mini-Review. P. Piot. 11.08.2005
3rd Harmonic on/off
3rd Harmonic on

## Slide 21: 3.9 GHz Cavity General Parameters
Number of cavities | 4
Active Length | 0.346 m
Gradient | 14 MV/m
Phase | -179 deg
R/Q | 750 
Epeak/ Eacc | 2.26
Bpeak (Eacc=14 MV/m) | 68 mT
Q_ext | 9.5 e+5
BBU limit for HOM, Q | <1.e+5
Total energy | 20 MeV
Beam current | 9 mA
Forward Power | 11.5 kW
Coupler power | 45 kW
Third harmonic cavity (3.9GHz) was proposed to compensate nonlinear distortion of the longitudinal phase space due to cosine-like voltage curvature of 1.3 GHz cavities.
3.9 GHz Cavity: Parameter List
180 MeV
-20 MeV
V3 = V1 / 9
N. Solyak

## Slide 22: Frequency shift due to Lorentz forces
Displacement of the cell wall due to Lorentz force. (wall thickness = 1.5 mm)
HFSS simulation of half cell
– P = (μ0 Η 2 − ε0 E2)/4
  data exchange (HFSS-ANSYS)
ANSYS simulation of stresses in half cell
  different wall thickness
  Yung modulus, Poisson's ratio
Frequency shift due to Lorentz force (Slater’s Theorem)
2 2
Eacc = 15MV/m
1.5 mm | 200 Hz
2.8 mm | 90 Hz
Wall Thikness
Cavity bandwidth  4kHz No Stiffening ring
N. Solyak

## Slide 23: Extensive HFSS Calculation @ Fermilab
E/H boundaries. Red/green lines for different beam polarization (x/y). Few modes have Q>105
Radiation boundaries. Three pass-bands are heavily dumped
HFSS 3D 9 cells cavity model with:
2 High Order Mode (HOM) couplers,
matched Main coupler port,
different type of beam pipe terminations,
distributed and phased current sources.
Calculations in driven mode.
Monopole(left) and Dipole (right) passbands for mid-cell of the 3rd harmonic cavity
Trapped modes in 5th dipole passband
3rd Harmonic Module mini-Review. T. Khabiboulline. 11.08.2005

## Slide 24: Qualification tests on Cu Cavity Prototypes
9 cells Cu cavity measurements with:
2 High Order Mode (HOM) couplers,
Main coupler port with matched termination,
Beam pipes with metal plates,
Excitation and pick-up from different ports. Bead-pull and S-parameter measurements for single cavity and double cavity system.
Dipole modes with high Qext (single cavity)
1st dipole band.
F = 4979.6 MHz. Q=2200
2-nd dipole band “6/9Pi” mode. F=5418.7 MHz. Q=11600.
2-nd dipole band “Pi” mode. F=5325.2 MHz. Q=14000.
5-th dipole band.F=9029.1 MHz. Q=32000.
3rd Harmonic Module mini-Review. T. Khabiboulline. 11.08.2005

## Slide 25: 3.9 GHz RF Coupler Design: Parameters
Ppeak = 45 kW (Ib=9mA) (processsing at 80kW) Pulse =1.3 ms
Rep. rate = 5Hz
3.9 GHz RF Coupler Main features
30mm/ 13mm coaxial line
Standard copper waveguide
Fix coupling
No DC biasing
Cold window: DESY TTF3 cylindrical ceramic
Warm window: CPI 3.9 GHz WG window
Two sets of bellows (flexibility)
All internal parts are copper plated (30 µm inner and 10 µm outer part of coax)
All part are brazed
Pick-ups and glass window for diagnostics
Good pumping performances
N. Solyak
In Collaboration with CPI

## Slide 26: 3.9 GHz RF Coupler Design: cut view
4K
Cold Window
Bellows section
Coax-to-WG transition
Pick-up
80 K
80 K
4 K
300 K
Coax-to-wg, no pumping holes 0.7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0.6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0.5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0.4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0.3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0.2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0.1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0 | 3.5 |  | 3.6 |  | 3.7 |  | 3.8 |  | M3H.9z |  | 4 |  | 4.1 |  | 4.2 |  | 4.3
S11
N. Solyak
In Collaboration with CPI

## Slide 27: 3rd Harmonic Cryomodule for TTF2
Don Mitchell

## Slide 28: ACC39 Cryomodule designed at Fermilab
Don Mitchell

## Slide 29: ACC39 Design derived from INFN Cry 2/3
Module 1, 2 & 3 in TTF I
Cry 2
Cry 3
ACC39

## Slide 30: Cry2 to Cry3: Diameter Comparison

## Slide 31: 3rd Harmonic Cavity String
Don Mitchell

## Slide 32: Cavity String closeup
Don Mitchell

## Slide 33: Magnetic Shield closeup

## Slide 34: ACC39 @ FLASH
Pei Zhang

## Slide 35: ACC39 Module from Fermilab to FLASH

## Slide 36: Commissioning of Fermilab Contribution

## Slide 37: Phase Space Linearization Acheived

## Slide 38: Contents
Longitudinal Phase Space Linearization
ACC39 made by Fermilab for FLASH
AH1 made by INFN-LASA for European XFEL

## Slide 39: INFN In-Kind Contribution to the E-XFEL

## Slide 40: Same Scheme in the 3 major XFELs
Hans Weise @ FEL2021

## Slide 41: E-XFEL WP46 - 3rd Harmonic Module
Due to alternating couplers requirement, for coupler kick compensation, and to the position of the 2-phase pipe there are two dressed cavity configurations (left and right)
Blade tuner updated to the “slim” type, concept derived from ILC tuner work by INFN. Lighter, cheaper, motor to the side.
Design of the Module is “Plug compatible” with XFEL modules

## Slide 42: E-XFEL 3rd Harmonic Module
10 3.9 GHz cavities produced and treated by the industry
Naked cavities Vertical tested at LASA
Integrated at the industry
Equipped with Power Coupler and assembled in the string at DESY
String moved into the cryomodule for final installation
Module in E-XFEL tunnel by end of September ‘15.
First beam in E-XFEL Injector by the end of ‘15,
Cavities after mechanical fabrication
Cavities ready for Vertical Test @ LASA
Cavity after He-tank integration with tuner and motor
String of cavities with Power Coupler after roll out from Clean Room @ DESY
3rd Harmonic Cryomodule at the final installation stage

## Slide 43: Module Assembly by INFN at DESY

## Slide 44: WP46 - Cavity Fabrication and Test
Weld inspection
Cavity Tests
Clean Room at INFN
VTA at INFN
BCP at EZ
RF testing
VT preparation
All cavities above specifications!
XFEL Injector’ Beam
3rd Harm Off
3rd Harm On
String Assembly

## Slide 45: XFEL 3rd harmonic: cavites and Cryomodule

## Slide 46: E-XFEL in a nutshell
1.3 GHz SRF linac with 17.5 GeV, 5 kA bunches for an FEL operating in the 1-0.5 Å regime
  27000 e- bunches/s (0.6 ms flattop @ 10Hz, 2700 b/pulse)
  1 klystron driving 4 8-cavity modules in vector sum mode
Beam quality (emittance at high currents) is the key
  Three bunch compression stages at 130 MV, 600 MeV, 2.4 GeV to raise the bunch current
AH1
300 kW
A2
A3
A4
A5
A6
A1
SASE1
SASE2
SASE3
1 Module
300 kW
300 kW
5 kW
0.24 kW
A24
n.c.Gun
1.3 GHz
6 MeV
LH, Dogleg, BC0
130 MeV
BC1
600 MeV
BC2
2.4 GeV
Collimation
6 to 17.5 GeV
40 m
240 m
470 m
1460 m
2130 m
2440 m
3100 m
3300 m
0 m
P. Pierini, SRF2017, Lanzhou

## Slide 47: 3rd Harmonic for Longitudinal Phase Space
EXFEL needs longitudinal phase space manipulation before the bunch compression stages
  A proper current profile along the bunch for lasing is thus obtained by control of energy chirp, curvature, skewness in the longitudinal phase space
    Removing the RF curvature from the 1.3 GHz module caused by the long bunch length at the injector
    Compensating wake fields in the main linac, BC non linear optics, space charge effects…
How? Add a (third) harmonic voltage and properly set its amplitude and phase relative to the main accelerating voltage
M. Dohlus, T. Limberg, “Bunch compression stability dependence on RF parameters”, 27th FEL Conference (2005) p. 253

## Slide 48: Phase space manipulation in a glance
With third harmonic manipulation
Off crest operation creates chirp+curvature
After AH1 (130 MeV)
AH1 removes curvature and prepares for BC
After A1 (130 MeV)
Using only A1 to chirp the beam (no AH1)
Longitudinal phase space
Current along bunch
chirp+curvature!
At final compression stage good current profile
Beam flattened for good FEL emission
👍🏻
After BC2 (2.4 GeV)
After L3+CL (17.5 GeV)
At final compression stage current spike
Large current spike but low charge for FEL!
👎🏻
After A1 (150 MeV)
50 mm
10 mm
1 mm
P. Pierini, SRF2017, Lanzhou

## Slide 49: What is in the AH1 module?
The third harmonic system (AH1) is functionally like a standard main XFEL module, but contains 8 cavities at 3.9 GHz (3 times the frequency, therefore 1/3 of the size)
IN-KIND Contribution to XFEL by INFN (50%: Cavities and module) and DESY (50%: Couplers, RF and infrastructure)
  Joint: installation, technical commissioning and initial operation
A1
AH1
Beam
P. Pierini, SRF2017, Lanzhou

## Slide 50: Cavity production and testing
3 prototypes and 2 batches of 10 cavities procured by INFN
  Mechanical production & BCP treatment at Vendor
  Preparation to test and VT at INFN-LASA
1st batch (X3M1)
2nd batch (X3M2)
11
MV/m
15
MV/m
P. Pierini, SRF2017, Lanzhou

## Slide 51: VT Qualification summary
 | Eacc [MV/m] | Q0 [109]
First Batch | 20.4±1.1 | 2.39±0.29
Second Batch | 19.9±2.4 | 2.77±0.65
 | 20.1±1.9 | 2.58±0.45
RBCS: as expected from the f2 scaling
R0: Follows JLAB scaling R0=5.3+1.89 (f[GHz]) [nW]
<10 mG in VT
P. Pierini, SRF2017, Lanzhou

## Slide 52: Behavior at high field
All cavities quench at around 20-22 MV/m
  Dissipated power on the cavity in the 20-100 W range
  Thermal equilibrium model with field dependent BCS reproduces the slope of Q0 vs Eacc curves at different T
  Thermal breakdown around 20 MV/m seems the limiting mechanism of 3.9 GHz structures with BCP
J.T. Maniscalco et al., ”The importance…”, JAP 121, 043910 (2017)
P. Pierini, SRF2017, Lanzhou
Heat transfer can be linearized
assuming weak quasi-particle overheating
Overheating
parameter
A. Gurevich, “Reduction of Dissipative Nonlinear…”, arXiv:1408.4467 (2014)

## Slide 53: Validation test in AMTF (March 2015)
No module test prior to installation!
Horizontal test for the cavity package qualification
  Cold Tuning System & Coupler assembly
Open loop operation at 20 MV/m
  Quench at 24 MV/m,10 Hz, 1.3 ms
  VT: 21 MV/m (quasi CW)
P. Pierini, SRF2017, Lanzhou

## Slide 54: Major AH1 Assembly Milestones
September 23 2015
July 3 2015
P. Pierini, SRF2017, Lanzhou

## Slide 55: The assembly in Halle III (14 weeks)
P. Pierini, SRF2017, Lanzhou

## Slide 56: Final Preparation stages in tunnel
Assembly WG distribution
Injector String Integration
Dec 10: Start cooldown
Dec 15, Cryo OK- cavity pre-tuning
Dec 16, calibration: AH1 Ready
November 11 2015
P. Pierini, SRF2017, Lanzhou

## Slide 57: RF Distribution layout
Vector Sum
  8 cavities
1 Pulsed Klystron (Max. 80 kW)
Fixed coupler
3-stub tuners for QL adjustment cavity phasing
Klystron up to 60 kW
P. Pierini, SRF2017, Lanzhou

## Slide 58: First operation at nominal gradient on Day 1
18 December 2015
  Operation with no beam
  First rough calibration (LLRF)
    Assume Pcav=Pkly/10
  Nominal pulse structure
    Fill: 750 us/FlatTop: 650 us
  Gradient well above nominal
    40 MV of VS voltage
    First quench > 45 MV
  Cavity phasing missing and QL values not yet tuned
  LLRF in FB mode
Arbitrary calibration/need beam
P. Pierini, SRF2017, Lanzhou

## Slide 59: Beam Based calibration: Cavity Phases
January 2016, on beam
  Beam transients
  Phase Calibrations
Preliminary to :
  Phase Tuning
  QL tuning
Large initial cavity phase spread
  WG assembled in tunnel, no cal.
Beam induced cavity gradient changes
Cavity transient, QL determination and phase calibration
Tune with
  3-stub tuners
  WG Spacers
160°
After operation of a few stub tuners
P. Pierini, SRF2017, Lanzhou

## Slide 60: QL tuning & Phase alignment
1 February 2016, AH1 moved 1 ms after the beam
  Allow injector commissioning while aligning cavity phases
Individual maps of all 3-stub tuner positions
QL-Phase region
Case of design in range of tuner
QL-Phase region
Case of design outside range of tuner
WG spacers installed on 3 cavities
P. Pierini, SRF2017, Lanzhou
QL tuning & Phase alignment

## Slide 61: Started regular operation in injector
10 February 2016
  QL aligned well within the 10% requirement
  Phases within 15°
16 February 2016
  Back on beam
  Moved to -180°(wrt on-crest), calibration with beam energy
P. Pierini, SRF2017, Lanzhou

## Slide 62: Quench Gradients (VT vs Module)
RF based calibration in tunnel initially did not correlate too well with VT quench gradients
  Due to large uncertainties in WG distribution details
  Good agreement after beam based calibrations
P. Pierini, SRF2017, Lanzhou

## Slide 63: HOM performance
Cav | QH1 | QH2
C1 | 7.29E+09 | 5.64E+11
C2 | 1.14E+12 | 5.72E+10
C3 | 8.70E+10 | 1.33E+11
C4 | 1.91E+09 | 6.29E+11
C5 | 3.18E+11 | 2.68E+11
C6 | 8.32E+11 | 5.05E+11
C7 | 1.36E+11 | 6.28E+10
C8 | 4.50E+11 | N/A
Cavity Q0 is 2E9 (VT measure)
Qt is 1E10 (VT calib)
C1 HOM1 suboptimal tuning
C4 HOM1 detuned (cavity Q0)
However, stable thermal behavior at 1.3 ms, 10 Hz operation up to SP in excess of 40 MV
~40 MV, 0.5 K temperature rise
in C4 Hom region
Thermal sinking is sufficient for stability (at 1% d.f.)
P. Pierini, SRF2017, Lanzhou

## Slide 64: Beam Based Calibration of Module voltage
RF calibration did not give sufficient consistency in A1/AH1 correlation. BB calibration using dispersive section.
A1/AH1 need to be in good relative calibration (phase and amplitude) to control the beam with Sum Voltage Controls
  Improved consistency in VT/XTIN quench fields
  Important to check after RF calibrations are done
P. Pierini, SRF2017, Lanzhou

## Slide 65: RF Curvature linearization by AH1
Beam image on screen in the spectrometer beamline
← AH1 off
AH1 on →
X (i.e. E)
Y
Beam image on screen in the spectrometer beamline, switching on the Transverse Deflecting Structure
← AH1 off
AH1 on →
Vector Sum Control of the sum RF field of the two modules allows to set the beam shape parameters (e.g. chirp, curvature, skewness) for proper matching to the downstream compression stages
Y (i.e. t or s along bunch)
X (i.e. E)
P. Pierini, SRF2017, Lanzhou

## Slide 66: Summary of 3.9 GHz Module Experience
RF commissioning and operation of the 3.9 GHz module in the tunnel was a success
  Achieved performances above nominal during the early injector commissioning stages in December 2015, with the AH1 pulse shifted in time from the beam
Module in regular operation with beam since January 2016 in the Injector run and ready for operation at the start of the XFEL commissioning phase in January 2017
First XFEL lasing at 9 Å on May 4th 2017 (then 2 and 1.5 Å reached in summer): final confirmation of proper third harmonic system performance
  (and of course of many other important systems…)
Since then, AH1 is a crucial part of the European XFEL user facility reliably operating in Hamburg

## Slide 67
Thank you for your attention