## Slide 1
Pheripheral Electronics
Mauro Citterio
--------
INFN Milano

## Slide 2
Index
Fanout layer 0 considerations
HDI considerations
Tail and Transition card ...
  Very little

## Slide 3: DAQ reading chain for L0-L5
3
High rad area 15Mrad/year
Off detector
low rad area
Optical Link
2.5 Gbit/s to ROM
Counting room
Std electronics
FEB
DAQ chain independent on the chosen FE options
Optical 1 Gbit/s
~1-2 m
LV1
Data Encoder IC .... Specs are under discussion
Rad-hard serializer to be finalized
 looking into a low power/low speed version
Copper tail: lenght vs data transfer to be studied
fibers
Example of a read-out section
Detector
HDIs
C
Front-end chips
Copper bus
UPILEX+Cu (?)
Transition card
Serdes
or FPGA
ROM

## Slide 4
Fanout (layer 0)
 Based on this numbers, the number of output lines exceeds 6x128
  Details need to be defined …………….
Hp: Aluminum/Kapton 2 layer fanout
  Sketch presented in Frascati (Dec. 2011).
  Based on the assumption of staggering the two layers to “match” sensor pitch
  Real design in progress IF fanout min. pitch is 85 um (~ twice IC pad pitch)
    Bonding always toward detector side (Stefano/Filippo concern resolved)
    Fanout resistance and inter-trace capacitance not estimated yet (Ref. 2W/cm, 6 pF)
    Narrow pitch needed over a length of ~ 25 mm
    Overall fanout widht not less than 35.9 mm
  If adjacent sensor lines do not correspond to adjacent IC lines then overall thickness could be less (~ 30-31 mm)
Layer 0 dimensions |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Physical |  | Length (mm) |  | 104 |  |  |  |  |  |  |  |  |  | 
 |  | Width (mm) |  | 13.9 |  |  |  |  |  |  |  |  |  | 
Frame Size (mm) |  |  |  | 0.5 |  | Hypothesis Stefano |  |  |  |  |  |  |  | 
Active |  | Length (mm) |  | 103 |  |  |  |  |  |  |  |  |  | 
 |  | Width (mm) |  | 12.9 |  |  |  |  |  |  |  |  |  | 
Trace (mm) |  |  |  | 0.025 |  |  |  |  |  |  |  |  |  | 
Space (mm) |  |  |  | 0.025 |  |  |  |  |  |  |  |  |  | 
Pitch (mm) |  |  |  | 0.05 |  |  |  |  |  |  |  |  |  | 

## Slide 5
HDI
Collaboration with Aurel is progressing
  Technical meeting in Milano on Monday January 29th
    Better definition of the “trial samples”
    Schedule agreed upon (Milano is charged of characterizing samples)
    Exercise completed by end of March
Size of HDI
  Similar to Babar +/- 10%
    Size stay ~ the same by taking advantage of improved trace resolution
    Not sure I understand “gangling”, “pairing” …. (Help from …..)
      How many ICs on each HDI type
    Number of layers again similar to Babar HDI
    What on the hybrid beside the ICs and the passive components
      It strongly depends from the digital input/output of the IC
        LVDS? All of them?
        How many lines are proprietary per chip? How many can be shared?
          3 clocks (System clock, Time Stamp clock, readout clock)
          1 Data In
          1 Reset
          1 Trigger

## Slide 6
HDI
    How many Output Data lines?
      From 1 to 4 ………… programmable quantity?
      Status …..
  The overall quantity of IN/OUT lines will tell us if we need a MUX/ENCODER (+SERIALIZER?) on the HDI
    Goal has to limit the complexity of the “tail” between HDI and transition card
      Hp: transmission at this point is on copper
      Hp: we are using magnet wires
        The tail length is ~ 20-30 cm
        How to bundle them is related to the communication speed
    The encoding is done in the IC?
      It should be consistent with what be used in the transition card where the transition to optical fiber need to be done
    MUX/ENCODER and tail in common to all layers will be advisable
MUX/ENCODER
  Guess: we will end up having at least a MUX
    At least in the innermost layers
    In any case the IC has to be capable of driving the tail (test on bench on a 50 cm tail length, 6 lines “all/few on”, max rate, using prototype tail ) and receiving data from the tail (assuming “compatible transmission” from the tail)

## Slide 7
HDI
  Design of the MUX or MUX/ENCODER or MUX/Encoder/Serializer
    Size of this IC
      The only reference that we can have is the CERN GBT project
        Taking away some blocks?
          Some of the slow control maybe
        Die size is …. < 2 x 2 mm …… reasonable
      Size is not a stopping block
      Using GBT has pros and cons
        It does not look absolutely necessary
      Such an IC is a challenging project
        It is a overall problem (see Aloisio’s talks)
        The functions really needed …….
      Technology of choice
        Milano/Bari would like to adopt TSMC 65 nm
        No more SOS
        Not worthwhile IBM
        Capable of standing against radiation
Power distribution
  HP: IC can not withstand voltages higher than 1.5 V
    Even in case of interruption of sensing

## Slide 8
HDI
  Hp: current absorbed is ~ 1 Amp or more per HDI
  An intermediate voltage regulation point IS NEEDED
    DC-DC converter, LDO not yet decided
    Where the max voltage is 2.5 Volt
      More if a shunt LDO is used
    The breaking point is as near as possible on the HDI
      Nearest place is the transition card
        Space required on the transition card at least 9 cm^2
        Cooling required > 3 W on the card
          Strongly dependent from the voltage drop absorbed by the transition card
    “Step-Down” ratio is
      Minimum 2, maximum is 5.5 if LDO
      Minimum 2, reasonable maximum is 10-12 if DC-DC conversion
      High Step down is better ….. Cable’s AWG increases
    The devices at the breaking points must be rad-tolerant
      Rad-tol DC-DC converter ?
      Rad-tol LDO …… difficult to get some or EXTREMELY expensive
    Remote power supply can NOT avoid this problem …

## Slide 9
HDI
  Connection between HDI and Transition Card (envelope on HDI W x L x H …….)
    Detector bias
      Not yet addressed
    Supply Bias
      2x4 wire (2 power, 2 sense), twist in quad + drain + shield
        Grounding-shielding rules undefined
      {2x[2xAWG28+2xAWG32]+drain+shield}
      2-5 mW contact
      Connector?
        Strongly related to cable specs
          Cable diameter
          [~ 7-8 mm (not necessary round)]
        Low mass aluminum
          Hermetic class ….if any
          How this was done in Babar? …………
    Data lines
      Magnet wire (AWG36 maybe AWG 38)
        2x HDI Data Out Lines
          No Mux example > 6x4x2x1.5mm^2
        Interesting Panasonics connector
          Maybe usable also for HV and LV also

## Slide 10
HDI
  Connection between HDI and Transition Card
    Detector bias
      Not yet addressed
    Supply Bias
      2x4 wire (2 power, 2 sense), twist in quad + drain + shield
        Grounding-shielding rules undefined
      {2x[2xAWG28+2xAWG32]+drain+shield}
      2-5 mW contact
      Connector?
        Strongly related to cable specs
          Cable diameter ~ 7-8 mm (not necessary round)
        Low mass aluminum
          Hermetic class ….if any
    Data lines
      Magnet wire (AWG36 maybe AWG 38-40)
        Taking away some blocks?
Summary of what is on the HDI
  Front-end Ics
  MUX/ENCODER maybe
  Connector HDI/Tail
  Passive components

## Slide 11
Tail and Transition Card
Tail
  Magnet wires …. Many ideas, few results
  IN/OUT connectors, again preference for the Panasonics
  Length (two conflicting constraints)
Transition Card
  It contains at least bi-directional electro/optical transmission (SERDES maybe, Laser Driver, VCSEL, …. )
    I am trying to copy the info from the Versatile Project
  It contains also the electronics for the voltage breaking point
  It contains also the HV, LV connection
    Not details yet
  Mechanical aspects
    Not yet addresses
      Important the interface established between Pisa and Milano mechanical engineers
      We need an overall envelope
    Cooling is needed ….. 0.2-0.3 W/cm^2 … and growing ……