## Slide 1: SuperB SVT Definition of sensor design and z-side connection scheme
Irina Rashevskaya, Lorenzo Vitale, Livio Lanceri, Luciano Bosisio
INFN-Trieste e Università di Trieste
*

## Slide 2: Layer 1-5 - Sensor dimensions
We assume the layer dimensions given by Filippo
  the r-φ cross-section remains the same as in BaBar
  the length of the barrels is increased by a factor of ~1.5
  the wedge sensors retain the same size as in BaBar
We minimize the number of sensors in each ladder, with the following constraints:
  8 different sensor models, fitting within a 150 mm wafer (a dedicated sensor for each barrel ladder type, plus the wedge sensor)
  Even number of sensors in each ladder, allowing symmetric forward-backward readout

## Slide 3: Microstrip Sensor design for Layers 1 - 5
Ladder composition, sensor models and dimensions have been defined
Physical dimensions, number of strips and pitches for the nine different sensor models.
Active area is:
0.7 mm inside the physical sensor area in Ly 1 – 5 (300 µm thick)
0.6 mm inside the physical sensor area in Ly 0 (200 µm thick)

## Slide 4: Ladder Composition
Number of the different sensor types per module, and total required number of sensors,
including one spare module per module type (two for layer 0).
For layers 1 – 5 :
Total sensor area 1.51 m2
Total number of sensors 300
Total number of wafers 254 (two wedge sensors can fit in a 150 mm wafer)

## Slide 5: Sensor Suppliers
Possible suppliers of double-sided sensors on 150 mm wafers:
  Micron
    200 µm and 300 µm thickness OK
    5 mm minimum clearance from wafer edge
  Sintef
    300 µm thickness only
    8 mm minimum clearance from wafer edge
  Hamamatsu
    320 µm minimum thickness
    5 mm minimum clearance from wafer edge
  CiS (Erfurt, D) presently only 100 mm, 150 mm within 2013 (?)
  FBK-irst (Trento) presently only 100 mm, 150 mm within 2014 (?)
  E2V (UK) is evaluating the possibility to fabricate DSSD.

## Slide 6: z-side readout: ganging of strips
The number of readout strips exceeds that of available amplifier channels => at least a part of the readout channels must be connected to more than one strip.
In BaBar we choose to gang together two far apart strips:
In the SuperB SVT the increased length of the modules will force us to gang together up to three strips in Ly 4 & 5, with a further increase in capacitance and noise.

## Slide 7: An alternative option: ‘pairing’ of strips
At small theta angles (large incidence angles) the track traverses several z-strips (up to 9 in the inner layers!) and the signal becomes ~ proportional to the strip pitch ( < wafer thickness)
This suggest to bond two or more adjacent strips to a single fanout trace, effectively increasing the strip pitch and the signal into a readout channel, with a less than proportional increase in capacitance.
This gives better S/N and efficiency at small theta angles compared to non-paired strips. The improvement is more important when compared to ganging, for which the strip capacitance is proportional to the number of strips ganged together, but the signal is that of a single strip. Moreover, in the pairing scheme the fanout capacitance too is lower, because of the doubled trace pitch.
In addition, at small theta angles pairing is expected to give better spatial resolution with respect to ganging.
To preserve spatial resolution, two strips can be paired only when the track projection exceeds 2 times the pitch.

## Slide 8: Inner Layers: Pairing only
Proposed z-side strip connection for Layers 1, 2, 3.
Layer | # of channels with NO pairing | # of channels with pairing x 2 | # of channels with pairing x 3 | Total # of readout channels
1 | 688 | 208 | 0 | 896
2 | 627 | 132 | 137 | 896
3 | 957 | 196 | 127 | 1280
A prototype fanout for layer 3 is being produced with this pairing configuration.

## Slide 9: Outer Layers: Pairing + Ganging
Proposed z-side strip connection for Layers 4, 5.
Pairing alone (2 or 3 strips, depending on position) is not enough: we must in addition gang together 2 and 3 strips.
Note: on wedge sensors the track incidence angle is not large enough to allow pairing of strips: the track projection along z never exceeds 2 x readout_pitch (= 2 x 210 µm).
Layer | Total number of strips | Number of channels with the indicated pairing multiplicity |  | Number of channels needed with pairing only | Number of readout channels available | Ganging factor needed | Number of channels with the indicated ganging multiplicity |  | 
 |  | x 1 | x 2 |  |  |  | x 1 | x 2 | x 3
4a | 1398 | 1108 | 145.0 | 1253 | 640 | 1.96 | 27 | 613 | 
4b | 1448 | 1134 | 157.0 | 1291 | 640 | 2.02 |  | 629 | 11
5a | 1761 | 1241 | 260.0 | 1501 | 640 | 2.35 |  | 419 | 221
5b | 1815 | 1265 | 275.0 | 1540 | 640 | 2.41 |  | 380 | 260

## Slide 10: Outer Layers: Pairing + Ganging
Example: Proposed connection scheme for Layers 5b z-side fanout.
 | Fanout for Layer 5b |  |  | 
Sensor # | From strip | To strip | Pairing | Ganging
1 | 1 | 260 |  | x 3
 | 261 | 499 |  | x 2
2 | 1 | 141 |  | 
 | 142 | 401 |  | x 3
 | 402 | 449 |  | x 2
 | 450 | 499 | x 2 | 
3 | 1 | 499 | x 2 | 
Wedge | 1 | 58 |  | 
 | 59 | 318 |  | x 3

## Slide 11: Next steps
Urgent: Review the strip parameters needed for evaluating the performance of the front-end (C, R_series, R_parallel, I_leak after irradiation).
We are going to measure the capacitance of different pairing configurations on a BaBar-like FBK-irst sensor
  two sensors glued on fiberglass boards, for measurements on p-side and n-side, respectively
  bonding and measurements to start next week
Paired strip capacitance will also be evaluated with simulation.
The final design should be based on a realistic evaluation of S/N and spatial resolution, obtained through an ad hoc MC simulation of the detector response.