## Slide 1: EuPRAXIA@SPARC_LAB FEL beamlines
F. Villa, INFN-LNF
On behalf of the EuPRAXIA@SPARC_LAB collaboration

## Slide 2: Outline
Preliminary FEL simulations results
Scientific case and timeline
AQUA beamline
  Layout
  Optics and diagnostics
  Open questions
Discussion

## Slide 3: EuPRAXIA@SPARC_LAB
Accelerator area 62m
Undulators area 38m
FEL User area 50m
Clean rooms area 32m
HEP experimental area 49m
Synchronization
Lasers (photocathode, HP)
HP laser users
HEP users with electrons (and HP laser)
RF supply area 55m
Photoinjector
X-band linac (and compressor)
Plasma acceleration

## Slide 4: FEL beamlines
AQUA beamline: SASE FEL from 4(3) to 10(15)nm with polarization tunability, in the EuPRAXIA@SPARC_LAB TDR
ARIA beamline: seeded FEL from 50 to 150 nm with polarization tunability, recently approved with regione Lazio funds (still in early phase of design)

## Slide 5: Undulators
Undulator parameters | ARIA | 
 | Modulator | Radiator
Period (mm) | 100 | 55
Active length (m) | 3.0 | 8.4
Seeding laser | OPA configuration | 
Seeding wavelengths (nm) | 320-400 + 600-800 | 
Seeding energy | >20 µJ | 
Seeding duration | 200 fs | 
Undulator parameters | AQUA
Period (mm) | 18
Maximum strength (k) | 1.47
Minimum gap (mm) | 6
Active length (m) | 19.8
APPLE X undulator allow for polarization tuning
(from linear to circular)
Seed laser
tunability

## Slide 6: Expected FEL radiation at undulators end
AQUA PWFA
circular
AQUA PWFA
linear
 | AQUA FEL parameters (Linear Polarization) | AQUA FEL parameters (Circular Polarization)
Central wavelength range | 4.0 nm, 310eV | 4.0 nm, 310eV
Spectral bandwidth (rms) | 0.088% | 0.117%
Beam length (rms) | 3.50 fs | 3.76 fs
Beam transverse size (rms) | 133 um | 132 um
Beam divergence (half angle) | 0.023 mrad | 0.022 mrad
Photons per pulse | 2.33*10^11 | 2.77*10^11
Polarization | H | C
Repetition rate | 100 Hz | 100 Hz

## Slide 7: First S2E WP: AQUA SASE beamline

## Slide 8: Stability (AQUA SASE beamline)

## Slide 9: ARIA seeded beamline, preliminary simulations

## Slide 10: AQUA beamline scientific case
Coherent imaging
X-ray spectroscopy
Raman spectroscopy
Photo-fragmentation of molecules
(Large) Viruses
Organelles
Bacteria/Cells
Metals
Semiconductors
Superconductors
Magnetic materials
Organic molecules
Experimental techniques and typology of samples

## Slide 11: ARIA beamline scientific case
Photoemission
Spectroscopy
Photoelectron Circular Dichroism
Raman spectroscopy
Photo-fragmentation of molecules
Time of Flight Spectroscopy
Gas phase & Atmosphere
(Earth & Planets)
Aerosols
(Pollution, nanoparticles)
Molecules & gases
(spectroscopies, time-of-flight)
Proteins
(spectroscopies)
Surfaces
(ablation & deposition)
Defining experimental techniques and typology of samples (and applications)

## Slide 12: Timelines
Courtesy A. Falone

## Slide 13: Photon beamlines
AQUA beamline

## Slide 14: AQUA beamline
10 m
(6 m from undulators)

## Slide 15: AQUA beamline
11 m

## Slide 16: AQUA beamline
39 m

## Slide 17: AQUA beamline losses
System | Transmission | #
Mirror chamber | 0.80 (0.85) | 1
BDA | 0.99 | 2
BPM | 0.98 | 2
Spectrometer | 0.75 (0.80) | 1
Monochromator | 0.08 to 0.02 | 1
Intensity monitor | 0.99 | 2
Time measurement | 0.99 | 1
Split & delay | 0.41 (0.52) | 1
attenuators | 1 to 0 | 3
YAG screens | 1 or 0 | 13
K-B focusing | 0.64 (0.72) | 1
Total transmission
without monochromator and S&D: 34% (with R=85% mirrors: 44%)
with Split & Delay: 14% (23%)
with monochr. 1-g: 2.6% (3.3%) x
with monochr. 2-g: 0.8% (1.0%) x
with monochr. 2-g + S&D: 0.32% (0.52%) x
 | AQUA FEL parameters (Linear Polarization) | AQUA FEL parameters (Circular Polarization)
Central wavelength range (nm, eV) | 4.0 nm, 310eV | 4.0 nm
Spectral bandwidth (rms, % to the central wavelength) | 0.088% | 0.117%
Beam length (rms, fs) | 3.50 fs | 3.76 fs
Beam transverse size (rms, um) | 133 um | 132 um
Beam divergence (half angle, mrad) | 0.023 mrad | 0.022 mrad
Photons per pulse (number) | 2.33*10^11 | 2.77*10^11
Polarization (direction) | H | C
Repetition rate (Hz) | 100 | 100

## Slide 18: Open questions: S&D line
39 m
8m
~26 ps delay
~100s fs delay

## Slide 19: Open questions: Monochromator

## Slide 20: Open question: time and polarization measures
Gas ionization ToF array + THz streaking
Nature Phot 12, 215 (2018)
Opt. Expr., 22, 12869 (2014)
Transient reflectivity encoding of arrival time