## Slide 1
Mimosis_1

## Slide 2
MIMOSIS-1
1024 x 504 pixels
Pixel pitch: ~30 x 27 µm
200 kfr/s
31 mm
17.2 mm
13.55 mm
Clk PLL
(40MHz)
Slow control
I2C
Output Clk (160MHz)
Data Marker (5µs)
1 to 8 Data Output
(320MHz)

## Slide 7
0 | 1
3 | 2
1007 | 
PE 0
PE 7
0 | 
1007 | 
Pixel dimension: 26.88 µm (height) x 30.24 µm (width)
1 region = 8 Priority Encoder

## Slide 8: ANALOG FRONT END AS MEMORY
STATE
(Latch)
STROBE
OUT_D
OUT_A
Particle hit
PIX_IN
Pulse duration
The front-end acts as an analogue delay line
  2 µs peaking time
When STROBE is asserted, the front-end binary output is latched into the pixel state register
Hit driven architecture
  Pixel state register readout by a zero suppression circuit based on priority encoding
2 us Peaking time
Particle hit
ΔV = Q/C : ~ 10 ns
Reset : ~1 ms
t1
t2
ANAOUT[0]:
ANAOUT[1]