## Slide 1: ASPIDES WP1- ASIC and design verification
F. Licciulli – INFN Bari

## Slide 2: WP1 – Specifications for sensors and readout electronics
Requirements | Dual readout calorimetry | Cherenkov (eg RICH, IACT) | DM | Neutrino
SiPM Unit area (mm^2) | 1 x 1 | 2 x 2 | 1 cm x 1 cm | 6 x 6
Micro-cell pitch (um) | 25 - 40 | 25 - 40 | 25 - 30 | 50 - 150
Macro-pixel area (um^2) | 500 x 500 | 1000 x 25 / 1000 x 40 |  | 
PDE (%) | > 20 | > 40 | > 45 | > 35
DCR (kHz) | <100 kHz/mm2 | very low for single pe detection | <0.1 Hz/mm2 (at LN) | <0.2 Hz/mm2 (at LN)
AP (%) | <1 | few |  | <5%
Xtalk (%) | few | few |  | <35%
Xtalk (%) | few | few | Total Correlated Noise Probability (Xtalk + AP) < 60 % | 
Trigger | external, self | self, external | self | 
Output data: light intensity | no. of fired cells in 1 or 2 time windows (10's of ns long) | No. of fired cells |  | 
Output data: time | time of arrival of the first photon in the window, possibly of the last photon (TOT) | ToA and ToT | ToA and TOT | 
Time resolution (ps) | < 100 | < 100 single pe |  | 
Module size and form factor | strip with 8 units (1mm x 16 mm), pitch of 2 mm | Strips on N units (1 mm or 2 mm in height and length according to the requirements) |  | 

## Slide 3: WP1 – MPW planning
News from LFoundry
  Only one MPW shuttle run in 2025: 15th September 2025
  There is another M6 user: the extra budget can be divided into 2 quotes
  The option of having two separate designs is valid: extra price for dicing and backgrinding is around 800 € t.b.c.
MPW Si Area
  ASPIDES budget for prototype: 50 k€ -> 40.980 € NOT VAT
  LFoundry CMOS 110nm cost: 2.520€/mm2
  M6 extra cost 18.800 € -> 9.400 € to be considered due to the second user
  Two design option -> 800 €
  Si Area for MPW = 30.780 € / (2.520 €/mm2) = 12,2 mm2
  Prototype proposal:
    Two designs of equal area (6 mm2): aspect ratio?

## Slide 4: WP1 – to do list
Fill the LF TAPE-OUT form twice, one for each design:
  Almost completed, to be checked with other designers
Ask quotation for packaging: suggestions for package?
Design!