## Slide 1
Motivations
KM3Net VEOC
Based on developments on solid cable at NEMO and Antares project and proto cable of Seacon.
Optimizing properties like;
flexibility
weight
drag resistance
costs
KM3NeT VEOC (Vertical Electrical Optical Cable)

## Slide 2
KM3Net VEOC
Goals
-Design
-Cable Specs
-Layout
-Pressure Balanced Oil Filled cable design (PBOF)
-Storage
-Connection to DOM (BEOC)
-Prototyping
-Prototype VEOC I & VEOC IIa (pressure tests)
-Prototype VEOC III, VEOC IV, VEOC IIb (spiral test)
-Summery of tests
-Conclusion
-Outlook
KM3NeT VEOC (Vertical Electrical Optical Cable)

## Slide 3
KM3Net VEOC
Specifications of the VEOC |  |  | 
Type | specs | value | comments
Optic/ electronic | Optical 12 | Attenuation <1 dB/Km los | 
 | 400 Vdc | Voltage window 350-400 Vdc | Power inventory
Du Specs Mechanical | Density | =water (1048 kg/m3) | reduce load on Dyneema cable
 | Projected area | <0,45 M2 | reduce load on Dyneema cable
 | Storage of cable for deployment | Cable flexible Bending radius <120 mm | package
 | DU life time | 15 Years | 
Environment | Pressure | 60 MPa | 
 | Chemical | Sea water | 
 | Temperature | 15 °C | 

## Slide 4
Cable characteristics.
VEOC Cable
1
2
3
4
Cross section of the
pressure balanced cable
1) Outer shell ¼ LDPE Tube
2) 11 optical fibers
3) 2 Electrical wires
4) Oil Filling middle
Comparing Diameters
PBOF= Pressure balanced oil filled Solid= cable of MacArtney just as example
 | VEOC | Drift | buoy | ropes | Weight
 | mm | m | N | mm | Kg/km
PBOF | 6.35 | 167 | 6000 | 4 | 11
PBOF | 10 | 199 | 7600 | 5 | 6.9
solid | 10 | 225 | 8620 | 5 | 82
Just as example for trends

## Slide 5
Layout
860 Meter
Veoc 1
Veoc 2
DWDM
Connecting 11 DOM’s
Connecting 9 DOM’s
KM3Net VEOC
Veoc
Beoc
Dom
Connector
DWDM

## Slide 6
Cable layout spiral dimensions
KM3Net VEOC
D 68
D 149
624
624
Detector unit
Detector unit pallet
Storage

## Slide 7
Test Rope management July 2011
4 m
Dyneema® Reel
VEOC
Roll Stabilility
KM3Net Rope & Cable management VLVnT11

## Slide 8
Connection to DOM (BEOC)

## Slide 9
KM3Net Rope & Cable management VLVnT11
Prototype VEOC I & VEOC IIa (pressure tests)
VEOC I Layout
VEOC II
100 meter Cable by.
22 fibers 1” tube 4 electrical wires
under pressure 60 MPa
Optical Attenuation 0,55 dB/Km
Nikhef , Seacon & NIOZ
210 meter Cable by
13 fibers in a bundle 2 electrical wires.
¼ “ LDPE tube
(fibers are bend bright 15 mm bend radius)
Test at pressure 60 MPa
Optical Attenuation 0,55 dB/Km
Nikhef, Baas, NIOZ & Seacon.

## Slide 10
Coiling
Heating
Steam Boiler
-100 °C
-5 min
-.1 MPa
Prototype VEOC III VEOCIV & VEOC IIb spiral testing
d1
d3
d2
D1 =167 mm 110 °C during 1 hour
D2 =190 mm 90 °C during 1 hour
D3 =320 mm no heat treatment
KM3Net Rope & Cable management VLVnT11

## Slide 11
Break Out Box
Connector Box
VEOC Spiral
Layout of VEOC III spiral Cable
KM3Net VEOC
Spiral Storage 45 m
Break Out Box
13 loose Fiber standard SMF 28 2 electrical wires 18awg
¼” LDPE tube

## Slide 12
40 m
Not stretched
Attenuation 11 dB/Km
Stretched
Attenuation 12 dB/Km
Stretched over a length
Green laser 125 mW
KM3Net VEOC
Sharp bend < 30 mm
Attenuation

## Slide 13
Problems with loose fibers
-Because of length differences in tube
optical fiber twist at some points in the tube
resulting in a small bend < 30
-Standard SMF28 fibers have a min. bend radius of 30 mm
Test of the proto type
KM3Net VEOC
conclusion of VEOC III spiral Cable

## Slide 14
KM3Net VEOC
Layout of VEOC IV spiral, Cable for better understanding of the spiraling process
40 M
¼ LDPE Tube 2 electric wires, 5 loose fibers standard SMF28
(fiber length 213 m, 1 Connector)

## Slide 15
40 m
Layout of Prototype IV Loose fibers Standard SMF 28 . Fiber Length 210 M
proto 2
New 40 meter Cable, Optical 1,1 dB/Km 5 fibers standard smf28
KM3Net VEOC

## Slide 16
Spiral
OTDR
Prototype IV Loose fibers Standard SMF 28 . Fiber Length 210 M
No bends smaller than 30 mm radius
But still a lot of bend < 40 mm
Loss 0,7 dB/Km
KM3Net VEOC

## Slide 17
Status
KM3Net VEOC
Spiral
0,37 dB/Km 100 C
Prototype IV Loose fibers Standard SMF 28 . Fiber Length 210 M

## Slide 18
Status
KM3Net VEOC
Sharp bend < 30 mm
3,6 dB/km
Prototype IV Loose fibers Standard SMF 28 . Fiber Length 210 M

## Slide 19
Status
KM3Net VEOC
3.6 dB/km
1,6 dB/km
Prototype IV Loose fibers Standard SMF 28 . Fiber Length 210 M

## Slide 20
Status
KM3Net VEOC
30 M
Build Up of test
Fibers are connected in series,
24 connections
Cable length is 210 meters
Spiralized over a length of 30 meters
Cable Build up:
2 x AWG 18
bundle of 12 Bend Bright fibers,
supplied by DRAKA
Test of cable with BendBright fiber and with Seacon connectors build by BAAS b.v.
210 m
Total Fiber length 2520 m
connector

## Slide 21
KM3Net VEOC
Attenuation after Heating 7,8 dB
Attenuation after stretching the spiral 8 dB
2
1
Total attenuation: Connectors + Fiber (2,4) km 7.86 dB
Attenuation @ 100°C 7,6 dB
Test of cable with BendBright fiber and with Seacon connectors
Losses due to Connectors

## Slide 22
Test of Nikhef Prototype
KM3Net VEOC
Cable | Oil filling | Tube diameter | Fibers/ Electric | Spiral test | Pressure Test (60MPa) | State of measurement | Attenuation | Fiber Type
VEOC I (100 m) | Oil | 25,4 mm | 12/4 | no | Yes |  |  | SMF 28
VEOC II (210 m) | Oil | 6,35 mm | 12/2 | no | Yes | Under pressure | 0.55dB/Km | BendBright
VEOC III (100 m) | Oil | 6,35mm | 12/2 | Yes | no | Spiral relaxed Spiral stretched | 11dB/km 12 dB/km | SMF 28
VEOC IV (40 m) | - | 6,35 mm | 12/2 | Yes | no | Coiling Cooled down Spiral stretched Spiral massage Spiral stretched | 0.7 dB/km 1,53 dB/Km 3,7 dB/Km 0.9 dB/km 1,6 dB/km | SMF 28
VEOC II (210 m) (spiral) | Oil | 6,35 mm | 12/2 | Yes | no | Spiral cooled down Spiral stretched | 0,55 dB/km 0,7 dB/Km | BendBright

## Slide 23
Blocked expansion
Status
Most interesting Conclusion of spiral test
KM3Net VEOC
Conclusion :
From the test it is clear the heat treatment used,
Were by the Cable is clamped in the aluminum tube preventing
the LDPE cable to expand . Resulting in plastic deformation and as result
giving the tube a sorter length. Calculated at 1% of the cable length.
This will bend the fibers and resulting in small fiber radius<30mm
..
Aluminum tube
VEOC
100 C
deformation and as result
the tube has a sorter length
Cooled down
Start
Shorter
Fiber

## Slide 24
Free expansion
Status
So some room for improvement in the spiral production
KM3Net VEOC
Conclusion :
From the test it is clear the heat treatment used,
Were by the Cable is clamped in the aluminum tube preventing
the LDPE cable to expand . Resulting in plastic deformation and as result
giving the tube a sorter length. Calculated at 1% of the cable length.
This will bend the fibers and resulting in small fiber radius<30mm
Aluminum tube
VEOC
100 C
No deformation and as result
the tube has the same length
Cooled down
Start

## Slide 25
Status
KM3Net VEOC
Conclusion :
BendBrightTM fibers significantly improve the cable optical performance when spiralized
(straight cable is already optimal in performance)
Heat Treatment has little influence because BendBright allows for smaller
bending radius (15 mm compared to 30 mm)
The new method for heating the cable will improve the optical performance
But more tests are needed to give an number

## Slide 26
Status
Are we meeting the VEOC specifications ? |  |  | 
Type | Specs | Values | comments
Optic/ electronic | Optical 12 fibers | Attenuation <1 dB/Km loss 0,7dB/km | 
 | 400 V dc | Voltage Drop <30 V | 
Du Specs Mechanical | Density | =water (1000 kg/m3) 1300 kg/m3 | 
 | Projected area | <0,45 M2 | 
 | Storage of cable for deployment | Cable flexible Bending radius <120 mm Bending radius >60mm | Package as Spiral is possible
 | Du life time | 15 Years ? | 
Environment | Pressure | 60 MPa With the PBOF pressure is no problem | 
 | Chemical | Sea water LDPE HDPE middle oil Resistant to Sea water | Used oil is environmentally friendly
Cost | Low | No splicing needed | 

## Slide 27
KM3Net VEOC
-optimizing production system
-Tooling for pulling fibers.
-Tooling for spiraling the cable. -Interests
Hydro group: consider this as most favorable solution but has no interest to participate
JDR: consider this as possible solution but they are specialist on solid cables
Seacon and MacArtney have there doubts to participate because they are
focused on solid cable.
VEOC V sections spiraled and sections straight for sea test at Catania VEOC VI & VEOC VII two cables for the mini-tower; 7 x interval with 2 active breakouts, tested in pressure tank VEOC VIII a 500m piece as planned for a real tower.
BEOC -Lead time ~10 wks. Seacon model, 5 weeks Nikhef model
(used for Antares connection)
Out Look

## Slide 28: Alternatives
Splices on each floor for each continuing fiber (manpower, reliability, attenuation)
For a complete solid vertical cable of 2 x 10 floors = 88 extra splices are needed
(average splice time is 5 – 10 min per splice)
Pressure resistant box (water blockers, etc.)
Solid Cable

## Slide 29
?