## Slide 1: Nuclear Physics Applications to Energy
Marco Ripani
INFN Genova
INSPYRE –INFN Legnaro National Laboratories – July 14 – 18 , 2025
The views and opinions expressed herein do not necessarily reflect those of the ITER Organization.

## Slide 2: What is energy?
We are familiar with situations where we consume energy…

## Slide 3
…or others in which energy is stored in some form

## Slide 4: The forms of energy
Electromagnetic
MechanicalKinetic(*)
MechanicalPotential
Chemical
(Potential)
Nuclear
(Potential)
Heat, too…
(thermal energy)
(*) kinetic energy = energy of motion

## Slide 5: Energy transforms
From potential to kinetic…

## Slide 6
From chemical to kinetic (or mechanical) …

## Slide 7
From chemical to kinetic (or mechanical) and electromagnetic (light)…

## Slide 8: Matter under a magnifying glass

## Slide 9
Snowflake
(from about 0,1 mm to a few mm)

## Slide 10
Onion cells
(about 0,01 mm)

## Slide 11
A pentacene sample…
C
H
Atomic force microscope
Pentacene atoms
(0,00000012-0,00000017 mm – a fraction of a millionth of a mm)

## Slide 12
Atoms are very many…
In one liter of water there are 33 million billion billion molecules

## Slide 13: Heat
Water molecules in steam move and hit each other at a very high speed, about 500 meters per second (1,800 km/hour)
Heat is nothing but mechanical (kinetic) energy

## Slide 14: The atom
What if we were able to see even smaller things?
Atomic nucleus
(about 0,000000000001 mm – one thousandth of a billionth of a mm)
Composed of protons (positive electric charge) and neutrons (no electric charge)
Simplest atom: Hydrogen  just one proton and no neutrons
“Orbiting” around are the electrons (negative electric charge)
The figure does not show the correct proportions: the nucleus is 100,000 times smaller than the atom!

## Slide 15: The atomic nucleus
Protons (positive electric charge)
Neutrons (no electric charge)
Electric charges with the same sign repel each other
Neutrons act as the "glue" that holds the nucleus together (it's called «strong nuclear force»)
The larger the nucleus, the more neutrons it needs
For example, Oxygen has 8 protons and 8 neutrons
The most abundant type of Lead in nature has 82 protons and 126 neutrons
But there is also Lead with 124 and 125 neutrons  "isotopes“  same chemical properties, different nuclei

## Slide 16: Radioactivity
Certain atomic nuclei are «unstable», that is, they tend to break up, releasing energy
Uranium 238 (92 protons, 146 neutrons)
Thorium 234 (90 protons, 144 neutrons)
Helium (2 p, 2 n)
Alpha (α) decay

## Slide 17: Elements and isotopes
There are many nuclear species
They are classified with two numbers:
Z = number of protons, which determines the chemistry
A = total number of nucleons (protons + neutrons)
each nuclear species is uniquely determined by its A and Z
about 4400 known (A,Z) combinations (species)
about 250 stable (minimum energy: equilibrium)
the rest: radioactive (unstable)
Some species decay in seconds...
...others in million (or even billion) years
N(t)=Number of decaying nuclei
time
=
Each radioactive substance has a characteristic time T1/2 in which its radioactivity is halved.

## Slide 18: The three main types of radioactivity
alpha
Very often, alpha and beta radiation lead to the formation of nuclei in excited states which decay by gamma radiation
emission of an alpha particle (= helium nucleus)
beta
a neutron transforms into a proton (or a nucleus with N neutrons and Z protons transforms into a nucleus with N-1 neutrons and Z+1 protons, emitting an electron (beta particle) and an antineutrino
gamma
emission of a gamma ray (=photon, such as radio waves, microwaves, infrared, visible, ultraviolet, X-rays:
the only difference is the wavelength or, if you prefer, the energy)
Radiation is part of our everyday life on earth

## Slide 19: Radiation around us
they can break DNA and cause mutations
probably plays a role in evolution
≈ 6000 decays per second of Potassium-40 (40K) per m3 of sea water
From air: about 10 atoms per second (Radon, Polonium, Bismuth, Lead) disintegrate in the lungs releasing alpha, beta, gamma
From diet: about 4500 atoms per second (Potassium-40) disintegrate in our body, releasing beta and gamma; also, about 2 atoms per second of natural uranium release alpha
From the ground and buildings: about 56,000 gamma per second pass through our body
From the sky: about 30 neutrons and 120 cosmic rays pass through our body per second

## Slide 20: What are the biological effects of radioactivity ?

## Slide 21: Biological effects of radioactivity
Radioactivity can be dangerous to the environment and humans due to cell damage (by direct exposure or by inhalation or ingestion)
Uranium 238 (92 protons, 146 neutrons)
Thorium 234 (90 protons, 144 neutroni)
Helium (2 p, 2 n)
Alpha decay (α)
Cell

## Slide 22: Is it possible to break up a nucleus ?
proton
neutron
Some (radioactive) nuclei can split on their own, but many do not (stable) or do so with difficulty
We suppose that a certain force must be applied
Put another way, you will need to supply a certain amount of energy

## Slide 23
distance
Potential energy
Kinetic energy
proton
neutron
Coulomb repulsion barrier (electrical repulsion)

## Slide 24
distance
Potential energy
Kinetic energy
I have to supply energy to overcome the barrier
If I can do that,
I will have produced nuclear energy
This process is called Nuclear Fission

## Slide 25: A special case, Uranium 235
Potential energy
If a neutron approaches this nucleus and is sucked in, it releases enough energy to jump the barrier very easily
The nucleus splits but more neutrons are also emitted
distance
92 protons
143 neutrons

## Slide 26: Nuclear fission
I created a fission chain reaction
Natural uranium, as found in mines
 0.7 % U 235 + 99.3 % U 238
235 U splits even when it absorbs an almost a very slow neutron, while 238 U needs a very fast neutron, so the reaction is more difficult  235 is «fissile», 238 is not
The two fragments possess a lot of kinetic energy transferred to atoms  heat
neutron
Uranium-235
(92 protons, 143 neutrons)

## Slide 27: How much energy is produced ? And what are the reaction products ?
The mass of the two fragments plus the mass of the neutrons makes a little less than the mass of the initial uranium nucleus  about a thousandth of the mass of the nucleus has been transformed into energy, according to Einstein's famous relationship
E = m c2
Fission provides 20 to 50 million times more energy than a chemical reaction
The biggest part of the energy released by the fission process is converted into heat
This energy is shared among
Kinetic energy of the two fragments
Kinetic energy of the 2-3 emitted neutrons
Gamma rays (electromagnetic energy)
antineutrinos (practically massless particles that pass through matter as if it were transparent)
With 1 gram of U-235, about 7,000 washing machines run for an hour
The same job would require almost 3 tons of coal

## Slide 28: Neutron radiative capture
 radiation
 radiation
electron
antineutrino
 radiation

## Slide 29: Nuclear energy and radioactive products
The two nuclei resulting from fission are called «fragments or fission products»  most of them are radioactive
Furthermore, we have seen that it is Uranium 235 that produces fission. Uranium 238 instead, with high probability absorbs the neutron, giving rise to a transformation chain that produces heavier elements, including Plutonium (that doesn’t exist in Nature)
However, plutonium can also give rise to fission, so it can be used as fuel
Other materials of the plant, subjected to the intense flux of neutrons, can also become radioactive (activation)
Example: Plutonium production from Uranium
n+ 238U  239U + g  239Np + b + anti-n  239Pu + b + anti-n
Other elements (Transuranics: elements heavier than Uranium) not existing in Nature are formed beyond Plutonium: the so-called Minor Actinides (Americium, Curium, etc.), typically with very long lives  they make handling and disposing of spent fuel more challenging
Example: 60Co production in steel
n + 59Co  60Co + g  60Ni + b + anti-n

## Slide 30: How it is built in practice
Fission 1
Fission 2
Absorption in other plant materials
Fission 3
Absorbing element
Neutron bounced back by"reflective" material
Neutron from fission
Loss
Reactor «core»
Fuel

## Slide 32: The“thermal” reactor
Coolant (usually water)
Uranium rod
235
Control rod (neutron absorbing material)
238
238
238
238
Absorption
238
235
Lost neutron
235
238
Fissione
Fission
Absorption
Neutrons hit water molecules and slow down  fission more probable
Uranium rod
Neutron
In the thermal reactor, neutrons are slowed down to have maximum burn-up of fissile Uranium 235

## Slide 33: The fast reactor
Coolant: e.g. liquid metal, gas
Fuel rod
235
238
238
238
238
Capture
238
Escape
235
Pu239
Fission
Fission
Capture
Scattering
Fuel rod
Control rod (e.g. Boron)
238
Fission
In the fast reactor, neutrons are not slowed down  possibility to produce and burn more Plutonium and also to burn other radioactive nuclei beyond Plutonium formed by neutron capture

## Slide 34: Radioactive waste production (from fission)
Nuclear power plants
Surface repository
Radioactive waste drums
Activated materials
Spent fuel
Cooling pools
Geological repository
casks

## Slide 35: How much nuclear waste is there? And what to do with it?
Therefore, the used fuel rods must be stored in safety for very long periods
when the plant is dismantled, the other activated materials must also be kept in isolation
Some countries are already using or are planning to use underground repositories, to store the spent fuel and other highly activated components, and then close the access to the repository, letting the radioactivity run out on its own  after about 200,000 years the material is no longer dangerous
However, it is also possible to partially recycle the spent fuel  it can be treated to extract Uranium and Plutonium to be used a second time
Spent fuel casks
In one year, a typical high power reactor produces about 1200 kg of radioactive substances in the fuel, of which 400 kg are radioactive for long periods, from a few hundred to a few hundred thousand years  they must be kept isolated

## Slide 36: INFN contributions to monitoring radwaste

## Slide 37: Nuclear Fusion
Currently we do not know how to build reactors capable of maintaining a stable regime for long enough
Ongoing research (JET, ITER, DEMO) is long term
This is called Nuclear Fusion: it is the mechanism at work in stars
(actually, not with D-T, the Sun works mainly with p+pD+e++)
Deuterium (2H)
Tritium (3H)
Neutron
Helium (4He)
Fusion does not produce directly radioactive fragments
(but Tritium is radioactive and neutrons activate structural materials)
 It provides cleaner energy with respect to Fission
The neutrons have about 14 MeV kinetic energy  transferred to water around the apparatus  Heat
Helium nuclei have about 3 MeV  they give some contribution to heating the plasma

## Slide 38: Fusion reaction candidates
3He
p+14.7 MeV
4He+3.6 MeV
2H
2H
n+2.45 MeV
3He+0.82 MeV
2H
2H
p+3.02 MeV
3H+1.01 MeV
2H
Deuterium-Tritium
has maximum probability to occur at the conditions that we can be able to reach in our fusion plants and provides a significant amount of energy
3H
n+14.1 MeV
4He+3.5 MeV
2H
Q-value is sum of energy acquired by final nuclei  energy released in exoergic reactions

## Slide 39: Conditions for Fusion
At such high temperatures, a plasma is created  a gas of electrons and nuclei (ions) moving independently
To make fusion happen, Coulomb repulsion between (positive) nuclei has to be overcome  necessary to reach VERY high temperatures  Deuterium-Tritium gas mixture must be heated to several million degrees
The plasma is so hot that it must be trapped (confined) such as to avoid touching the reactor walls  Confinement is achieved through magnetic fields
or the mixture can be compressed by using high power lasers («inertial» fusion)

## Slide 40: The (magnetic) fusion reactor
Using a doughnut-shaped device works better (tokamak)
And here is a real one…
TOKAMAK
токамак, an acronym of either:
"тороидальная камера с магнитными катушками"
(toroidal'naya kamera s magnitnymi katushkami)
toroidal chamber with magnetic coils
or
"тороидальная камера с аксиальным магнитным полем"
(toroidal'naya kamera s aksial'nym magnitnym polem)
toroidal chamber with axial magnetic field

## Slide 42: Heating the plasma
Tplasma in the tokamaks: ~100-150x106 degree to trigger fusion D + T  4He + n (*)
Plasms heating is obtained essentially by Ohm effect (but at lower temperatures as plasma resistance decreases with temperature), RadioFrequency (electron and ion Cyclotron Resonance) and injection of neutral atoms (Neutral Beam Injectors, NBI)
(*) The Chinese Experimental Advanced Superconducting Tokamak (EAST) established a new world record in 2021 by reaching a plasma temperature of 120 million degrees for 101 seconds and 160 million degrees for 20 seconds

## Slide 43: The fusion roadmap: ITER
One of ITER’s goals is to get 10 times more fusion energy than the energy used to heat the plasma
Overall Project Schedule for new Baseline
Cryostat Closure
Full Field
Start DD
Divertor Plasma operation
Full Ip & BT
Q=10
>50s
Q=10
>300s
Assembly-I
IC-I
Assem IC
SRO
FPO-I
FPO-II
-V
Mar. | Oct. | Dec. | Dec. Sep. | Sep. | Sep. | Sep. | Sep.
2033 | 2034 | 2036 | 2038 2039 | 2041 | 2043 | 2045 | 2047
18
Months
27 Months | bly-II 24 Months | -II 10 M | Operation 16 Months Maintenance | Operation 16 Months Maintenance | Operation 16 Months Maintenance | Operation 16 Month Maintenance
 |  |  | 8 Months | 8 Months | 8 Months | 8 Months
FPO-III FPO-IV FPO
s Operation 16 Months
Target dates:
DT-2
IC: Integrated Commissioning SRO: Start of Research Operation FPO: Fusion Power Operation

## Slide 44
© 2022, ITER Organization
Joint EPS-SIF International School on Energy 2025, 26 June 2025 7
IDM UID: E597RB
Construction site today
16 Oct. 2024

## Slide 45: ITER: assembly in progress
Vacuum Vessel
Toroidal Field coils
Poloidal Field coils

## Slide 46: The ITER divertor
Divertor: the fusion «exhaust», it absorbs gases that escape confinement and contaminants that accumulate during the fusion process
Situated at the bottom of the vacuum vessel
Extracts heat and ash produced by the fusion reaction, minimizes plasma contamination, and protects the surrounding walls from thermal loads
As the high-energy plasma particles strike the targets, their kinetic energy is transformed into heat and the heat is removed by active water cooling
Source: http://www.iter.org

## Slide 47: The Divertor Tokamak Test (DTT) project in Frascati
Goal: test different options for the DEMO divertor
ITER will use a “traditional” approach which may not work in DEMO
in addition to the divertor, various possible solutions suitable for DEMO can be studied at DTT

## Slide 48: New technologies for DTT at INFN: additive manufacturing (3D printing)
Prototype accelerator grids for DTT Neutral Beam Injector, 3D-printed in Copper-Chrome-Zirconium alloy

## Slide 49: DTT@INFN: Electron Cyclotron Heating Mirrors and Ion Cyclotron Heating Antenna
Maps of electric fields at the antenna
Improved curved antenna model
Mirror prototype
in AISI 316 steel
Mirror in CuCrZr fully machined and provided with cooling connections

## Slide 50: The challenge of materials
IFMIF:
International Fusion Materials Irradiation Facility
Reactor materials are subjected to a great deal of stress (neutron bombardment)  it is necessary to test them
The IFMIF project foresees a powerful deuteron accelerator (deuterons, 40 MeV and 125 mA  5 MW beam power !)  Engineering Validation stage (EVEDA) going on at Rokkasho, Japan, with the goal to reach 9 MeV, 125 mA
The deuterons will hit a liquid lithium target, producing neutrons with intensity and energy spectrum similar to that of the fusion reactor, allowing to test certain materials (e.g. types of steel)
Europe will build DONES, with one accelerator

## Slide 51: IFMIF and DONES@INFN
RFQ
Construction
IFMIF RFQ: the supermodule (3.3 m)
The prototype assembled in Japan

## Slide 52: Summary
Radioactivity is a natural phenomenon and radioactive materials have been around us forever
Nuclear energy will still be one of the sources of low-emission «baseload» in many countries (including several new ones) for several years (and not only baseload, see small-scale reactors…)
There are solutions for the safe management of nuclear waste  they are also important for sectors other than energy (for instance, disposal of waste from the past and medical and industrial waste)
INFN applies its detector technologies to monitoring the radwaste
Fusion plants are at the center of a very intense experimental research program and could become a new source of energy around 2050
The fusion research program involves several challenges that require the development of many technologies, with a significant impact on industry
INFN gives a contribution to new experimental machines like DTT and applies accelerator technology to a powerful neutron source for material testing