## Slide 1
Matteo Alberi
alberi@fe.infn.it
N. Irem Elek lkenmr@unife.it https://www.fe.infn.it/radioactivity
Exploring the radioactivity

## Slide 2
Who are we?

## Slide 3
What is radioactivity?
How do we measure it?
Why is it important?

## Slide 4
Approaching the nucleus
Proton | 
Charge | + 1.602 10-19 C
Mass | 1.6726 10-27 kg
 | 938.272 MeV/c2
Radius | ~ 10-15 m
Spin | 1/2
Lifetime | > 2 1029 yr
Neutron | 
Charge | /
Mass | 1.6749 10-27 kg
 | 939.565 MeV/c2
Radius | ~ 10-15 m
Spin | 1/2
Lifetime | 881.5 s
Electron | 
Charge | - 1.602 10-19 C
Mass | 0.911 10-30 kg
 | 0.511 MeV/c2
Distance e-nuc | ~ 10-10 m
Spin | 1/2
Lifetime | > 6.6 1028 yr
[E] = 1 eV = 1.6 10-19 J
~ 1 MeV

## Slide 5
If I say "radioactivity", what do you think of?

## Slide 6
Radioactivity
Radioactivity is a natural physical phenomenon that occurs when the nucleus of an unstable atom reaches a new equilibrium state by emitting radiation
1 Bq = 1 decay/s
Alfa decay
Beta decay
Gamma decay
Notes: And this decay in which you emit from the nucleus an electron and anti-utrino again starting from this point reaching this new configuration. The new configuration is in term of stability is better than before. Sometime you can get also the emission of energy

## Slide 8
Alpha Decay (α-decay)
Typical of nuclides with a high number of both protons and neutrons
Occurs when atomic number Z > 83 and mass number A > 220
The nucleus emits an alpha particle (⁴₂He), reducing both Z and A
Beta Decay (β⁻-decay)
Characteristic of nuclei with an excess of neutrons compared to protons
To stabilize, the nucleus increases its number of protons
Emits a fast electron (β⁻ particle) and an anti-neutrino
Gamma Decay (γ-decay)
Emission of photons (γ) after an α or β decay
Atomic number Z and mass number A remain unchanged
The nucleus releases energy by emitting a gamma photon
Notes: So basically you start with a nucleus with a number of proton and a total uh mass number is nuclear plus proton in the nucleus. Okay. And for some reason because it's not in equilibrium at certain moment it decide to decay. Okay. What's happen in this case? Two proton are released because number of Z is decreased by factor two. So basically you release two proton and two neutron which correspond to a nucleus . This is alpha decay. So if you imagine when this happen, when the atomic number is pretty high. So Z more than 80.
So uh beta decay basically Z improved by one. This means that we have more proton but the number of a doesn't change. So basically one neutron become a proton.

## Slide 9: Penetration and Shielding
Penetration power
α stopped by paper
β penetrates paper but stopped by ~1 mm of aluminum
γ requires thick lead (>10 cm) or dense materials to be significantly attenuated

## Slide 10
Earth's radioactivity is due to naturally occurring radioactive elements with half-lives comparable to the age of the earth
g
Element | Radioisotope | Isotopic abundance | Half-life | Typical abundance
Potassium | 40K | 0.012% | 1.3 × 109 year | 0.02 g/g [2%]
Uranium | 238U | 99.3 % | 4.5 × 109 year | 3 µg/g [ppm]
Thorium | 232Th | 100 % | 14.1 × 109 year | 10 µg/g [ppm]
We can quantify the presence of radioactive elements using a scintillation detector
Potassium-40 and some radioisotopes belonging to the decay chains of uranium and thorium emit γ rays with energy of the order of MeV and can be easily detected by spectroscopy γ
Radioactivity around us

## Slide 11
Potassium
Source | K abundance (%)
Rocks | ~ 2
Banana | 0.36
Human body | 0.25
Tap water | 0.0001 – 0.0005
Chemical properties
  Highly reactive alkali metal; reacts vigorously with water.
Physical properties
  Soft, silvery metal; low melting point (63.5 °C); excellent conductor of electricity.
Potassium-40 (⁴⁰K)
  A naturally occurring radioactive isotope of potassium

## Slide 12
Potassium 40: decay and gamma spectrum
g
Electron capture (EC) A nuclear process in which an inner orbital electron is captured by the nucleus, leading to the conversion of a proton into a neutron with the emission of an electron neutrino.
β⁻-decay

## Slide 13
Uranium decay chain
g
g
g

## Slide 14
Uranium gamma spectrum

## Slide 15
Thorium decay chain
g
g
g
g

## Slide 16
Thorium gamma spectrum

## Slide 17
How radioactive are terrestrial rocks?
Granite (intrusive igneous rock)
~1000 Bq/kg
Tuff (pyroclastic rock)
~1800 Bq/kg
Marble (limestone)
Gypsum (sedimentary)
~100 Bq/kg
~100 Bq/kg
Granite: is an intrusive igneous rock (magmatic rock solidified within the earth's crust) composed mainly of quartz, feldspar and mica. These minerals may contain traces of radioactive elements Tuff: it is a light volcanic rock formed by the compaction of volcanic ash and pyroclastic fragments. The presence of materials derived directly from volcanic eruptions can lead to increased radioactivity Gypsum: it is an evaporitic sedimentary rock formed by the precipitation of calcium sulphate. Usually, it does not contain high levels of radioactive elements Marble: it is a metamorphic rock derived from the recrystallization of limestone. Although it may contain traces of radioactive minerals, it generally has lower levels of radioactivity

## Slide 18
… in lab
~ 0.1 m
How can we measure the gamma radioactivity?

## Slide 19
… in situ
~ 10 m
… in lab
~ 0.1 m
How can we measure the gamma radioactivity?

## Slide 20
… airborne
~ 100 m
… in situ
~ 10 m
… in lab
~ 0.1 m
How can we measure the gamma radioactivity?

## Slide 21
Introducing RockyRad
Detects β and γ radiation using a Geiger-Müller glass tube and displays real-time CPM (counts per minute) and ambient dose rate in nSv/h.
Connects to mobile devices via Bluetooth, with a dedicated Android app for real-time monitoring, data storage, and sharing.
Logged data can be exported in CSV format for easy analysis with external software.

## Slide 22
​The RockyRad app provides, with a user-friendly interface, the real-time control over the measurement process. The user can specify measurement intervals and start new measurement. Following Bluetooth and Wi-Fi connection, users can use their phone to take a photo of the detector, set acquisition time.
The RockyRad is a portable Geiger–Müller counter with a mobile interface to manage the Geiger counter acquisition. This detector is sensitive to both beta and gamma radiation, but it cannot discriminate between them.

## Slide 23
GammaEDU
https://www.caen.it/products/gamma-edu/

## Slide 24
Scintillation Detector (NaI(Tl)):
Sodium iodide crystal doped with thallium (0.2%) emits visible light flashes when gamma photons interact with it, enabling detection.
Scintillation Mechanism:
A gamma photon transfers energy to an electron, exciting it across the band gap. Upon returning to the ground state via activator levels, the electron emits a visible photon (~1 eV).
Material Properties:
NaI(Tl) is dense (3.7 g/cm³), transparent, efficient, but hygroscopic; its crystal structure defines the energy levels critical for scintillation performance.
Detection of gamma radiation

## Slide 25
Schematic diagram of a scintillation detector
The MCA allows to convert the pulse obtained at the end of the charge amplification stage into a digital signal
MCA
The intensity of the output current pulse is proportional to the energy of the incident photon

## Slide 26
We interpret the gamma spectrum
Chart: Channels
Photopeak
(40K 1460 keV)
Photopeak
(208Tl 2614 keV)
Photopeak(214Bi 1764 keV)
Cosmic radiation
In a gamma spectrum we recognize the photopeaks, which correspond to the photons that arrive at the detector with energy equal to that with which they were emitted and that have deposited all the energy in the detector.
We know these energies from the physics of decay

## Slide 27: The field of view
If the detector is placed 5 cm above the ground, its field of view is 70 cm

## Slide 28
Measurements must be made on an area at least 10 m away from artifacts

## Slide 29
Frascati National Laboratories – April 2025
In-situ measurement

## Slide 30
Frascati National Laboratories – April 2025

## Slide 31
Cementry Sample;
K-40: 1.3 ±0.2 %
Bi-214: 3.6±0.9 1 ppm
Tl-208: 5.3±1.9 ppm

## Slide 32
Take note of the surrounding environment
Set the acquisition time
Take a photo of the measurement site
Acquire GPS coordinates
Let’s start to measurement!!

## Slide 33: Discover environmental radioactivity!
The operator can acquire and analyze the gamma spectrum in real time to determine the abundance of K, U, and Th.
Interpretation of the characteristics of the gamma spectrum

## Slide 34: Share the results!
The KML file reports the measurement points, each assigned with the corresponding radionuclide abundances and an image of the acquisition site.. The file is ready to be viewed on Google Earth and shared
KML

## Slide 35
Set the acquisition time
Take a photo of the measurement site
Take note of the surrounding environment
GrassOlives

## Slide 36
Thank you for exploring Environmental Radioactivity with us!
We hope this presentation has sparked your interest in learning more about our incredible field. Keep asking questions, stay curious, ad enjoy discovering more about the world around you!!!

## Slide 38
Principal interaction mechanisms of gamma-ray with matter
  Photoelectric effect
  Compton scattering
  Pair production
In the photoelectric effect, the incident photon completely transfers its energy to a bound electron, which is ejected from the atom.
The photoelectric effect dominates at low gamma energies
In the Compton scattering, the incident photon interacts with a bound electron resulting in the deflection of the photon. The photon transfers a portion of its energy to the recoiling electron.
Compton scattering dominates at intermediate energies.
In general, in pair production the energy is directly converted to matter.
This interaction dominates at high energies.
Annihilation
threshold energy
(>1.02 MeV)
The operating principle of a gamma-ray detector is based on the interaction of the incident photons with the detector material

## Slide 39
Spectrometry with NaI(Tl) detectors
Chart: Channel
photopeak
(40K 1460 keV)
Compton continuum
photopeak
(208Tl 2614 keV)
photopeak
(214Bi 1764 keV)
Cosmic radiation
In a gamma spectrum we recognize the photopeaks, which correspond to the photons that interact with and deposit in the detector an energy equal to that which have been emitted from the unstable nucleus.

## Slide 40
ɣ spectrum
All photons, no matter how complex their mode of interaction, ultimately deposit all of their energy in the detector.
Channel/Energy
Photopeak (full energy peak)
Compton continuum
When Compton scattering events occur and the scattered photon generally may escape from the detector without further interaction, gives rise to the Compton continuum
For a monoenergetic incident photon beam
1460.86 keV
Spectrum: a histogram of events classified according to the energy deposited
inside the detector

## Slide 41
Energy calibration
In order to understand which is the energy corresponding to a given acquisition channel, the spectrum must be “energetically calibrated", which means determining the linear relation existing between channel and energy on the basis of well known spectral structures
A = (ETh ,ChTh )
B = (EK ,ChK, )
A
B

## Slide 42
The energy transferred per unit of mass by the ionizing radiation is called dose D (Gy = Gray = J/kg).
To quantify the impact of ionizing radiation on the organisms it’s necessary to take into account the type of radiation and the radiosensitivity of the organs.
The equivalent dose HT (Sv = Sievert = J/kg) measures the dose absorbed by the tissue T according to the "type" of radioactivity:
Radiation | WR
e ; g ; X | 1
alpha | 20
Organs | wT
Gonads | 0.20
Bone marrow, colon, stomach, lungs | 0.12
Bladder, breast, liver, esophagus, thyroid, other organs | 0.05
Skin, bone surfaces | 0.01
Interaction between radiation and the human body
The effective dose E (Sv = Sievert = J/kg) is the tissue-weighted sum of the equivalent doses in all specified tissues and organs of the human body and takes into account the different radiosensitivity of the irradiated organs:
where wR is a weighting factor dependent on the type of the radiation
where wT is the organs’ weighting factor

## Slide 43
Mean effective dose absorbed by the population due to the "natural background": 2.400 µSv/year.
Average exposure of the population to ionizing radiation *
* UNSCEAR 2000 Report - United Nations Scientific Committee on the Effects of Atomic Radiation
…and absorbed during a human life
Mean effective dose absorbed in a year…
Terrestrial
radiation
Radon
Cosmic rays
Food and
water
Medical
radiation
Human
activities

## Slide 44
Total effective dose (outdoor)
ingestion
inhalation
cosmic radiaton
terrestrial radiation
medical radiation
other