## Slide 1
Structured Light Laser-Wakefield Acceleration
Victor Malka
Aaron Liberman, Sheroy Tata, Anton Golovanov, Anda-Maria Talposi, Santosh Krishnamurthy, Arujash Mohanty, Eitan Levine, Salome Benracassa, and Eyal Kroupp
Slava Smartsev, Igor A. Andriyash, Ronan Lahaye, and Cedric Thaury
1
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025

## Slide 2
Laser-Wakefield Acceleration
The Dephasing Limit
Structuring Light: Near Field - STCs
Structuring Light: Far Field - Axiparabola
Axiparabola Velocity Measurement
Femtosecond Relativistic Electron Microscopy (FREM)
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025

## Slide 3
The Breakdown Issue
18 GeV electrons 2 km
Laser wakefield acceleration: Limitation
Max Field < 100 MV/m
over kms
Laser
~ tens of microns
Plasma wave
Max Field > 100 GV/m
over mms-cms
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025

## Slide 4
Laser guided wakefield in plasma channels
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025
R. Lehe
7.5
3
4
8.0
8.5
7.0
9
6
3
0
20 cm-scale plasma discharge
1 PW
laser
Fragile, 2 additional laser beams, difficult to
use: no future for real applications
E. Rockafellow et al., PoP (Accepted 2025);
J.E. Shrock et al., in preparation
30 cm-scale OFI plasma channel
Very promising approach with already excellent results
pC/mrad
Beam energy (GeV)
Gonsalves et al., PRL (2019)

## Slide 5
Also 10 GeV with OFI plasma channel
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025
R. Lehe
20 cm
200 µm
diffractive axicon
gas jet:
SL
magnets
LA1
M2
LA2
P2
2-color probe
gas flow
P1
M1
< 15 J, 45 fs
x-y pointing
Fluctuations 9 µm
(e)
200μm
200 m
200 m
Extended multi-valve generation VI supersonic gas jet for meter-scale, low density waveguide developed at UMD
B. Miao et al., Phys. Rev. Lett. 129, 074801 (2020), L. Feder et al., Phys. Rev. Res. 2, 043173 (2020), B. Miao et al., Phys. Rev. Accel. Beams 27, 08132 (2024), E. Rockafellow et al., PoP (Accepted 2025); J.E. Shrock et al., in preparation

## Slide 6
Solution 1: Laser-Waveguide
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025

## Slide 7
Laser-Wakefield Acceleration
The Dephasing Limit
Structuring Light: Near Field - STCs
Structuring Light: Far Field - Axiparabola
Axiparabola Velocity Measurement
Femtosecond Relativistic Electron Microscopy (FREM)
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025

## Slide 8
Dephasing in laser wakefield
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025
Typical value for 100 TW to PW 30fs laser system at density of 1018cm-3, Ldeph is of the order of 1 cm (larger than zR.)
R. Lehe
Since the laser group velocity is < c, when electrons energy is getting ~c they diphase,
electrons reach the center of the cavity and start to be deccelerated
Ldeph.= gp2lp/2 = l0 (nc/ne)3/2
zR = πw02/λ0

## Slide 9
Dephasing in laser wakefield
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025
Typical value for 100 TW to PW 30fs laser system at density of 1018cm-3, Ldeph is of the order of 1 cm (larger than zR.)
R. Lehe
Since the laser group velocity is < c, when electrons energy is getting ~c they diphase,
electrons reach the center of the cavity and start to be deccelerated
Ldeph.= gp2lp/2 = l0 (nc/ne)3/2
zR = πw02/λ0

## Slide 10
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025
Typical value for 100 TW to PW 30fs laser system at density of 1018cm-3, Ldeph is of the order of 1 cm (larger than zR.)
R. Lehe
Since the laser group velocity is < c, when electrons energy is getting ~c they diphase,
electrons reach the center of the cavity and start to be deccelerated
Ldeph.= gp2lp/2 = l0 (nc/ne)3/2
zR = πw02/λ0
Dephasing in laser wakefield

## Slide 11
Benefit of luminal wakefield
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025
C. Caizergues et al., Nature Photonics 14, 475–479 (2020), J. Palastro et al.,
Phys. Rev. Lett. 124, 134802 (2020), A. Debus et al., Phys. Rev. X 9, 031044 (2019)
γ ∝ 1/τ²
γ ∝ EL
Up to 50 GeV in 50 cm
with a 1 PW, 15 fs laser

## Slide 12
The Dephasing Limit
Problem: Relativistic electrons outpace laser in plasma
Solution: Need to speed up the bubble (and therefore the laser driver)
J. P. Palastro et al., 2020.
10,000 m
200 m
4 m
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025

## Slide 13
Laser-Wakefield Acceleration
The Dephasing Limit
Structuring Light: Near Field - STCs
Structuring Light: Far Field - Axiparabola
Axiparabola Velocity Measurement
First Electrons
Femtosecond Relativistic Electron Microscopy (FREM)
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025

## Slide 14
Spatiotemporal couplings spatially-dependent chromatic effects
For Gaussian:
1st order couplings - spatially dependent pulse front delay
No STC Pulse Front Curvature Pulse Front Tilt
Time [fs]
X
Spatio-Temporal Couplings (STCs)
-
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025

## Slide 15
Laser-Wakefield Acceleration
The Dephasing Limit
Structuring Light: Near Field - STCs
Structuring Light: Far Field - Axiparabola
Axiparabola Velocity Measurement
First Electrons
Femtosecond Relativistic Electron Microscopy (FREM)
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025

## Slide 16
Smartsev et. al., Opt. Lett. 44, 14 (2019)
parabola
axiparabola
The Axiparabola
f
f
δ
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025

## Slide 17
Caizergues et. al., Nat. Phot. 14, 475–479 (2020)
axiparabola
“Appearance” velocity is superluminal
Intensity Propagation Dynamics
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025

## Slide 18
Axiparabola + STCs: Phase locked acceleration
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025
Caizergues et. al., Nat. Phot. 14, 475–479 (2020)

## Slide 19
Laser-Wakefield Acceleration
The Dephasing Limit
Structuring Light: Near Field - STCs
Structuring Light: Far Field - Axiparabola
Axiparabola Velocity Measurement
First Electrons
Femtosecond Relativistic Electron Microscopy (FREM)
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025

## Slide 20
Electron Acceleration
Liberman et al., CLEO Proceedings 2024
Longer Manuscript in Prep.
Data
Simulation
High Energy Events
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025

## Slide 21
Laser-Wakefield Acceleration
The Dephasing Limit
Structuring Light: Near Field - STCs
Structuring Light: Far Field - Axiparabola
Axiparabola Velocity Measurement
Femtosecond Relativistic Electron Microscopy (FREM)
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025

## Slide 22
Femtosecond Relativistic Electron Microscopy
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025
Liberman et al., ArXiv:2503.01516

## Slide 23
FREM Pulse Front Curvature Comparison
PFC = -0.0019 fs/mm2
PFC = 0.02 fs/mm2
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025
Liberman et al., ArXiv:2503.01516

## Slide 24
Linear and Nonlinear Fields
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025
Liberman et al., ArXiv:2503.01516

## Slide 25
Comparison to Parabola
Parabolic
Axiparabolic
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025
Liberman et al., ArXiv:2503.01516

## Slide 26
Summary
LWFA - promising due to unprecedented acceleration gradients
Dephasing limits the achievable electron energy – hurts potential applications
To mitigate dephasing - increase propagation velocity of laser driver
Structuring light using STCs and an axiparabola – possible solution
Experimentally demonstrated ability to tune propagation velocity
Used FREM to probe the structure of this novel wakefield
Provide new insights into this regime
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025

## Slide 27
Thank You
ExCoMet
WIS-CNRS (IPR LAMA)

## Slide 28
Summary
EAAC 2025, 7th European Advanced Accelerator Conference, Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy, 21–27 Sept 2025
Refractive doublet for PFC Control:
Effect scales with beam size
Axiparabola Velocity Measurement
Kabacinski et al. J. Opt. 23 (2021), Liberman et al., Opt. Let. 49 (2024)