## Slide 1: Collider-quality electron bunches from an all-optical plasma photoinjector
Marcus Babzien, Michael Downer, Arohi Jain, Chandrashekhar Joshi, William Li, Warren Mori, John Palastro, Mark Palmer, Jacob Pierce, Mikhail Polyanskiy, Roman Samulyak, Tanner Simpson, Navid Vafaei-Najafabadi, Jiayang Yan
Stony Brook University, University of Rochester, UCLA, BNL

## Slide 2: Synthesis
Plasma accelerators create accelerating gradients that are hundreds of times higher than conventional accelerators
A “plasma photoinjector” for a collider application needs to create
  Low emittance (<100 nm)
  High charge (order of nC)
  Trapezoidal shape for low energy spread in subsequent accelerating plasma stages
Such plasma photoinjector can be generated by applying the spatiotemporal pulse shaping to two-color ionization injection.

## Slide 3: Synthesis
Plasma accelerators create accelerating gradients that are hundreds of times higher than conventional accelerators
A “plasma photoinjector” for a collider application needs to create
  Low emittance (<100 nm)
  High charge (order of nC)
  Trapezoidal shape for low energy spread in subsequent accelerating plasma stages
Such plasma photoinjector can be generated by applying the spatiotemporal pulse shaping to two-color ionization injection.

## Slide 4: Synthesis
Plasma accelerators create accelerating gradients that are hundreds of times higher than conventional accelerators
A “plasma photoinjector” for a collider application needs to create
  Low emittance (<100 nm)
  High charge (order of nC)
  Trapezoidal shape for low energy spread in subsequent accelerating plasma stages
Such plasma photoinjector can be generated by applying the spatiotemporal pulse shaping to two-color ionization injection

## Slide 5: Collider quality electron beam
In addition to energy, beam quality is a critical consideration
In colliders, quality is measured by Luminosity
C.B. Schroeder et al 2023 JINST 18 T06001
DOI 10.1088/1748-0221/18/06/T06001
Beam charge High charge
Focusability low emittance and energy spread
& & Q
Beam collision rate High rate
Plasma Collider: kHz
Plasma Collider: pC ,
Plasma Collider:
Emittance, nm
Energy spread, 1%
Notes: Having a high acceleration gradient is not enough, you also need a high quality beam
Luminosity determines number of events (collisions) per second

## Slide 6: Two-color ionization injection
Yu, PRL 112, 125001 (2014)
Schroeder, European Conference on Lasers and Electro-Optics (2015)
See also Xu, PRSTAB, 17, 061301 (2014)
Schroeder, PRSTAB 17, 101301 (2014)
Long-wavelength laser to drive the wakefield
Short-wavelength laser to trigger ionization within the wakefield
Drive laser needs large to form plasma wakefield, but we want low field to avoid prematurely ionizing the gas
Injector laser needs high field to ionize the gas, but low to avoid emittance degradation
Low emittance
Excellent phase space
Very intense, small
Less intense, large

## Slide 7: We propose a method for generating collider quality electron beam
Acceleration stage
Trapezoidal electron bunch
Driver
Beam
Plasma cell m
20 GeV beam
energy spread
Injection stage
Trapezoidal electron bunch
Ionization laser
Flying focus laser
CO2 laser
Plasma cell mm

## Slide 8
Injection Stage
Injection stage
Trapezoidal electron bunch
Ionization laser
Flying focus laser
CO2 laser
Plasma cell mm

## Slide 9: Varying the location of ionization is possible through spatiotemporal control of the ionizing laser
By varying the chirp, the region of peak intensity (focus) can be made to travel at any velocity
D. H. Froula, Nature Photon 12, 262–265 (2018)
While maintaining the same spot size, the focus region can be extended to be much longer than the Rayleigh length
A chirped laser pulse focused by a chromatic lens exhibits a dynamic, or “flying”, focus

## Slide 10: Osiris simulations performed on Perlmutter@Nersc and SEAWULF@SBU
code features
Scalability to ~ 1.6 M cores
SIMD hardware optimized
Parallel I/O
Dynamic Load Balancing
QED module
Particle merging
GPGPU support
Xeon Phi Support
osiris framework
Massivelly Parallel, Fully Relativistic Particle-in-Cell (PIC) Code
Visualization and Data Analysis Infrastructure
Developed by the osiris.consortium
UCLA + IST
Ricardo Fonseca: ricardo.fonseca@tecnico.ulisboa.pt
Frank Tsung: tsung@physics.ucla.edu
Jacob Pierce: jacobpierce@physics.ucla.edu
http://epp.tecnico.ulisboa.pt/ http://plasmasim.physics.ucla.edu/

## Slide 11
Varying the location of ionization is possible through spatiotemporal control of the ionizing laser
Conventional laser-
Flying Focus (FF) laser-
Driver (both):
,
,
s,
See W. Li, Sep. 25, 5:50 PM

## Slide 12: The injected beam is gradually assembled with the motion of the ionization front
Charge= 17 pC
Charge= 220 pC

## Slide 13: Charge and emittance are consistent with collider requirements
 | 20 GeV Demonstrator Facility* | Two Color FF Injector
Q (pC) | 200 | 220
 | 100 n | 76 nm
 | 100 | 170 nm
 | 20 GeV Demonstrator Facility* | Two Color FF Injector
Q (pC) | 200 | 220
 |  | 76 nm
 |  | 170 nm
*C.B. Schroeder et al 2023 JINST 18 T06001

## Slide 14
Acceleration stage
Trapezoidal electron bunch
Driver
Beam
Plasma cell m
20 GeV beam
energy spread
Injection stage
Trapezoidal electron bunch
Ionization laser
Flying focus laser
CO2 laser
Plasma cell mm

## Slide 15
Acceleration Stage

## Slide 16: Beam generated in this photo injector can be accelerated in subsequent stages at 10 GeV/m and at high efficiency
,
Final Emittance:
nm rad
nm rad
Transfer efficiency: 43%
a
b
c
d
Energy Gain 20 GeV
Energy Spread<1%

## Slide 17: This method can easily be scaled to higher charge, albeit with higher emittance
a
b
c

## Slide 18: Beam loading of the nC beam
,

## Slide 19: Conclusions
Introduced novel plasma photoinjector approach for collider-quality electron beams
Flying focus laser pulse creates a moving ionization front for efficient electron injection
Beam parameters align with Snowmass requirements, showcasing the feasibility for future compact accelerators.
Produced trapezoidal-shaped electron bunches with 220 pC charge and low emittance
Efficiently accelerated the shaped bunch to 20 GeV in a 2-meter acceleration stage.

## Slide 20
Thank you!

## Slide 21: Beam energy after injection stage
nm rad
Peak energy=10MeV
FWHM=6 MeV
%

## Slide 22: Beam loading
A trailing beam with a particular density profile result in flattening of the wakefield [1]
for a fully blowout bubble
How to maintain low energy spread during acceleration?
Ideal beam loading
M. Tzoufras, Phys. Rev. Lett. 101, 145002 (2008)

## Slide 23: Integration of Ti:Saph at ATF
Parameter | Value | Comments
Energy (compressed) | >15 mJ (@1.5 Hz) | Compressed on target. <5% std long-term variation To be increased to 100 mJ @ 12 Hz
Energy (stretched) | >200 mJ | Out of 4-pass amplifier <8% std long-term variaiton
Duration | <70 fs | FWHM
Focused spot size | <4 µm FWHM | With F/1.5 OAP <1µm std pointing stability (~25µrad std)
Polarization | Vertical | Horizontal available upon request
Synchronization | Synchronized to the facility 81.6 MHz master clock | Rough timing (ns) by SRS delay generators. Fine adjustments (~10fs) by phase tuning the oscillator (Coherent Vitara+Synchrolock)
Transport line+ compressor transmission | 60% | 
Peak intensity | >1018 W/cm2 | 
Beam size in transport | <1.5” | Limited by aperture of vacuum line between Nd:YAG and Gun Hutch rooms
Addition of Ti:Saph represents an important upgrade in the capabilities of ATF

## Slide 24: The injected beam is gradually assembled with the motion of the ionization front

## Slide 25: A relatively low-power LWIR laser generates a clean, highly nonlinear wakefield
Strength of ponderomotive force scales with , so LWIR drivers () can reach with modest intensities (at ~20 TW power)
can be reached by LWIR laser without triggering self-injection in LWFA*
Bubble created by LWIR driver can be >100 µm, providing the ability for precise alignment of multiple beams with respect to the bubble
P. Kumar, Physics of Plasmas, 28, 013102 (2021)
,
P=20 TW,
𝜏=0.5 ps,
cm-3
* See A. Jain, Proceedings of AAC 2022
Notes: LWIR drives clean wakefield

## Slide 26: CO2 and flying focus (FF) laser intensities are chosen based on Kr8+ Kr9+ ionization rates
Simulation Parameters
FF laser- , ,
CO2 laser- , , s,
Plasma: , mm
Notes: Also below the level of self injection

## Slide 27: Motion of the ionization location and the shape of the function result in injection of a trapezoidal profile
A. Jain, in preparation
CO2
laser
FF laser
(a)
(b)
(c)
Plasma formed by ionization of Krypton gas
Plasma wake driven by CO2 laser pulse

## Slide 28: Flying Focus Injection Theory
CO2
laser
FF laser
(a)
(b)
Plasma formed by ionization of Krypton gas
Plasma wake driven by CO2 laser pulse

## Slide 29
BNL’s Accelerator Test Facility (ATF) has unique infrastructure
for developing such photoinjector.
New York
RHIC
NSLS
ATF
Multi-TW discharge-pumped CO2 laser
• 8J, 2 ps (2024)
• 10 J, 0.5 ps (projected 2027)
TW – class Ti:Sapphire Laser
Dr. Rafal
Zgadzaj
Dr. Irina
Petrushina
Synched S-band
linac (50 MeV, 100 fs)

## Slide 30
Solution:
Inject a trapezoidal beam and flatten the plasma wakefield through beamloading
M. Tzoufras, Phys. Rev. Lett. 101, 145002 (2008)
Shortcomings:
The charge produced is low (3-30 pC)
Lack of beam loading results in relatively large energy spread (few %)
Key constraint is a very localized injection of high-quality electrons

## Slide 31: Summary
A “plasma photoinjector” for a collider application needs to create
  Low emittance ( 100 nm)
  High charge (order of nC)
  Trapezoidal shape for low energy spread in subsequent accelerating plasma stages
By applying the spatiotemporal pulse shaping to two-color ionization injection, such plasma photoinjector can be demonstrated at ATF, BNL