## Slide 1: Progress on the Flat beam PWFA experiment at AWA
Pratik Manwani1, Alex Ody2, Yunbo Kang1, Joshua Mann1, Nathan Majernik2, Kai Huang1, Gerard Andonian1, B. Naranjo1, Phillipe Piot2, Doran Scott2, Eric Wisniewski2, Wahming Liu, John Power2, and James Rosenzweig1
1: University of California, Los Angeles
2. ANL, Lemont, Illinois
3: Stanford Linear Accelerator Center (SLAC)

## Slide 2
Motivation
Theory - General formalism
  Beam and plasma blowout ellipticity
  Matching conditions
  Features and Insights
Experiment at Argonne Wakefield Accelerator(AWA)
  Plasma source development
  Simulations – Beam plasma interaction
  Experimental runs : Flat beam generation and final focus
Conclusion and future steps
Outline

## Slide 3
Plasma wakefields driven by flat beam is an underdeveloped topic in current research
  Asymmetric spot sizes and emittance :
  These beams yield a blowout cavity that is elliptical in cross section which leads to interesting physics.
In colliders, these beams mitigate beam-beam effects (beamstrahlung) at the interaction point.
Direct applications for:
  Plasma afterburners
  Asymmetric plasma lenses
Motivation
A. Golovanov et al,
PRL (2023)
Beamstrahlung , Luminosity

## Slide 4
Linear regime: For low densities ()
  Plasma perturbation follows beam transverse profile
Nonlinear regime (
  For high beam densities, there is a formation of an elliptical blowout cavity
  The ellipticity () reduces with beam density
  Question: How elliptical?
  Linear wake (
  Weak blowout (
Asymmetric wakes
J. Rosenzweig et al, PRA (1991)
W. Lu et al, PRL (2006)
A. Golovanov et al, PRL (2023)

## Slide 5
Given the elliptical boundaries ( and )
This can be used to find the wakefields:
Potential and wakefields
Asymmetric and linear!
No longer uniform
Need sheath distribution!
Plasma current reversal
Wake potential
Setting for simplicity

## Slide 6
In the long beam limit (), we can neglect the longitudinal variation of the fields
Equating the forces at the boundaries for a plasma electron, and approximating to be transversely isotropic, we get
  +
This allows us to get the elliptical boundaries, and the corresponding matching conditions of the beam
Finding the blowout boundaries
Center slice (XY)
Long beam ()
Ellipticity vs beam density
Wake potential
Ion potential
Beam potential

## Slide 7
In the long beam limit (), we can neglect the longitudinal variation of the fields
Equating the forces at the boundaries for a plasma electron, and approximating to be transversely isotropic, we get
  +
We can also get the correct quadratic dependence of the longitudinal fields
Detailed in :
Finding the blowout boundaries
Correct quadratic dependence! No plasma current reversal
Long beam ()
Wake potential
Ion potential
Beam potential

## Slide 8
Features and Insights
Solid: PIC
Dotted: Equations
Longitudinally varying focusing
  Can mitigate hosing instability (resonance between head and tail)
Asymmetric linear fields
  Can be slice-by-slice emittance matched
  Leads naturally to asymmetric plasma lenses
  Asymmetry can break resonant x-y emittance mixing in presence of nonlinearities. Flat beam ion motion breaks it too
Modified Quadrupole instability – Blowout keeps getting asymmetric if mismatched
  Significant head erosion in one dimension
Energy spread due to quadratic transverse dependence
S. Diederichs et al,
PRL(2024)
DH. Whittum et al, PRL (1991)
C. Huang et al, PRL(2007)

## Slide 9
Features and Insights
Using long beam model
Longitudinally varying focusing
  Can mitigate hosing instability (resonance between head and tail)
Asymmetric linear fields
  Can be slice-by-slice emittance matched
  Leads naturally to asymmetric plasma lenses
  Asymmetry can break resonant x-y emittance mixing in presence of nonlinearities. Flat beam ion motion breaks it too
Modified Quadrupole instability – Blowout keeps getting asymmetric if mismatched
Significant head erosion in one dimension
Energy spread due to quadratic transverse dependence
S. Diederichs et al,
PRL(2024)
DH. Whittum et al, PRL (1991)
C. Huang et al, PRL(2007)

## Slide 10: Flat beam PWFA Experiment at the AWA facility

## Slide 11
Argonne Wakefield Accelerator Facility (AWA) has capabilities to produce flat beams
  Emittance ratio: 100:1
  High charge
  Diagnostics for longitudinal and transverse characterization of the beam are available
Weak blowout can be accessed ()
  Plasma source with peak density of
  (developed at UCLA)
Flat beam PWFA experiment at AWA
AWA facility
Flat beam parameters at AWA

## Slide 12
Macor - 4 mm diameter, 8 cm length
10 kV, 100 A (1 s) peak current
Argon gas, Backing pressure 100 psi
Valve opening time : 5 ms
Peak density increases with voltage
Capillary discharge-based plasma source @UCLA
Mach Zehnder based HeNe interferometer
4 cm, 4 mm
Lower density (Peak:
)

## Slide 13
We can use our long beam model for the vacuum-plasma transport
The ellipticity () increases with increase in plasma density
Note: Matched beta functions depend on
Peak = 1.7
AWA beam parameters at of (QuickPIC)
Beam-plasma interaction
Using long beam model

## Slide 14
Longitudinally varying focusing
  OTR foil at entrance and exit of capillary viewed by streak camera
  Two screens downstream for angle and emittance measurements
Energy spread will be measured using a transverse deflecting cavity and a dipole spectrometer
Experiment observables
Spot size evolution(QuickPIC)
After beam – plasma interaction (QuickPIC)
x-
y-
z-
x-
y-
x-

## Slide 15
Axial magnetic field at photocathode inside solenoid results in a magnetized beam :
This is converted to mechanical angular momentum  CAM dominated beam
Three skew quads remove the correlation and split the emittances
  ,
Experimental runs-Flat beam generation
SQ1
SQ2
SQ3
Skew quadrupoles
YAG5
YAG4
Quad scan
Magnetization
Y. Sun et al,
PRSTAB (2004)
CAM dominated beam

## Slide 16
We focus the beam at two locations
  Interaction point
    (needed): 10 mm (needed): 7 mm
  Window location (Be 50 um)
    Used for gas-vacuum separation
    Disproportionate emittance increase (220:20 um rad)
Challenging to achieve spot sizes
  Optimize for emittance ratio
  Vary charge and bunch length (plasma density) to achieve blowout
We use OPAL+ELEGANT for the final focusing lattice
Two foci – Window and plasma chamber
2.04 mm
: 171 um
: 576 um : 317 um
Recent experimental runs
(Final focusing lattice
will be modified)
Be Window
IP
Notes: 9 T/m

## Slide 17
Flat beam PWFA has unique features – advantages as well as challenges
We developed a simplified theoretical model that has been successfully validated with PIC simulations
Used this model to design experiments:
  AWA propagation experiment
    Plasma source commissioned at UCLA
    Propagated flat beam to IP
    Need to optimize for emittance ratio after window – Early 2026
    Integration of plasma source to AWA beamline – Early 2026
  FACET-II : Asymmetric plasma lens
    Collaborating with the E-308 group to use asymmetric driver for passive plasma lens
Conclusion and Future steps

## Slide 18: References and Acknowledgements
Manwani, P., Kang, Y., Mann, J., Naranjo, B., Andonian, G., & Rosenzweig, J. B. (2025, August 26). Analysis of the blowout plasma Wakefields produced by drive beams with elliptical symmetry. PRL doi: https://doi.org/10.1103/28c4-blhg
W. Lu, C. Huang, M. Zhou, W. B. Mori, and T. Katsouleas, Nonlinear theory for relativistic plasma wakefields in the blowout regime, Phys. Rev. Lett. 96, 165002 (2006).
Golovanov, A., Kostyukov, I. Yu., Pukhov, A., & Malka, V. (2023). Energy-conserving theory of the blowout regime of Plasma wakefield. Physical Review Letters, 130(10). https://doi.org/10.1103/physrevlett.130.105001
Barov, N., Rosenzweig, J., Conde, M., Gai, W., & Power, J. (2000). Observation of plasma wakefield acceleration in the underdense regime. Phys. Rev. ST Accel. Beams, 3, 011301.
W.Kellog, Foundations of Potential Theory, (Dover Publications,New York,1953), p. 192
Xu, T., Conde, M., Ha, G., Kuriki, M., Piot, P., Power, J., & Wisniewski, E. (2019). Generation High-Charge of Flat Beams at the Argonne Wakefield Accelerator. In 10th International Particle Accelerator Conference. 10.18429/JACoW-IPAC2019-WEPTS094
https://link.aps.org/doi/10.1103/PhysRevSTAB.3.011301
Mihalcea, Daniel & Piot, P. & Stoltz, P.. (2012). Three-Dimensional Analysis of Wakefields Generated by Flat Electron Beams in Planar Dielectric-Loaded Structures. Physical Review Special Topics - Accelerators and Beams. 15. https://doi.org/10.1103/PhysRevSTAB.15.081304
Funded by DOE Grant No. DE-SC0017648
Thank you for your time!
Acknowledgements
Alex Ody2, Yunbo Kang1, Joshua Mann1, Nathan Majernik2, Kai Huang1, Gerard Andonian1, B. Naranjo1, Phillipe Piot2, Doran Scott2, Eric Wisniewski2, Wahming Liu, John Power2, and James Rosenzweig1

## Slide 19: Backup Slides

## Slide 20
We have Poisson’s equation with boundary condition
    Elliptical coordinates ()
    Elliptical blowout boundary :
    Focal length of ellipse:
Converting back to Cartesian coordinates:
Elliptical wake potential ( sheath)
  Weak blowout (

## Slide 21
For simplicity, we assume an angle independent confocal elliptical sheath having thickness
Conservation of S in each slice:
To first order:
Extendable to more arbitrary distributions
Elliptical wake potential ( sheath)

## Slide 22
Gaussian and flattop beams
Gaussian beam leads to a broadening of the plasma sheath
Studied in detail for transport
Y. Kang et al,
IPAC (2024)

## Slide 23
Observables – Elliptical blowout
Axisymmetric case ()
Transverse dependence of the longitudinal field
Curvature is observed
Signature of elliptical blowout
Difficult measurement – Slit?
No transverse dependence
No curvature is observed
Asymmetric case ()
x-
y-
(x,y)-

## Slide 24
Opening time : 1 ms
Opening time : 3 ms
Longitudinal profile – Plasma light (Preliminary)