## Slide 1
Terahertz-driven compression for femtosecond bunching and laser-electron temporal locking of relativistic electron beams.
Christopher T. Shaw (PDRA)
The Cockcroft Institute & Lancaster University
Representing the Terahertz Acceleration Group
Isola d'Elba, Italy, 21st - 27th September 2022

## Slide 2
Terahertz acceleration group @ The Cockcroft Institute
Dan Lake
Christopher Shaw
Laurence Nix
Connor Mosley
Beatriz
Higuera Gonzalez
Darren Graham
Sergey Siaber
Joseph Bradbury
Morgan Hibberd
Graeme Burt
Steven Jamison
Rob Appleby
Dave
Walsh
Tom
Pacey
Matt
King
+ STFC staff
THzAG.uk
25th September 2025

## Slide 3
Introduction: Why Terahertz?
RF
>2 GV/m
to match
THz
20 MV/m
TRF > 300 ps
Electron bunch
<1 ps
Energy gain
Energy loss
Multi-cycle
THz pulse
fTHz = 0.39 THz
TTHz = 2.56 ps
fRF = 3 GHz
High quality femtosecond relativistic electron beams desired for applications such as:
  Free electron laser pump probe experiments
  Ultrafast electron diffraction
  Future high-energy physics colliders
Few-femtosecond bunches achieved by existing accelerators such as:
  Advanced free electron laser facilities
  Laser plasma accelerators
The problems:
  Fine femtosecond level control
  Stability and synchronisation to external laser
The solution:
Terahertz!
25th September 2025

## Slide 4
Experimental Setup Overview
Terahertz dielectric lined waveguide
PPLN wafer stack terahertz source
5.5 MeV
35.5 MeV
Magnetic dogleg
3 GHz RF linac
1 m
Magnetic chicane compressor
Electron bunch
<1 ps
Energy gain
Energy loss
Multi-cycle
THz pulse
fTHz = 0.39 THz
TTHz = 2.56 ps
Compact Linear Accelerator for Research and Applications
25th September 2025
Short bunch:
400 fs rms
2 pC charge
Long bunch:
2.5 ps rms
30 pC charge

## Slide 5
Experimental Setup: The Terahertz source
THz beam profile
PPLN wafer stack
THz phase shear plate
Drive laser
THz pulse
THz frequency
Domain period (2x wafer thickness)
F. Lemery et. al. Commun. Phys. 3, 150 (2020)
P. J. Dalton et. al. Appl. Phys. Lett. 125, 141101 (2024)
Drive Laser:
Up to 600 mJ pulses
800 nm central wavelength
50 fs transform limited duration  750 fs chirped in use
500 mJ·cm-2 fluence at stack
THz source:
10 Cycle (20 wafer) pulse
120uJ pulse energy
0.03-0.1% conversion efficiency
Converted to free space quasi-TEM01 mode
C. D. W. Mosley et al. Optics Express. 3, 4041-4054 (2023)
25th September 2025

## Slide 6
Experimental Setup: Dielectric lined waveguide
30 mm
THz DLW
Time
Energy
Long injected bunch
Time
Energy
Short injected bunch
Single bunch compression
Multi Bunch Train
Time
Energy
Multi-cycle modulation
Time
Energy
Sub-cycle chirping
460μm
DLW exit
600 μm
DLW assembly
Dielectric lining results in: Longitudinal Section Magnetic modes (LSM)
LSM11 for acceleration
Dimensions matched to give the LSM11 THz the same phase velocity as the electron beam velocity ve = c (1 - 10-4)
3.18 mm
3.25 mm
Coupler entrance
L. J. R. Nix et. al. Phys. Rev. Accel. Beams 27, 041302 (2024)
25th September 2025

## Slide 7
Experimental Setup: The Terahertz interaction extrapolated
30 mm
THz DLW
Time
Energy
Single compressed
bunch
Time
Energy
Multi-cycle modulation
Time
Energy
Micro-bunch
train
Time
Energy
Long injected bunch
Time
Energy
Short injected bunch
Time
Energy
Sub-cycle chirping
THz beam profile
PPLN wafer stack
THz phase shear plate
Drive laser
5.5 MeV
35.5 MeV
Magnetic dogleg
THz pulse
CLARA
3 GHz RF linac
1 m
Magnetic chicane compressor
Single bunch compression
Multi Bunch Train
25th September 2025

## Slide 8
Multi Bunch Train
25th September 2025
Measured
Simulated Phase Space

## Slide 9
Multi Bunch Train
25th September 2025
Measured
Simulated Phase Space

## Slide 10
Multi Bunch Train
Long bunch:
2.5 ps rms
30 pC charge
450 keV FWHM
25th September 2025
No THz
THz on
Energy Spectrometer Images

## Slide 11
Multi Bunch Train
Time
Energy
Multi-cycle modulation
Time
Energy
Micro-bunch train
Magnetic chicane compressor
37 fs rms
2 ps spacing
Long bunch:
2.5 ps rms
30 pC charge
450 keV FWHM
25th September 2025

## Slide 12
Single bunch compression
THz off
Deceleration
Acceleration
Chirping
25th September 2025

## Slide 13
Time
Energy
Single compressed
bunch
Time
Energy
Sub-cycle chirping
Single bunch compression
15 fs rms
400 fs rms
25th September 2025
Magnetic chicane compressor

## Slide 14
Temporal Locking: Modelling elements
THz DLW
Time
Energy
Time
Energy
5.5 MeV
35.5 MeV
Magnetic dogleg
CLARA
3 GHz RF linac
1 m
Magnetic chicane compressor
25th September 2025
Time
Energy
RF
THz
Drift + Dogleg
Drift + chicane
Greatest change in electron bunch chirp at THz zero cross phase
THz source
Converts electron bunch chirp to compression around THz zero cross phase

## Slide 15
System | Set-point | Jitter (rms) | Comment
 | 5.5 MeV | 2 keV | 
 | 0 fs | 200 fs | 
 | 30 MeV | 8 keV | 
 | 0° | 10-3 rad 53 fs | Single bunch
 | -15° | 10-3 rad 53 fs | Bunch Train
 | 133 keV | 3 keV | Single bunch
 | 104 keV | 2 keV | Bunch Train
 | 0 fs | 200 fs | 
System | Set-point | Jitter (rms) | Comment
 | 5.5 MeV | 2 keV | 
 | 0 fs | 200 fs | 
 | 30 MeV | 8 keV | 
 | 0° |  | Single bunch
 | -15° |  | Bunch Train
 | 133 keV | 3 keV | Single bunch
 | 104 keV | 2 keV | Bunch Train
 | 0 fs | 200 fs | 
Jitter suppression
Laboratory Reference Frame:
25th September 2025
Terahertz Drive Laser Reference Frame:
New laser locked reference point
Long Bunch
Short Bunch

## Slide 16
Summary
25th September 2025
Long Bunch Initial:
2.5 ps rms
30 pC charge
37 fs rms
2 ps spacing
Short Bunch Initial:
400 fs rms
2 pC charge
Long Bunch Final:
37 fs duration electron bunches
RF phase controlled ps spacing
69 fs timing jitter to laser
Ideal for plasma wakefield applications
Short Bunch Final:
15 fs duration electron bunches
25 fs timing jitter to laser
High peak current for charge of bunch
Extremely stable ultrashort bunch for further experimentation
15 fs rms
400 fs rms

## Slide 17
Thank You Any Questions?
Dan Lake
Christopher Shaw
Laurence Nix
Connor Mosley
Beatriz
Higuera Gonzalez
Darren Graham
Sergey Siaber
Joseph Bradbury
Morgan Hibberd
Graeme Burt
Steven Jamison
Rob Appleby
Dave
Walsh
Tom
Pacey
Matt
King
+ STFC staff
THzAG.uk
25th September 2025
M. Hibberd et. al. arXiv:2508.20685 [physics.acc-ph]