## Slide 1: High Gradient Electron Injector for external injection for AWAKE Run 2C
EAAC2025, ELBA, Italy, September 21st-27th
Steffen Doebert, CERN
Introduction to AWAKE Run 2C
New electron injector and high-power RF systems
High gradient developments
Outlook

## Slide 2: AWAKE Run 2, from acceleration to accelerator
Demonstrate possibility to use AWAKE scheme for high energy physics applications in mid-term future!
Start 2021! Staged program for ~ 10 years
Accelerate an electron beam to high energy (gradient of 0.5-1GV/m)
Preserve electron beam quality as well as possible (emittance preservation at 10 mm mrad level)
Demonstrate scalable plasma source technology (e.g. helicon prototype)
Goals:
  Need to work in blow-out regime and do beam-loading
  New electron beam based on x-band: 150 MeV, 200 fs, 100 pC, σ = 5.75 µm

## Slide 3: Run 2C, parameters for both injectors
 | Beam Energy | Energy Spread | Energy stability | RMS Bunch Length | Bunch Charge | Emittance | Beam size plasma focus
Injector 1 |  |  | 1 x 10-2 |  |  | 2 - 5 | 
Injector 2 |  |  | 1 x 10-3 |  |  | 2 | 
 | Beam Energy | Energy Spread | Energy stability | RMS Bunch Length | Bunch Charge | Emittance | Beam size plasma focus
Injector 1 |  |  | 1 x 10-2 |  |  |  | 
Injector 2 |  |  | 1 x 10-3 |  |  |  | 
Flexibility in the beam parameters which can be delivered keeping good energy spread and emittance Energy: +- 10%, Charge: up to 400 pC, Bunch length: 0.2-1 ps, beam size
Constraint space for hardware
Excellent timing stability and synchronisation with laser and self-modulation device; ~ 30 fs stability

## Slide 4: 150 MeV injector – beam dynamics design
Very compact electron injector
Simulated parameters within specifications
 | 0.14 |  | 0.44 | 9 | 
 | 0.14 |  | 0.44 |  | 
Parameter | RF Gun | Buncher | Acc. I-III
Frequency |  |  | 
Gradient |  |  | 
N. Cell |  |  | 
Parameter | RF Gun | Buncher | Acc. I-III
Frequency |  |  | 
Gradient |  |  | 
N. Cell |  |  | 
262 |  | 1.0 |  | 0.1-1.0
262 |  | 1.0 |  | 0.1-1.0
Laser parameters
RF parameters
Length ~ 5 m

## Slide 5
S-Band RF System Layout
~ 20 m difference for injection points = 67 ns
S-band, 45 MW
A
j
15 MW, SW, 120 MV/m
circulator
10 MW, SW,
100 MV/m
10 MW, TW, 18 MV/m
j
We will use a single high-power klystron to power all 3 GHz cavities
less waveguides
same rf source and timing jitter
easier to maintain
coupling of the operation of the two injectors

## Slide 6
Solenoid
X
X
X
X
X
X
X
X
X
X
X
X
X
X
15 MW, S-band
25 MW, x-band
Long waveguides 40-50 m
Round or double height WG needed
PC, 120-130 MW
50 MW, x-band
3 structures at 55 MV/m
Solenoid
A, j
150 MeV injector – X-band RF layout
PC, 90 MW
j
This solution gives a bit more margin in 12 GHz power and makes optimal use of contributed equipment from CLIC (cost savings)

## Slide 7
Electron Source Integration status
Quite challenging integration due to space constraints and equipment density in the area

## Slide 8
Current 3D model of Injector 2

## Slide 9
Shunt Impedance [MΩ/m] | 100
Group Velocity vg/c [%] | 2.4
Q-Factor | 7061
Attenuation [1/m] | 0.7
Length [m] | 0.9
X-band structure developments
Travelling wave Constant Impedance
Designed by INFN Frascati, D. Alesini, M. Diomede,
for CompactLight and EuPraxia
Mechanical design made at CERN
CLIC style tolerances
Vacuum brazing design
Structure to be inserted in a solenoid of 150 mm diameter bore radius
Buncher structure has 30 cells and the accelerator 105 regular cells

## Slide 10: Buncher: E-field simulations
30 regular cells + 2 coupler cells

## Slide 11
First short prototype build at CERN
Verify mechanical design, brazing assembly and tolerances needed.
Low power RF measurements
C. Capelli, N. Chritin

## Slide 12
First short prototype with cells made at CERN

## Slide 13
Structure Awake - 3 brazing steps
+
x5
x2
Machining
Brazing
x4
x8
x2
+
AgCuPb10 : 850°C
AgCuPb5 : 810°C
AgCu : 780°C

## Slide 14
AWAKE 12 GHz accelerating structure prototype
Mechanical, vacuum and RF measurements done to evaluate prototype, finally being cut for further analysis
Rolf Wegner

## Slide 15
AWAKE 12 GHz accelerating structure prototype

## Slide 16
C. Capelli, N. Chritin
Next prototype and final structure
External cooling to simplify
C. Capelli, N. Chritin
30 cm
90 cm

## Slide 17: I-FAST structure
Unfortunately, not leak tight
Straightness measurement showed cell alignment problems
RF measurements show large losses

## Slide 18: Pulse Compressor Optimization Process
Rs: Effective Shunt Impedance
For each value of the filling time of the accelerating Structure there is a value of β and Q of the storage cavities wich maximizes Rs*
To optimize:
+
r, Q, vg, τs
Q0, β
L=0,9 m
τs =125 ns
Jordan Arnesano
“Classical” SLED at
CERN- Xboxes
Barrel Open cavity for CLIC

## Slide 19: Waveguide distribution and pulse compressor
Losses:
49 m circular waveguide (ø50mm)
10 mode converters
Power | MW
Klystron output | 21
PC input | 16.6
Input structure | 8.3
SLED:
Attenuation | %
Circular WG | 11.23
WR90 | 5.69
MC | 5.59
Total | 20.96

## Slide 20
ARTI in CTF2
Screen BTV1
Spectrometer
F-Cup
RF-GUN
1 us
200 ns
600 ns
800 ns
400 ns
Brazing free RF-Gun from INFN
RF-gun conditioned to 120 MV/m on the cathode
GUN contributed by INFN, D. Alesini
Notes: .

## Slide 21: RF-Gun operation with beam
Miguel Martinez Calderon and Anton Eager
Solenoid scan
Qe-measurements of copper cathode
QE ≈ 1.34 x 10-4

## Slide 22: Summary
AWAKE needs a challenging injector for external injection
Design well established, procurement for high-power RF-system started
Development program at CERN for the high-gradient x-band structures ongoing
Test set-up for the electron source is operating with good results
Installation of the injector is planned for the second half of 2027

## Slide 23: CTF2 QE measurements
Fluence calculated with the FWHM spot sizes measured by Anton, taking the lowest values (“x” beam size) to be in the worst-case scenario
Even at the highest Fluence tested in the last tests, we still do not reach the ablation threshold.
Single-pulse ablation threshold for Copper using fs-pulses and UV wavelength should be well above 100 mJ/cm2
Exact data for ablation threshold with UV fs-pulses is hard to find but there are many references using different wavelengths (please note that also ablation threshold data is normally calculated using the 1/e2 spot size and here we are plotting FWHM) [1-3].
[1] Jan Winter, et. al. "Ultrashort single-pulse laser ablation of stainless steel, aluminium, copper and its dependence on the pulse duration," Opt. Express 29, 14561-14581 (2021)
[2] Byskov-Nielsen, J., et al. Ultra-short pulse laser ablation of metals: threshold fluence, incubation coefficient and ablation rates. Appl. Phys. A 101, 97–101 (2010).
[3] Ultrafast laser ablation of copper with GHz bursts: A numerical study on the effects of repetition rate, pulse number and burst fluence on ablation efficiency and heat-affected zone. Optics & Laser Technology 158, Part A, February 2023, 108803
Miguel Martinez Calderon and Anton Eager

## Slide 24: Timeline & Milestone Overview
Start of experiments
Now
Run 1a: Successful
Self-Modulation
Run 1b: First Electron Acceleration
Run 2a: Control of
Self-Modulation
Run 2b: Stabilization of
Wakefield Amplitude
Run 2c: Acceleration with
Quality Control
Run2d:
Demonstration of
Scalability
DPS Operation
in AWAKE
2017
2018
2021
2023

## Slide 25
PROPOSAL C
Length: 46 and 49m
Length: 34m
90°
90°
90°
Electron Source Integration status Waveguide routing study
This version is currently our preferred one  base line we will study this one in more detail

## Slide 26: Seeding with an Electron Bunch
PhD Student
 Wakefields driven by an electron bunch also allow for seeding in pre-ionized plasmas
To build an accelerator, the wakefield phase and amplitude must be reproducible.
Electron bunch drives
Seed wakefields
SMI: Self-Modulation instability
Process starts from noise
SSM: Seeded Self-Modulation
Process starts from seed
e-

## Slide 27: Single cell
Parameter | Value
[GHz] | 11.9932
 | 7054
 | 14028
 | 2.41
 | 1.94
[mA/V] | 2.91
[mA/V] | 0.45
Parameter | Value
 | 11.9932
 | 7054
 | 14028
 | 2.41
 | 1.94
 | 2.91
 | 0.45
E-field
H-field

## Slide 28: Linac: E-field
105 regular cells + 2 coupler cells

## Slide 29: Reference design
Mohsen Dayyani Kelisani