## Slide 1: Target Area Fraunhofer project @HI Jena: Synchronized High Power Laser Experiments
Alexander Sävert, Marco Hornung, Dominik Hollatz, Peter Hilz, Andreas Winnefeld, Hendrik Wöhl, Marcus Ostermann, Thomas Köhler, Frank Schorcht, Dirk Hieronymous, Malte C. Kaluza, Matt Zepf, Thomas Stöhlker
EAAC 2025, 25.09.2025

## Slide 2: HI Jena extension (2022) & TAF project
New 140 m2 Target Area Fraunhofer (TAF)
Fraunhoferstraße

## Slide 3: High intensity lasers @ HI Jena
JETi200
POLARIS
NIR option
Wavelength: 800 nm
Energy: 2 mJ
Pulse duration: 3 fs - 30 fs
SWIR option via OPA + NDFG
Wavelength: 1.1 µm – 7 µm
Energy: 1 mJ – 5 µJ
Pulse duration: few-cycle
Wavelength: 800 nm
Energy on target: 5 J
Pulse duration: 17 fs Peak power: 300 TW
Short pulse NIR probing system
Wavelength: 750 nm
Energy: 200 µJ
Pulse duration: < 5 fs
Wavelength: 1030 nm
Energy on target: 16 J (54 J)
Pulse duration: 100 fs
Peak power: 160 TW (500 TW)
Short pulse probing system
Wavelength: 800 nm
Energy: 20 µJ
Pulse duration: 11 fs
JETi ONE

## Slide 4: Major tasks for TAF project
Synchronisation of all beams in space (< 3 µrad (rms)) and time (< 20 fs (rms))
Increase the peak power of POLARIS for novel experiments & applications
Readiness of the laser systems for joined experiments and autonomous control for machine learning to optimize these

## Slide 5: Beam Transport Towers & Frames, stablity analysis
JETi200 Periscope (~ 3m)
JETi200 turning chamber above wedding chamber (~ 3 m)
POLARIS turning chamber (~ 5 m above ground)
Beam shaping chamber (~ 6 m x 2m x 1.5 m)
TAF layout & beamline
25 m
15 m
10 m
JETi200 & JETiONE
POLARIS
1
2
4
3
VC-G: strongest criteria for REM und TEM with sub-Ångström resolution.
1
2
3
4

## Slide 6: Foundation Work for JETi-Beamline and Beam-Shaping Chamber
JETi200 Periscope
Wedding Chamber
Beam Shaping Chamber

## Slide 7: New 54°- AOI Pulse Compressor
24.09.2025
7
Grating compressor
Turning
chamber
Turning
chamber
Periscope
Switchyard
Key features
54° AOI, 5.8 m separation length
500 TW peak performance
190 mm circular aperture
Monolithic compressor
MLD design possible
1480 l/mm gold gratings
6.5 m
Existing (old) chambers
Optical design:
500 TW peak performance with 190 mm aperture
TAF

## Slide 8: Pulse Compressor Vacuum System
Pend < 1x10-7 mbar
12 x breadboard-base
View into the compression chamber
First eigenfrequency > 200 Hz

## Slide 9: Large Aperture Mirrors, Adaptive Optics and Mounts
45° single pass reflected wavefront w/o PWR and AST, PV = 86 nm, 3 nm RMS, 230 x 230 mm²
560 mm
370 mm
Ultra-Stable Mirror Mount
Prototype in development
Monolithic basement
Ultra-stable bearing
High-precise Adjustment
+- 3° adjustment range
Mechanical RMS pointing stability < 50 nrad is envisioned
Deformable mirror systems for JETi200 & POLARIS
170 mm & 220 mm clear aperture
53 actuators
Closed loop with HR WFS
8 large aperture mirrors POLARIS
2 pieces: 440 x 320 x 80 mm³
12 pieces: 320 x 230 x 50 mm³
Surface < l/10 measured @ 1053 nm
Damage threshold > 1 J/cm² @ 100 fs
2023 FGI 0023
6 large aperture mirrors JETi200
6 pieces: 320 x 230 x 50 mm³
Damage threshold > 0.1 J/cm² @ 20 fs
Surface < l/30 measured @ 800 nm

## Slide 10: Wedding chamber & TAF experimental chamber
25 m
15 m
10 m
6.3 x 2.3 x 1.5 m³
Breadboard: 5.8 x 2.1 x 0.08 m³
1 m free height above breadboard
Decoupled breadboard
combining JETI200, JETiONE and POLARIS
POLARIS
JETi200 & JETiONE

## Slide 11: Beam Shaping Chamber – Pulse compression to PW level
delivery in Q4/2025
Key parameters:
switch yard for POLARIS and JETi200
support for double plasma mirror
long focal length focusing mirror (f = 8 m & f = 17 m)
Pulse compression with gas or solid targets POLARIS: < 30 fs, JETI200: < 10 fs

## Slide 12: New control systems for JETi200 and POLARIS
old system was installed in 2013 and running since then
active control for optimization experiments requires access to the laser control system
new control system installed in 09/2025
Hardware upgrade
Software update
open source device driver for cameras and gas control systems developed
smaller work packages for our implementation
Vision package for cameras

## Slide 13: State of the art synchronisation - locations

## Slide 14: TAF timing system at HI Jena
OSAT: December 2024
2022 FGI 0008
2023 FGI 0022
Temperature stabilized platform for low noise optical master oscillator.

## Slide 15: Phase Noise Measurement
JETi ONE (VITARA)
POLARIS (FLINT)
JETi200 (ELEMENT 2)
rms jitter = 4.2 fs
rms jitter = 2.0 fs
rms jitter = 1.6 fs

## Slide 16: Jitter measurement (Out-Of-Loop) FLINT-Vitara
Total integrated jitter (1 MHz – 60 µHz): 34 fs (rms)
Timing drift: 4.8 fs rms (5 hours)

## Slide 17: Jitter measurement (Out-Of-Loop) FLINT-Element2
Total integrated jitter (1 MHz – 30 µHz): 12 fs (rms)
Timing drift: 5.2 fs rms (10 hours)

## Slide 18: Conclusion and Outlook for 2026
Major vacuum chambers are installed.
Timing system performing quite well .
Bringing POLARIS back online
Finish vacuum installation in TAF (pumps, …)
Manufacturing of optomechanics
Post-compression schemes for few-cycle pulse generation
First experiments in 2027

## Slide 19: First flagship experiments @ TAF (2027 and beyond)
Few-cycle option for probing from 800 nm up to 7 µm wavelength.
Linear/non-linear Breit-Wheeler experiments
Light by light scattering
Radiation Reaction
Temporal (~10s fs) and spatial overlap (< 3 µrad) crucial.
Dissertation D. Hollatz
JETi200
JETi ONE

## Slide 20: Acknowledgements
S. Borneis
20
A. Winnefeld
M. Ostermann
T. Köhler
H. Wöhl
D. Hieronymous
F. Schorcht
M. Hornung
A. Sävert,
D. Hollatz
P. Hilz
M. Hellwing
G. A. Becker
M. B. Schwab
Y. Azamoum
A. Kessler
J. Hein
M. C. Kaluza
M. Zepf
T. Stöhlker
R. Pattathil
D. Symes
A. Stallwood
S. Hundack
A. Hahn
D. Marx