## Slide 1: Research opportunities at Brookhaven's Accelerator Test Facility supported by multi-wavelength lasers combined with an electron beam
Brookhaven National Laboratory
William Li

## Slide 2: Content
Introduction to Accelerator Test Facility (ATF)
Accelerator research at ATF
Long-wave infrared (LWIR) upgrade plans
Prospects for future colliders with LWIR-driven LWFA

## Slide 3: Introduction to ATF
Notes: No notes

## Slide 4: ATF overview
Department of Energy Office of Science User Facility for the Accelerator Stewardship program
Proposal-driven, peer reviewed
Over 30 years of operation for user experiments
Over 130 user experiments completed
40 PhDs defended
20 experiments are currently active

## Slide 5
ATF capabilities
  Linac
  Nd:YAG Laser
  LWIR Laser
hn
e-
0.266 µm
1.06 µm
9.2 µm
75 MeV
  Experimental Area
2.86 GHz
81.6 MHz
  OPA
0.8 µm
  TiS Laser
LINAC
high-brightness photocathode
20-75 MeV
energy spread 0.1%
norm. emittance 1mm
LWIR Laser
high-pressure, isotopic, CPA, l = 9.2 mm CO2 laser
peak power 5 TW
pulse energy 5-15 J
NIR lasers
Ti:S l = 0.8 mm and Nd:YAG l = 1.06 mm
energy 80 mJ 100 mJ
pulse width: 75 fs 14 ps
pulse FWHM 2.0 ps
repetition rate 0.05 Hz
single bunch 10 ps – 200 fs
charge ~1 nC
multi-bunch trains
Unique combination of synchronized high-peak-power lasers and a high-brightness electron linac.
Last year, ~40% of experiments used all 3 capabilities!

## Slide 6
CO2
CO2
Compressor
Stretcher
OPA seed pulse generator
High-pressure, isotopic
gas amplifiers
5 TW
2 ps
State of the art ATF laser system
Solid-state OPA front end
High-pressure isotopic CO2 amplifiers
First CPA CO2 laser system
String of innovations:

## Slide 7: Accelerator research at ATF

## Slide 8
A brief (incomplete) history of accelerator research at ATF
First high-brightness beams from photocathode RF gun:
X. J. Wang et al., NIMPR A 356, 159-166 (1996)
First seeded FEL high-gain harmonic generation
A. Doyuran et al., PRL 86, 5902-5906 (2001)
First staged laser acceleration (IFEL)
W. D. Kimura et al., PRL 86, 4041 (2001)
Demonstration of SASE at visible wavelengths
A. Murokh et al., Phys. Rev. E 67, 066501 (2003)
First high-gradient, controlled PWFA
E. Kallos et al., PRL 100, 074802 (2008)
Development of masking technique for electron microbunches
P. Muggli et al., PRL 101, 054801 (2008)
First demonstration of seeding of self-modulation instability in plasma
Y. Fang et al., PRL 112, 045001 (2014)

## Slide 9
1.7 MeV protons
1TW CO2
532 nm probe
Energy spread 4% (record-narrow for laser acceleration)
Spectral brightness 1012 proton/MeV/str
Proton energy up to 3.2 MeV
Proton acceleration from H2 jet
Low critical plasma density (1019cm-3) allows driving ions out of gas target.
Shock wave mechanism of monoenergetic acceleration.
C. A. J. Palmer et al., PRL 106, 014801 (2011)
C. A. J. Palmer et al., J. Plasma Phys. 81, 365810103 (2016)

## Slide 10: Wavelength scaling for LWFA
= 0.8 um, 25 TW, 30 fs
ne = 2e19 cm-3
= 10 um, 25 TW, 500 fs
ne = 1e16 cm-3
Equivalent bubble with Ti:sapph would require PW peak powers
Simulations courtesy of G. Shvets

## Slide 11: Adding e-beam to laser plasma research
CO2 pulse
Injected
electron
bunches
500 fs CO2 laser, ao=4, no=1016cm-3, =800 MeV
Seeding electrons into acceleration stages
Model
Experiment
Wake field tomography
Combination of high-power lasers and electron linac allows pioneering studies of electron injection into laser wakefields as well as detailed wakefield visualization.
laser
e-beam
laser
e-beam
Courtesy of M. Downer (UT Austin)
A. Gaikward et al., Proc. of 66th Annual Meeting of APS Div. of Plasma Phys. (2024)

## Slide 12: Two-color ionization injection
Yu, PRL 112, 125001 (2014)
Schroeder, European Conference on Lasers and Electro-Optics (2015)
See also Xu, PRSTAB, 17, 061301 (2014)
Schroeder, PRSTAB 17, 101301 (2014)
In progress…
Long-wavelength laser to drive the wakefield
Short-wavelength laser to trigger ionization within the wakefield
Drive laser needs large to form plasma wakefield, but we want low field to avoid prematurely ionizing the gas
Injector laser needs high field to ionize the gas, but low to avoid emittance degradation
Low emittance
Excellent phase space
Very intense, small
Less intense, large

## Slide 13: LWIR laser roadmap

## Slide 14
Power (TW)
500 fs 20 TW
100 fs 40 TW
Now (10 µJ seed)
Gain spectrum
2 ps 6 TW
1 optical cycle = 31 fs
Roadmap to multi-petawatt femtosecond LWIR
10 mJ seed
Post-compression
14

## Slide 15: Optical pumping
4.3 µm
3ν3
1.44 µm
ν3
2.8 µm
T
2ν3
ν3
ν3
ν1
ν3+ν1
Past
No viable solid-state option
Present
(Er,Cr):YSGG
Future - Yb:YAG + OPA
- Cr:YAG

## Slide 16
With ~60 mJ absorbed in the multiatmosphere CO2 cell, we generated a single picosecond pulse with an energy ≥2 mJ.
Demonstration of compact 15 atm CO2 amplifier pumped at 2.8 um
Neptune Laboratory
Er:YSGG
Q-switched
laser
NaCl
wedge
Optically pumped 12 cm CO2 cell
DM
Calorimeter
10 μm regen
DM
2.8 μm pump: 100 mJ, 90 ns
Lens
MCT detector
10 μm filter
F=0.7 meters
R10.6=0.5%
R2.8=1.5%
SS
0.4 μm Ti:saph. >1.6 mJ, 50 fs
TOPAS/DFG System 10.3 (10.6) μm seed >10 mJ, 500 fs
Output pulse:
~10 μm ≤2 mJ, 3-5 ps
10 Atm CO2-He
15 Atm CO2-He
1/40 GHz=25 ps
Amplified 10.3 mm beam
S. Tochitsky, D. Mateo, E. Geske et al. Amplification of 10 μm picosecond pulses in a compact optically pumped multiatmosphere CO2 laser Under per review Opt. Express (2025)

## Slide 17: Next-generation LWIR laser architecture (≥25 TW, ≥10 Hz)
BAT laser architecture
(LLNL)
1.5 J, 270 fs, 1 Hz operation demonstrated
DiPOLE laser architecture (CLF RAL, UK)
100 J, 10 ns, 10 Hz
systems exist: - CLF, UK
- HiLASE, Czech Republic
- European XFEL, Germany
ALL CRITICAL TECHNOLOGIES ARE WITHIN REACH
~3-cycle

## Slide 18: Prospects for future colliders with LWIR-driven LWFA

## Slide 19
5TeV
~3 km 500 stages
~3 km 500 stages
5 TeV
5 TeV
Prospective 10 TeV e-e+ Collider
P5 recommendation
Advanced accelerators could provide the necessary cost savings to make it feasible
Plasma-based accelerator with demonstrated 100 GeV/m gradient is a possible solution.
Geometric Luminosity
= 1035 cm-2 s-1
Higher bunch charges and smaller emittance are favored
19

## Slide 20: Two optimized examples
Parameter | Ti:S | CO2
Laser wavelength (mm) | 0.8 | 9.2
Plasma density (×1016cm-3) | 11 | 0.35
Plasma wavelength (mm) | 99 | 560
Bubble volume (mm3) | 10-3 | 0.17
Laser pulse duration (fs) | 130 | 700
Laser radius (mm) | 63 | 360
Laser peak power (TW) | 300 | 75
Normalized field 0 | 1.06 | 1.07
Accelerating field (GeV/m) | 12.6 | 2.2
Single stage interaction length (m) | 0.79 | 1.1
Energy gain per stage (GeV) | 10 | 2.4
Number per bunch (×109) | 4 | 23
Collision rate (kHz) | 10 | 0.3
Laser energy per stage (J) | 40 | 52
Average laser power per stage (kW) | 400 | 16
Number of stages | 500 | 2083
Total laser power (MW) | 200 | 33
Parameter | Ti:S | CO2
Laser wavelength (mm) | 0.8 | 9.2
Plasma density (×1016cm-3) | 11 | 0.35
Plasma wavelength (mm) | 99 | 560
Bubble volume (mm3) | 10-3 | 0.17
Laser pulse duration (fs) | 130 | 700
Laser radius (mm) | 63 | 360
Laser peak power (TW) | 300 | 75
 | 1.06 | 1.07
Accelerating field (GeV/m) | 12.6 | 2.2
Single stage interaction length (m) | 0.79 | 1.1
Energy gain per stage (GeV) | 10 | 2.4
Number per bunch (×109) | 4 | 23
Collision rate (kHz) | 10 | 0.3
Laser energy per stage (J) | 40 | 52
Average laser power per stage (kW) | 400 | 16
Number of stages | 500 | 2083
Total laser power (MW) | 200 | 33
Following “Physical considerations for a laser-plasma linear collider” C. B. Schroeder et al, 2010
where
0.3×
20
Bigger sized bubble facilitates low-emittance beams
Higher charge
reduces quadratically repetition rate
resulting in relaxed average laser power
and total power
Factors affecting collider luminosity:

## Slide 21: Conclusions
The Brookhaven Accelerator Test Facility operates three capabilities: electron beam, NIR lasers, and LWIR laser
Long history of pioneering accelerator science
Unique multi-beam multi-wavelength experiments
Roadmap established for 25 TW+ LWIR with high repetition rate
Get in touch if you have interesting ideas to test!
Point of contact: ATF director, Igor Pogorelsky igor@bnl.gov

## Slide 22: Thank you!

## Slide 23: Backup slides

## Slide 24
SWIR
MWIR
LWIR
NIR
Compilation: Sara Bucht (LLE) ~2018
CO2 amplifiers
CO2 lasers are the only choice for delivering TW power in LWIR

## Slide 25
Seed
Generator
10 mJ
300 fs
7 mJ
140 ps
20 J
140 ps
14 J, 0.5 ps
20 TW
@ 9.3 mm
Can we do better than 2 picoseconds?
Strong, broadband seed pulse
Possible routes to
ultra-fast CO2 lasers:
Nonlinear post-compression (NLPC)
Seed: 10 µJ
Two CO2 amplifiers
Seed: 10 mJ
Single CO2 amplifier
x108
x104
x104

## Slide 26
,
Strong, broadband seed pulse
Possible routes to
ultra-fast CO2 lasers:
Nonlinear post-compression (NLPC)
  Self-phase modulation due to Kerr effect in a nonlinear material results in a quasi-linear frequency chirp.
n(t) = n0 + n2I(t)
Self-phase modulation
Dispersive compression
=
compressible linear chirp
Can we do better than 2 picoseconds?
  A chirped pulse gets compressed in a material with a negative group dispersion.

## Slide 27
D ~50 GHz
Gain spectrum affects the pulse time envelope
~20 ps
=
Inverse Fourier transform
Periodical line structure of the CO2 gain spectrum splits a single picosecond pulse into a train.
High-pressure collisional broadening, combined with mixing different CO2 isotopes, overlaps individual rotational lines into continuum, and pulses as short as 0.5 ps can be amplified without distortion.

## Slide 28: Reaching strong field regime
7x1018 W/cm2 @ 9.3 mm gives 0=23
This is equivalent to 1021 W/cm2 with Ti:Sapph
Opportunities for reaching higher intensities through
  tighter focusing
  using bigger amplifier (>150 TW)
This can bring us to ~1020 W/cm2 or 0=87
Radius (mm)
Simulated focus of 40-TW
9.3 mm laser
Bigger amplifier available at BNL
Present final amplifier
150 TW CO2 laser could be equivalent to 15-150 PW solid state laser!
(not taking into account typically 10x longer pulse)
At equal power, CO2 laser provides the same ponderomotive action within ~l2 (100 times ) bigger area
~l3 (1000 times) bigger volume.

## Slide 29: Optical pumping
4.3 µm
1.44 µm
2.8 µm
2 µm

## Slide 30: LWIR single stage LWFA
3D PIC simulations performed for a 400 fs, 60 TW CO2 laser focused to w0=262.5 mm at the entrance to a 3.2x1015cm-3, matched, parabolic plasma channel.
Simulations by Wei Lu, Tsinghua Un.
Distance [cm]
Electron Energy [GeV]
0 20 40 60 80
3
2
1
0
0
200
400
600
Laser Spot Size [mm]

## Slide 31
Custom high-pressure x-ray ionized CO2 amplifier operated at BNL/ATF
X-ray pre-ionized electric discharge
Discharge volume 10x10x100 cm3
Pressure 10 atm
Amplified ps pulse 20 J
ATF high-pressure laser amplifier

## Slide 32: Submit proposal get approved safety review get beam time
User’s and Proposal Steering Committee meetings
Your experiment
www.bnl.gov/atf/
Approval of user experiments

## Slide 33: Representative sets of laser and plasma parameters for LWFA 10-TeV c.m. e−e+ collider
Parameter | #1 | #2 | #3 | #4 | #5 | PIC* | #6
Laser wavelength (mm) | 0.8 | 9.2 | 9.2 | 0.8 | 9.2 | 10 | 9.2
Plasma density (×1016cm-3) | 11 | 11 | 1.1 | 1.1 | 0.35 | 0.32 | 0.11
Plasma wavelength (mm) | 99 | 99 | 313 | 313 | 560 | 585 | 990
Laser pulse duration (fs) | 130 | 130 | 390 | 390 | 700 | 400 | 1300
Laser radius (mm) | 63 | 63 | 200 | 200 | 360 | 262 | 630
Laser peak power (TW) | 300 | 2.3 | 23 | 3000 | 75 | 60 | 230
Laser energy per stage (J) | 40 | 0.3 | 9 | 1200 | 52 | 24 | 300
Number per bunch (×109) | 4 | 4 | 13 | 13 | 23 | 12 | 40
Single stage interaction length (m) | 0.79 | 0.006 | 0.19 | 25 | 1.1 | 0.6 | 6
Accelerating field (GeV/m) | 12.6 | 12.6 | 4.3 | 4.3 | 2.2 | 3.8 | 1.25
Energy gain per stage (GeV) | 10 | 0.075 | 0.75 | 100 | 2.4 | 2.3 | 7.5
Number of stages | 500 | 66660 | 6660 | 50 | 2080 | 2170 | 660
Collision rate (kHz) | 10 | 10 | 1 | 1 | 0.3 | 1.2 | 0.1
Average laser power per stage (kW) | 400 | 3 | 9 | 1200 | 16 | 30 | 30
Linac length (stages 0.5m apart) (km) | 0.65 | 3.3 | 4.66 | 1.25 | 4.48 | 2.4 | 4.3
Total laser power (MW) | 20 | 20 | 6 | 6 | 2.6 | 6.5 | 2
33
PRAB 19, 091001 (2016)
Notes: Someone may ask: How we know that case is optimum? Why not to let TiS laser to operate at low plasma density if it is so beneficial?
We check what happening if we reduced the plasma density for TiS 10x, which is still 3x above the optimum CO2 case.
We see that the regime is becoming hardly affordable due to huge individual laser and stage length.
Then we do similar exercise for CO2 laser trying to use it under conditions optimum for Ti:Sapph laser.
We see that stage length is extremely short due to 100 times smaller depletion length. This results in small acceleration per stage and huge number of stages.
If anyone wants to take deeper dive into this problem and a table, I can address you to this reference.

## Slide 34: Experimentally accessing physics relevant to plasma research
Time
Length
Density
~3 fs
~1 μm
~1021 cm-3
☹️
Near-IR
~30 fs
~10 μm
~1019 cm-3
LongWave-IR
😃
Easier to resolve experimentally
Too short
Too small
EM Field
Same effect at less power
Same process at less density
Too dense
Laser-plasma interactions can be normalized to reference frequency:

## Slide 35
Specular reflection of an incident laser beam.
At high intensities (>1016 W/cm2 @ 10mm), laser field drives relativistic oscillation of the plasma surface.
This induces a Doppler effect on the reflected beam, resulting in a periodically distorted reflected waveform, the spectrum of which consists of a comb of high-order harmonics.
Relativistic Oscillating Mirror (ROM)
Broad spectrum
Ultra-short pulses
Intensity boost
Spot size ~
Potential ATF advantages:
Better control of plasma thickness <l.
Optical plasma diagnostic.
Availability of e-beam to analyze the focused field via electron deflection or Compton scattering.
Possibility of using a blast wave in plasma for a target.
      after High Power Laser Sci. Eng. 9, e6 (2021)
Notes: However, there are other opportunities for entering relativistic regime of high harmonic generation from target.
In this case plasma oscillations induce Doppler effect on the reflected beam, resulting in a periodically radiated bursts, the spectrum of which consists of a comb of high-order harmonics.
LWIR laser might allow better control over plasma thickness which needs to be less than lambda.
We can also use optical plasma diagnostic for better control of the process.
Availability of e-beam will allow to analyze focused field via electron deflection or Compton scattering. Note that focused fields in vacuum is difficult to measure otherwise.
Also, interesting possibility could be using blast wave in plasma as a target

## Slide 36
Scaling proton acceleration
with CO2 lasers
Production of hot electrons is the key.
Their energy strongly depends upon the laser wavelength
Proton acceleration from foil
10-mm laser with the intensity of 1016 W/cm2 performs like 1-mm laser of the 1018 W/cm2 intensity.
36
This was confirmed by ATF TNSA experiment.
Nucl. Instrum. Meth. Phys. Res. A620, 67 (2010)
Notes: Turning to user experiments on ion acceleration, we notice again the importance of favorable scaling of electron energy that forces electrons to escape target and pull protons and heavier ions along.
Here we explicitly demonstrated that 10-um laser with intensity of 1016 W/cm2 produces the same proton spectrum as 1-um laser of 1018 W/cm2 in the so-called Target Normal Sheaf acceleration.

## Slide 37
Scaling shock wave acceleration
37
Proton energy scales ~
=87 might give 4.5 GeV protons
Nat. Phys. 8, 95 (2011),

## Slide 38
Relativistic mirror
Upon reflection on such a mirror, the laser pulse wavelength is Doppler shifted by 1/4γ2 and compressed in time by the same factor.
Assuming perfect reflection, the light beam energy then gets boosted by 4γ2 and intensity by 16γ4 (in strongly relativistic case).
Assuming perfect focusing total intensity enhancement 64γ6 covering a gap to a Schwinger limit.
      after High Power Laser Sci. Eng. 9, e6 (2021)
Basic idea of a relativistic mirror

## Slide 39
Plasma wake as relativistic mirror
The reflected intensity is limited by recoil effect: or
        - condition where energy density in reflected pulse is much less than energy in electron layer.
        Example: 4 PW, ~1 kJ TiS laser drives a wake in 1018 cm-3 plasma that reflects =1.8x1015 W/cm2 (=0.3) of 10-mm light to =4x1025 W/cm2 @ l=2.5 nm compared to 4x1027 W/cm2 @ l=0.25 nm for 1-mm laser.
        Note that parameters are equivalent while the focus area for 10-mm laser case is 100x bigger!
Possible implementation with plasma wake at wave breaking
Wave breaking leads to singularity in the electron density distribution.
Reflection from singularity is typically very low (~0.1% @ =10) when driver and signal wavelengths are equal.
implying 10% for CO2 laser.
Focusing by such parabolic singularity adds to the overall intensity boost reaching ~ .
Gain in is canceled by diffraction.
        after T.M. Jeong, S.V. Bulanov et al, Rev. Modern Plasma Phys. (2024)
signal
plasma
drive
Notes: .

## Slide 40: Directed energy applications
Po-210
Detection of a radioactive source
2 cm
Wavelength scaling of laser filaments and secondary processes have been explored in recent ATF user experiments.
TW power can be transmitted in a single cm-thick filament over km distance
Δ
Phys. Rev. Applied 23, 034004 (2025)
Nat. Photon. 13, 41 (2019)

## Slide 41
Nonlinear Compton scattering
Energy of the electron quiver motion in laser field
Need 1016 W/cm2 to reach relativistic energy with CO2 laser
Also, bigger number of laser photons per Joule.
Angle distribution of high harmonics (simulation)
Laser acts as a virtual wiggler
First observation of nonlinear component in ICS at =0.3
With a stronger laser the ICS spectrum turns into a super-continuum with the maximum shifted to high harmonics.
Can be used for measuring peak laser intensity.
3rd harmonic and red shift at =0.6 PRST-AB 18, 060702 (2015)

## Slide 42: Other novel radiation mechanisms
Relativistic Instability Modulated Emission (RIME)
Can produce EUV order of magnitude more intense than reflected harmonics
Burst Intensification by Singularity Emitting Radiation (BISER)
Strong x-ray radiation from near-critical singularities in a plasma wave envelope
A.S. Pirozhkov et al. Sci. Rep. 7, 17968 (2017)
M. Lamac et al. PRL 131, 205001 (2023)

## Slide 43: Probing B-fields generated by plasma instabilities
Pioneering studies of dense plasma instabilities lead to better understanding of Universe and fast ignition.
LWIR driver is ideal because it strongly affects plasma temperature, Te~ , and has a low critical plasma density, ncr~l-2, allowing optical diagnostic in gas plasma.
Phys. Plasmas 31, 072108 (2024)