## Slide 1: Algorithmic optimisation of ionisation injection in laser wakefield acceleration
Michael Backhouse
EAAC 2025 | 25 September
Zulfikar Najmudin

## Slide 2: Outline
Part 1
Part 2
Vanilla Bayesian optimisation (BO) of ionisation injection in an experiment.
Motivation and implementation
Experimental results
PIC simulations
Multi-Task, Multi-Objective BO (MT-MOBO) of ionisation injection at PW scale facilities.
Motivation
MT-MOBO introduction
Toy problem: beams for FEL

## Slide 3: Experimental setting
1

## Slide 4: Background and Motivation
R. J. Shalloo et al. (2020)
S. Jalas et al. (2021)

## Slide 5: Background and Motivation
Our study:
Can vanilla BO produce low-energy spread, low dark current beams, starting from a very large energy spread?
Can this be done with a simple gas target – no shocks, localised dopant regions, etc.
Can it be done by only varying the input laser?
R. J. Shalloo et al. (2020)
S. Jalas et al. (2021)

## Slide 6: Experiment setup
Laser energy: 800 mJ
Central wavelength: 800 nm
Pulse length: 42 fs
Spot width: 12 m
Energy within FWHM: 43%
Peak a0: 2.15
“Classic” laser wakefield acceleration setup
L. T. Dickson et al. (2022)

## Slide 7: Experimental results

## Slide 8: Experimental results
Focus: -0.47mm
(before plateau)
GDD: 500 fs2
TOD: -3300 fs3
FOD: +4485 fs4

## Slide 9: Demonstrating the sensitivity to temporal shape
PIC simulations in FBPIC
Using a realistic reconstructed laser spatial intensity and phase profile
Focal position and chirp work together to localise injection
Optimial TOD matches pulse shape to the wake to deepen the potential

## Slide 10: Simulation setting
2

## Slide 11: Algorithmic optimisation motivation
Bigger lasers mean more expensive simulations
Greater target flexibility – dimensionality is growing
Domain size/scale length ratio can be much larger
Different users want competing objectives
Increasing complexity
Astra-Gemini vs EPAC
C. Hvarfner et al. (2021)

## Slide 12: Multi-objective BO and Multi-Task BO
Multi-Objective Bayesian Optimisation
Multi-Task Bayesian Optimisation
Determining optimal tradeoffs between objectives
Attempting to maximise the hypervolume enclosed by the best achieved objectives in the output space
Example: Energy-charge trade-off
Transfer learning between discrete settings
Maximise the objective of the main ‘online’ task
Example: transfer learning between simulation codes
F. Irshad et al. (2023)
A. Ferran Pousa et al. (2023)

## Slide 13: MT-MOBO for inter-task Parato front optimisation
Task 1:
Task 2:
Objective 2
Objective 1
Inter-task knowledge transfer
Surrogate model maps from inputs to a vector with one entry for each objective-task pair.
Kenel mixes task and spatial information for restricted transfer learning
MT-MOBO schematic for two tasks and two objectives
Outperforms regular MOBO on benchmark problems
Expected hypervolume improvement
M. P. Backhouse et al. (2025) (submitted)

## Slide 14: Example – FEL injector from EPAC
Toy problem: explore possible gas targets for an LWFA based FEL injector
FEL parameter:
Total Power
Lasing wavelength
Optimisation metric 1: Peak energy (E)
Optimisation metric 2: Brightness (B)
25 September 2025
ne,1
N2%
L2
ne,2
ne,3
L1
L3
 | Online | Offline
Resolution (z) | 1/20 | 1/10
PPC | 32 | 16
Radius | 120um | 100um
Speedup |  | >5x

## Slide 15: Results – FEL ready beams located after only 10 iterations
Ionisation injection optimised by a density up ramp to rephase the electron beam
Brightnesses of > 1016 A m-2 generated after fewer than 10 optimisation epochs.
M. P. Backhouse et al. (2025) (submitted)

## Slide 16: Summary
Demonstrated Bayesian optimisation in a “classic” LWFA setup
  Starting from a broadband spectrum
  Maximised spectral density with only laser parameters
Identified the key role pulse shape plays in maximising performance
  Positive skew required for maximising beam charge
Introduced Multi-Task, Multi-Objective Bayesian Optimisation
  Well-suited to large complex parameter spaces with multiple competing objectives.
Used to explore the energy-brightness frontier for FEL applications
  - Configurations that could generate brightnesses > 1016 A m-2 were found.

## Slide 17: Thanks for listening!
Acknowledgements
L. T. Dickson, I. Moulanier, F. Massimo,
C. C. Cobo, F. Filippi, C. Gustafsson,
E. Lofquist, K. Svendsen, M. J. V. Streeter,
R. J. Shalloo, O. Vasilovici, C. Ballage,
S. J. D. Dann, C. D. Murphy, Z. Najmudin,
S. Dobosz Dufrénoy, O. Lundh, B. Cros

## Slide 18: Modelling spatial and spectral phase

## Slide 19: Input and output
Focus
Chirp
TOD
FOD
Negative
Positive
0
Propagation

## Slide 20: Demonstrating the sensitivity to temporal shape
  Highly sensitive to pulse shape independently of intensity
  Relies on carefully matching the longitudinal laser profile to the wake at injection
Parameter scans around the optimum
Injection mechanism