## Slide 1
Laser Wakefield Acceleration Experimental Area at the CLF Extreme Photonics
Applications Centre
Daniel Symes
Central Laser Facility
Rutherford Appleton Laboratory
7th European Advanced Accelerator Conference, September 2025
Notes: The abstract pattern can be removed or repositioned if required. Be careful to ‘Send to Back’ so that it does not obscure any important information.

## Slide 2
EPAC is a major facility development at the STFC Rutherford Appleton Laboratory
10 Hz PW laser based on DiPOLE DPSSL technology
High Power Laser User Facility
Development of plasma accelerators for applications
Notes: Delete boxes as required

## Slide 3
EPAC 10 Hz PW laser
~ 1J OPCPA front end
DiPOLE DPSSL pump
Ti:Sa amplifier
Gold and MLD gratings
30 J, ≤ 30 fs @ 10 Hz
Development of high peak and high pulse rate drivers for accelerators: opportunities and challenges
Mariastefania De Vido, Thursday am plenary
Notes: Delete boxes as required

## Slide 4
Ground Floor – experimental areas
Experimental Area 1
40 m x 10 m
Long-focus configuration
Primarily gas targets
Experimental Area 2
18 m x 10 m
Short-focus (f/3) configuration
Primarily solid density targets
Experimental Area 3
9 m x 7 m
Future development
Notes: Delete boxes as required

## Slide 5
EPAC Experimental Area 1
Off-axis parabola: focal length 10 m (f / 45)
Intensity mid-1018 W cm-2 (a0 ~ 1 – 2)
1 Hz and 10 Hz operating modes
10 Hz energy limited by gold gratings
Turning chamber
Beam focusing
Interaction chamber
Notes: Delete boxes as required

## Slide 6
Focusing chamber
Installed on movable granite block
(up to 14.5 m focal length)
Day-one 10 m focal length parabola
Adaptive optic from ISP-system
Notes: Replace this guidance text with your own bullet pointed content.
For further guidance please see https://www.bdadyslexia.org.uk/advice/employers/creating-a-dyslexia-friendly-workplace/dyslexia-friendly-style-guide

## Slide 7
Interaction chamber
LWFA target (up to metre-scale)
Plasma optical diagnostics
Transition radiation diagnostics
Quadrupole magnets
Option for close-in spectrometer
Notes: Replace this guidance text with your own bullet pointed content.
For further guidance please see https://www.bdadyslexia.org.uk/advice/employers/creating-a-dyslexia-friendly-workplace/dyslexia-friendly-style-guide

## Slide 8
Exit mode chamber
Optics to attenuate and collimate
Diagnostics for beam profile, wavefront, pulse shape, spectrum
Notes: Replace this guidance text with your own bullet pointed content.
For further guidance please see https://www.bdadyslexia.org.uk/advice/employers/creating-a-dyslexia-friendly-workplace/dyslexia-friendly-style-guide

## Slide 9
We are producing gas jet targets for EA1
Slot nozzles up to 100 mm in length
Designed and manufactured in-house
Aiming to develop metre-scale targets based on Maryland designs
Will need J-level auxiliary beam for HOFI channels
Metre-scale gas jet
Rockafellow Phys. Plasmas 32, 053102 (2025)
Notes: Delete boxes as required

## Slide 10
Plasma mirror for laser removal
Tape drives
Robust and high positional stability
EMP and debris protection
Liquid targets
Colliding streams (SLAC design)
Also considering Ohio liquid crystals
Notes: Delete boxes as required

## Slide 11
Permanent quadrupoles for capture array
Electro-magnet quadrupoles for focusing
Electro-magnet dipoles for measurement
Electron beamline
B. D. Muratori et al., A Modular Quadrupole Array Capture Line for Plasma-Accelerated Electrons, submitted to PRAB
Notes: Delete boxes as required

## Slide 12
Electron beamline
B. D. Muratori et al., A Modular Quadrupole Array Capture Line for Plasma-Accelerated Electrons, submitted to PRAB
Start with flat-top gas jet ~ 1 GeV electrons
4 x PMQs (~400 Tm-1), 3 x EMQs (~40 Tm-1)
Focus on spectrometer screen
Single-shot emittance with bow-tie method
Notes: Delete boxes as required

## Slide 13
LWFA commissioning from Summer 2026
Stable electron and x-ray performance:
Test stabilisation feedback routines
Machine-learning for stability & LWFA optimisation
Electron beam characterisation and control:
Diagnostic installation & testing
E-beam focusing & steering
Proof-of-principle imaging:
10s keV phase contrast with betatron
> MeV high resolution radiography
Aim to open for user access in 2027
Notes: Delete boxes as required

## Slide 14
We are using Gemini TA2 as a
5 Hz, 50 MeV LWFA test beamline
~500 mJ, 40 fs
Building on previous Bayesian optimisation work [Shalloo et al Nature Comm. 2020]
Adapting code for robust multi-objective optimisation for EPAC
Looking at the SLAC Xopt platform
Notes: Replace this guidance text with your own bullet pointed content.
For further guidance please see https://www.bdadyslexia.org.uk/advice/employers/creating-a-dyslexia-friendly-workplace/dyslexia-friendly-style-guide

## Slide 15
Optimizing image quality for XCT applications
FOV ~ 3 mm, 25 mm
Resolution 6 μm, 50μm
Increased beamline length & detector development to achieve high resolution with betatron (10 – 100 keV)
Control over Brems and ICS properties to improve contrast and resolution (1 – 10 MeV)
Notes: Replace this guidance text with your own bullet pointed content.
For further guidance please see https://www.bdadyslexia.org.uk/advice/employers/creating-a-dyslexia-friendly-workplace/dyslexia-friendly-style-guide

## Slide 16
User access to EPAC
We will run a certain number of operational weeks in a year
Access time is split between:
  Academic access (peer-reviewed through independent panel)
  Source development
  Industrial access (collaborative or proprietary)
Expecting 3 weeks for academic experiments
  Week 1: set up (no laser)
  Week 2: shot preparations (alignment modes)
  Week 3: data taking (~ 100k shots per day)
Notes: Replace this guidance text with your own bullet pointed content.
For further guidance please see https://www.bdadyslexia.org.uk/advice/employers/creating-a-dyslexia-friendly-workplace/dyslexia-friendly-style-guide

## Slide 17
EA1 future development
Four auxiliary beams
Probes
HOFI / injection / collision
High energy, long pulse
Beam combinations
SF-QED
Compton scattering
Staged LWFA
Pump-probe / bimodal imaging
Application beamlines
X-ray tomography
Femtosecond XAS
FEL experiments
Electron beam irradiation
Second high-power beamline
Duplicate 10 Hz, PW
Multi-PW
100 Hz, 100 TW
Notes: Delete boxes as required

## Slide 18
www.clf.stfc.ac.uk
CLFINDUSTRY@stfc.ac.uk
Notes: Replace this guidance text with your own bullet pointed content.
For further guidance please see https://www.bdadyslexia.org.uk/advice/employers/creating-a-dyslexia-friendly-workplace/dyslexia-friendly-style-guide