## Slide 1
Smart*Light
Commissioning of the compact, tunable ICS based x-ray source
European Advanced Accelerator Conference 2025
September 25, 2025
Coen Sweers, Ids van Elk, Peter Mutsaers and Jom Luiten

## Slide 2
Inverse Compton scattering
1
Structure
Smart*Light beamline
2
2
x-ray results
3

## Slide 3
x-ray results
3
Inverse Compton scattering
1
Structure
Smart*Light beamline
2
2

## Slide 4
Inverse Compton Scattering
animation: Brian Schaap
Inverse Compton Scattering

## Slide 5
Inverse Compton Scattering
Micron source size
Highly directional emission
λ0 = 800 nm
Ekin= 20 MeV
λX = 0.1 nm
radiation wavelength
Figure: Daniel Nijhof

## Slide 6
x-ray results
3
Inverse Compton scattering
1
Structure
Smart*Light beamline
2
2

## Slide 7
Figure: Daniel Nijhof
Electron injector
X-band LINAC
interaction chamber
300 cm
Smart*Light beamline

## Slide 8
Courtesy of Daniel Nijhof
Electron injector
100 keV DC photogun
bunch charge 10 pC
emittance 400 nmrad
pulse length 1 ps
repetition rate 1 kHz
fs UV pulse
ps electron bunch
For ICS e-beam brightness is crucial!

## Slide 9
X-band accelerator
Photo by Bart van Overbeeke
Adapted design based on CLIC TD26 structure
Figure by Xavier Stragier
First 3 cells adapted for 100 keV injection
26 cells 50 cells
Design performance
30 MeV at 20 MW RF power
1 kHz repetition rate
More info: Stragier, X.F.D., et al. A traveling wave X-band accelerating structure with low-beta front end for a compact inverse Compton scattering x-ray source. Eur. Phys. J. Spec. Top. (2025).

## Slide 10
Interaction Chamber

## Slide 11
Interaction Chamber
x-rays!
est. September 2024

## Slide 12
Inverse Compton scattering
1
Structure
Smart*Light beamline
2
2
x-ray results
3

## Slide 13: Photon distribution
x-ray results
70% of prediction! Very stable and repeatable!
Counts per shot: 1200
Counts per shot: 1700
short pulses
polarization switch
More info: van Elk, I. J. M., et al. "First x-rays from a compact and tunable LINAC-based Compton scattering source." arXiv preprint arXiv:2504.11897 (2025). accepted for publication
partial coherence

## Slide 14: Continuous energy tunability
4% x-ray energy spread (FWHM)
1% electron energy spread (FWHM)
x-ray results
Special thanks to
Matthieu Boone and Pieter Tack! (UGent)
x-ray results
More info: van Elk, I. J. M., et al. "First x-rays from a compact and tunable LINAC-based Compton scattering source." arXiv preprint arXiv:2504.11897 (2025). accepted for publication

## Slide 15
Background suppression
Causes
Reduced detector efficiency at high energy
Bremsstrahlung from e-beam
Dark current from accelerator
Background suppression
Solutions
Spatial filtering with optics
Fresnel zone plate
Temporal filtering with ultrafast detectors
Timepix3

## Slide 16
Background suppression
Unfiltered
SNR 20:1
Unfiltered
SNR 0.9:1
keV
Filltered
SNR 80:1
17.5 keV
Filtered
SNR 5:1
Background suppression

## Slide 17
 | Current status | improvements | Future developments
x-ray flux in 1%BW (ph/s/1%BW) | 1×104 | 2 ×106 | 109
brilliance (ph/s/mm2 /mrad2 /0.1%BW) | 2×105 | 3×108 | 1013
energy range (keV) | 5 – 17 | 5 – 20 | 0.1 – 20
x-ray status and improvements
Coming Year
Following Years
Coming Year:
Increase repetition rate
Smaller interaction spot
Flux
Brilliance
Future developments:
Burst mode

## Slide 18
Phase contrast imaging
Image: Zhou, Shu-Ang, and Anders Brahme, Physica Medica 24.3 (2008): 129-148.
Refractive index:
Phase shift
absorption
Soft tissue with 10+ keV x-rays:
Nylon wire 500 μm
10 keV x-rays
First testing
19-09-2025
150 cm from detector
10 cm from detector

## Slide 19
Phase contrast imaging
10 cm from detector
3 cm
Air
leaf
150 cm from detector
1.5 cm
First testing
19-09-2025

## Slide 20
K-edge subtractive imaging
Ni
Cu
Zn
Zn
Cu
Ni
Cu
Zn
Ni
Images taken with TimePix3 detector

## Slide 21
Concluding remarks
Compact tunable x-ray source based on a X-band LINAC
Conclusion
Future
Demonstration experiments for medical applications
(and many other)
Competitive with state-of-art
x-ray tubes
with continuous energy tunability
Works as advertised

## Slide 22
Thank you for your attention!
Poster session

## Slide 23
Background suppression
Solutions
Spatial filtering with x-ray optics
ICS x-rays
Bremsstrahlung
pinhole
Fresnel zone plate
Background suppression
Under construction
winter 2025
Images: appliednt.com/zone-plates/#hard-x-ray

## Slide 24
Background suppression
Background suppression
Temporal filtering with ultrafast detectors
RF pulse length 200 ns
x-rays pulse length 1 ps
Time resolution TimePix3 1.5 ns
Laser off
Laser on
Conventional camera
TimePix camera
Figure: ASI scientific instruments
Solutions
ICS x-rays
Bremsstrahlung
ICS x-rays

## Slide 25
Soft x-rays
20 MeV electrons
Soft x-rays
Grazing collision
5 MeV electrons
Soft x-rays
Head on collision
20 MeV electrons
Hard x-rays
x-ray Brightness for different x-ray energies
Head on ICS
Grazing ICS
Change the interaction angle without loss of spatio-temporal overlap
Continuous energy tunability over several orders of magnitude
Patent Pending

## Slide 26
x-ray results
partial coherence

## Slide 27: Polarization
Change laser polarization
Change x-ray polarization
Change x-ray distribution
x-ray results

## Slide 28
x-ray results

## Slide 29
Future developments
Burst mode
Repetition rate limited by Klystron and laser (500-1000 Hz)
Solutions: new source that accelerates 300 e-bunches per Klystron pulse + couple laser pulse into cavity