## Slide 1
Plasma density manipulation in gas-filled discharge capillaries designed for the EuPRAXIA@SPARC_LAB project
Angelo Biagioni | LNF-INFN
on behalf of the SPARC_LAB collaboration
7th European advanced Accelerator Conference
Isola d’Elba 2025, Italy
21-27 September

## Slide 2
Angelo Biagioni | LNF-INFN | EAAC 2025 | Page 2
Outline
Gas-filled discharge plasma sources at SPARC_LAB test facility
Plasma density manipulation by means of segmented discharge capillaries
Combined discharge capillaries
Driver-witness separator by means of plasma devices
Very long plasma sources designed for the EuPRAXIA@SPARC_LAB project

## Slide 3
Gas-filled discharge capillary
Region of uniform neutral gas contained by differential pumping at two input/output extremities and realized by a thin capillary
Modulation of longitudinal gas distribution by special geometric shapes
Small gas flow to operate in steady state regime with continuous flow (P < 1 bar)
There is no movable parts
Small dimension of the HV source to produce plasma
Plume of gas from front and back of cell, plasma ramps to be controlled
Density easily adjusted by controlling gas flow, geometry or voltage in the range: 1015 - 1019 cm-3
Erosion of the plasma channel due to the electrical discharges to form plasma
Gas inlets
Electrode
HV pulse
Plasma channel
Density profile
(x1017)
Spatial profile
Time profile
Acceleration
Angelo Biagioni | LNF-INFN | EAAC 2025 | Page 3

## Slide 4
Cigar-shape
inlet
Cigar-shape capillary
Angelo Biagioni | LNF-INFN | EAAC 2025 | Page 4
Plasma ramps manipulation

## Slide 5
Angelo Biagioni | LNF-INFN | EAAC 2025 | Page 5
Plasma ramps manipulation
After 2 μs the profile stabilizes at a squared cosine like plasma profile, with an approximation of the line made of 20 segments.
For this kind of ramp a solution that satisfy the matching condition at the plateau
Courtesy of S. Romeo

## Slide 6
Angelo Biagioni | LNF-INFN | EAAC 2025 | Page 6
Segmented discharge capillary
Plasma sources in the m-scale with HV pulses less than 10 kV
Longitudinal density modulation depending on both discharge voltage and recombination time
Uniform profiles for very long plasma sources
Modulated profiles for integrated components
HV
HV
Common ground
+
+

## Slide 7
Logitudinal plasma density modulation
Angelo Biagioni | LNF-INFN | EAAC 2025 | Page 7
Also, in the case of uniform profiles, the main advantage is offered by the possibility of sectioning the supply voltage, avoiding values of many tens or hundreds of kV, which would not be easy to produce.
The same plasma source could provide either uniform profiles to be used to achieve high energies in m-scale devices or tailored profiles to realize different elements within the same structure or optimize particle beam matching.

## Slide 8
Staged discharge capillary
Angelo Biagioni | LNF-INFN | EAAC 2025 | Page 8
APLs
Accelerator
The main advantages of a plasma device that integrates
multiple functional elements within the same
structure lie in :
its compactness (19 cm)
the simplification of the neutral gas distribution and injection system
the intrinsic mechanical alignment ensured by the joint fabrication of all components.
- 500-200-500 A ionization current
- 2x1015 cm-3 accelerator
- 150 MV/m acc. gradient

## Slide 9
Angelo Biagioni | LNF-INFN | EAAC 2025 | Page 9
Active Plasma Lens Remove System
The focusing is provided by two active-plasma lenses (APLs)
Collimator remove the driver bunch overfocused to a spot size much larger than the collimator aperture.
Two goals:
transport the witness bunch by preserving its charge, normalized emittance, and peak current;
remove the high-charge driver bunch during the transport to completely discard it before the FEL undulator beamline.
500pC
490pC
70pC
70pC
stdx (um)
nemitt (um)
Courtesy of Martina Carillo
Driver
witness

## Slide 10
60 cm long discharge capillary for EuPRAXIA@SPARC_LAB
Angelo Biagioni | LNF-INFN | EAAC 2025 | Page 10
The geometry allows the longitudinal plasma distribution to be controlled
In particular, internal ramps are an important tool for optimising the match between the input beam and plasma density.
10 injectors of constant diameter and progressively closer together
10 injectors progressively closer together and having progressively increasing diameters
20%
60cm

## Slide 11
Plasma density manipulation for 40 cm long capillary
6x1mm inlets to feed te plasma channel
10 cm long internal ramps to match the beam
20 cm long uniform electron distribution
55% density decreasing in 10 cm long rmps
40cm
55%
20 cm
10 cm
inlet
80
40
60
60
Angelo Biagioni | LNF-INFN | EAAC 2025 | Page 11

## Slide 12
Plasma density manipulation for 40 cm long capillary
Angelo Biagioni | LNF-INFN | EAAC 2025 | Page 12
10 cm
32%
New inlets
80
25
25
15
35
35
25
12x1mm inlets to feed te plasma channel injectors of constant diameter and progressively closer together
32% density decreasing in 10 cm long internal ramps (with respect to 55% of the previous geometry)
20 cm long uniform electron distribution
32% density decreasing in 10 cm long rmps
Internal ramps can be controlled to make the matching with the beam
Half-capillary

## Slide 13
60 cm long discharge capillary for EuPRAXIA@SPARC_LAB
Angelo Biagioni | LNF-INFN | EAAC 2025 | Page 13
60 cm long Plasma accelerating module (1 GV/m)
100 cm long X-band structure (60 MV/m )
  Fabrication by machining
  10 increasing diameter
  Density range 1016 -1017 cm-3
  13 kV with 500 A
  100 Hz rep Rate (Ceramics)

## Slide 14
Conclusions
Density easily adjusted by controlling gas flow, geometry or voltage in the range: 1015 - 1019 cm-3
Longitudinal profiles, in particular plasma ramps, can be tailored to match the electron beams in order to optimize the interaction
Compact devices based on plasma formation through electrical discharges can be designed to integrate different components.
Active plasma lens removal system for Driver–Witness beam separation in Particle-Driven Plasma Acceleration
Very long plasma sources based on electrical discharge can be realized on the m-scale by appropriately designing the longitudinal profiles required to optimize the interaction with electron beams.
Angelo Biagioni | LNF-INFN | EAAC 2025 | Page 14

## Slide 15
Angelo Biagioni | INFN_LNF
Angelo.Biagioni@lnf.infn.it
Thank you for your attention
Angelo.Biagioni@lnf.infn.it | EAAC 2025