## Slide 1: Experimental Progress of Passive Plasma Lens at FACET-II
EAAC 2025
Sep. 25, 2025
Elba, Italy
Authors: Michael Litos (speaker, CU Boulder), Shutang Meng(CU Boulder) On behalf of E-308 collaboration
Notes: Done

## Slide 2: Co-Authors
Alexander Knetsch (SLAC National Accelerator Laboratory) Brendan O'Shea (SLAC National Accelerator Laboratory) Chandrashekhar Joshi (UCLA) Chaojie Zhang (UCLA) Christopher Doss (Lawrence Berkeley National Laboratory) Claire Hansel (University of Colorado Boulder) Claudio Emma (SLAC National Accelerator Laboratory) Doug Storey (SLAC National Accelerator Laboratory) Elena Ros (University of Colorado Boulder) Erik Adli (University of Oslo, Norway) Jiawei Cao (UiO) Ken Marsh (UCLA) Mark Hogan (SLAC National Accelerator Laboratory) Nathan Majernik (SLAC National Accelerator Laboratory) Robert Ariniello (SLAC National Accelerator Laboratory) Prof. Sebastien Corde (Laboratoire d'Optique Appliquée) Spencer Gessner (SLAC) Thamine Dalichaouch (University of California Los Angeles) Valentina Lee (University of Colorado, Boulder)
(Apologies if incomplete!)

## Slide 3: Research Funding and Facility Credit
U.S. Department of Energy, Office of Science, Office of High Energy Physics, under Award Number DE-SC001796.
This research used resources of the Facility for Advanced Accelerator Experimental Tests II (FACET-II), which is a DOE Office of Science User Facility.

## Slide 4: Thin, Underdense, Passive Plasma Lens (TUPPL)
Thin – PWFA much shorter than one betatron period
Underdense – Nonlinear blowout regime
Passive – No reliance on externally driven current
Plasma Lens – Transverse focusing impulse with negligible energy change

## Slide 5: Thin, Underdense, Passive Plasma Lens (TUPPL)
Thin – PWFA much shorter than one betatron period
Underdense – Nonlinear blowout regime
Passive – No reliance on externally driven current
Plasma Lens – Transverse focusing impulse with negligible energy change

## Slide 6: Attractive Features of TUPPL
Extremely strong focusing
  Orders of magnitude beyond electromagnets, PMQs, APL
Axisymmetric focusing
  Single lens can achieve symmetric focus in x & y
Ultra-compact
  Plasma lens itself: ~400 µm
  Gas jet & laser hardware: <1 cm footprint along beam line
Rapidly and easily tunable
  Strength scales with density  gas pressure
  Strength scales with length  laser energy / focus/ height above gas jet
  Density length product  plasma expansion
Self-aligning
  Central axis of blowout determined by electron beam

## Slide 7: Comparison to other focusing optics
PPL focusing strength is orders of magnitude stronger than magnets of equivalent phase advance (normalized length).
Phase advance (normalized length):
Quadruple Magnet
Adapted from Taylor, SLAC-PUB-5621 (1991)
Type | g [kT/m] | K [m-2] | L [mm] | f [cm]
Quadrupole Electro-magnet | 0.01 | 0.3 | 84 | 3990
Permanent Magnetic Quadrupole | 0.5 | 15 | 12 | 564
Active Plasma Lens | 3.6 | 108 | 4.4 | 210
Thin PPL (blowout theory, ) | 1468 | 44000 | 0.22 | 10.4
Thin PPL (June 2025 exp., preliminary) | 437 | 13100 | 0.4 | 19
Type | g [kT/m] | K [m-2] | L [mm] | f [cm]
Quadrupole Electro-magnet | 0.01 | 0.3 | 84 | 3990
Permanent Magnetic Quadrupole | 0.5 | 15 | 12 | 564
Active Plasma Lens | 3.6 | 108 | 4.4 | 210
 | 1468 | 44000 | 0.22 | 10.4
Thin PPL (June 2025 exp., preliminary) | 437 | 13100 | 0.4 | 19

## Slide 8: Ε-308 Experimental Setup
Laser, 3 mJ
E-beam
Chaojie Zhang et al 2021 Plasma Phys. Control. Fusion 63 095011
Top view
E-beam
5mm ; ~50 psi
Laser
Laser-ionized H2 gas jet
Plasma

## Slide 9: Plasma Requirements
Maximize focusing strength: minimize focal length  maximize npL
Remain in thin lens regime: keep phase advance ≲ 0.2  keep sqrt(np)L low
Remain in underdense blowout regime: 2 np ≲ nb  keep np sufficiently low
Summary: Requirements push toward lower density and longer length.
Experimental conditions made it challenging to optimize np and L.
Result: operated in overdense thin lens regime during previous run.
Improved modeling, diagnosis, and control of plasma source expected next run.

## Slide 10: Plasma Source Modelling
Fluent simulation
Radial neutral density profile
assume 1e17
Max L: 132 um
Need to rely on plasma expansion to reach target plasma length ~ 500 um.
Split-step Fourier ionization code
Laser
E-beam
Laser energy was limited to 3 mJ to avoid damaging final mirror  limited initial plasma lens length
Fluid models used to estimate gas density above jet nozzle, but large uncertainty on backing pressure in experimental device (no local gauge)
Challenging to reach low densities with minimum operating backing pressure
Solution: ionize small volume at high density and allow plasma to expand

## Slide 11: Plasma Length Estimation
Laser / e-beam arrival delay scan performed to find good working point
  Set electron imaging spectrometer to parallel-to-point
  Scanned delay and looked for strong divergence increase of witness beam
Two different Working Points (WP) studied:
Both produced very similar results
Laser position scan performed to estimate plasma lens length
  Assumed azimuthally symmetric plasma profile w.r.t. laser axis, perp. to e-beam
  Translated laser above/below e-beam axis until interaction ended
  Measured movement of laser to find the plasma length L ≈ 400 µm for both WP’s
No Interaction
Interaction
 | Working Point 1 | Working Point 2
Nozzle Height | -1.5 cm | -1.0 cm
Delay Time | 3 ns | 20 ns
Drive
Wit.
x’
x’
E

## Slide 12: Electron Beam Configuration: Two Bunches
PIC Simulation
(HiPACE++)
TCAV measurement
time
Drive
Witness
Two-bunch configuration generated using notch collimator with chirped beam
Long, roughly linearly chirped witness beam
Can sample long region inside wake
Chirp permits longitudinally resolved measurement of focusing with imaging spectrometer
Drive Bunch: ~780 pC
Witness Bunch: ~650 pC
Δz gap: ~40 µm

## Slide 13: FACET-II Electron Imaging Spectrometer
Plasma Lens
OTR Screen
Beam Direction
Point-to-Point scans of object plane and Parallel-to-Point scans of M12 were performed to analyze beam dynamics.
Chromaticity of imaging spectrometer must be taken into account during analysis.
Dispersed beam after Imaging Spectrometer
x
E
Chromaticity for object plane scans from zlens to zlens + 50 cm

## Slide 14: Strong Focusing of Witness Beam
No chromatic correction
um
21 cm
um
14 cm
PIC simulation results
First wake
Object plane scan preliminary results (still need chromatic correction)
Observed strong focusing of 200-300 pC witness bunch
Reduced min. spot size to σ* ≈ 11-14 µm from initial value of 20 µm
Reduced min. beta function to β* ≈ 14-21 cm from initial value of 75 cm
Moved waist upstream by 20-30 cm
Rear of witness beam was beyond first wake period and defocused
Defocused
WP1 Data
Focusing along bunch
front
rear
E5: front
E1: rear

## Slide 15: Witness Bunch Emittance Analysis
Data Analysis:
Analyzed emittance of 20 energy slices of ~10 MeV
Used object plane and M12 scan data
Fit to equation:
Preliminary Observations
Significant emittance growth in plasma lens
  Roughly factor of 2
  Not in underdense regime
  kp σr ≳ 1
Beta function reduced due to emittance growth in addition to focusing
WP1 Witness Bunch Emittance
front
rear

## Slide 16: Drive Bunch Emittance Analysis
WP1 Drive Bunch Emittance
Preliminary Observations
No appreciable growth for most of the bunch
Small emittance growth at very tail of bunch
Strong wake must start to develop near tail of drive bunch
Agrees well with simulations
front
rear

## Slide 17: Summary
Observed strong focusing of witness bunch in a thin, passive plasma lens
  200-300 pC, σ*: 20 µm  11-14 µm, β*: 75 cm  14-21 cm, Δz*: 2-30 cm
  Preliminary results – chromatic correction required
Did not reach the underdense blowout regime
  Emittance growth by factor of ~2 due to nonlinear focusing fields
  Tail of bunch extended beyond first wake period
Expect optimized performance in underdense regime next run
  Better plasma source modeling, diagnostics, and control
  Will lower plasma density and increase length
Will eventually use in combination with other experiments at FACET-II
  Strong focusing for matching into a PWFA
  Focusing boost prior to multi-foil transition radiation focusing device
  Asymmetric driver and blowout (w/ Pratik Manwani, UCLA)
  Transverse gradient TUPPL
  Divergence control of plasma-injected beams

## Slide 18: Publications
S. Meng, et al., [strong focusing with a passive plasma lens, in preparation]
C. E. Doss, et al., “Laser-ionized, beam-driven, underdense, passive thin plasma lens”, Phys. Rev. Accel. Beams 22, 111001 (2019) https://doi.org/10.1103/PhysRevAccelBeams.22.111001
C. E. Doss, et al., “Underdense plasma lens with a transverse density gradient”, Phys. Rev. Accel. Beams 26, 031302 (2023) https://doi.org/10.1103/PhysRevAccelBeams.26.031302

## Slide 19: Publications

## Slide 20: Evidence of passive plasma lensing
5 energy slices
Object plane scan with no chromaticity correction
E1  E5 with increasing energy
Very clear upstream shift of and reduction in !
E1
E2
E3
E4
E5
E1
E2
E3
E4
E5

## Slide 21: Preliminary PIC simulation studies
Simulation parameters:
  Gaussian transverse profile with 20 um spot size and 75 cm beta that match x-plane measurement.
  Current profile from BMAD simulation generated by Claudio, similar to TCAV measurement.
  Plasma density ~ ; plasma length ~ 400 um.
Witness beam samples three regions: first wake, defocusing region, front of the second wake.
Good agreement!
150 um
Simulation value scaled by 6%

## Slide 22: Plasma Expansion Simulation
Beam direction
Initial boundary
Initial density:
Agrees well with the 400 measurement!
Some magnification
No magnification

## Slide 23: Density Length Product Evolution
Lorentzian fit
scaled
Not scaled