## Slide 1
Making a brighter future through advanced accelerators
Transition of CLARA Facility at Daresbury Laboratory to User Facility
Deepa Angal-Kalinin
ASTeC, STFC Daresbury Laboratory
and The Cockcroft Institute
, Elba, 24th September 2025
On behalf of the CLARA Team

## Slide 2
Making a brighter future through advanced accelerators
Outline
CLARA upgrade to 250 MeV
FEBE beamline and hutch
Current Status
Potential for Novel Acceleration R&D
Summary
D. Angal-Kalinin | EAAC25, Elba | 24/09/2025

## Slide 3: CLARA
Accelerator Hall
~90 m x 3.5m x 3m
D. Angal-Kalinin | EAAC25, Elba | 24/09/2025
250 MeV normal conducting S-Band electron beam facility.
Two successful novel acceleration experiments with ‘CLARA Front End’ at 35 MeV (2018-2022).
3
CLARA Gun
S-band Linac
Arc to FEBE hutch
FEBE hutch
Characterise in 6D
Accelerate + Manipulate + Accelerate
Generate
Experiment

## Slide 4
Up to 250 MeV
250 MeV – 2 GeV
250 – 600 MeV
ICT
CTR
ICT
FEL ready high brightness beam
120 TW laser + electron beam in FEC1
Highly instrumented beamline to support setup & characterisation of novel accelerated beam
Full Energy Beam Exploitation (FEBE) Beamline
4
D. Angal-Kalinin | EAAC25, Elba | 24/09/2025

## Slide 5
Configuration
Accelerator length ~ 85 m to final beam dump
Shielded FEBE
Experimental Hutch
Access to CLARA electron beam within a shielded hutch for users.
The hutch can be accessed whilst the accelerator is operating (and FEBE beamline magnets off), enabling users to set up their experiments and access the hutch during experiment without switching off the accelerator.
  Beam stability and fast turn around.
D. Angal-Kalinin | EAAC25, Elba | 24/09/2025

## Slide 6
FEBE Hutch Overview
Hutch footprint: 10 × 5.4 × 3 m3, Shielding: Total beam power 6 W Flexibility with bunch charge (maximum 250 pC), bunch repetition rate (maximum 100 Hz), beam energy (50 MeV – 250 MeV)
CLARA
250 MeV e-
D. Angal-Kalinin | EAAC25, Elba | 24/09/2025
Two identical chambers: more flexible, provides diagnostic support, and a route towards ambitious interaction/transport/application

## Slide 7
FEBE Hutch Beamline
CLARA
250 MeV e-
Laser from roof
FEC1
FEC2
FMBOX1
FMBOX2
D. Angal-Kalinin | EAAC25, Elba | 24/09/2025

## Slide 8: Electron Beam Parameters
To be delivered at Interaction Point in FEC1 and/or FEC2 chambers.
D. Angal-Kalinin | EAAC25, Elba | 24/09/2025
Parameter | High charge | Low charge
Energy [MeV] | 250 | 250
Charge [pC] | 250 | 5
RMS t [fs] | 100 | 50
σE/E [%] | <5 | <1
RMS x [µm] | 100 | 20
RMS y [µm] | 100 | 20
εN x [µm] | 5 | 2
εN y [µm] | 5 | 2
Snedden, E. W., et al. PRAB 27.4 (2024): 041602. https://doi.org/10.1103/PhysRevAccelBeams.27.041602
Parameter | High charge | Low charge
Energy [MeV] | 250 | 250
Charge [pC] | 250 | 5 → <5
RMS t [fs] | 100 → 50 | 50 → <50
σE/E [%] | <5 → 1 | <1
RMS x [µm] | 100 → 50 | 20 → ~1
RMS y [µm] | 100 → 50 | 20 → ~1
εN x [µm] | 5 → <5 | 2 → 1
εN y [µm] | 5 → <1 | 2 → <1
  R&D: Meeting these parameters will require upgraded and/or new diagnostics
Future potential
Day 1

## Slide 9: Electron Beam Pulse Shaping
9
D. Angal-Kalinin | EAAC25, Elba | 24/09/2025
Photoinjector Laser longitudinal shaping
  Machine Learning driven
  Large number of possibilities
Tungsten mask in FEBE Arc
  Configurable and changeable
  Drive-witness, pulse trains…all possible

## Slide 10: FEBE Laser System
10
D. Angal-Kalinin | EAAC25, Elba | 24/09/2025
A commercial 5 Hz, 120 TW laser system (Arco, Amplitude) based on top of the hutch.
Laser room
FEBE hutch
Laser control room
Parameter | F = 3.5 m OAP
Wavelength [nm] | 800
Energy [J] | 2.6
τFWHM [fs] | 23
ω0 [µm] | 30
Ipk [Wcm-2] | 8.0×1018
a0 | 1.93
Estimated laser properties at IP using standard OAP with co-linear geometry.

## Slide 11: FEBE Laser System
11
D. Angal-Kalinin | EAAC25, Elba | 24/09/2025
e- @ 250 MeV
Input from laser room periscope (compressor above)
Deformable mirror
Wavefront
Sensor
OAP
Probe line
IP1
FMBOX1
FEC1
FMBOX2
Dump
CLARA
250 MeV e-

## Slide 12
CLARA: Current Status
D. Angal-Kalinin | EAAC25, Elba | 24/09/2025

## Slide 13
250 MeV at 100 Hz, 50 pC, Copper Photocathode
13
D. Angal-Kalinin | EAAC25, Elba | 24/09/2025

## Slide 14
Photocathode change from Cu to Cs2Te (Sep 25)
14
Copper photocathode was recently replaced with Cs2Te photocathode.
Laser transport was designed and modified to address expected QE increase.
Increase in QE from Cu Photocathode ~ 10-5 to ~ 12 x 10-2
  Lot of headroom to deliver 250 pC over operational period & for laser pulse shaping
Dark current lower than Copper photocathode and expect to reduce over time.
D. Angal-Kalinin | EAAC25, Elba | 24/09/2025

## Slide 15: Current Status
Technical systems commissioning with beam in the accelerator hall ongoing.
Targeting first electron beam threading through FEBE hutch – early October 25
Day 1 parameters – January 2026
First friendly user experiments without laser– February/March 2026
FEBE 120 TW Laser has been installed. Targeting SAT Completion Q3 25
Laser transport in the hutch will be commissioned Q2 26.
D. Angal-Kalinin | EAAC25, Elba | 24/09/2025

## Slide 16: Potential for Novel Acceleration R&D at CLARA
16
D. Angal-Kalinin | EAAC25, Elba | 24/09/2025
External Injection – LWFA
External Injection – LWFA
Higher energy gain & Energy stability
Interstage optics tests for PWFA staging
Several R&D challenges to demonstrate high quality beam driven plasma acceleration can be potentially addressed at CLARA.
Only ideas! Many potential possibilities!
Witness beam stability & Staging challenges

## Slide 17: Novel Acceleration R&D – EAAC25
17
D. Angal-Kalinin | EAAC25, Elba | 24/09/2025
Y. Saveliev, Monday, PS2
C. Lindstrøm, Monday, PS1
G. Xia, Monday, PS1
J. Zhang, Tuesday, PS7

## Slide 18: Potential for Novel Acceleration R&D at CLARA
18
D. Angal-Kalinin | EAAC25, Elba | 24/09/2025
S. Jamison, Tuesday, PS1

## Slide 19: Potential for VHEE RT R&D at CLARA
19
D. Angal-Kalinin | EAAC25, Elba | 24/09/2025
International Workshop on Very High Energy Electron Radiotherapy (VHEE’25) (15-17 September 2025): Overview · STFC Indico
Details of VHEE/FLASH RT R&D on CLARA in Facility Update Session

## Slide 20
Making a brighter future through advanced accelerators
Summary
CLARA has achieved design beam energy (250 MeV), bunch charge (250 pC) and rep rate (100 Hz).
Beam threading through the FEBE hutch is planned in October 2025.
CLARA will transition next year into fully operational user facility.
  First friendly user experiments likely to be in February/March 2026.
  Open user call will be issued sometime in 2026 and then on a regular basis.
There is a huge potential to exploit the full flexibility and performance of the CLARA Beam & the FEBE Hutch.
If you are interested to use CLARA for R&D, please contact thomas.pacey@stfc.ac.uk; deepa.angal-kalinin@stfc.ac.uk
20
D. Angal-Kalinin | EAAC25, Elba | 24/09/2025

## Slide 21
Thank you for listening
Any Questions?
Notes: The abstract pattern can be removed or repositioned if required. Be careful to ‘Send to Back’ so that it does not obscure any important information.