## Slide 1: Efficient high energy and high-repetition-rate proton acceleration from cryogenic hydrogen foil targets
Stefan Assenbaum1,2, M. Rehwald1, P. Ordyna1,2, J. D. Schilz1,2, M. Müller1,2, T. Streil1,2, J. Garreis1,2, T. Kluge1, R. Gebhardt1, S. Bock1, S. Göde3, M. Gauthier4, C. Schoenwaelder4, M. Ikeya4, S. Glenzer4, U. Schramm1,2 and K. Zeil1
(1) Helmholtz-Zentrum Dresden-Rossendorf e.V. (HZDR), Institut für Strahlenphysik, Bautzner Landstraße 400, 01328 Dresden, Germany
(2) Technische Universität Dresden, 01069 Dresden, Germany
(3) European XFEL GmbH, Holzkoppel 4, 22869 Schenefeld, Germany
(4) Stanford Linear Accelerator Center (SLAC), 2575 Sand Hill Road, Menlo Park, CA, 94025, USA
7th European Advanced Accelerator Conference
26.09.2025, Elba, Italy

## Slide 2
Laser-driven proton acceleration: A brief overview
2020 Roadmap on Plasma Accelerators, NJP 2021
Indirect, highly non-linear processes
Exact knowledge and control of target and laser parameters required
Predictive 3D Particle in cell (PIC) simulations
Utilize advanced acceleration mechanisms
From back-illuminated photo anode to bulk acceleration in quasi co-moving schemes at near-relativistically critical density (near-RCD)
Proton energy scaling remains challenging:
More laser power?
Can we Increase acceleration efficiency?
Target-normal sheath acceleration (TNSA)
Notes: Extreme spatial, temporal and energy scales
Zoo of mechanisms. Reality also: combinations/cascades
WICHTIG:
Advanced acc physics is subject to research of the whole community in the last 10 years. Not really our work but all efforts combined
 We have our niche: PW, fs, near-RIT regime

## Slide 3
Near-RCD ion acceleration: Laser-target matching
Dover, Ziegler et al. (2023) Light Sci. Appl. 12:71
T. Ziegler et al. (2024) Nat. Phys. 20 1211–1216
To access the near-RCD acceleration regime,
Laser and target conditions must match.
Use intrinsic pre-expansion by the rising laser pulse flank:
Optimal matching:
Matching target thickness to laser contrast for optimal proton energies
Large fluctuations even at optimal matching
Only at ideal conditions: cascade of acceleration mechanisms
For solid density targets like plastic foils:  Target pre-expansion
250nm Formvar
250nm Formvar:

## Slide 4
Open Questions and tasks:
Further improve the matching of laser and target properties
  Use different target materials
  Scan laser energy instead of target thickness
Investigate and reduce fluctuations
  Record Larger data sets
Explore new and different acceleration schemes and cascades
  PIC simulations
High-repetition-rate cryogenic solid hydrogen target platform

## Slide 5
Cryogenic jet source
Hydrogen is liquefied at ~20 K, ~5 bar
The cryogenic solid Hydrogen jet platform: laser ion acceleration and plasma benchmark experiments
Cryogenic liquid Hydrogen is ejected into vacuum through µm sized aperture at high velocity
V ~100 m/s
Evaporative cooling causes rapid freezing (~500 µm below source)
Continuous jet of solid Hydrogen
J. Kim, Rev. Sci. Instr., (2016)
L. Obst, Sci. Rep. (2017) C. Curry, JoVE (2020)
Pure hydrogen, low solid density, (simple p+ / e- plasma)
→ facilitates near-RCD ion acceleration
→ simplifies numerical modelling

## Slide 6
Cryogenic jet source
Hydrogen is liquefied at ~20 K, ~5 bar
The cryogenic solid Hydrogen jet platform: laser ion acceleration and plasma benchmark experiments
V ~100 m/s
Optical probing system
5µm
High power laser
Pure hydrogen, low solid density, (simple p+ / e- plasma)
→ facilitates RCD ion acceleration
→ simplifies numerical modelling
Debris free, self-renewing
→ High repetition rate capability
Free standing geometry
→ Facilitates probing
C. Bernert Phys. Rev. Appl. (2023)
Continuous jet of solid Hydrogen

## Slide 7
The cryogenic solid Hydrogen jet platform
Jet target als einzigartige Plattform, um verschiedenste Aspekte von Lasergetriebenen Festkörperplasmen zu studieren
Different exp. Usecases vor dem Hintergrund des „Testbed“ – also zum prinzipiellen, grundsätzlichen Verständnis der verschiedenen Aspekte von LPA
  Entweder wie Constantin – sortiert über die Intensität nicht gut, da es das Konzept des Kontrast benötigt
  Oder losgelöst davon, dann aber dennoch logisch miteinander verknüpfen
Verbindende Elemente: simple Plasmabeschreibung (Simulationen), Repetitionsrate
A universal testbed to study different aspects of laser-target interaction
Log(Intensity)
Time
Laser-induced breakdown (LIB) I ~ 1012 - 1014 W/cm2
C. Bernert et al. Phys. Rev. Appl., 10, 14070 (2023) S. Assenbaum et al. PPCF 67 015032 (2025)
Plasma expansion and simulation benchmarks I ~ 1018 W/cm2
L. Yang et al. Commun. Phys. 6, 368 (2023)
TNSA
MVA
RTF-RPA
Controlled target pre-expansion, enhanced proton acceleration I ~ 1021 W/cm2
M. Rehwald et al., Nat. Com. 14, 4009 (2023)
courtesy of L. Fletcher
Short-pulse ineractions and thermalization I ~ 1016 - 1017 W/cm2
XRTS (x-ray Thomson scattering)
 direct measure-ments of Te
S. Assenbaum, et al. in preparation

## Slide 8
Adapting the cryogenic Hydrogen target to near-RCD acceleration from foils
4µm
20 µm
Planar sheet
Width: ~ 25 µm
Thickness: ~500 nm
Shape the H2 jet while still in it‘s liquid state using a slit aperture:
 Introduces transversal flow  Forms alternating orthogonal leafs
At the right operation parameters: The freezing of H2 preserves the shape
freezing
Frozen solid
100 m/s
Foil-like, high-repetition-rate, pure solid hydrogen target at fixed thickness
25 µm
5 µm
M. Rehwald, S. Göde, S. Assenbaum et al. in preparation
Cylincrical rims
Ø 5 µm
8 mm below cryostat
Rotation: 45°
Jitter: ~3 µm
20 µm
Real-time target position monitoring at 10 Hz
M. Gauthier
S. Goede
L. Obst, Scientific Reports (2017), C. Curry, JoVE (2020)
Nicht immer on-demand
Immer noch subject to day to day fluctuations
Liquid Jet
Stability at ideal conditions
Notes: Nicht immer on-demand
Immer noch subject to day to day fluctuations

## Slide 9
Other diagnostics:
Target alignment & optical probing
Reflected/transmitted light
Online Laser diagnostics
…
Draco PW
f/2.2 OAP  2.5 µm FWHM
intrinsic contrast
1.6J – 4.5∙1020 W/cm2 2.7J – 7.8∙1020 W/cm2
Up to 1Hz repetition rate
Cryogenic H2 foil: experimental setup at Draco
Proton diagnostics
Magnet spectometer (15° and 45°) equipped with Lanex scintillator (and multichannel plate)
Time of flight (0°, 31°) Monocrystalline diamond
Target: Cryogenic hydrogen jet
Foil-like geometry with cylindrical rims
45°
15°
31°
0°

## Slide 10
Efficient proton acceleration at 1 Hz
1.6 J laser energy (50TW laser power)
1 Hz repetition rate.
In 45° direction (target normal axis):
>1000 consecutive shots without any corrections necessary
Median cutoff energy: 29 MeV
Up to 50 MeV maximum proton energy
45°
We have removed the content of this slide.
For a low resolution preview of it, pleare refer to the presentation of Ulrich Schramm on Tuesday April 23rd in the ion acceleration session. (title „Efficient laser proton acceleration in the near critical density regime”)

## Slide 11
Proton emission angle
Laser forward direction
Target normal direction
1011 shots, 1.6 J laser energy | 1 Hz repetition rate.

## Slide 12
1011 shots, 1.6 J laser energy, 1 Hz repetition rate.
>50 MeV detected in all spectrometers
Highest average cutoff energies and smallest cutoff energy spread in in 31° and 45° direction
Reduced stability in 0° and 15° direction
Proton emission angle: statistics
High particle numbers up to ~12 MeV in all directions
Flat spectral region in high energy shots
Sometimes modulated spectra (spectral gaps)
Notes: 0° mean: 18 MeV, median: 12.7 MeV
15° mean: 25 MeV, median 25 MeV
31° mean: 32.7 MeV, median 34.8 MeV
45° mean: 28.2 MeV, median 28.7 MeV

## Slide 13
Increasing laser energy
Spektren eher weg.
Stattdessen lieber:
histogramme, if reasonable
Energy scan weiter hoch zu 5J case
2.7 J laser energy (80TW laser power) | 0.2 Hz repetition rate.
Notes: 0° mean: 26.2 MeV, median: 22 MeV
15° mean: 32.4 MeV, median 30.2 MeV
31° mean: 43.5 MeV, median 46.4 MeV
45° mean: 39.4 MeV, median 41.8 MeV

## Slide 14
Increasing laser energy:
Reduced cutoff energies in all directions except 0°
Strong increase of transmitted light
2.7 J laser energy (80TW laser power) | 0.2 Hz repetition rate.
5.3 J laser energy (160TW laser power)
Increased cutoff energy in all directions
  Median >40 MeV in 45° and 31°
  >60 MeV in 0° and 15°
Increased cutoff energy spread in 45° and 31°
Spectral Modulations are more common
Notes: 0° mean: 26.2 MeV, median: 22 MeV
15° mean: 32.4 MeV, median 30.2 MeV
31° mean: 43.5 MeV, median 46.4 MeV
45° mean: 39.4 MeV, median 41.8 MeV

## Slide 15
Direct comparison with Formvar foils
Matching thin formvar foils to the given laser parameters Best shots per data set
H2 foils give higher energies and Particle numbers than for Formvar foils
Median H2 energy similar to highest Formvar energy
Foil comparison:
Start simple with 45°, one large plot.
Show best shot @1.6J
Add a random, normal TNSA spectrum from the recent campaigns – should be much more particles (??)
Show the real mean or at least a more „median“ spectrum – what to expect reliably.
Then compare to Foils. Take best shots each but remind that statistics is low here
Comparable proton numbers
Less energy than best H2, but comparable to median of H2
  Reminder: thickness sampling is rather rough
Only then: generalize to different directions
  Show 15° direction data (but with abs calib = lanex data!)
  ToF‘s saturated
1.6 J laser energy on target
2.7 J laser energy on target
Notes: Higher energies doesn‘t make sense beacuse H2 starts to burn through.
(verify by TL)

## Slide 16
Energy scaling
DRACO-PW 2025
500nm solid H2 – 1 Hz (0.2 Hz) median performance
DRACO-PW 2025 Formvar – thickness matched
Near-RCD scaling?
DRACO-PW 2025 500nm solid H2 – laser power matched
Notes: Überleitung zu Sim dann: wie kommt es zu den ganz ganz hohen Energien? And can we find some systematics in the emission angle characteristics?

## Slide 17
~32ps takes approx. 7 days on 4 v100 GPUs
Here: „All in one“ approach:
Use real, measured temporal profile of laser pulse (including pedestal)
Start at -32 ps: Experimentally measured Laser-induced breakdown
Simulate full interaction including main pulse in one PIC simulation
PIC simulations: modelling pre-expansion
2D3V, a0=14.5 (4.5 ∙ 1020 W/cm2)
Courtesy of Paweł Ordyna
Laser Induced Breakdown ionization starts here
N. Dover et al. Light Sci. Appl. 12:71 (2023)
L. Yang et al. Commun. Phys. 6, 368 (2023)
A. Hirsch Passicos et al. in preparation
C. Bernert et al. Phys. Rev. Appl., 10, 14070 (2023)
S. Assenbaum et al. PPCF 67 015032 (2025)
Near-RCD laser ion acceleration requires correct modelling of pre-expansion
Typically: combination of PIC and hydrodynamic simulations
-32 ps
LIB measured with off-harmonic optical probing
Notes: High average efficiency

## Slide 18
~32ps takes approx. 7 days on 4 v100 GPUs
PIC simulations: a first look
Including the rims
Highest ion energies at 15° to laser axis
Reproduces near-RCD acceleration from Formvar
2D3V, a0=14.5 32 ps: from LIB to peak
Nearly uniform angular emission. Slightly reduced cutoff energy
Electron density
Electron density
Simple foil geometry
15°
0° | Laser
31°
45°
15°
0° | Laser
31°
45°
Notes: Übergang zwischen sims: 45° passt garnicht

## Slide 19
PIC simulations: The influence of the rim
0 fs
20 fs
40 fs
80 fs
110 fs
200 fs
300 fs
Proton density
Forward accelerated protons from foil bulk
Compression by surface current
Isotropic proton emission from right rim
Ion are affected by accelerating fields from foil + rim
Angular proton spectra depend on relative timing of field evolutuion from foil and rim
3
1
2
4
Further details + full 3D sims: work in progress
central hit
left hit
right hit
Position of laser focus strongly influences the dynamics
15°
0° | Laser
31°
45°

## Slide 20
freezing
Frozen solid
100 m/s
Liquid Jet
Cryogenic solid Hydrogen jet target adapted for near-RCD proton acceleration from foil targets
High efficiency high repetition rate high stability proton acceleration 50 MeV from 1.6J energy
Comparison to Formvar targets
2D PIC simulation for pre-expansion and acceleration
Summary

## Slide 21: Thank you for your attention
HZDR:
Martin Rehwald, Joshua D. Schilz, Thomas Streil, Maximilian Müller, Julian Garreis, Paweł Ordyna, Thomas Kluge, Arthur Hirsch-Passicos, Constantin Bernert, Milenko Vescovi, Tim Ziegler, Hans-Peter Schlenviogt, Josefine Metzkes-Ng, Florian Kroll, Marvin E.P. Umlandt, Radka Štefaníková, Thomas Cowan, Ulrich Schramm and Karl Zeil
René Gebhardt, Uwe Helbig, Thomas Püschel, and Stefan Bock
Christoph Eisenmann, Simon Grams
HED group from EuXFEL
Sebastian Göde
HEDS group from SLAC:
Maxence Gauthier, Christopher Schönwälder, Megan Ikeya, Siegfried Glenzer
And thanks to all my colleagues and collaborators

## Slide 22
Backup

## Slide 23
Conversion efficiency
Assumptions:
Use spectrum from 0° / 15° / 31° / 45° spectrometers
Spectrum is representative for
  +-7.5° (horizontal plane)
  +-10° (vertical)
Only use E>5MeV protons
45°
15°
31°
0°
Mean conversion efficiency: ~3%
Peak conversion efficiency: 8%
  Dominated by large particle numbers in 0° (too large??)

## Slide 24
Laser contrast and laser-induced breakdown (LIB)
Expectation:
LIB at 48 ps ??
Mismatch between prediction and measurement
Try adjusting contrast manually until LIB time matches:
Laser contrast 6x better:
LIB at 32.5 ps
small pre-pulse
at 31.3 ps
Reflective
Transmittive
C. Bernert et al., Phys. Rev. Appl., 10, 14070 (2023)
S. Assenbaum et al. PPCF 67 015032 (2025)
LIB = ne in conduction band > nc
Change of laser-target interaction mechanism
Start of plasma formation and pre-expansion
Direct LIB time measurement in acceleration experiment
LIB at 32 ps

## Slide 25
Optimal sheet jets for laser-ion acceleration
Jet starts to freeze
Liquid Jet
~500 µm to nozzle
Jet fully frozen
Solid Jet
~20 µm
Different sizes and aspect ratios
4x20 µm Planar slit nozzle shows promising results at high pressures
Width: >30 µm, Thickness: ~500 nm
M. Rehwald, S. Göde, S. Assenbaum: in preparation
Find optimal nozzle aspect ratio + ideal operation parameters
Straight slit nozzle characterization study

## Slide 26
Chopper: Different approaches
New design (2020 – 2024):
synchronous motor with LIDAR Polygon motor driver
https://thorlabs.com
Option 1:
Rotating blade:
High velocity
Timing is tricky
Design by S. Göde (2021/22)
Initial design (2018):
modified commercial optical chopper
Option 2:
Piezo-actuator
~1mm
1.5 mm
~2.5 mm
Cryostat
Timing is easy
Low velocity
Chopper
Cryostat
~1 m/s, <<1 µs timing jitter
laser ~1.5 mm from cryostat
10 m/s, 20 µs timing jitter
laser ~ 10mm from nozzle
30m/s, 2 µs timing jitter
laser ~ >3 mm from nozzle (limited by chopper blade)
~5 mm
25mm
20mm
Courtesy of S. Göde

## Slide 27
Rotating Chopper
After 20k shots ~ 1019 Wcm-2
Long term operation
After 4k shots
5∙1020 Wcm-2
Nozzle
Large experiment at EuXFEL (2023)  New effects observed:
Solution:
No damage to Cryosource!
Piezo Chopper
Radiation shield
Cryogenic source
Option 1: Faster and wider chopper
  covers more area during shot
Option 2: Encapsulate the source with full radiation shield:
  Prevents heat influx and damage
  Tradeoff: + 1 mm distance to nozzle
„Shadow“ of piezo chopper
„Shadow“ of rotating chopper
Design for Draco Setup:
Copper „bell“, flanges to cryostat Ø 60 mm
Ø 1.5 mm stainless steel orifice for jet thickness: 500 µm
> 1020 W/cm2
Damage accumulation
Transient temperature spikes
Full radiation shield

## Slide 28
Protecting the cryogenic source
Laser-driven relativistic plasma close to source can:
damage the Nozzle
de-stabilize the target after each laser shot
Solutions:
radiation shield
„Chopper“
Rotating Chopper
Target: solid hydrogen sheet jet
Cryogenically liquified H2
Challenges on the way to 1 Hz operation
M. Rehwald, S. Göde, S. Assenbaum in preparation
15 µm
8 mm below nozzle
Rotation: 45°
Jitter: ~2 µm
Slit nozzle creates alter- nating, orthogonal sheets
Evaporative cooling freezes the jet into a solid H2 foil
  Width: ~ 25 µm
  Thickness: ~500 nm
  Cylincrical rims Ø 5 µm
Very stable, HRR capable, debris-less foil-like target
freezing
Liquid Jet
Frozen solid
4µm
20 µm
M Rehwald, et al, 2023 J. Phys.: Conf. Ser. 2420 012034
5∙1020 W/cm2
Cryogenic source

## Slide 29: Longitudinal Probing: on pump laser axis
OAP
z
y
Imaging with Laser OAP
515nm
OAP introduces image plane tilt
y
x
Low magnification
Large field of view
  Restricted by image plane tilt
Dielectric Beamline mirror
Target plane
real on-axis probing
no additional expensive objective
Inspired by:
Robert M. Malone et al., Proc. SPIE 6288, Current Developments in Lens Design and Optical Engineering VII, 62880Z (1 September 2006)