## Slide 1: Higher Order Modes in Accelerating Structures for Flat Beams
Gerard Andonian (UCLA)
21-27 September, 2025
EAAC 2025, Isola d’Elba

## Slide 2: Outline
Background
Skew wakefield experiment
    Theory and Modeling
    Experiment Results
    Reconstruction algorithm
Alternating DWA experiment
    Preliminary Results
Summary

## Slide 3: Background
Beam-driven structure wakefield acceleration (SWFA)
  Dielectric wakefield acceleration (DWA)
  Corrugated metal structures, etc.
High frequencies accessible
  dependent on material, geometry
  Scale to THz (sub-mm) scale structures
Applications
  HEP: future collider (Ez ~ GeV/m)
  Compact Light Source driver
  Radiation Source (THz)
  Phase Space Manipulations
    Self wake interactions (dechirper, shaper)
  Diagnostics - streaker
Bettoni PRAB 19, 021304 (2016)
Djikstal PRR 4, 013017 (2022)
100 µm
Notes: Electron bunch drives wakefield in dielectric structure
Wakefields accelerate trailing bunch
Dependent on structure geometry

## Slide 4: Important results in DWA
High gradient acceleration observed
  ~2 GeV/m peak field in cylindrical structure
  300 MeV/m in drive witness mode
Novel geometry
  Planar, Bragg, 3D-photonic (woodpile)
  BNL ATF experiments
DWA driven by positrons
  FACET experiment
  Similar spectral results and behavior e-driven
  Possible application to e+ -e- collider
Pertinent issues:
  Transverse wakefields accompany longitudinal fields
  Majernik, PRR 4, 023605 (2022)
  O’Shea Nat. Comm. 7, 12763 (2016)
200 MeV

## Slide 5: Flat beams in planar structure
Beam breakup (BBU) instability
  Consequence of driving transverse fields
  Off-axis excitation – higher order mode wakefields
  Emittance growth, BBU
  Limits on accelerating voltage
External strong focusing (i.e. PMQ) may help
Flat beams (ex >> ey) in planar geometry
  Infinite sheet beam has no transverse wakefield
  Elliptical beams (sx>> > sy)– mitigate transverse effects
Theoretical model
  Growth rate of fields as function of ellipticity
Experiment at FACET
  Observe beam drift in planar structure
  Suppression of transverse mode for elliptical beams
  O’Shea, PRL 124, 104801 (2020)
  Baturin, PRAB 21, 121302 (2018)
  Li, PRST-AB 17, 091302 (2014)
  Tremaine, PRE 56 7204 (1997)
Elliptical beam
Round beam
Wz
Wy
Ellipticity
  Saveliev, PRAB 25, 081302 (2022)

## Slide 6: Skewed-wakefields in DWA
Further examine flat beam interaction in DWA
  Important for future flat beam applications (i.e. collider luminosity)
Simple analytic model
  Baturin, PRAB 21, 121302 (2018)
  Two particle model proxy for flat beam
Wakefield map shows higher order modes
  Quadrupole mode dominant
  Skew quadrupole mode with incoming angle
Flat beam (red) going into page
Dielectric
Metal
W. Lynn, PRL, 132 165001 (2024)

## Slide 7: Skewed wake model
Single-slab structure
  Simple analytic model
  BAR, PRAB 21, 121302 (2018)
Wakefield has higher order mode content
  Dipole mode and quadrupole modes
  Skewness observed with incoming angle
Flat beam (red) going into page
W. Lynn, PRL, 132 165001 (2024)
Dielectric

## Slide 8: Skewed wake experiment at AWA
Argonne Wakefield Accelerator (AWA)
  Demonstrator facility for SWFA and PWFA
  Round-to-flat-beam transformer
    Magnetized beam at cathode
    Remove angular momentum with skew quadrupoles
    Flat beam (up to 100:1 ratio)
  Focus through planar DWA structure
    Diagnostics: transverse distribution
Drift
Single slab
Simulation
Dielectric Surface
AWA

## Slide 9: Skewed wake experiment - structure
Dielectric material: Alumina
  e = 9.4 (Al2O3)
  Width = 40mm
  Length =150 mm
  Thickness = 5mm
  Half-gap (a) = 5 mm
  Coated with thin metal layer
  Fixed spacers
Alumina
Installed on AWA beamline
Rails for adjustable gap
Two independent motors
for single slab or double slab
Can operate in fully-open mode (“no structure”)
15cm

## Slide 10: Skewed Wake experiment - Results
Single sided slab
  Beam injection
  0.9mm away from slab surface
  Injection angle varied (2˚ and 7˚ shown below)
Transverse wake induced effect
  Agreement with two-particle model and simulations (WARP)
YAG2
YAG3
(no slab)
YAG3 (slab)
q = 2˚
q = 7˚
q = 2˚
q = 2˚
q = 7˚
q = 7˚
q = 7˚
q = 2˚
Simulations
DWA
q
q = 7˚
q = 2˚

## Slide 11: Reconstruction algorithm
N. Majernik, et al Phys. Rev. Accel. Beams 26, 094601 (2023)
Extract transverse info from diagnostic screens
Single-shot technique
High dimensional parameter space explored efficiently
Multipole components of transverse wakefield
OUTPUT
Binning
Error map
Drift only
(no structure)
INPUT
Notes: Inputs:
  transverse screen image of beam at same location, with and without structure
Steps:
  Generate particle distribution
  Apply transformation
  Compare error plot
  Iterate to convergence threshold
Output: kick vector map

## Slide 12: Reconstruction algorithm - output
Algorithm test with simulations (WARP)
Simulate screen distributions
Use arbitrary number of modes in expansion
Convergence with higher modes (n=4)
Structure
No structure
n = 2
n = 4
n = 6
Experimental Data
n = 6
n = 3
n = 1
No structure,
7˚ e-beam tilt
Single-slab structure,
7˚ e-beam tilt
Reconstructed
Field maps
WARP

## Slide 13: Alternating DWA Concept
Manipulation of transverse wakefields
Asymmetry in beam to structure
  Quadrupole dominated wake
  90˚ rotation each period
  Analogous to alternating gradient focusing
  Focus beam in both planes
Potentially stabilizing effect
  May be competitive with magnetic quadrupoles & beam energy spread for damping
Kick map experienced by a test particle
Kick map rotates with structure
after one period
beam direction

## Slide 14: Alternating DWA experiment
Compare ADWA to planar slab DWA
Adjustable gap in both planes
Remove one axis for planar DWA
Diagnostic: transverse screens
Longitudinal dependence of wakefield
Focusing in core of beam after ADWA
ADWA
Planar DWA
ADWA
ADWA
Planar DWA
Planar DWA
Drift (no structure)
Drift (no structure)
z
z
z
x
x
x
y

## Slide 15: ADWA experiment at AWA
4 independent motors
Hold gap fixed in x, vary y spacing
Observe: transverse distribution and z-dependence

## Slide 16: Experiment results ADWA (preliminary)
Transverse beam distribution at screen downstream (23cm)
x-gap constant at 1.31mm but y-gap varies
Change structure from symmetric ADWA to planar
Functionally tune the net effect of the quadrupole-like transverse mode
Symmetric focusing
Path towards controlling beam size with wakefields
Transverse Distributions on YAG screen

## Slide 17: Summary
Flat beams in SWFA generate higher order modes
  Tradeoffs with longitudinal gain and competing effects
  Skew transverse wakefields observed
  Reconstruction method for wakefield analysis
Future work in transverse dynamics of flat beams
  Novel solutions and hybrid schemes under study
  Extendible to other applications (Flat beam driven PWFA – see P. Manwani Thursday)
  Analysis on alternating DWA imminent
Acknowledgements
W. Lynn, N. Majernik, P. Manwani, S. Baturin, J. Power, G. Ha, T. Xu, P. Piot, S. Kim, S. Doran, E. Wisniewski, A. Ody, J. B. Rosenzweig
Support from US DOE DE-SC0017648
Thank you for your attention!

## Slide 18: BACKUP SLIDES