## Slide 1: THz streaking for ultrashort beam measurements at UCLA Pegasus
P. Musumeci
UCLA Department of Physics and Astronomy

## Slide 2: Acknowledgements
M. Lenz, B. Schaap, P. Denham, A. Kulkarni, D. Garcia, Z. Liu (UCLA)
Y. Yang, R.K. Li (Tsinghua University)
M. Ota (Osaka University)
A. Murokh, G. Andonian. RadiaBeam Technologies
Work supported by DOE grants DE-SC0009914 and DE-SC0021190
Photocathode development funded by Center for Bright Beams NSF grant PHY-1549132

## Slide 3: Outline
Ultrashort high brightness electron beams applications
Generation of fs electron beams
Measurements of fs electron beams
THz streaking structures
Conclusions

## Slide 4
Advanced accelerator injection
Coherent radiation generation
Ultrafast electron diffraction
Free electron lasers
Applications of ultrashort relativistic e-beams

## Slide 5: Pegasus Laboratory High peak brightness beam research at UCLA
3-14 MeV student-run university-size accelerator beamline optimized for sub-pC beams
Ultralow charge beams with high peak brightness or phase space density:
  Single shot imaging / UEM
  High resolution ultrafast electron diffraction
  ACHIP: few fs acceleration bucket, sub-micron aperture
  THz acceleration / amplification
Sol
Sol
Linac
Gun
Dipole
Spectrometer
Quads
Deflector
6 m
E. Curry et al. Meter-scale THz-driven acceleration of a relativistic electron beam. Phys. Rev. Lett. 120, 094801 (2018)
D. Cesar et al., Onset of non-linear effects in high gradient dielectric laser accelerator. Communications Physics 1, 46 (2018)
D. Cesar, et al., Demonstration of single-shot picosecond time-resolved MeV electron imaging using a compact permanent magnet quadrupole based lens. Phys. Rev. Lett., 117, 024801 (2016)
J Maxson, et al., Direct measurement of sub-10 fs relativistic electron beams with ultralow emittance. Phys. Rev. Lett., 118 154802 (2017)
Notes: One of the few/only MeV high brightness beamlines in a university. Much different environment than National Laboratory
Education and outreach (here is me trying to explain to 4th graders what is it that we do).
Focus on low charge high brightness beam research.
Don’t have time to show highlights here, just point you to the list of recent publications from the laboratory

## Slide 6: How to generate fs beams ?
Bunch length controlled by different methods
Maxson et al., PRL 118, 154802 (2017)
L. Zhao. Phys. Rev. X 8, 021061 (2018)
Longitudinal phase space manipulation using RF cavities
Standard technique in accelerator and beam physics
Suffers from timing jitter
High harmonic linearization for even shorter bunches
Multi bend achromat or alpha magnet for jitter-free compression
Laser-based THz compression to synchronize
H. W. Kim et al., Nat. Phot., 14, 245 (2020)
F. Qi et al., Phys. Rev. Lett. 124, 134803 (2020).
Y. Yang et al. https://arxiv.org/abs/2508.03946 (2025)

## Slide 7
Limitations of RF compression: longitudinal phase space nonlinearities
Vacuum dispersion [1]
[1] K. Floettmann (2014) NIM-A ,740, 34 [2] J. Maxson (2017), PRL 118, 154802
[3] P. Denham (2023), Instruments 7:49.
RF curvature
Drift length
In our case typical 10 - 100 fs in focus due
to vacuum dispersion alone
Phase advance in compression point
Electric field
in RF cavity
However, short bunch at cathode results in more uncorrelated energy spread due to stronger Coulomb forces, which
limits bunch compression (or charge)
Solution: start with short initial bunch [2]
Phase

## Slide 8
RF compression at Pegasus beamline
Short pulse on cathode, limited by space charge

## Slide 9
Long pulse on cathode, limited by vacuum dispersion and other nonlinearities introduced in the gun
RF compression at Pegasus beamline

## Slide 10
Long pulse and phase space linearization using X-band accelerator
Phase space linearization for RF compression at Pegasus beamline
Linear chirp + 2nd order curvature
2nd order curvature
Curvature removed
Deacceleration field
Linear chirp
[1] Denham (2023),
Instruments, 7(4), 49

## Slide 11
Long pulse and phase space linearization using X-band accelerator
?
?
Deflection cavity cannot be used since we have only one X-band klystron
Use linac to rotate longitudinal phase space and measure energy spectra: tomography
Longitudinal phase space
Sinogram
Tomography of longitudinal phase space linearization

## Slide 12
Tomography of longitudinal phase space linearization
for the generation of attosecond electron bunches [1]
[1] Schaap (2025) PRAB, 28, 012802
x-band on
x-band off
x-band on
x-band off
Reconstruction algorithm: neural-network assisted algebraic reconstruction technique
Rf curvature induced by photo-injector on 7 ps beam characterized
Measured phase space compensation by x-band for generation of sub-femtosecond bunches
Next: measuring of bunch length at compression point

## Slide 13
Electro-optic sampling of the relativistic Coulomb field
An indirect measure of the bunch length at compression point
EOS is a tool for characterizing fields that are slowly varying (with respect to the probing optical cycle) such as THz radiation [1,2] or Coulomb fields [3,4] inducing a temporary birefringence in an electro-optic crystal
[1] Q. Wu (1995) Appl. Phys. Lett. 67, 3523–3525
[2] M. Lenz (2022) Optics Express 30, 19, 33804-33816
[3] R. Pompili (2014),NIM-A, 740, 216-221
[4] E. Roussel (2022) Light: Science & Applications 11, 14
Field electron bunch given by convolution of single particle field and density distribution
Rest frame
Lab frame
Ota, M, (2022) IRMMW-THz
Coulomb field of particle in uniform motion in vacuum
Known limitation due to frequency response of EO crystal

## Slide 14
ebeam
vacuum
chamber
ZnTe
detector
polarizer
polarizer
Electro-optic sampling of compressed bunches
Looking at EO effect amplitude (not time-trace)
An indirect measure of the bunch length at compression point
Measured
Analytic
Longitudinal slice
Transverse slice
Example: 20 pC bunch, 5 MeV
Results:
Compressed bunches allow for EOS of very low charges <100 fC
Potentially bunch length measurement above THz absorption resonance in Zn Te
Signal strength is measure for bunch length
(more sensitive if length < waist)

## Slide 15
THz streaking
A direct measure of the bunch length at compression point
Mapping temporal distribution to transverse with time-dependent deflecting field
Streaked rms bunch size
ebeam
~5 MeV
~100 fC
vacuum
chamber
iCCD
grating
structure
780 nm, 4 mJ, 100 fs
0.4 THz, 20 uJ, single cycle
screen
Mg:LiNbO3
HWP
f75
f500
THz generation by optical rectification in lithium niobate with pulse front tilted femtosecond laser pulse
Short period of THz wave compared to RF
significantly boosts streaking power (angle/time).
Streaking with laser synchronized wave (direct time of arrival measurement for applications)
Final temporal resolution also determined by unstreaked beam size and screen psf
Mg:LiNbO3 prism (stoichiometric, 62∘ cut)
Optical rectification with tilted pulse front
Two lens telescope system for pulse front tilt tuning
Pump: 4mJ, 100fs, 785nm
Output: 20 uJ 0.4THz single cycle THz pulses
0.5% IR to THz conversion efficiency at room temperature (outcoupled)
Zhao, Lingrong, et al. "Terahertz streaking of few-femtosecond relativistic electron beams." Physical Review X 8.2 (2018): 021061.
Li, R. K., et al. "Terahertz-based subfemtosecond metrology of relativistic electron beams." Physical Review Accelerators and Beams 22.1 (2019): 012803.

## Slide 16
Streaking power from different structures
Tsinghua Horn structure [1]
Parallel plate waveguide (UCLA)
High frequencies lead to strong streaking power ~35 murad/fs
Even larger streaking power at 3 MeV gun only
To compare, streaking power in Maxson experiment (500 kV x-band deflector) ~1 urad/fs
Nondispersive, more transmission due to larger opening ~20 murad/fs
[1] Yang (2025), arXiv:2508.03946v1
Pixel resolution at L =1.3 meter downstream YAG ~ 200 – 500 as/pxl!
THz streaking calibration

## Slide 17
THz streaking of femtosecond bunches
Preliminary results
Operating at compressing gun phase:
short pulse in buncher
~5 fs bunch length (record at Pegasus)
at low charge <10 fC
Next step is to use linearizer to go to even shorter bunches (at higher charge)
Unstreaked
Streaked

## Slide 18: Conclusions and next steps
Towards sub-fs electron beams for coherent radiation generation and ultrafast electron diffraction by linearized RF compression
Benchmarking beam dynamics
  Indirect tomographic LPS measurements
  EOS amplitude based peak current reconstruction
Direct THz streaking.
  Novel waveguide structures
  Record streaking power
  Sub-fs resolution