## Slide 1
Jiaqi Zhang1,2, Hossein Saberi1,2, Guoxing Xia1,2, Oznur Apsimon1,2, Stewart Boogert1,2, Thomas Pacey3,2, Toby Overton3,2
1Department of Physics and Astronomy, University of Manchester, UK
2Cockcroft Institute, UK
3Accelerator Science and Technology Centre (ASTeC), STFC Daresbury Laboratory, UK
European Advanced Accelerator Conference
21–27 Sept. 2025, Isola d'Elba, Italy
Machine learning-based optimisation of plasma density ramps
@ CLARA FEBE

## Slide 2
Gradient:
  By achieving GV/m-scale [1] acceleration gradients, plasma wakefield acceleration (PWFA) offers a promising pathway toward more compact and cost-effective alternatives to traditional RF-based accelerators.
Beam quality:
  Existing energy doubling experiments [2] focused on the gradient, which normally sacrifices the beam quality
Background & Motivation
An 85-cm-long plasma cell
Peak gradient: 52 GV/m
Several pC charge got energy doubled
[1] P. Muggli et al., Comptes Rendus Phys. 10, 116 (2009).
[2] I. Blumenfeld et al., Nature 445, 741 (2007).

## Slide 3
Why plasma density ramp?
Reduction of the phase velocity, trapping more plasma electrons
Limited implement in PWFA
@ DESY:
  Gaussian ramps are more realistic than linear ramps [1], based on measurements through the gas cell [2].
Background & Motivation
The real gas cell
Measured electron density vs. the gas cell axis
[1] A. Martinez De La Ossa et al., Phys. Rev. Accel. Beams 20, 1 (2017).
[2] O. Kononenko et al., Nucl. Instrum. Methods Phys. Res. A 829, 125 (2016)

## Slide 4
@ SPARC LAB:
  The linear plasma density ramp is used for theoretical simplifications [1].
  A third-order polynomial fitting function was used to model a tapered plasma capillary [2].
  An example of the real plasma density profile [3].
Background & Motivation
Gas-filled discharge capillary
Plasma density in tapered capillary
[1] A. Marocchino et al., Nucl. Instrum. Methods Phys. Res. A 909, 408 (2018).
[2] F. Filippi et al., Nucl. Instrum. Methods Phys. Res. A 829, 326 (2016).
[3] C. Mariani et al., Politecnico di Milano, 2022.
Channel diameter: 1 mm
Air pressure: 800 mbar
Discharge: 7 kV ~ 380 A

## Slide 5
Facility
FEBE beamline [1]
[1] E. W. Snedden et al., Phys. Rev. Accel. Beams 27, 41602 (2024).
Parameters | Commissioning | Developing
Energy (MeV) Charge (pC) RMS bunch length (μm) RMS transverse size (μm) Energy spread (%) Emittance (mm mrad) | 50 – 250 5 – 250 15 – 30 20 – 100 < 5 < 5 | 50 – 250 5 – 250 <<15 – 30 1 – 100 ~1 ~1
FEBE specifications [1]
CLARA FEBE
Notes: The Compact Linear Accelerator for Research and Applications (CLARA) at the Daresbury Laboratory, capable of producing 250-MeV electron bunches. Recently, a new beamline attached to CLARA, the Full Energy Beam Exploitation (FEBE) facility, has been designed to provide ultra-short and low-emittance electron bunches.

## Slide 6
Schematic of PWFA Experiments @ CLARA FEBE[1]
Driver/witness configuration is generated by the mask technology.
The discharge method is planned to form the ramp plasma density profile.
Diagnostics include 6D beam characterisation.
Energy Doubling Scheme
[1] E. W. Snedden et al., Phys. Rev. Accel. Beams 27, 41602 (2024).

## Slide 7
Particle-in-cell: FBPIC[1]
LBNL, open-source, developed in 2018
Quasi-3D cylindrical coordinate
Maxwell solver in the spectral space
Significantly reduces the spurious numerical dispersion
GPU support
Running on STFC SCARF and CSF3 in UoM
Simulation Code
[1] R. Lehe et al., Comput. Phys. Commun. 203, 66 (2016).

## Slide 8
Research Objectives:
  Obtain the optimal beam quality based on the neural network
  Review beam quality stability around the optimal parameter point.
Applications:
  Free electron lasers (FELs) [1]
  Future high-energy physics experiments [2]
Objectives & Applications
[1] P. G. O. Shea et al., Science 292, 1853 (2001).
[2] B. Foster et al., New J. Phys. 25, (2023).

## Slide 9
Simulation Parameter Settings
Initial stage (S1): Fixed 2.8×1016 cm-3
Up-ramp stage (S2): Gaussian profile to be optimised
Plateau stage (S3): One of the parameters
Down-ramp stage (S4): A symmetrical Gaussian profile
Final stage (S5): Fixed 2.8×1016 cm-3
Simulation Parameter Settings
Parameters | Driver | 10 pC witness
Beam density (cm-3) Charge (pC) Energy (MeV) Bunch length (μm) Transverse size (μm) Energy spread (%) Emittance (mm mrad) | 1.19×1015 150 250 10 50 1 5 | 1.98×1015 10 250 10 10 1 5
S1
S2
S3
S4
S5

## Slide 10
Training Parameter Settings
Architecture of the Neural Network
Layer (Type) | Output Shape | Param #
Input Layer (Dense) Hidden Layer 1 (Dense) ReLU Activation 1 (ReLU) Hidden Layer 2 (Dense) ReLU Activation 2 (ReLU) Hidden Layer 3 (Dense) ReLU Activation 3 (ReLU) Output Layer (Dense) | (None, 3) (None, 128) (None, 128) (None, 64) (None, 64) (None, 32) (None, 32) (None, 3) | 0 512 0 8256 0 2080 0 99
Total parameters: 32843

## Slide 11
Learning process
Model Training and Evaluation
A total of 1000 simulations were performed, with 20% reserved for validation.
The training loss (based on seen data) decreases rapidly within the first 10 epochs.
The training curve remains smooth and stable throughout.
The validation curve (based on unseen data) closely follows the training curve, with no signs of significant overfitting.

## Slide 12
Model Evaluation
Model Training and Evaluation
Mean Absolute Error (with percentage):
0.006 pC (0.063%), 0.015% (0.290%), 0.043 mm mrad (1.366%)
The surrogate model achieved all MAPEs below 2%.

## Slide 13
Bayesian optimisation & Final Quality
Optimal parameters (predictions):
zstart = 2.49 cm, Q = 9.52 pC (9.54)
nmax = 4.24×1016 /cm3, σE = 4.75% (4.74)
Lramp = 1.19 cm, εN = 3.06 mm mrad (2.95)
Quality = 0.655 (0.682)
Beam quality definition [1]:
[1] A. Giribono et al., Phys. Rev. Accel. Beams 26, 83402 (2023).
Final quality for energy doubling:
Non-ML: Q = 8.60 pC, σE = 5.77%, εN = 6.50 mm mrad, Quality = 0.229
ML: Q = 9.54 pC, σE = 5.84%, εN = 2.74 mm mrad, Quality = 0.596 (160% higher)
Notes: Acquisition function：Upper Confidence Bound

## Slide 14
Robustness & Parameter Sensitivity
Tolerance analysis (1000 LHS samples):
Q : mean = 9.514 (-0.27%), σ = 0.122 (1.28%)
σE : mean = 4.765 (0.53%), σ = 0.095 (1.99%)
εN : mean = 2.977 (0.91%),, σ = 0.031 (1.04%)
Parameter Variation:
zstart = 2.24 – 2.74 cm (±10%), nmax = 4.03 – 4.45×1016 /cm3 (±5%)
Lramp = 1.09 – 1.33 cm (±10%)

## Slide 15
Robustness & Parameter Sensitivity
Sobol sensitivity analysis (218 LHS samples):
Main effects dominate, explaining 87% of the variance:
Sensitivity ranking: Lramp > zstart > nmax.
Pairwise interactions account for ~12% (~91% of total interaction effects).
Higher-order interactions contribute < 2%.
Parameter Variation:
zstart = 2.0 – 5.0 cm, nmax = 3.5 – 4.5×1016 /cm3, Lramp = 0.5 – 5.0 cm

## Slide 16
We performed machine learning-based optimisation of PWFA for the energy-doubling scheme at CLARA FEBE.
The surrogate model achieved mean absolute percentage errors below 2%.
Using Bayesian optimisation, we identified the optimal parameters and obtained a final-energy beam quality of 0.596, representing a 160% improvement compared with the non-ML baseline.
Tolerance analysis confirmed that the mean beam quality remains within 1%, with deviations below 2%.
Sensitivity studies further revealed that the main effects dominate the variance, with the sensitivity ranking following Lramp > zstart > nmax.
Conclusions
Acknowledgements
This project has received funding from the European Union’s Horizon 2020 Research and Innovation programme under Grant Agreement No 101004730 'I.FAST’.
We acknowledge the support from the Cockcroft Institute Core Grant No. ST/V001612/1.
Computing resources are provided by STFC Scientific Computing Department’s SCARF cluster.

## Slide 17
点击添加文本
点击添加文本
点击添加文本
点击添加文本
Thanks for your attention!
Thanks for your attention!
Thanks for your attention!
Thanks for your attention!
Thanks for your attention!
Thanks for your attention!
Thanks for your attention!
Thanks for your attention!