## Slide 1
Laser-Driven Very High Energy Electrons for Femtosecond-Scale Irradiation of In Vitro Cell Lines
EAAC 26th September 2025
Hannah Maguire

## Slide 2
EAAC 2025
Motivation
Very high energy electrons (VHEEs, >50MeV) can:
achieve excellent dose conformity and deep penetration depths
enhance the sparing of critical structures while providing similar/superior target coverage than photons
show reduced susceptibility to tissue inhomogeneities
laser systems achieve accelerating gradients >10s GV/m
[1] A. Hart et al. (2024). doi: 10.1109/JSEN.2024.3353190
[2] B. Palma et al. (2015). doi: 10.1118/1.4925419
[3] K. Kokurewicz et al. (2021). doi: 10.1038/s42005-021-00536-0

## Slide 3
EAAC 2025
Proof of Principle Experiments
Single-shot, Gy-scale irradiation at dose rates >1013 Gy/s
significant increases in RBE following femtosecond VHEE irradiation
Single-shot, Gy-scale irradiation at dose rates >1010 Gy/s
no significant differences in RBE following picosecond electron beam irradiation
McAnespie et al. (2025)
McAnespie et al. (2024)

## Slide 4
EAAC 2025
Astra-Gemini Laser, CLF

## Slide 5
EAAC 2025
Astra-Gemini Laser, CLF
e- beam characteristics:
VHEE beams (100-800 MeV)
τb = ~150 fs
= 1.8 ± 0.4 nC
Low divergence (1.4 ± 0.4 mrad)
>3 Gy per shot over cm2 areas
Dose rates >1013 Gy/s

## Slide 6
EAAC 2025
TARANIS Laser, QUB

## Slide 7
EAAC 2025
TARANIS Laser, QUB
e- beam characteristics:
1-8MeV (T = 1.6 MeV)
τb = ~10-20ps
Ne = ~2.9 x1011
Large divergence (560 mrad)
>8 Gy per shot over cm2 areas
Dose rates >1010 Gy/s

## Slide 8
EAAC 2025
Radiation Sources
Conventional X-ray source (CONV)
X-Ray energies < 160keV
2.4 Gy/min
fs VHEE Irradiation
250-700 MeV
Gy/s
ps Irradiation
1-8 MeV (T = 1.6MeV)
Gy/s
FLASH-RT source
4-20MeV
40-1000 Gy/s

## Slide 9
EAAC 2025
Clonogenic Assays
Cell survival 12 days following irradiation
Survival dependant on delivered dose (D/Gy)
7 different cell lines
DU145 (prostate)
MCF7 (breast)
HeLa S3 (ovarian)
H460 (lung)
RPE-1 (retinal)
E2 (glioblastoma)
AGO 1552D (skin)
Radioresistance
Surviving Fraction
Relative Biological Effectiveness
Parameters and RBE calculations were obtained using MCMC sampling with emcee.
Statistical analysis: Wilcoxon Rank-Sum test;
ns, not significant, *p < 0.05, **p < 0.01.

## Slide 10
EAAC 2025
Cell Response to fs VHEE Irradiation
Significant increases in RBE
P values <0.01 for majority of dose points
Consistent with results obtained in McAnespie et al. (2025).

## Slide 11
EAAC 2025
Cell Response to ps Irradiation
No significant differences in RBE at low doses
FLASH-like sparing effect observed at higher doses- first demonstration at dose-rates >1010 Gy/s
Consistent with results obtained in McAnespie et al. (2024).

## Slide 12
EAAC 2025
Conclusions and Next Steps
Significant increase in RBE was observed for all cell lines following irradiation with fs VHEE beams
No difference in RBE was observed following irradiation with ps electron beams at low dose
  - At higher doses, a FLASH-like sparing effect was shown for 4/6 cell lines, indicated as significant increases in SF
  First demonstration of FLASH-like effects at dose-rates >1010 Gy/s
53BP1 Immunofluorescent Assays- analysis ongoing
3D Spheroid Models (CLF, Jan 2026)
  Spheroids mimic the 3D structure and cellular environment of tumors advancing towards future in vivo applications
Dosimetry of ultra-short electron beams is not trivial:
  Plane-parallel ionisation chambers experience charge collection inefficiency at high dose-rates
  RCFs are suitable for high dose-rate VHEE dosimetry but fail to provide dose measurements in real-time

## Slide 13
EAAC 2025
QUB Mathematics and Physics
Conor McAnespie
Elias Gerstmayr
Luke Calvin
Temour Foster
Daniel Molloy
Gagik Nersisyan
Matt Streeter
Gianluca Sarri
Acknowledgements
QUB PGJCCR
Carla McDonnell
Stephen McMahon
Kevin Prise
National Physical Laboratory, UK
Pankaj Chaudhary
Giuseppe Schettino
Central Laser Facility, Harwell Campus, UK
Stan Botchway
Sarah Needham
Oliver Finlay