## Slide 1
EuPRAXIA@SPARC_LAB status
Massimo Ferrario,
INFN-LNF
This project has received funding from the European Union´s Horizon Europe research and innovation program under grant agreement No. 101079773
EuRONNAC Meeting
September 27, 2025

## Slide 2: The Concept of User Facility in the EuPRAXIA Project
In the EuPRAXIA project, the user facility is conceived as a cutting-edge, distributed European research infrastructure that provides open access to advanced plasma-based accelerator technologies and associated beamlines. It is designed not only to serve the needs of the scientific community but also to act as a platform for innovation, integrating academia, industry, and technology developers. A distinctive element of the EuPRAXIA user facility is its commitment to open innovation, where collaboration between research institutions, industrial partners, and technology providers is central to the development and application of new accelerator concepts.
Mission | Serve a broad community of users in physics, material science, biology, medicine, and industrial applications through plasma-based electron beams and associated radiation sources.
Access | Open to external users (academic and industrial) through peer-reviewed proposals, ensuring scientific excellence and societal impact. Pilot user access is foreseen from 2031.
Distributed Model | EuPRAXIA is a distributed research infrastructure wich will operate through multiple nodes under a unified governance framework (AISBL) and coordinated access policy.
Beamlines & Instruments | Users will access beamlines including plasma-driven FELs, betatron and ICS X-ray sources, and ultrashort electron and positron beams.
Sustainability | Focus on energy efficiency (e.g., high-efficiency laser systems and RF modules), minimization of physical footprint through compact accelerator designs, and adherence to EU green transition objectives.
Data & Open Science | EuPRAXIA promotes open data policies and integration with the European Open Science Cloud (EOSC), enabling FAIR access to results and infrastructure services.

## Slide 3
Funded by the European Union
EuPRAXIA Scientific Goals
www.eupraxia-facility.org
Flagship Science Goal 2: EuPRAXIA will deliver betatron X rays with about 10^10 photons per pulse, up to 100 Hz repetition rate and an energy of 5-18 keV to users from the medical area. The much reduced longitudinal length of the X ray emission area (point-like emission) leads to an important improvement in image resolution compared to other techniques.
Flagship Science Goal 1: EuPRAXIA will deliver free-electron laser (FEL) X rays with 10^9-10^13 photons per pulse to user areas, covering wavelengths of 0.2 nm to 36 nm. The EuPRAXIA FEL pulses are naturally short (down to 0.4 fs) and will therefore provide users with tools for investigating processes and structures in ultra-fast photon science at a reduced facility foot print.
Flagship Science Goal 3: EuPRAXIA will deliver positron beams at energies from 0.5 MeV to 10 MeV and a repetition rate of 100 Hz for material science studies. Per pulse about 10^6 positrons will be produced in a time duration of 20-90 picoseconds on the sample, allowing time-resolved studies. EuPRAXIA will here advance the capabilities of existing positron sources in flux and time resolution.
Flagship Science Goal 4: EuPRAXIA will deliver electron and positron beams at energies from a few 100 MeV up to 5 GeV for high energy physics related R&D (detectors, linear collider topics). R&D goals include the demonstration of a linear collider stage, a "table top" HEP test beam and studies on positron transport and acceleration towards a linear collider.
Flagship Science Goal 5: EuPRAXIA will deliver photons from an inverse Compton scattering (ICS) source. The photons of up to 600 MeV and with narrow-band spectrum will enable precision nuclear physics and highly penetrative radiography for users.
Flagship Science Goal 6: EuPRAXIA will provide access to a multi-stage, high-repetition rate plasma accelerator in the GeV range to users from accelerator science. This R&D platform will allow the testing of novel ideas and concepts, full optimisation of a plasma collider stage, certain fixed target experiments (also in combination with lasers) and performance studies of conventional versus novel accelerator technology.
Flagship Science Goal 7: EuPRAXIA will provide access to cutting edge laser technology with short pulse length in combination with high energy photon pulses and short electron/positron bunches. Novel schemes of pump probe configurations and ultra-precise timing will be researched, feeding back into laser science.
  Free Electron Laser
  Betatron Radiation Source
  Positron Beams
  e+ / e- beams
  ICS Photon Beams
  High Rep. Rate Laser
  Laser Technology

## Slide 4: WP.15 Objectives, Milestones and Deliverables
April 2026
Feb. 2026
Nov. 2025

## Slide 5: The TDR structure
The Technical Design Report (TDR) for the EuPRAXIA@SPARC_LAB facility presents a comprehensive technical framework for the construction and the scientific exploitation as user facility.
The TDR is structured to:
Define the scientific and technological objectives of the facility
(Ch: Executive Summary, 1-3)
Outline the scientific use cases and user applications (Ch: 4)
Demonstrate feasibility through simulations and design studies (Ch: 5-6)
Deliver a technical description of all facility components (Ch: 7-23)
Establish technical readiness and assess potential risks (Ch: 24-25)
Support funding efforts and stakeholder engagement (Ch: 26)

## Slide 6: Introduction
The purpose of the EuPRAXIA@SPARC_LAB User Facility is to establish a research infrastructure that pioneers the use of plasma wakefield acceleration (PWFA) for driving a high-brightness Free-Electron Laser (FEL) in the soft X-ray regime.
Its first user beamline, AQUA, will deliver ultrashort femtosecond soft X-ray pulses within the biologically relevant “water window” spectrum, enabling real-time imaging, advanced materials development and investigation of chemical processes with unprecedented spatial and temporal resolution.
As one of the two core pillars of the pan-European Plasma Research Accelerator with eXcellence In Applications (EuPRAXIA) Research Infrastructure, EuPRAXIA@SPARC_LAB will be located at the INFN Frascati National Laboratories (LNF) and will serve a dual role as both a scientific instrument for users and a technological demonstrator. It will validate the integration of high-gradient plasma acceleration and X-band RF technology, into a user-grade light source, laying the groundwork for future compact user facilities. This will enhance their sustainability by significantly reducing the size, energy consumption, and operational costs typically associated with conventional accelerator-based light sources, making advanced photon science more accessible and environmentally responsible in the long term. The user facility is expected to begin operations in 2031.
By transitioning plasma-based accelerators from proof-of-concept to operational systems and validating them under real user facility conditions, EuPRAXIA@SPARC_LAB closes a critical gap in the technology readiness level (final TRL > 7) chain. This will position Europe at the forefront of global innovation in compact accelerators and strengthens its capacity to lead future high-energy physics, photon science, and interdisciplinary research programs. The inclusion in the ESFRI roadmap since 2021 marks the the strategic importance of the project at the European level.
The realization of the facility entails the construction of new buildings to host the accelerator systems, experimental halls, and support laboratories. This new infrastructure, to be built within the INFN LNF site, represents the project's first major challenge. From the outset, the design and construction will prioritize incorporating energy-efficient solutions, environmentally responsible materials, and infrastructure choices aligned with long-term ecological and operational resilience.

## Slide 7: FEL is a well established technology (But a widespread use of FEL is partially limited by its size and costs)
The choice of using a Free-Electron Laser (FEL) as the first application has been determined by the fact that FELs are extremely sensitive to the quality of the electron beam, making them an ideal testbed to demonstrate the capabilities of plasma-based accelerators. In addition a plasma-driven FEL is immediately attractive to a broad scientific user base, facilitating the transition from accelerator R&D to real-world applications and justifying further investment.

## Slide 8
EuPRAXIA@SPARC_LAB
S-band Injector
X-band Linac
Plasma module
Undulators
AQUA Beamline
ARIA Beamline
Photon beamlines
17.5 m
33.5 m
9 m
28.5 m
54 m
Plasma chamber: 3.5 m
Plasma capillary: 0.6 m

## Slide 9: The Italian Pillar: EuPRAXIA@SPARC_LAB User Facility
The facility aims to operate in two modes: a full-RF mode for initial commissioning, and a hybrid RF+PWFA mode that serves as a demonstrator for plasma-driven FELs user operation. Full-RF mode user operation is also possible.
The facility is expected to begin operations in 2031
•Moderate Energy with High Impact: Operating at around 1 GeV, will deliver Soft X-rays radiation in the “water window”.
•Compact Design: With an accelerating length shorter than 50 meters, it is the most compact facility in the soft X-rays list, at least by a factor 3.
•Technology Demonstrator: it will be also a strategic testbed for integrating advanced acceleration schemes and short period undulators into user-oriented FELs marking a paradigm shift toward compact and cost-effective light sources.

## Slide 10: The Italian Pillar: EuPRAXIA@SPARC_LAB User Facility
Facility | Location | Wavelength Range [nm] | Wavelength Range [nm] | Linac Length [km] | Electron Energy [GeV] | RF Band And Gradient [MV/m] | Key Features
Soft X-rays radiations |  |  |  |  |  |  | 
AQUA | Frascati, Italy | 4–10 |  | < 0.05 | 1.0 – 1.2 | X/Plasma 60/1000 | Compactness. Targets the water window; 3D bio-imaging.
FLASH | Hamburg, Germany | 4.1–45 |  | 0.2 | 1.25 | L 30 | Pioneering SASE FEL; test facility for RF Super-Conductivity and FEL technologies.
FERMI | Trieste, Italy | 10–100 |  | 0.15 | 1.67 | S 28 | Seeded FEL; high spectral purity in VUV–soft X-ray range.
Hard X-rays radiation |  |  |  |  |  |  | 
LCLS 1 | SLAC, USA | 0.13–6.2 |  | 1 | 14 | S 25 | First hard X-ray FEL; ultrafast imaging capabilities.
European XFEL | Hamburg, Germany | 0.05–4.7 |  | 2.1 | 17.5 | L 24 | High repetition rate; multiple beamlines.
SACLA | Harima, Japan | 0.06–0.2 |  | 0.4 | 8.5 | C 38 | More compact design; operates in hard X-ray regime.
SwissFEL | Villigen, Switzerland | 0.1–5.0 |  | 0.5 | 5.8 | C 28 | Two beamlines covering hard and soft X-rays.
PAL-XFEL | Pohang, South Korea | 0.06–4.5 |  | 0.78 | 10 | S 27 | Covers both hard and soft X-rays.
LCLS
LCLS-II
SACLA
SHINE
FLASH
E-XFEL
SwissFEL
FERMI
PAL
XFEL
EuPRAXIA

## Slide 11
EuPRAXIA@SPARC_LAB
365 m
1.7 GeV
Undulator hall
159 m
45 m
Accelerator hall
Experimental hall
Lasers clean rooms
Laser and particle user rooms
Klystron & power supplies hall
Technical rooms
Preparations labs
1 (=>2+) GeV

## Slide 12: Scientific Case and Applications
Application Area | Scientific Focus | Techniques | Key Impact
Renewable Energy | • Charge transport in solar cells & catalysts • Photocatalytic H₂ production • PFAS/PClAS analysis | XAS, XES, PI-MS | • Efficient solar materials • Clean hydrogen production • Environmental remediation
Warm Dense Matter (WDM) | • Extreme temperature/density • Astrophysics & fusion | Time-resolved XAS, TR-XES | • Stellar/planetary modeling • Fusion research support
Battery Technology | • Ion migration & interfaces • Solid-state battery study | XAS, non-linear X-ray spectroscopy | • Safer, longer-life batteries • High energy density
Structural Biology | • Live-cell imaging • Cellular processes (stress, DNA damage) | CDI, XAS, CEI | • Real-time biomolecular studies • Disease mechanism insight
Health & Radiobiology | • DNA damage by radiation | X-ray pump–probe, photo-fragmentation | • Radioprotection • Cancer treatment improvement
Atmospheric Chemistry | • VOC/NOx oxidation • Aerosol dynamics | PI-MS, ion spectroscopy | • Pollution models • Climate studies
Astrochemistry | • Radiation chemistry in space • Organic molecule formation | XAS, photochemistry | • Space molecular evolution

## Slide 13: Technological Readiness Level
Sub - systems | TRL | Comments |  |  |  |  |  |  | 
Injector | 9 | S-Band injectors are widely used in many facilities including SPARC_LAB. S-Band technology is fully available in the market. |  |  |  |  |  |  | 
X-Band Linac | 6 | X-Band Linacs are relatively new. Impressive progress has been made and the final testing of the acc. section full prototype will upscale the corresponding TRL level in the upcoming months. |  |  |  |  |  |  | 
Plasma Module | 5 | Extensive R&D has been made to validate the plasma capillary technology and solid results have proved the validity of the technical choice. A full system proven in a real environment is expected to be done in the next year |  |  |  |  |  |  | 
AQUA Undulators | 7 | Technology demonstrated in other facilities (FERMI, SwissFEL, etc.) |  |  |  |  |  |  | 
FEL Beamline | 8 | Most of the components of the photon beamline are implemented at other facilities are commercially available, few systems (needed only for a subset of possible experiments) are still in development |  |  |  |  |  |  | 
RF power system | 8 | X-Band RF power system has been already tested and operated in normal condition in the test-stand. The final operational test will prove the validity and reproducibility of the technical choices in the real setting |  |  |  |  |  |  | 
Laser system | 9 | Photocathode laser is now a proven technology tested in real facilities (including SPARC_LAB). The systems are full available in the market almost as off-the shelf products |  |  |  |  |  |  | 
General elements | 9 | Other elements (Control, mechanics etc) are based on standardized components daily used in other facilities and in other context (e.g. industrial context) |  |  |  |  |  |  | 
TRL LEVEL | TRL Description
TRL 1 | Basic principles observed – Scientific research begins to be translated into applied research and development (R&D).
TRL 2 | Technology concept formulated – The basic principles are explored and practical applications are identified.
TRL 3 | Experimental proof of concept – Active R&D is initiated, including analytical and laboratory studies to validate predictions.
TRL 4 | Technology validated in lab – Basic technological components are integrated to establish that they work together.
TRL 5 | Technology validated in relevant environment – The technology is tested in a simulated or relevant environment
TRL 6 | Technology demonstrated in relevant environment – A prototype system is tested in an environment similar to the operational one.
TRL 7 | System prototype demonstration in operational environment – A working prototype is demonstrated in a real operational setting.
TRL 8 | System complete and qualified – The technology is proven to work in its final form and under expected conditions.
TRL 9 | Actual system proven in operational environment – The technology is fully commercialized and operational in its intended setting.
Risk Mitigation: Two dedicated test facilities, SPARC_LAB and PLASMA_LAB, are actively supporting the development and validation of plasma acceleration concepts, while the TeX facility is dedicated to high power testing of X-band performance. Achieving a Technology Readiness Level (TRL) above 7 for these subsystems will only be possible following the successful operation of the EuPRAXIA@SPARC_LAB facility.

## Slide 14: X-band linac structures
Describe the X-band accelerating module we want to implement in terms of:
  RF structure design and parameters (electromagnetic design, cooling, etc.)
  Waveguide components (DC, pumping, etc.)
  Expected performance (RF, vacuum, etc.)
  Supports
  Parameters of the power sources (with reference to the dedicated chapter)
Magnetic chicane layout and main parameters.
Quadrupoles and diagnostics
D. Alesini, X-Band LINAC, 9° EUPRAXIA@SPARC_LAB TDR Review meeting, LNF 16-18 June 2025

## Slide 15: 1st X band full scale structure ready for high power test
D. Alesini, X-Band LINAC, 9° EUPRAXIA@SPARC_LAB TDR Review meeting, LNF 16-18 June 2025

## Slide 16: Plasma Accelerating Module

## Slide 17
Plasma Accelerating Module

## Slide 18: AQUA beamline: Undulators
 | Units | PWFA | Full RF
𝜌 (3D) |  | 0.77 | 1.49
Saturation length |  | 20.5 | 20.0
Radiation wavelength |  | 4.0 | 4.0
Photon Pulse Energy |  | 16 | 156
Photon per pulse |  | 3.2 | 31.3
Photon Bandwidth |  | 0.4 | 0.5
Photon pulse length (rms) | fs | 1.0 | 14.1
 | Units | PWFA | Full RF
𝜌 (3D) |  | 0.77 | 1.49
Saturation length |  | 20.5 | 20.0
Radiation wavelength |  | 4.0 | 4.0
Photon Pulse Energy |  | 16 | 156
Photon per pulse |  | 3.2 | 31.3
Photon Bandwidth |  | 0.4 | 0.5
Photon pulse length (rms) | fs | 1.0 | 14.1
10 Apple X undulators for SASE FEL in the water window with variable polarization

## Slide 19: AQUA Beamline: Photon Beamline
GDM
Mirror
Aperture
Spectrometer
Filters
Radial ion. chamber area
Monochromator area
Split & delay line area
Gas absorber
K-B mirrors
Exp. Chamber area
BPM
GDM
BPM
GDM
Filters

## Slide 20: The Building
The maximum expected power demand of the project, used for the electrical installation design, is about 2.8 MVA for all the site.
The expected power consumption for the AQUA operation at 100 Hz repetition rate, delivering up to 1.2 GeV electron beams is 1.32 MW
Electrical loads | kW
RF Modulators | 575
Magnet PSU | 360
Laser | 15
Experimental users | 10
Vacuum, electronics and controls | 30
Cooling magnet + RF | 180
HVAC | 150
Total Expected power consumption | 1320

## Slide 21: Project Cost, Timeline, and Management
As expected, the cost of the Plasma Module is significantly lower than that of the High Energy Line, almost one fifth, despite delivering the same energy gain, underscoring the economic advantage of plasma-based acceleration technologies in comparison to conventional radio-frequency systems.
The implementation timeline targets 2029 for building readiness and 2031 for minimum operational status, aligned with ESFRI Landmark designation requirements. EuAPS is expected to run as User Facility from 2026

## Slide 22: TDR Status and Plans
2025
June 20 - TDR first draft has been delivered for first review
October 21 – TDR Final version ready for evaluation
November 3-5 – Last TDR Review Committee Meeting
November (M36) - M15.3 Report on “R&D achievements supporting EuPRAXIA@SPARC_LAB technical design”
2026
February (M40) - M15.4 Report on the “Integration of EuPRAXIA@SPARC_LAB activities in the EuPRAXIA context”
April (M42) - D15.2 Report on “TDR status for EuPRAXIA@SPARC_LAB”

## Slide 23
Thanks for your attention

## Slide 24
Funded by the European Union
EuPRAXIA Scientific Goals
www.eupraxia-facility.org
Flagship Science Goal 2: EuPRAXIA will deliver betatron X rays with about 10^10 photons per pulse, up to 100 Hz repetition rate and an energy of 5-18 keV to users from the medical area. The much reduced longitudinal length of the X ray emission area (point-like emission) leads to an important improvement in image resolution compared to other techniques.
Flagship Science Goal 1: EuPRAXIA will deliver free-electron laser (FEL) X rays with 10^9-10^13 photons per pulse to user areas, covering wavelengths of 0.2 nm to 36 nm. The EuPRAXIA FEL pulses are naturally short (down to 0.4 fs) and will therefore provide users with tools for investigating processes and structures in ultra-fast photon science at a reduced facility foot print.
Flagship Science Goal 3: EuPRAXIA will deliver positron beams at energies from 0.5 MeV to 10 MeV and a repetition rate of 100 Hz for material science studies. Per pulse about 10^6 positrons will be produced in a time duration of 20-90 picoseconds on the sample, allowing time-resolved studies. EuPRAXIA will here advance the capabilities of existing positron sources in flux and time resolution.
Flagship Science Goal 4: EuPRAXIA will deliver electron and positron beams at energies from a few 100 MeV up to 5 GeV for high energy physics related R&D (detectors, linear collider topics). R&D goals include the demonstration of a linear collider stage, a "table top" HEP test beam and studies on positron transport and acceleration towards a linear collider.
Flagship Science Goal 5: EuPRAXIA will deliver photons from an inverse Compton scattering (ICS) source. The photons of up to 600 MeV and with narrow-band spectrum will enable precision nuclear physics and highly penetrative radiography for users.
Flagship Science Goal 6: EuPRAXIA will provide access to a multi-stage, high-repetition rate plasma accelerator in the GeV range to users from accelerator science. This R&D platform will allow the testing of novel ideas and concepts, full optimisation of a plasma collider stage, certain fixed target experiments (also in combination with lasers) and performance studies of conventional versus novel accelerator technology.
Flagship Science Goal 7: EuPRAXIA will provide access to cutting edge laser technology with short pulse length in combination with high energy photon pulses and short electron/positron bunches. Novel schemes of pump probe configurations and ultra-precise timing will be researched, feeding back into laser science.
  Free Electron Laser
  Betatron Radiation Source
  Positron Beams
  e+ / e- beams
  ICS Photon Beams
  High Rep. Rate Laser
  Laser Technology

## Slide 25: The pan-European EuPRAXIA Project
To match the dimensions of the plasma bubble—typically 100–300 µm in length and 10–30 µm in width—both the driver and witness beams must be significantly shorter and narrower than the plasma wavelength, while maintaining high charge densities. This demands beams of exceptional quality: ultrashort duration, low emittance, narrow energy spread, and high peak current. Achieving and maintaining these beam parameters represents one of the key technological challenges at the heart of the EuPRAXIA project.
The first EuPRAXIA User Site is under development at INFN- LNF in Italy. This site will host EuPRAXIA@SPARC_LAB, a plasma–beam-driven (PWFA) free-electron laser (FEL) user facility. The second User Site has recently been awarded to the ELI Beamlines facility in Dolní Břežany, Czech Republic, which will focus on the laser-driven (LWFA) branch of the project. Additional Nodes distributed across Europe will contribute to the two User Sites through R&D, component prototyping, training, and technical support.

## Slide 26: Achievements: Only referred to the X band accelerating module components
Sub - systems | TRL | Comments
X band Power Source | 6 | The nominal X-band power source has been acquired and is ready to be tested at TEX to reach the nominal parameters.
X band structure | 6 | The final full-scale prototype is ready to be tested. The tuning-free fabrication has been successfully completed, except for a relatively small detuning with respect to the nominal parameters (which can be corrected by setting the operating temperature to 18 °C). A 20-cell prototype has been successfully tested with uncompressed pulse at 50 Hz, 60 MV/m, reaching the nominal performance in terms of accelerating field.
Mode converter rectangular to Circular waveguide | 8 | Prototype fabricated and tested at 21 MW, 50 Hz, 1 us (nominal 25 MW, 100 Hz, 1.5 us).
Pumping unit circular waveguide | 8 | Prototype fabricated and tested at 21 MW, 50 Hz, 1 us (nominal 25 MW, 100 Hz, 1.5 us).
Pumping unit rectangular waveguide | 7 | Prototype tested at 45 MW, 1 us, uncompressed pulse, 50 Hz. Needs to be tested at 100 Hz with compressed pulse 70-35 MW, 0.13 us.
Directional coupler | 7 | Prototype tested at 45 MW, 1 us, uncompressed pulse, 50 Hz. Needs to be tested at 100 Hz with compressed pulse 70-35 MW, 0.13 us.
BOC pulse compressor | 6 | Device ready to be tested with the nominal power source now installed at TEX. Device already tested in other laboratories, but at reduced repetition rate and peak power.
3dB splitter | 6 | Fabricated but still to be tested at TEX at nominal full power. Already tested in other lab but at a reduced power.
Rf load | 8 | Fabricated and tested at nominal peak and average power (50 Hz, 0.6 us)
D. Alesini, X-Band LINAC, 9° EUPRAXIA@SPARC_LAB TDR Review meeting, LNF 16-18 June 2025

## Slide 27: Achievements: Technological Readiness Level (Sub-Components)
Sub - systems | TRL | Comments
Plasma chamber | 8 | Plasma chambers designed for differential pumping are widely used in many facilities, including SPARC_LAB. Actual system proven in operational environment (System complete and qualified – The technology is proven to work in its final form and under expected conditions)
Vacuum pumping system | 8 | Pumping systems appropriate to the gas quantities required for plasma formation in acceleration experiments have already been tested at the SPARC_LAB and other facilities.
HV source | 8 | The high voltage system to produce ionization of 60 cm long gas columns in thin capillaries has been fully designed and tested in the laboratory at the operating frequencies
Plasma source (Gas-filled capillary) | 5 | Extensive R&D has been made to validate the plasma capillary technology and solid results have proved the validity of the technical choice. A full system proven in a real environment is expected to be done in the next year
Magnetic separation | 5 | The separation chicane between the driver and witness in plasma accelerators has never been experimentally tested and, although it exists at the design level, it has not yet been technically implemented
Plasma Module | 5 | Extensive R&D has been made to validate the plasma capillary technology and solid results have proved the validity of the technical choice. A full system proven in a real environment is expected to be done in the next year (Technology validated in relevant environment – The technology is tested in a simulated or relevant environment)