## Slide 1: The EuAPS project: WP2
Alessandro Cianchi
University of Rome Tor Vergata
On behalf of the EuAPS collaboration

## Slide 2: Outline
Goal of WP2
Design of the source and the components
Status of installation of the facility
Open problems, critical aspects

## Slide 3: Betatron radiation emission
The radiation has its own characteristics of both FELs and synchrotrons
  Large bandwidth as Synchrotrons
  Short pulse duration like a FEL

## Slide 4: Expected Parameters
Parameter | Value | unit
Electron beam Energy | 100-500 | MeV
Plasma Density | 1017-1019 | cm-3
Photon Critical Energy | 1 -10 | keV
Number of Photons/pulse | 106-109 | 
Repetition rate | 1-5 | Hz
Beam divergence | 3-20 | mrad

## Slide 5: Possible applications
In order of increasing difficulty
1- Static imaging ​
2- Static absorption spectroscopy​
3- Static emission spectroscopy
​4- Time-resolved pump-probe absorption spectroscopy
​5- Time-resolved pump-probe emission spectroscopy​
6- Time resolved imaging (plasma dynamics).
Courtesy F. Stellato

## Slide 6: Budget
Chart: Hardware budget
| INFN-LNF | INFN-Mi | UTOV | CNR PZ | CNR Mt.Lib
 | 5673400 | 267000 | 400000 | 1000000 | 500000

## Slide 7: Where?
The source will be hosted at LNF-INFN
Several parts are realized at CNR (Photon Diagnostics) and at Tor Vergata (User end station)
INFN-Mi takes care of the simulation and data analysis
Activity | Where | Target
2.1 | INFN-Mi | Simulation & Data Analysis
2.2 | LNF-INFN | Plasma source
2.3 | LNF-INFN | Synchronization
2.4 | CNR-Potenza | Photon Diagnostics
2.5 | Tor Vergata | End user station
2.6 | CNR- Montelibretti | Photon time diagnostics

## Slide 8: Laser upgrade System 2.263.867,38 euro vat included
The upgrade of the pump lasers of the last FLAME amplifier with TITAN YAG, 20 J of pump energy at 532 nm at 5 Hz, with an almost flat-top single pump laser profile and energy stability — for each individual laser and for the amplified laser — of 1.2%. Power supplies and cooling units are also included.
The new optical compressor.
A set of optics for the existing compressor at FLAME (4 gratings, 2 rectangular mirrors for the retroreflector, and 2 flat mirrors for beam redirection toward the compressor output).
A set of Titanium-Sapphire crystals for the 3 FLAME amplifiers (a square crystal with 6 mm sides for MP1, a round crystal with a 16 mm diameter for MP2, and two square crystals with 50 mm sides for MP3).
Two periscopes for polarization change, with a height difference between input and output beam centers of 17 cm.
A half-wave plate with a 90 mm optical aperture and AR coating at 0° in the wavelength range between 700 and 900 nm, including the mount for polarization control inside the cleanroom.
A set of spare parts for the TITAN lasers, including a full set of flashlamps and filters, a two-channel power supply, a chiller, a pumping chamber for the oscillator and one for an amplifier, and a set of optics (two dichroic mirrors, a Pockels cell, and an LBO crystal).

## Slide 9: Laser Upgrade Front end 533.375,46 euro VAT included
Terra 527-50-M
Upgrade of existing Booster and Regenerative Amplifier to 100 Hz
Regenerative Amplifier optical kit
Saturable Absorber
Stretcher Grating
Terra and Inlite II integration kit
Dazzler HR 800
Mazzler
Single shot autocorrelator
Wizzler 800
Inlite II pump laser
Spectrometer
Hardware for Laser 4.0 HE upgrade

## Slide 10: Laser Upgrade Diagnostics and adaptive optic 173.240 euro VAT included
Wizzler 800
Deformable mirror
The total laser upgrade is 2.970.482,84 euro VAT included

## Slide 11: 2.293 keuro vs 2.970.842= 677.482
Laser oscillator (300k+66k)
Optics for laser focusing system (350k+77k)
Laser beamline diagnostics (50k+11k)
High intensity laser extraction system (200k+44k)
Ultra stable femtosecond laser for pump and probe (100k+22k)
New compressor for FLAME laser (optics+vacuum) (300k+66k)
Laser compressor near the interaction region (300k+66k)
Dazzler (100k+22k)
New Optical beamline(180k+40k)

## Slide 12: Design of the interation region
A dedicated gas Extraction System (ES) has been developed to ensure the pressure can be at the level of 10-4 mbar in the parabola at 1 meter of distance.
The supersonic gas jet, adopted for the experiments, is characterized by a divergent nozzle, with inner and outer diameters of 0.5 mm and 2.8 mm, respectively, and an angle of 14°.
The gas conveyor is located 6 mm above the nozzle with an aperture of 6 mm.

## Slide 13: Test bench for vacuum test
L. Crincoli, A. Biagioni
V. Lollo

## Slide 14: Results of the vacuum tests
L. Crincoli, A. Biagioni
V. Lollo
Notes: FRG=Full rage Pirani Penning
PG Pirani Gauge
TP Transition Pipe
IC Interaztion Chamber
ES Extraction system.

## Slide 15: Outline of the source
Our source is designed to operate in dual mode
In the FLAME bunker to perform R&D on the laser and components, and fine-tuning
In the SPARC bunker to give the beam to users
FLAME INFERNO
FLAME PARADISO
SPARC Bunker
S. Lauciani

## Slide 16: FLAME building and SPARC building
The distance between the two buildings is about 8 meters
SPARC bunker is shared with SPARC linac
The simultaneous use of two facilities in the same place obviously poses security and organizational problems
S. Lauciani

## Slide 17: Flame paradise
Laser is coming from laser room
There are two different paths:
  In one line, the beam is directed to FLAME hell uncompressed, to be delivered in the SPARC bunker
  In the second line, the beam is compressed and then sent to the FLAME INFERNO
S. Lauciani

## Slide 18: Installation progress
S. Lauciani, F. Fransesini

## Slide 19: FLAME Hell
There are two pipes that are coming from paradise, related to the Main and the Probe pulse.
If the beam must be used here, the Main is compressed; otherwise, not, and the beam is transported to the SPARC bunker
S. Lauciani

## Slide 20: Installation progress
S. Lauciani

## Slide 21: SPARC Bunker installation in progress
S. Lauciani

## Slide 22: inside the EuAPS@SPARCbunker interaction chamber
probe laser pulse for interferometry
main laser pulse
hexapod
dipole
gas extraction system
G. Costa, M. Zottola

## Slide 23
Tape driver
dipole stage
lanex plates for electrons
G. Costa, M. Zottola

## Slide 24: Tape driver issues
The hexapod has only relative movements and not absolute
This means that every time it does the home its movement can bring it to touch the tape driver
We need to evaluate the weight of the tape driver to see if it is possible to anchor it to the hexapod
Alternatively, we are studying another system in parallel

## Slide 25: Alternative solution
400 nm*100mm*100mm aluminum foil
In our case, we would be below the threshold if the aluminum is in front of the target (around 1.3 m) and with a 45° angle if the threshold is verified.
CON: It is really difficult to design a frame for a 400 nm of Al.
LIDT in different papers in the literature from 0.03 to 2 J/cm2
Paper 1 | https://www.researchgate.net/publication/260152592_Laser-induced_damage_thresholds_of_bulk_and_coating_optical_materials_at_1030_nm_500_fs/figures | 
Paper 2 | https://arxiv.org/pdf/2012.02574 | 
M. Galletti

## Slide 26: CHARACTERISATION CHAMBER CNR-ISM
P. Bolognesi, J. Chiarinelli

## Slide 27: Characterization chamber
It consists of three independent sections for pulse characterisation, shot-by-shot:
a/ Double slit chamber with four independent motorised slits with for current reading  1/ Beam shape definition
b/ Bellows for distance adjustment towards the main chamber
c/ Main chamber with motorised tool holder (linear and rotational degree of freedom) allocates 5 interchamber ‘characterisation tools’ . Currently:
YAG:Ce on Al metal ring (15 x 0.02 mm, 40 x 0.1 mm, 40 x 0.2 mm, chromium pattern 1x1 mm)
YAG:Ce on Al metal ring (40 x 0.2 mm with central hole dia. 3 mm, chromium pattern cel size 1x1 mm)
Faraday cup
Windows at +/- 40°, 90° with respect to beam for EM-CCD.  2/ Beam shape/stability/relative intensity distribution shot-by-shot
d/ Filter Chamber with motorised filter holder allocates 3 filters to position in front of X-Ray camera  3/ Caratterizzazione of the shot-by-shot spectral distributions.
  Currently available Al, Cu, Fe of different thickness
  X-Ray camera for ‘single photon counting’. Linear translator with 500mm drive
P. Bolognesi, J. Chiarinelli

## Slide 28
Side view
Each section of the characterisation setup can be used independently
of the others or together.
Removing the section will allow moving closer to the source.
1
2
3
4
5
6
1/ Double slits
2/ Bellows
3/ Main chamber
4/ Filter chamber.
5/ X-Ray camera
6/ Frame
P. Bolognesi, J. Chiarinelli

## Slide 29: Experimental chamber
This experimental chamber is built around the idea of allowing different kinds of experiments, starting from simpler and more rounded ones and ending with complex measurements in pump-probe mode.
We have designed the chamber as composed of three different modules: each one of them can be detached and used independently from the others or rearranged to accommodate complex optical geometry.
This will permit us to have the best possible chamber for each application (Imaging, Spectroscopy, pump-probe).
F. Galdenzi, V. Lollo

## Slide 30: Inside the chamber
1 - Linear stage XY, 25 mm travel range, 25 N load max, 133x35x20 mm size, 0,73 kg weight, stainless steel/aluminium.
2 - Rotary stage, 360° rotation, 0.125 Nm maximum torque, 50 N max load, ±20 mdeg accuracy, 0,7 kg weight, 194x90x70 mm size, Stainless Stee.
3 - Hexapod, ±17 mm travel range, 5 kg load capacity, Repeatability to ±0.06 µm, 2.2 kg weight, lower circular base 136 mm, higher circular base 100 mm, height 114 mm, stainless steel/aluminium
4 - Linear stage (z-direction, perpendicular to the ground), 40 mm travel range, 0,02 mm Spindle pitch, 0,05 µm resolution, 150 N max load, 0,3 Nm Min. Drive Torque, weight 7.5 kg, size 170x170x90 mm, aluminium.
Not Numbered - Custom-built sample holder, 200 g weight, 133x23,5x7 mm size (with angular step for bolts), stainless steel.
F. Galdenzi, V. Lollo

## Slide 31: Other open issues
Dipole design and construction require more than expected, mainly due to overlap with other activities
Authorizations to run the facility are under way but a clear estimation is not yet available
There are two main authorization processes, one for FLAME and the other for SPARC bunker.
The CCD-X camera in vacuum is not working yet

## Slide 32: Conclusions
WP2 is underway
The construction is mainly in the schedule, and we could foresee the first beam in early September, depending on the authorizations
Risk mitigation strategy:
  In case of having only FLAME authorization before the end of the project we will run a small pilot experiment in FLAME hell
  But this will impact CNR and Tor Vergata that deliver the main components for SPARC bunker.
  Other suggestions are more than welcome