## Slide 1: Phonon mediated Quantum sensors for Dark Matter
Rakshya Khatiwada
Illinois Institute of Technology & Fermilab
09/22/2025
Tenerife, Spain
View of North Atlantic Coastline from Roque de Taborno

## Slide 2
Quantum Technology
(for this talk)
Superconducting Qubit and its variants
2

## Slide 3: CosmiQ group
Started in 2020
IIT/Northwestern students/postdocs and Fermilab postdocs along with PIs
Above-ground and underground (low background) labs.
LOUD facility FNAL
QUIET facility FNAL
CosmiQ group FNAL/IIT/NW
3

## Slide 4: Ideal Quantum Detector for Dark Matter
Low energy threshold
Quantum non demolition measurement
No background coupling
Couples to only DM interaction mode
High precision
Fast response time
Scalable
Hard to get all of these in one detector!
4

## Slide 5: Superconducting Qubits
Qubits (artificial atoms) with customized energy levels.
qubit on a Sapphire substrate
4-Qubit device fab by Sara Sussman
Size: 1cm X 1 cm
Qubit
Readout
Resonator
Quadratic energy potential of a QHO reshaped by Josephson Inductance to a sinusoidal potential
qubit schematic
JJ: Non-linear
dissipation less
Inductor
Josephson Junction
Phase difference Φ
between the two
superconducting
(Cooper pair) wave functions

## Slide 6: How can we detect particles with qubits?
Qubit
dummy
4-Qubit device fab by Sara Sussman
Size: 1cm X 1 cm
JJ: nm
Qubit
Readout
Resonator
Substrate (Silicon or Sapphire)
Superconductor
(Al, Nb, Ta)
Insulator (Al2O3)
Josephson
Junction (JJ)
What kind of energy sensitivity can we get with Qubits?

## Slide 7: How can we detect particles with qubits?
Substrate (Silicon or Sapphire)
Superconductor
(Al, Nb, Ta)
Insulator (Al2O3)
Josephson
Junction (JJ)
Cooper pair
(paired
electrons)
Cooper pair breaking energy
(2Δ bandgap)
in the superconductor
governs energy scale!
(Al: 0.3 meV , Nb: 3 meV and Ta: 1.5 meV)
What kind of energy sensitivity can we get with Qubits?

## Slide 8: How can we detect particles with qubits?
Substrate (Silicon or Sapphire)
Superconductor
(Al, Nb, Ta)
Insulator (Al2O3)
Josephson
Junction (JJ)
Quasiparticles can tunnel through JJ
Individual tunneling event can be seen in
qubit readout
Broken
Cooper
Pair
(quasi-
particles)
Qubit Even and
Odd Parity
bands
odd
even
e-
What kind of energy sensitivity can we get with Qubits?

## Slide 9: There are many types of Qubit Readout!
1) Qubit Lifetime, T1
2) Qubit decoherence, T2 (Ramsey)
3) Charge Parity
3) Ramsey Tomography
f state
e state
g state
4) Spectroscopy
Kester Anyang, IIT
Cs-137 source
(Gamma: 661 keV)
f->h transition
Data Analysis in
progress
NEXUS
Increased
parity switching
rate (higher qp
tunneling)

## Slide 10: There are many types of Qubit Readout!
1) Qubit Lifetime, T1
2) Qubit decoherence, T2 (Ramsey)
3) Charge Parity
4) Spectroscopy
3) Ramsey Tomography
f state
e state
g state
Which one of these gives the best sensitivity to sub-eV energy?
Current resolution and threshold not enough.
Need background reduction to achieve better
sensitivity and resolution
READOUT

## Slide 11: Excess quasiparticles in Superconductor
Substrate (Silicon or Sapphire)
Superconductor
(Al, Nb, Ta)
Insulator (Al2O3)
Josephson
Junction (JJ)
Higher density of excess quasiparticles seen
in superconductor
What causes excess quasiparticles?
It impacts coherence times and sensitivity
Big fraction comes from pair breaking radiation
Broken
Cooper
Pair
(quasi-
Particles)
Nqp~5*10-10 normalized to Cooper pair density in best case
What kind of energy sensitivity can we get with Qubits?

## Slide 12: How do we couple DM particles to the qubits?

## Slide 13
Substrate (Sapphire)
Phonons (crystal
lattice vibrations)
Through phonons
10 - 100 meV
DM
DM
What kind of energy sensitivity can we get with Qubits?

## Slide 14
Substrate (Sapphire)
Phonons (crystal
lattice vibrations)
Through phonons: down-conversion
10 - 100 meV
DM
DM
down-converted phonons
What kind of energy sensitivity can we get with Qubits?

## Slide 15
Substrate (Sapphire)
Phonons (crystal
lattice vibrations)
Through phonons: simulation (G4CMP)
Phonon Caustic
in Sapphire (G4CMP)
phonon simulation in a 6-qubit silicon chip using G4CMP
Israel Hernandez, IIT
10 - 100 meV
DM
DM
QSC
Ziyu Cai, IIT
What kind of energy sensitivity can we get with Qubits?
CaWO4, LiF, GaAs, Al2O3, CaF2 + Superconductors: Al, Ta, Nb

## Slide 16: Through phonons: Device response simulation
Qubit Device
Rendering with
G4CMP
High phonon
collection efficiency
necessary
Limited Ground Plane
Meshed Ground Plane
Israel Hernandez
IIT
QUBIT
DESIGN
With T1 relaxation scheme and Si substrate,
Estimated Eth ~ 0.44 eV and resolution 88 meV
Expected to push this threshold lower with
Charge parity readout and Sapphire

## Slide 17
Substrate (Silicon or Sapphire)
Phonons (crystal
lattice vibrations)
Through phonons: Gap Engineering
Northwestern U.
10 - 100 meV
DM
DM
Low bandgap materials to amplify the
quasiparticle signal.
Instead of Al, use AlMn, Hf
GAP
ENG.
What kind of energy sensitivity can we get with Qubits?

## Slide 18
Substrate (Silicon or Sapphire)
Phonons (crystal
lattice vibrations)
Through phonons: Microphysical processes
10 - 100 meV
How does Energy transfer from Particle to Qubit?
Phonon production and down-conversion
Phonon-superconductor interface
Phonon-quasiparticle dynamics
Quasiparticle diffusion in the superconductor
Quasiparticle recombination
Ryan Linehan, FNAL
Israel Hernandez, IIT
DM
DM
QSC
Micro.
processes
What kind of energy sensitivity can we get with Qubits?

## Slide 19: Possible Dark Matter detector (Complete Picture)
Particle like DM can
excite phonons
in qubit substrates
EDM < MeV
Ephonon ~ 40 to 100 meV
Qubit readout
QuantiSED 2.0
Khatiwada
What kind of energy sensitivity can we get with Qubits?
~2 eV Photon source + 4 qubit transmon data taking in October

## Slide 20: Also a Neutrino detector? Coherent neutrino-nuclear scattering
Reduced Environmental contribution
to quasiparticles  better readout
and high sensitivity
CeνNS
Neutrino
Littlejohn + Khatiwada
IIT, U Chicago, FNAL, NU, UCSD
DARPA (QuSen)
Qubit readout
Nucleus
What kind of energy sensitivity can we get with Qubits?
Neutrino

## Slide 21: Qubit Environment (Environmental Engineering necessary)
Cryogenic and
Microwave
Engineering
+
Quantum Science
+
Material Science
+
AMO
Fermilab CosmiQ
dilution refrigerator
Schematic from Yasunobu Nakamura’s Talk
University of Tokyo, RIKEN

## Slide 22: Qubit Environment Engineering
Qubit Coherence as a function of shielding, filtering and thermalization improvements over 3 runs
ENV.
IIT, NU, FNAL
Run 4

## Slide 23: Photon Background reduction: Stub filter design
Based on Berkeley group’s design
Daniel Molenaar, IIT
Broadband background radiation
Suppression filter
IR radiation can pass through < 1 mm cracks!
Box mode and low frequency (4-8 GHz)
radiation can induce qubit decay/Purcell effect
IR absorptive shield (Stycast+Carbon)
HFSS simulation of radiation attenuation by stub filter
top flange
bottom flange
Top flange
bottom flange
5-stub filter
Qubit enclosure

## Slide 24
Dilemma of designing qubits:
Qubits good for sensing also couple to background easily
24

## Slide 25
Can we use higher qubit energy levels to sense the background ?
25

## Slide 26: Qudit f->h Spectroscopy for background sensing
26
Kester Anyang, IIT
Cs-137 source on a Al2O3-Ta
(𝜸: 661 keV), f->h transition
47 hours of source on + off data
Fitting of observed qubit Offset charge
Need higher statistics to resolve quantized charge states
Need to understand Sapphire-Tantalum interface physics
This was not visible
in g  e T1 measurement
Source On
https://journals.aps.org/prxquantum/pdf/10.1103/PRXQuantum.3.030307
x

## Slide 27: Understanding the qubit device
What’s Next?
Address most consequential issues:
Background reduction
Qubit Readout Optimization
Phonon Collection Efficiency
Substrate-superconductor microphysics
Prototype demonstration
Looooooooong way to go!
Possibly will need Machine Learning to tag DM events
high certainty on results unlikely without ML.
27

## Slide 28: Acknowledgement
This manuscript has been authored by Fermi Research Alliance, LLC under Contract No. DE-AC02-07CH11359 with the U.S. Department of Energy, Office of Science, Office of High Energy Physics.
DOE-OHEP-QuantiSED
This material is based upon work supported by the U.S. Department of Energy, Office of Science, National Quantum Information Science Research Centers, Quantum Science Center.

## Slide 29
Pairbreaking sensors: MKIDs, TESes, SNSPDs, QCDs, SC Qubits and variants etc.
Coherent wave sensors: JPA, TWPA, KIPA, Squeezed state receivers, microwave to optical transducers, SRF cavities, cavities, etc.
AMO (interferometry, NMR, Optomechanical) clocks sensors: Neutral atoms, trapped ions, magnetometers, spin precession, optomechanical devices, entangled probes etc.
Novel materials & Theory: Quantum and metamaterials, Low bandgap materials (Dirac, Weyl, Sapphire), High Tc materials, spin liquids, NV centers etc. New theories/ideas that can be tested with detectors, specific technology model building etc.
Quantum and Superconducting sensors
Quantum Sensor : Any new quantum device or technique that has the potential to achieve greater reach towards beyond-the-standard-model physics than that achievable through conventional techniques traditionally used in HEP.  Not just superposition and entanglement based. (source BRN)
Coordinating Panel for Advanced Detectors (CPAD)
QCD
array
SRF cavities
Spin ensemble
/NMR
Phonon in Sapphire

## Slide 30: Quantum Capacitance Detectors
Island
capacitively
coupled feedline
(amplitude of quantum capacitance
As a function of illumination)
Measured amplitude as a
Function of illumination

## Slide 31: Summary
Building Quantum Sensing program at FNAL/IIT
Aboveground and Underground facilities at FNAL provide complimentary platform for radiation/background studies in superconducting devices
Particle simulation tools (G4CMP) to understand energy dissipation in qubits and novel materials
Hope to gain knowledge on device sensitivity and ways to optimize them further for Dark Matter searches
Da
Khatiwada Group
Fermilab Postdocs
Ryan Linehan
Sara Sussman
Dylan Temples
Northwestern Students
Arianna H Colon Cesani
Grace Bratrud
UT Arlington
Olivia Seidel
Daniel Molenaar
Ziyu Cai
Noah Beaman
Undergraduate

## Slide 32: Particle like Dark Matter Search overview
Processes:
--DM Scattering off of nuclei
--DM Scattering off of electrons
*Fraction of DM Energy transferred to the
target material (nuclear, electron recoil)
Underground to avoid background like cosmic muon
--Absorption of DM
DM Energy absorbed by the target material
https://www.osti.gov/servlets/purl/1659757
Eg: Super-CDMS-SNOLAB, LZ (LUX-ZEPLIN)

## Slide 34: Interesting findings from Quantum Community

## Slide 35: T2 Ramsey
Ramsey and Spectroscopy in Qudit

## Slide 36: Interesting findings from Quantum Community
Cosmic muon and terrestrial gamma impacts
Qubits -> correlated error in quantum computers
Can we use low background setup to study this?
unexplained background (excess quasiparticles) observed in superconducting devices

## Slide 37: Quantum Capacitance Detectors for Ultralight Dark Matter
M. D. Shaw, J. Bueno, P. K. Day, C. M. Bradford, and P. M. Echternach, Phys. Rev. B 79, 144511 2009.
QuantiSED
Photon
Photon
Jialin Yu, IIT GS
Collaboration: Fermilab
Caltech/JPL, Wisconsin Madison
QCD
array
far infrared spectroscopic missions (space telescope) Caltech/JPL
NEP < 10-20 W/Sqrt Hz at 1.5 THz – most sensitive far IR detector!
Applications for > 100 GHz
https://journals.aps.org/prl/abstract/10.1103/PhysRevLett.128.131801

## Slide 38: Impact of cosmic and terrestrial radiation on quantum computers
https://arxiv.org/abs/2104.05219
Direct measurement on google processor
Non localized impact of radiation in qubit
(quasiparticle absorb qubit energy and cause
excited state to decay)
Suppressed T1 throughout the device
Mitigation: shielding, underground operation
quasiparticle and phonon traps being studied
100 keV to MeV
muon or 𝛄 absorption
phonon reservoir Si substrate
Phonons break cooper pair
quasiparticle tunnel to the junctions
qubit decoherence
𝛕 = 25 ms
event rate:
1/7.6 s &
1/38 s
Study context: Quantum Error Correction
Why should we care?
Building superconducting devices (qubit)
based experiment for DM
Need to decrease dark rate of available SPD
Hasn’t been studied in detail before
High energy radiation: source of quasiparticle in qubits

## Slide 39: Qubit based wave-like Dark Matter search
Qubit array
Qubit detector
Temperature
10 mK
readout
cavity
qubit
𝝲
𝝲
photons
excellent
photon
detector
mixed state
g ~ d.E:
Δ: ωq-ωc
g2/Δ: Stark shift
qubit
Cavity
Harmonic
Oscillator
two level system

## Slide 40: Qubit based photon counter
mixed state
g ~ d.E:
Δ: ωq-ωc
g2/Δ: Stark shift
qubit
Cavity
readout
cavity
qubit
nonlinear oscillator
𝝲
𝝲
counts photons!
Non absorptive
photon counting
Photon shifts qubit transition
Excite qubit at shifted frequency
Measure flipped qubit by monitoring
cavity line shift
Akash Dixit
U Chicago
two level system

## Slide 41: Near and long-term Dark Matter search
Need low energy threshold systems < 1 eV !
Source: Basic Research Needs (BRN)

## Slide 49: Signal and noise rate
DFSZ, 0.45 GeV/cc, B=14T, C=1/2, Q=5x104@1GHz, V=13𝜆3, crit.coup
Assumes axion detection bandwidth
∆f ~ MHz
N QND measurements dark rate =
(10-2)N ∆f
Sensitivity limited only by signal photon shot noise.
Aaron Chou

## Slide 51: MEMS mirror allows for desired operating specifications:
~1.5” x 1.5” scanning area
<100μm spot size
~10μm position resolution
O(100)Hz scanning speed
O(μs) pulse width
>10mK operating temperature
Focusing optics
Stationary mirror
MEMS mirror

## Slide 52: Nature of Dark Matter
For mass < 70 eV, Pauli exclusion principle causes dark matter clumps to swell up to be larger than the size of the smallest dwarf galaxies. (Randall, Scholtz, Unwin 2017)
Wave like DM
Particle like DM
Fermions: 1 DM particle per mode volume (𝝺deBroglie)3

## Slide 53: Axion production
Fig 1:J. Ellis et al; arxiv:1201.6045v1
Global symmetry broken at scale fa
-- axion produced through misalignment
mechanism
-- during QCD phase transition, trough
tilted by ΛQCD4
PE ~ΛQCD4 released, makes up dark matter
-- oscillation of the QCD θ angle about
its minimum--vacuum energy to axions
QCD axion mass ma~ΛQCD2/fa
~ (200 MeV)2/fa
--- fa unknown
GHz frequencies at fa~ 1013 GeV scale
PE ~ΛQCD4
Notes: ----- Meeting Notes (3/1/18 20:12) -----
Misalignment: at QCD phase transition (100 MeV) non-perturbative effects generate a mass and the axion field relaxes to its minimum (PQ mechanism)
----- Meeting Notes (3/10/18 13:19) -----
Lambda QCD?

## Slide 54: Axion searches overview
Graham, et. al (2016)
Notes: ----- Meeting Notes (3/8/18 16:28) -----
--10-12 eV QCD axion limit from fa exceeding Planck scale
--Hot dark matter limit comes from processes involving quarks and gluons that give rise to axion during QCD color confinement. Pion + Pion -> Pion + Axion
--Yellow: possible theoretical models based on Electromagnetic and Color Anomaly E/N ratio
--
--Telescope: If axions are present in galaxies then their decay photons would appear as spectral lines
----- Meeting Notes (3/10/18 14:42) -----
Massive stars: Photon+He4=He4+A
----- Meeting Notes (3/10/18 15:52) -----
Brokeheaven and University of Florida haloscope with just HFETs

## Slide 55: Axion searches overview contd.
Adapted from G.R, J. Phys. G (2017)
Analytic and lattice
predictions of the
axion mass, given it
makes 100%
Dark matter
ADMX G2 Range
Notes: ----- Meeting Notes (3/8/18 16:28) -----
Don't follow a single procedure or model
Calculate parameter like Topological susceptibility related to mass of the axion.

## Slide 56: Quantum amplifiers
JPA
Josephson Parametric
Amplifier
dc SQUID
Why quantum amps.?
Intrinsically low noise (superconducting technology)
low resistance elements
low thermal dissipation
Add very low added noise during
amplification
=> Tunable in frequency
Only limited by Quantum Noise
wpump
wsignal
widler
wpump
wsignal
JPA
⍵ modulated
through non-linear
Inductor LJ
Energy transfer from pump to
two normal modes of swing
Notes: ----- Meeting Notes (1/11/19 14:59) -----
Measurement of extremely small signals in precision measurement experiments requires very low noise amplifiers. Generally these noise levels are achieved by SQUID amplifiers that add very low noise to the system while amplifying the small signal. I will discuss two main technologies called the Microstrip SQUID Amplifiers (MSA)s and Josephson Parametric Amplifiers (JPA)s which are used broadly in radio frequency based experiments.

## Slide 57: What’s causing these dark counts?
Eliminated cosmic muon and radioactive background
from suspects since qp poisoning suppressed over
longer ~ a week cooldown period
Used similar device to charge parity device like QCD
Microfractures due to GE Varnish and mounting
glue on Si substrate causing phonon bursts breaking
cooper pair -> qp poisioning

## Slide 58: What is a qubit?
App. Phys. Rev., 6, 2, 10.1063 (2019).
Quadratic energy potential of QHO
reshaped by Josephson Inductance
to sinusoidal potential
--Superconducting Transmon and its variants can be utilized for Dark Matter detection through several mechanisms of coupling
Josephson
Junction
two level system
EJ ≫ EC
Ec= e2/2C charging energy
EJ = IcΦ0/2π Josephson energy
where Φ0 = h/2e magnetic flux quantum
Non-linear
dissipation less
circuit element
resonator
Josephson
junction
Qubit and resonator
circuit on a Si
substrate

## Slide 59
Pairbreaking sensors: MKIDs, TESes, SNSPDs, QCDs, SC Qubits and variants etc.
Coherent wave sensors: JPA, TWPA, KIPA, Squeezed state receivers, microwave to optical transducers, SRF cavities, rf quantum upconverters, mechanical tuning of cavities, etc.
AMO (interferometry, NMR, Optomechanical) clocks sensors: Neutral atoms, trapped ions, magnetometers, spin precession, optomechanical devices, optical-RF-magnetic levitation, cantilevers etc. entangled probes that beat SQL with optical readout etc.
Novel materials & Theory: Quantum and metamaterials, Low bandgap materials (Dirac, Weyl, Sapphire), High Tc materials, spin liquids, NV centers etc. New theories/ideas that can be tested with detectors, specific technology model building etc.
One of the largest CPAD RDCs
We base collaboration and R&D ideas from Basic Research Needs (BRN) and particularly, QIS for HEP workshop, 2023.

## Slide 60: Sapphire Phonon modes
Sinead Griffin, Simon Knapen, Tongyan Lin, and Kathryn M. Zurek, Phys. Rev. D 98, 115034 – Published 27 December 2018

## Slide 61: Fermilab Quantum Network (FQNET)
High-fidelity quantum teleportation
PRX QUANTUM 1, 020317 (2020)
Picosecond level entanglement distribution and clock synchronization EEE JQE 59,1-7 (2023) doi: 10.1109/JQE.2023.3240756
Towards a metropolitan scale quantum network
Teleportation of entanglement: entanglement swapping
Quick-Quantum Network (QICK-QN): https://arxiv.org/abs/2304.01190
Collaboration: FNAL, Argonne, Caltech, Northwestern University.
Illinois Express Quantum Network (IEQNET)
Hosts photonics and optical fiber based local quantum teleportation nodes, between Chicagoland institutions
 High fidelity quantum teleportation was
achieved between multiple nodes (50 km
apart) at Argonne and Fermilab (2022)
using entangled photons
Picosecond level entanglement distribution and clock synchronization between two nodes.
Step forward in building Quantum networking over metropolitan distances
QuantiSED

## Slide 62: Fermilab Quantum Network (FQNET)
High-fidelity quantum teleportation
PRX QUANTUM 1, 020317 (2020)
Picosecond level entanglement distribution and clock synchronization EEE JQE 59,1-7 (2023) doi: 10.1109/JQE.2023.3240756
Towards a metropolitan scale quantum network
Teleportation of entanglement: entanglement swapping
Quick-Quantum Network (QICK-QN): https://arxiv.org/abs/2304.01190
Collaboration: FNAL, Argonne, Caltech, Northwestern University.
Illinois Express Quantum Network (IEQNET)
Hosts photonics and optical fiber based local quantum teleportation nodes, between Chicagoland institutions
 High fidelity quantum teleportation was
achieved between multiple nodes (50 km
apart) at Argonne and Fermilab (2022)
using entangled photons
Picosecond level entanglement distribution and clock synchronization between two nodes.
Step forward in building Quantum networking over metropolitan distances
QuantiSED

## Slide 63: Dark Matter Detector R&D
Towards a metropolitan scale quantum network
SNSPD R&D for axion detection experiments Appl. Phys. Lett. 122, 243506 (2023)
Broadband Axion Antenna (BREAD)
and Superconducting Nanowire
Single Photon Detector for Dark Matter
QuantiSED
Island
far infrared spectroscopic
missions (space telescope)
Caltech/JPL
Photon => superconducting
absorber => broken Cooper
pairs => tunnel into a small
capacitive island => causes
non-equilibrium quasiparticle
population to increase
NEP < 10-20 W/Sqrt Hz
at 1.5 THz – most sensitive far IR detector!
Photon
Photon
Quantum
Capacitance
Time (s)
SNSPD
BREAD concept
Quantum Capacitance Detector (QCD)
Caltech, JPL, FNAL etc.
JPL, FNAL, IIT, Wisconsin

## Slide 64: Quantum Instrumentation Control Kit (QICK)
Primary support through QSC
Broadly used: >30 labs in the US and abroad
> 20 science talks in APS March meeting!
(1.3.3.02)
AMD-RFSoC ZCU111 +QICK custom RF/DC amplifiers, bias
AMD-RFSoC ZCU216
QICK custom RF/DC amplifiers, bias under design
16 DAC outputs from DC to 10GHz all digital mixers.
  This is critical need for quantum. => Better experiments.
  Minimizes calibrations.
16 ADC inputs from DC to near 10GHz without analog mixers.
  Input noise 120K (i.e. 1.2dB)
8 x 20-bit DAC outputs for bias (BW of 10 or 100Hz) ultra low noise, ±10V outputs.
<200ns latency for error correction (fastest in the market).
Optimal filtering, no dead-time 3ns pulses.
100 pico-second pulses for QN.
Accurate timing readout 2ps resolution.
RF multiplexing of 10K detectors per board.

## Slide 65: Excess quasiparticle density