## Slide 1: Detectors for Nuclear Astrophysics in the LUNA collaboration
G.F. Ciani on behalf of LUNA collaboration INFN Bari
Perspectives at the Bellotti IBF 8-10 October 2025 Laboratori Nazionali del Gran Sasso

## Slide 2
TYPICAL EXPERIMENTAL SETUP IN NUCLEAR ASTROPHYSICS
Accelerator
High performance detector: - low intrinsic background
High efficiency
High energy resolution
HIGH DENSITY
AND STABILITY TARGET
REACTION PRODUCTS
a, p, n, g
Intense current beams
MY TURN!!!

## Slide 3
CNO Cycle 14N(p,g)15O
Carbon Burning
  12C+12C reactions
  Neutron capture nucleosynthesis 22Ne(α,n)25Mg 22Ne(α, g)26Mg
solar fusion reactions
3He(3He,2p)4He 2H(p,g)3He 3He(α,g)7Be
electron screening and stopping power
2H(3He,p)4He 3He(2H,p)4He
CNO, Ne-Na and Mg-Al cycles
14N(p,g)15O 15N(p,g)16O 22Ne(p,g)23Na 22Ne(α,g)26Mg
23Na(p,g)24Mg 25Mg(p,g)26Al 12C(p,g)13N 13C(p,g)14N
21Ne(p,g)22Na 20Ne(p,g)21Na 23Na(p,a)20Ne
Explosive hydrogen burning in novae and AGB stars
17O(p,g)18F 17O(p,α)14N 18O(p,g)19F 18O(p,α)15N
Big Bang nucleosynthesis
2H(α,g)6Li 2H(p,g)3He 6Li(p,g)7Be 6Li(p,a)3He
neutron capture nucleosynthesis
13C(α,n)16O
Over 30 year of Nuclear Astrophysics at LUNA (LNGS, INFN) and beyond
LUNA program @ IBF facility 2023-2027

## Slide 4: DETECTOR USED AT LUNA FOR..
g-rays
HPGe, BGO, NaI
Charged particles
Silicon detector array
Neutrons
He3 counters and scintillators
Main features:
- As high as possible efficiency, validated with Monte Carlo
Good characterization in terms of energy calibration and resolution
Intrinsic background minimized or under control

## Slide 5: CHARGED PARTICLE DETECTORS
«In order to suppress the background we had to use a new detector set-up, which consists of eight thick (1 mm) silicon detectors of 5x5 cm2 area placed around the beam. They form a 12 cm long parallelepiped in the target chamber, at 5.3 cm from its entrance»
Phys. Rev. Lett. 82, 5205 – Published 28 June, 1999

## Slide 6: CHARGED PARTICLE DETECTORS
Implanted Planar Silicon detectors (PIPS, active area 9 cm2 each; 5 with 300 μm +3 with 700μm thickness;
Arranged in two rows, at 135.0° and 102.5°.
In order to protect the detectors from the large flux
of elastically scattered protons, aluminised Mylar foils of about 2 mm thickness were mounted on the
inner copper dome
Efficiency of about 10% (simulation validated with a source)

## Slide 7: A NEW CHARGED PARTICLE DETECTOR (2025)
A new beamline dedicated to the detection of charged-particles has been installed at LUNA400@LNGS, supported by ELDAR (burning questions on the origin of the Elements in the Lives and Deaths of stARs) UKRI-ERC StG with an in kind contribution
3 MSPADs (nTDs,
4 channels each)
24 HAMAMATSU
PHOTODIODES
≃15% geometric efficiency from Geant4 simulation
Energy resolution: 16-20 keV @
Larger number of channels with respect to the previous setup
Higher sensibility to angular distribution
Temperatures of detectors around 42°C thanks to preamplifiers’ cooling system and dome being kept at liquid nitrogen temperature.
Reading of both sides of Silicon will reduce the background
SILVER DOME WITH ALUMINIZED MYLAR FOILS TO STOP SCATTERED BEAM PROTONS
Credits: C.Bruno & Lucia Barbieri

## Slide 8: NEUTRON DETECTION
4th October 2017
10 atm pressurised 3He counters with a stainless steel case
Intrinsic efficiency for slow neutrons > 90%
Low intrinsic background (a particles source of intrinsic background from U and Th impurities in the counters’ case)

## Slide 9
Array of 18 3He counters
arranged in 2 rings (r1 = 6 cm, r2=11 cm)
6 inner counters L=25 cm
12 outer counters L= 40 cm
Polyethilene as moderator (<En>=2.5 MeV)
External shielding of BPE (1 inch)
Background (n+a):3.3 counts/h in the ROI Efficiency Curve: simulated and validated with 51V(p,n)51Cr reaction at ATOMKI
Good point: PE cheap and easy to machine: the moderator and the setup can be easily optimised for specific occasions and for other measurements
Weak point: cannot measure the neutron energy because of moderation

## Slide 10: FAST NEUTRON DETECTORS
DETECTION «STRATEGY»
Hybrid detector array: 18 3He counters combined with 12 liquid scintillator EJ-309 in the SHADES experiment for the measurement of the 22Ne(a,n)25Mg reaction.
The EJ-309 provides energy, timing, and tagging information for the neutron, and the counters provide a measure of the number of neutrons thermalised in the system.
Credits of the plot: JINA-CEE
BIB REDUCTION APPROACH
Lowest detectable neutron energy in scintillator is 163 keV Characterization of a prototype indicates a coincidence time of 3-7 ms providing a suppression factor of 48% from background neutrons entering the counters
Use anticoincidence to select neutrons of the reaction from BIB
Notes: The EJ-309 provides energy,
timing, and tagging information for the neutron, and the counters provide a measure of the
number of neutrons thermalised in the system

## Slide 11
FAST NEUTRON DETECTORS: characterization
Low Beam induced background after
OFHC collimator + nitric acid bath
Deviation from experimental data by approximately 15%, likely due to inaccuracies in the thermal scattering cross sections used in Geant4
PRELIMINARY
Credits: A. Best & D. Mercogliano

## Slide 12: HIGH RESOLUTION g-rays PARTICLES DETECTORS
Array of HPGe detectors available also for angular distribution measurements.
Coupled wit Cryocooler to avoid operation of refilling and favor long measurements
Complex cascades request high resolution to distinguish all the g-rays emitted.
A recent example is the measurement of the 14N(p,g)15O reaction at IBF
 | Relative efficiency | FWHM at 1.33 MeV
HPGeBochum Camberra | 120% | ~2 keV
HPGe Genova Ametek | 120% | ~2 keV
HPGeDresda Camberra | 60% | ~2 keV
605 keV
1260 keV

## Slide 13: HIGH RESOLUTION g-rays PARTICLES DETECTORS
 | Relative efficiency | FWHM at 1.33 MeV
HPGe Pd 2 Ametek | 157% | 2.1 keV
30 l dewar for measurements longer thatn 10 days
 | Background rate [200-2700 keV]
unshielded | 6 034 800 (900) cpd
Lead+Cu | 4176(15) cpd
Lead+Cu+ N2 flushing | 3416(10) cpd
Proton and alpha channels of the 12C+12C reaction emit g-rays at 440 keV and 1634 keV, respectively. These signatures can be hampered by natural background.

## Slide 14: HIGH EFFICIENCY g-rays PARTICLES DETECTORS
Bismuth Germanate Oxide detector
Optimal solution for reactions with high Q-value
6 optically independent segments, each of them read out by one photomultiplier tube (Total Absorbtion Spectroscopy).
For each signal in each cystal, energy and timestamp are saved
Brass holder + steel chamber
Al holder+ Al chamber
steel chamber
Proper shielding and proper coupling with target holder for maximization of background reduction and efficiency

## Slide 15
Add-Back:By adding the energy of «coincident» events (Dt<35 ms) in the individual crystals, a total energy (sum, or add-back) spectrum can be obtained, while the energy deposition in the individual crystals allows to infer information on the individual g-rays emitted in the cascades
Coincidence analysis with the BGO setup
In spectrum 1  1 event of E1
In spectrum 3  1 event of E2
In the post processing sum spectrum  1 event of E1+E2 (Q+Ep,cm )
5.67
1.08
17O+p
Q = 5.6 MeV
5.56 MeV
0 MeV
g3
D+p
Q = 5.5 MeV

## Slide 16
β+ reaction products decay by emission of e+ particles,
annihilate with an e−.
The 511 keV γ-rays created in e+e− annihilation are emitted in opposite directions from the point of annihilation.
Because of the BGO segmentation and 4π geometry, this translates to a coincident detection
of two 511 keV signals in opposite crystals
Counting the number of nuclei produced in the reaction by detecting the 511 keV g-rays created in the e+e− annihilation following their decay is a form of
activation method
Coincidence analysis with the BGO setup

## Slide 17: g-rays PARTICLES DETECTORS
High efficiency detectors
NaI detectors: 109x109x254 mm each, coupled to a SiPM

## Slide 18: NaI APPLICATION
Detectors for Compton Veto
NaI(Tl) detector as a veto detector within the upcoming campaign. When g-rays stemming from these contaminations within the NaI(Tl) detector deposit energy in GePD2, their associated α and β particles
from the respective decay are expected to also induce
a signal in the NaI(Tl) detector and are therefore
automatically vetoed out
Array of 6 NaI for the measurement of the 22Ne(a,g)26Mg reaction in the framework of the Easy experiment starting from next year

## Slide 19: SIMLUNA mainly developed by Z. Elekes (ATOMKI)
Geant4-based simulation code including different setup used by LUNA collaboration

## Slide 20: LunaDAQ mainly developed by J. Skowroński and A. Compagnucci
This system integrates real-time data collection, analysis, and FAIR-compliant metadata management in a user-friendly web interface
Key Capabilities
Real-time Data Acquisition from multiple detector channels
Interactive Visualization of spectra and waveforms
FAIR Metadata Management for experimental runs
Secure User Authentication with role-based access
Dockerized Analysis Pipeline with XDAQ integration

## Slide 21: RECENT PAPERS ON DETECTORS (AND MORE WILL COME!!)
«Resonance strengths in the 17,18O(p,α)14,15N reactions and background suppression underground» Bruno et al Eur. Phys. J. A (2015) 51: 94
«Characterization of the LUNA neutron detector array for the measurement of the 13C(a,n)16O reaction», Csedreki et al Nuclear Inst. and Methods in Physics Research, A 994 (2021) 165081
«A prototype neutron-detector array for future deep- underground s-process studies», Chillery et al J. Phys. G: Nucl. Part. Phys. 52 075202 (2025)
«Advances in radiative capture studies at LUNA with a segmented BGO detector» Skowronski Et Al J. Phys. G: Nucl. Part. Phys. 50 045201 (2023)
«Detectors and Shieldings: Past and Future at LUNA», Ananna Et Al Universe 2024, 10(5), 228
«Detector characterization for a new 12C+12C reaction study at LUNA», Gesuè et al, J. Phys. G: Nucl. Part. Phys. 105296 (2025)
«Towards a comprehensive study of the 14N(p,g)15O astrophysical key reaction: Description of the experimental technique including novel target preparation», Compagnucci et al Eur. Phys. J. A (2025) 61:191

## Slide 22: WHAT’S NEXT?
Combine gamma detector and charged particle detector for the 12C+12C reaction and further reduce the background
Double the number of channels of the BGO detector
Thanks to the long and wide experience acquired with detectors, LUNA collaboration is ready to effort new challenges in Nuclear Astrophysics (and maybe more?!?!)

## Slide 23
THANK YOU FOR THE ATTENTION