## Slide 1: ASPIDES meeting 2
Tommaso Floris
21/03/2025

## Slide 2: Functions of the dSiPM
Count the number of photons
  parallel counter
Identify the ToA of the first and last photons
  two TDCs and the ANDtree
Reject spurious events
  time over threshold detector with programmable threshold
Possibility to enable and disable the single pixel
  memory element inside each pixel
Global signal to reset and enable the array

## Slide 3: Overall floorplan
ARRAY
TDCs
AND tree
Parallel
Counter (PC)
Last stages of ANDtree and PC
Threshold detector

## Slide 4: 2x2 pixel cluster
Pixels organized in 2x2 clusters represent the basic building macro for the matrix
Frontend
SPAD region
Routing region
Digital logic region (dSiPM)

## Slide 5: 2x2 pixel cluster
The pixel are organized in 2x2 cluster and represents the basic building macro for the matrix
Frontend
SPAD region
Routing region
Digital logic region (dSiPM)
FF = 48 %

## Slide 6: Array floorplan detail
In the final array there will be 16 rows of 16 2x2 cluster

## Slide 7: SPAD frontend

## Slide 8: AND tree
All input stimulated simultaneously
Changing the pulse width of the input signals

## Slide 9: AND tree
One input at a time stimulated with a pulse signal
Looking at how the pulse width changes

## Slide 10: AND tree
One input at a time stimulated with a pulse signal
Looking at how the pulse width changes

## Slide 11: AND tree
All input stimulated simultaneously performing a transient noise analysis
Looking at how the pulse width changes

## Slide 12: AND tree
All input stimulated simultaneously performing a transient noise analysis
Looking at how the pulse width changes

## Slide 13: AND tree performance
 | AND2 | AND4 | ANDH
Rising delay | 640,8 ps | 412,2 ps | 506,7 ps
Rising delay (Std Dev) | 12,05 ps + 23,01 fs | 14,35 ps + 10,64 fs | 13,91 ps + 20,06 fs
Falling delay | 754,2 ps | 679 ps | 725,8 ps
Falling delay (Std Dev) | 10,43 ps + 46,12 fs | 28,77 ps + 83,93 fs | 23,19 ps + 53,85 fs
Pulse width (Std Dev) | 1,784 ps + 51 fs | 14,83 ps + 84,35 fs | 10,65 ps + 57,15 fs