## Slide 1: Kaonic atoms at DAΦNE with HPGe detector
Damir Bosnar
Department of Physics, University of Zagreb, Zagreb, Croatia
Motivation: the charged kaon mass, positions of transitions lines in heavy
kaonic atoms, ideas in Luca’s talk, …
Preparations and measurements at DAɸNE during SIDDHARTA-2 runs
Some results and problems
Outlook
* Croatian Science Foundation
Project IP-2022-10-3878
* STRONG-2020 (GA ID 824093)
Workshop on Fundamental Physics with Exotic Atoms, LNF, 23.06.-25.06.2025

## Slide 2: Motivation – the charged kaon mass
The accuracy of the determination of the charged kaon mass (mK=493.677±0.016 MeV, 32 p.p.m.) is much less than the accuracy of the charged pion mass (mπ=139. 57061±0.00023 MeV, 1.6 p.p.m.), PDG2022.
Serious disagreement between the two precise measurements
->Large scaling factor: S=2.8
Kaon mass has large influence on the K-N scattering lengths and through them on the kaon-nucleon sigma terms and eventually degree of chiral symmetry breaking.
Kaonic atoms, charmed mesons, searches beyond standard model.

## Slide 3: PDG 2022:
PDG2020
The main disagreement is between the two most recent and precise measurements (x-ray energies from kaonic atoms):
mK=493.696±0.007 MeV
A.S. Denisov et al. JEPT Lett. 54 (1991)558
K- 12C, crystal diffraction spectrometer
(6.3 eV at 22.1 keV), 4f-3d
Average mK=493.679 ± 0.006 MeV S=2.8
mK=493.636±0.011 MeV
K.P. Gall et al. Phys. Rev. Lett. 60 (1988)186
K- Pb, K- W; HPGe detector (1 keV), K-Pb (9 -> 8),
K-Pb (11 -> 10), K-W (9 -> 8), K-W (11 -> 10),
mK=493.677 ± 0.016 MeV

## Slide 4: Previous measurements, motivation
PDG2022:
” While we suspect that the GALL 88 K− Pb (9 ->8) measurements could be the problem, we are unable to find clear grounds for rejecting it. Therefore, we retain their measurement in the average and accept the large scale factor until further information can be obtained from new measurements and/or from reanalysis of GALL 88 and CHENG 75 data”.
PDG conclusion:
It is sufficient that the new measurement has the same precision (10 keV) as the 2 previously mentioned measurements, which differ by 60 keV (PLB535 (2002)52):
-if the new result agrees with Denisov (and results from Gall are disregarded) the precision would be 5 keV (10 p.p.m)
-it the new results agrees with Gall, the precision would be 7 keV (14 p.p.m.)
-> substantial improvement in the precision

## Slide 5: Principles of measurements of kaon mass in kaonic atoms
Measure X-ray energies in kaonic atoms for transitions not influenced by strong interactions.
In order to determine the kaon mass, measured energies have to be compared with the calculated energies obtained with a certain K-mass value (corrections: vacuum polarization, electron screening, non-circular trasitions)
Measurements with HPGe detectors and with crystal diffraction spectrometer, TES, …

## Slide 6: Measurements of kaon mass, history
Q value K-->π++π-+π-
W.H. Barkas, Annu. Rev. Nuclear Sci. 15 (1965) 67 mK=493.75+0.16 MeV
Range measurements in emulsions
(A. Barbaro-Galtieri et al., Revs. Mod. Phys. 42 (1970) 87, mK=493.7+0.3 MeV;
L.M. Barkov et al. Nucl. Phys. B148 (1979) 53 (ɸ->K+K-)) mK=493.670+0.029 MeV
Energies of X-ray transitions in kaonic atoms, mK=493.677 ± 0.016 MeV
all with energetic kaons (PDG2022)

## Slide 7: Principles of measurements of kaon mass in kaonic atoms: X-ray energies in kaonic atoms
K-
e-
1) Kaon capture
2) Kaon cascade
3) Kaon absorption
X-ray
Interesting are X-rays from
the transitions in the middle
of cascading spectrum:
No influence from strong
interaction
avoid electron screening
of nuclei
->advantage – heavy atoms
Measurements with: HPGe detectors
crystal diffraction spectrometer, TES,…
Measured energies have to be compared with the calculated energies obtained with a certain K-mass value (corrections: vacuum polarization, electron screening, non-circular…

## Slide 8: Motivation: Precise determination of transition lines in heavy kaonic atoms

## Slide 9: SIDDHARTA-2 at DAɸNE Silicon Drift Detector for Hadronic Atom Research by Timing Application
SIDDHARTA-2 run: X-ray transitions in gaseous targets: deuterium, helium, …
DAɸNE:
e++e--- -> ɸ -> K+K-, EK ≈ 16 MeV
-> We performed a feasibility measurement with an HPGe detector during SIDDHARTA-2 run at DAɸNE - using the available space at the SIDDHARTA-2 interaction region and with a Pb target
Advantage: DAɸNE is producing low momenta kaon pairs – no need for degrader. No secondary hadronic particles in the beam.
Disadvantage: High background from the beam close to the interaction point (unknown!).
In both cases: background originating from the kaons absorbed in nuclei, GEANT4 simulations indicate it is acceptable

## Slide 10: Measurement at DAɸNE with HPGe during SIDDHARTA-2 run
Signal from the luminometer
(80x40x2 mm3) as a trigger
for HPGe detector.
Positions of the target
and the HPGe detector
is restricted by
SIDDHARTA-2 setup
Interaction point
Measurement of transit times
of the particles from IP to the
scintillator.
133Ba source for the calibration and monitoring of
the HPGe resolution.

## Slide 11: Measurement at DAɸNE with HPGe during SIDDHARTA-2
BSI HPGe detector with
transistor reset preamplifier (TRP)
HPGe active detector diameter ~60 mm, height ~60 mm.
(Analog electronics) and fast pulse digitizer.

## Slide 12: Laboratory tests of HPGe (BSI - TRP preamp) & analog electronics
CAEN spectroscopy amplifier N968, Canberra
Multiport II, Canberra Genius DAQ + analysis
60Co, 133Ba spectra,
resolutions: 0.870 keV at 81 keV
1.06 keV at 302.9 keV
1.11 keV at 356 keV
1.67 keV at 1330 keV
Pb lines
Signal from spectroscopy amplifier
Stability tests
Signal from preamp of HPGe with TRP

## Slide 13: Laboratory tests of HPGe (BSI - TRP preamp) & fast pulse digitizer, CAEN DT5781 4 ch, 14 bit,
Signal from spectroscopy amplifier ~20 μs (shaping time 6 μs),
restriction on the rate.
CAEN DT5781 4 ch, 14 bit, 10ns sampling time
Signal from HPGe with RC preamp
Signal from preamp of HPGe with TRP
Possible rates up to 150 kHz, something worse resolution
Digital Pulse Processing for Pulse Height Analysis firmware , based on
V.T. Jordanov et al. Nucl. Instr. Meth. A 353
(1994) 337
Coincidences – HPGe + luminometer

## Slide 14: Adjustment of the parameters for energy reconstruction
V.T. Jordanov et al. Nucl. Instr. Meth. A 353 (1994) 337
Resolution 1.3 keV at 302.9 keV
(1.06 keV with analog electronics)

## Slide 15: HPGe in the DAΦNE hall

## Slide 16: Simulations – GEANT4
To estimate the thickness of the target, setup configuration and HPGe efficiency.
To estimate background – from the kaon absorption and to determine optimal position of the detector and target and shielding .
To estimate required time for the measurements.
Not all parameters are known: beam background !? – test measurements with the beam are required.

## Slide 17: HPGe detector on d=110mm from the Pb target (closest position), 400 pb^-1
X-rays from Pb, in the peak at 291.6 keV there are approx 9.144 X-rays (yield 20%).
Approx. 9.000 X-rays in the 291.6 keV are needed for the required precisison
Only hadronic background, peaks are smeared with the detector resolution.

## Slide 18: GEANT4 “full” simulation
CAD drawing
GEANT4 simulation
CAD files for selected objects are converted in GEANT4 gdml files for geometry description,
different materials are taken into account
Kaons are generated uniformly in 4π
Only hadronic background., no background from e+e- beams

## Slide 19: GEANT4 “full” simulation
In principle, electromagnetic background should not have influence on this spectra
(coincidence luminometer + HPGe), but it can lead to pile-ups in the HPGe
Electromagnetic background ? -> Measurements in the hall

## Slide 20: Estimation of the requested number of X-rays in the peak (Pb, 9->8 transition,291 keV)
Estimation: A. Scordo
precision(trans.)
FWHM(302.9 keV)=1.1 keV -1.3 keV (depending on the
rate)
N≈6.000-9.000 X-rays in the peak (291.6 kEV)
to reach the precision of previous
measurements (10 keV).

## Slide 21: GEANT4 “full” simulation
Approx. 50 events (291.6 keV) / pb-1,
10 pb-1 /day -> approx. 500 events/day.
~9.000 events -> 10 keV precision (18 days)
~25.000 events-> 5 keV precision (50 days)

## Slide 22: Measurement at DAɸNE with HPGe during SIDDHARTA-2 run, 2023
Signal from the luminometer
(80x40x2 mm3) as a trigger
for HPGe detector.
+
Transit times from IP to luminometer
Positions of the target
and the HPGe detector
is restricted by
SIDDHARTA-2 setup
Interaction point

## Slide 23: Schematic representation of electronics: -HPGe trigger -transit times from IP to SC1

## Slide 24: Spectrum of 133Ba, without beam
Resolution at 302.9 keV = 4.39 keV
(close to (9->8) line in kaonic lead)
precision(trans.)

## Slide 25: Coincidences: HPGe, Luminometer and RF
Integral luminosity ~39.4 pb-1

## Slide 26: Cut on time correlations
Time correlation between signals in SC1 and HPGE
(time resolution of the digitizer is 10 ns)

## Slide 27: Transit times of particles from IP to the luminometer
2.7ns

## Slide 28: The spectrum in the HPGe – all cuts
Resolution at 292.47 keV – 3.92 keV (with 133Ba at 302.8 keV without beam – 4.39 keV).
No worsening of the resolution in the full beam conditions!

## Slide 29: Estimation of the time of measurement for the desired accuracy of 10 keV
Integral luminosity ~39.4 pb-1
Line (9->8): Integral luminosity 435 pb-1 (assumed resolution of 1.3 keV)
Clearly visible lines (10->9) and (8->7) which can also be used to additionally improve
the accuracy of the charged kaon mass.

## Slide 31: Complete analysis of all „good” data
Precision worse than in published data
Problems with calibration
Additional analysis ongoing
NIM data

## Slide 32: Conclusions
We can successfully reduce the background (originating
from the beams).
There is no worsening of the HPGe resolution in the full
beam conditions.
The estimated time of the measurement to reach the
desired accuracy is realistic.
There can be measured some transitions (e.g. 8->7)
in kaonic lead with better precision.
HPGe detector ???

## Slide 33: Thank you for your attention !

## Slide 34: Backup slides

## Slide 35: Estimation of the requested number of X-rays in the peak (Pb, 9->8 transition,291 keV)
Estimation: A. Scordo
precision(trans.)
FWHM(302.9 keV)=1.1 keV -1.3 keV (depending on the
rate)
N≈6.000-9.000 X-rays in the peak (291.6 kEV)
to reach the precision of previous
measurements (10 keV).