## Slide 1: MMX17 Multiplex Micromegas for X17 experiment

## Slide 2: Needs: ~ tracker
Detector specification
  Active area: 400 x 400 mm²
    0,78 pitch pixel connected in X and Y strip
    512 X and 512 Y strip
  Spatial resolution X and Y: ~200 µm
  Work in min TPC mode: 30 mm drift
  Standard drift field standard, ~ 3 Kv for 3 cm
  resist plain layer of ~5 Mohm/square
  Work with magnetic Field ~ 500 gauss (50 mT)
Electronics:
  Dream 1 card (512 ch) / detector
  4 MEC8 connector on 2 side
  Cable to 4 cards electronics in rack (x32)
Multiplexing independent (on ad hoc pcb)
Detector sketch
400 mm
450 mm
~480 mm

## Slide 3
Detector schematic
HV resist contact

## Slide 4
Y4
Y2
Y3
Y4
Y2
X2
X1
X3
X2
X1
X3
Y1
X4
X4
Y3
Y1
X strips connected to yellow pixels
Y strips connected to green pixels
YZ Cut view, along Y1 strip
X1 strip
X3 strip
X2 strip
X4 strip
Y1 strip
X2
X1
X3
X4
Y4
Y2
Y3
Y1
filling
512 pixel of 0,78 = 400 mm
262 144 pixel (512 x 512)
Connected with 512 X and 512 Y strip
Pixel
Pitch: 0,78 mm
700² µmcpixel
~80 µm inter
Via ~200 µm ring
Via Cu filled
Pixels layout

## Slide 5
Stacks
4) 512 X strip
1) Top: resist on kapton
Open on ground
3) 512x512 pixel
5) 512 Y strip
6) Ground
2) Kapton foil with resist silk-screen print and HV resist contact

## Slide 6
Stack Total thickness: 428 µm + 1 mm CF

## Slide 7
7
A
A
B
B
Coupe A-A
Coupe B-B
frame
Kapton
resist
HV contact
4mm large
mesh
25 mm
15 mm
Section view - Not in scale
25 mm
~40 ??? mm
Connector
(GMI 30)
Ground (3 mm large)
with soldering
joint
FR4

## Slide 8
~ 30 mm
~40 mm
Connector (GMI 30)
Pin spacer = 1,27 mm,
~12x60 mm²
4 vis M3
Connector
(MEC8 70 rigth)
450 mm
480 mm
~ 520 mm
Section view - Not in scale

## Slide 9
Multiplexing connectors
Multi plex PCB
Independent multiplexing PCB on each side
3 type on Multi PCB, M1, M2, M4
M1 = no multiplex
  512 channels
  8 MEC8 connector
M2 = multiplex by 2
  256 channels
  4 MEC8 connector
M4 = multiplex by 4
  128 channels
  2 MEC8 connector
Connectors
  Readout to Multi:
    No connector on readout = printed
  Multi to DREAM: MEC8 female on multi.
MEC8

## Slide 10
Pads close view
Pads close view + Y connections
Pads close view + X connections
Pads + x and Y lines
GMI Y connector
GERBER FILES

## Slide 11
Connector MEC8:
MEC8-135-02-L-D-RA1
Connector MEC8

## Slide 12: 3D MMX17 PCB with connectors
SHV connectors
Multiplexer PCB
Drif frame (30 mm)
Gas inlet
400x400 mm active area

## Slide 13
Detector Assembly

## Slide 14
Lower frame
CF back plate
MM PCB
Drift frame (30 mm)
Entrance window frame
Detector Assembly

## Slide 15
Work | Cost | Expected delivery
PCB design work –Gerber file | 2500 CHF | End of April
Design of the Mecahnical structure | Free of Charge | End of April
production of 8 boards (4 detectors working + one for testing) | 8 x 2300 CHF = 18400 CHF | End of June
tooling for producing the boards. | 750 CHF | 
production multiplexing of the strips ( 350 CHF per card ) | 1800 CHF for design and 600 CHF for tooling | End of June
Detectors shipping costs | 250 CHF | 
Total cost | 2500 + 18400 +750+250 = 21900 CHF | 
Production of mechanical structure | Free/2000 Eur | End of june
Serigraphy of the resistive layer | Free of charge | Half of July
Production of 4 bulk Micromegas (if everything goes well with photoresist replacement) | Free of charge | End of july
Integration and debug of one prototype | Free of charge | Second week of July
Integration of the remaning 3 detectors (If no modifications are needed) | Free of charge | End of July
Beam test | Free of charge | September
WORKING AND COSTS PLAN