## Slide 1: FLASH meeting WP3: RF Cavity
UPCT, LNF, IFIC (CSIC-UV)
FLASH Meeting
April 30th, 2025

## Slide 2: Results TM010 and TE111
        Refinement of the mesh in CST of the critical points of the gap.
        Calculation of Q factor for TM010 and TE111 modes.
        Variation of the original position of the gap.

## Slide 3: Mode TE111
Mode 1
Mode 2
With the refinement of the gap, two quasi-TE111 modes were found. One of them seems to be more affected by the gap than the other one.

## Slide 4: Comparative of the gap position for TE111
Old position (up-right)
New position (bottom-left)
We have also changed the initial position of the gap, to see if there is any variation. It seems like could be a factor to take into account since we obtain different results.

## Slide 5: RESULTS OF LARGE FLASH CAVITY (for different gap positions)
Quasi - TE Modes (old position) | 𝑸rad | 𝑸total | 𝒇𝒓 (MHz)
Mode 1 | 2.70e8 | 4.02e5 | 150.136
Mode 2 | 4.88e5 | 1.81e5 | 150.165
Old position (up-right)
New position (bottom-left)
Quasi - TE Modes (new position) | 𝑸rad (x105) | 𝑸total (x109) | 𝒇𝒓 (MHz)
Mode 1 | 1.65e8 | 4.08e5 | 150.124
Mode 2 | 5.28e4 | 3.07e4 | 150.231
With the old position, there is a frequency separation of 0.029 MHz while with the new position has a frequency separation of 0.107 MHZ, but has a lower quality factor as well.