## Slide 1: Attività Pisa Silici RD_FCC

## Slide 2: Studio del vertex detector
Inner vertex:
  studio del supporto conico, air cooling channels e integrazione con la beampipe

## Slide 3
Air cooling system to keep at a stable and uniform manageable temperature the silicon detectors
3D printed support with integrated air ducts
(High Temp Resin)
Layer 3
Layer 2
Layer 1
Bus
AIR
INLET
SUPPORT
AIR
OUTLET
SUPPORT
Bus
IP
Front view
3 separated ducts one for each of the layers
Aerodynamic fairing at the stave mounting screw locations
Split support for assembly

## Slide 4
Layer 3 ducts
Layer 2 ducts
Layer 1 ducts
6 sectors of 60° for each of the three indipendently powered layers
Rear view
Diffusers included in the 3D printed support with hose connection
IP
Diffusers
Need to be optimized in terms of length and pitch angle to allow for easy cables routing
Cables inlet/outlet

## Slide 5: Problema di integrazione con la beampipe
A I R
A I R
Due possibili soluzioni allo studio:
1) modifica della lunghezza della beam pipe  impedenze dei fasci da ricalcolare
2) soluzione integrata per il layer 1  permette di andare 2 mm più vicini in raggio
PARAFFIN
Outer jacket

## Slide 6: Studio dell’air cooling con il tunnel del vento
First test on a 60° circular sector of layer 3 including five staves
Next test on the same circular sector with all three layers

## Slide 7
Compressed air system under installation in Pisa
See ‘Vertex Detector Cooling simulations’, Baldinelli, Turrioni
https://indico.cern.ch/event/1439509/contributions/6289579/attachments/2995130/5276700/Baldinelli.pdf

## Slide 8
Maschera superiore per incollaggio
Trave con piattina

## Slide 9: Outer vertex and disks mockup
Per il mockup stiamo definendo il support tube e l’ancoraggio dell’outer tracker e dischi

## Slide 10: Positioning of the Inner and Outer Vertex
X,Y,Z
setting
Angular,Z
setting
Supporting Rib