## Slide 1
VERTEX DETECTOR STUDY
Gherardo Ammirabile
Daniele Benvenuti, Filippo Bosi, Maurizio Massa , Andrea Moggi, Fabrizio Palla
INFN Pisa
RD_FCC Pisa 29/05/2025

## Slide 2
Pisa, 29/05/2025
INTRODUCTION
Current vertex layout
Services of vertex:
  Inner vertex: air cooling and cables
  Middle/Outer vertex and discs: water cooling and cables
  Beam pipe cooling
  Constraints and requirements:
      Limit the LumiCal material budget below 130 mrad
      Minimize the material budget for the vertex and the drift chamber
      Facilitate assembly, opening and maintenance operations
Gherardo Ammirabile, INFN Pisa

## Slide 3
Current vertex layout
Outer vertex tracker:
ATLASPix3 based
Modules of pixel size
Intermediate barrel at 13 cm radius
Outer barrel at 31.5 cm radius
3 discs per side
Inner Vertex detector:
ARCADIA based
Modules of pixel size
3 barrel layers at
13.7, 23.7 and 34/35.6 mm radius
Pisa, 29/05/2025
Gherardo Ammirabile, INFN Pisa

## Slide 4
Layer 1:
15 staves of 6 modules each
Power budget ≈ 12 W
227.4 mm
13.7
Reticular lightweight support to provide stiffness:
Thin carbon fiber walls interleaved with Rohacell
2 buses (data and power) 1.8 mm wide and 250 μm thick
Layer 2:
24 staves of 10 modules each
Power budget ≈ 32 W
Layer 3:
36 staves of 16 modules each
Power budget ≈ 77 W
356.2 mm
23.7
549.4 mm
35.6
Inner vertex
Pisa, 29/05/2025
Gherardo Ammirabile, INFN Pisa

## Slide 5
Air cooling system to keep at a stable and uniform manageable temperature the silicon detectors
3D printed support with integrated air ducts
(High Temp Resin)
Layer 3
Layer 2
Layer 1
Bus
AIR
INLET
SUPPORT
AIR
OUTLET
SUPPORT
Bus
IP
Front view
3 separated ducts one for each of the layers
Aerodynamic fairing at the stave mounting screw locations
Split support for assembly
Pisa, 29/05/2025
Gherardo Ammirabile, INFN Pisa

## Slide 6
Next step: how to join supports with integrated ducts to the air supply and outlet
1. Axial inlet/outlet of air ducts
Conical support structure to allow connection to the inner vertex
Two different solutions
2. Radial inlet/outlet of air ducts
System of pipes attached to the support tube
Choice based on physical and mechanical constraints
Pisa, 29/05/2025
Gherardo Ammirabile, INFN Pisa

## Slide 7
1. Axial inlet/outlet
The conical structure, with the air ducts for the three layers inside, is fixed to the 3D printed support
Conical structure
3D printed support
Physics:
  Projective geometry
  Particles could follow the direction of the cones
  Passive material in front of the LumiCal and discs
Integration/Maintenance:
  Need to split the discs
  Uneasy in opening the detector
  Connection of the cones to the beam pipe and to air ducts at the end
Optimization of the shape still under study
Hyperbolic structure
(impact discs acceptance)
In the assembly, attention needs to be paid to
Pisa, 29/05/2025
Gherardo Ammirabile, INFN Pisa

## Slide 8
2. Radial inlet/outlet
Layer 3 ducts
Layer 2 ducts
Layer 1 ducts
6 sectors of 60° for each of the three indipendently powered layers
Rear view
Diffusers included in the 3D printed support with hose connection
IP
Diffusers
Need to be optimized in terms of length and pitch angle to allow for easy cables routing
Cables inlet/outlet
Pisa, 29/05/2025
Gherardo Ammirabile, INFN Pisa

## Slide 9
2. Radial inlet/outlet
Inner Vertex
Medium vertex
Lowering the innermost discs radius could provide a ‘telescope’ to align the LumiCal with tracks
Pipe system that wraps around the innermost disk:
Minimize the effect on the others
Necessity of an adequate assembly procedure
Pisa, 29/05/2025
Gherardo Ammirabile, INFN Pisa

## Slide 10
Possible assembly procedure
Layer 3 ducts
Layer 2 ducts
Layer 1 ducts
Beam pipe with inner vertex
1
2
Medium and outer vertex assembly
3
Inner vertex services assembly
Pisa, 29/05/2025
Gherardo Ammirabile, INFN Pisa

## Slide 11
Layer 3 ducts
Layer 2 ducts
Layer 1 ducts
Slots are required on the support tube to allow ducts entry and exit
The arrangement and shape of the slots must be studied to accomodate:
Air ducts of the three layers
Cooling water channels of discs, middle and outer barrels
Cables from the inner region
ADVANTAGES:
Easier routing of services
Full Discs
4
Discs assembly
SLOTS
Support tube closure
5
Possible assembly procedure
Pisa, 29/05/2025
Gherardo Ammirabile, INFN Pisa

## Slide 12
Experimental setup to evaluate the effectiveness of air cooling
Compressed air system to define:
Flow rate needed to cool the detectors
Pressure drop in the central region
Temperature increase between inlet and outlet
First test on a 60° circular sector of layer 3 including five staves
Next test on the same circular sector with all three layers
In progress
Pisa, 29/05/2025
Gherardo Ammirabile, INFN Pisa

## Slide 13
Compressed air system under installation in Pisa
Designed to:
Be adaptable
Be controlled
Allow CFD result verification
See ‘Vertex Detector Cooling simulations’, Baldinelli, Turrioni
https://indico.cern.ch/event/1439509/contributions/6289579/attachments/2995130/5276700/Baldinelli.pdf
Pisa, 29/05/2025
Gherardo Ammirabile, INFN Pisa

## Slide 14
Maschera superiore per incollaggio
Trave con piattina
Pisa, 29/05/2025
Gherardo Ammirabile, INFN Pisa

## Slide 15
Air-cooled Layer 1
Integrated design
With the integrated design solution:
ADVANTAGES:
Layer 1 stiffeners are eliminated
Layer 1 air ducts are eliminated
Small additional heat load (12 W compatible with the paraffin system performance)
Layer 1 is 2 mm closer to the interaction point
Easier integration of cooling systems
Contact between the detectors and the outer jacket mediated by a layer of electrical insulator:
Kapton
Ceramics
Need for a rigid support for the sensors:
Bonding
Centering
Assembly
Design under study
A I R
A I R
PARAFFIN
Electrical insulator
Pisa, 29/05/2025
Gherardo Ammirabile, INFN Pisa

## Slide 16
Integrated design
Allow the flow of paraffin inside
Support silicon detectors
Be thin to reduce the material budget
Conceptual design of the outer jacket
Modules with sensors wire-bonded:
On the r-φ side (ARCADIA like)
At the ±z ends (ALICE 3 like)
Lightening cut-outs
t = 0.35 mm
PARAFFIN
Outer jacket
Pisa, 29/05/2025
Gherardo Ammirabile, INFN Pisa

## Slide 17: Thank you for your attention!