## Slide 2: Contents
SRF Concieved for CW Operation
TESLA Technology developped for Pulsing
What’s needed to go back to CW
CW interpretation of the TESLA Technology

## Slide 3: Contents
SRF Concieved for CW Operation
TESLA Technology developped for Pulsing
What’s needed to go back to CW
CW interpretation of the TESLA Technology

## Slide 4: SRF Conceived for CW Operation
Argonne National Labs
ATLAS: Heavy-ion Linac
Originated at Caltech for b ~ 0.1
Stanford University
HEPL: Electron Linac for FEL
First multicell electron cavity: b = 1

## Slide 5: Before TESLA all Project asked for CW
“Livingston Plot” by Hasan Padamsee

## Slide 6: Superconducting RF vs NC-RF
Power dissipated on the cavity walls to sustain the field is:
superfluid helium
ambient pressure boiling He
Good, but the gain of up to 6 order of magnitudes is not guaranted and it’s not for free:
Cryogenics
Material & Surface Science
Clean Technology
……

## Slide 7: First Industrial Production in Japan (1988 – 1995)
The first mass-production of SRF Cavities in the world
SRF Cavity for TRISTAN at KEK
Bulk-Nb - 508MHz - 5-Cell Cavity
32 SRF cavities were fabricated by Mitsubishi and operated in TRISTAN

## Slide 8: LEP-2 Cavities for CERN in Industry

## Slide 9: Installed Cryomodules at TESLA time
TRISTAN - 1986
CEBAF - 1995
LEP-II - 1998

## Slide 10: Contents
SRF Concieved for CW Operation
TESLA Technology developped for Pulsing
What’s needed to go back to CW
CW interpretation of the TESLA Technology

## Slide 11: First Pulsing in 1983 by Campisi & Farcas

## Slide 12: In spite of technology ILC Linacs are pulsed
30 GHz-Warm
11.4 GHz - Warm
1.3 GHz - Cold
ILC Competing Technologies in the nineties
p mode
NC Traveling wave
SC Standing wave

## Slide 13: Luminosity is Proportional to Beam Power
Parameters to play with
Reduce beam emittance (εx .εy ) for smaller beam size (σx.σy )
Increase bunch population (Ne )
Increase beam power
Increase beam to-plug power efficiency for cost
nb = # of bunches per pulse
frep = pulse repetition rate
Pb = beam power
Ec.m.= center of mass energy
L = Luminosity
Ne = # of electron per bunch
σx,y. = beam sizes at IP
IP = interaction point
C. Pagani - ISLC08 - Lecture 1
Oak Brook, October 20, 2008

## Slide 14: Pulsed Operation for Conversion Efficiency
All the LCs must be pulsed machines to improve Plug Power to Beam Power conversion efficiency. As a result:
duty factors are small
pulse peak powers can be very large
RF Pulses
Bunch Train
Beam Loading
<10-200 ms
<1 µs-1ms
1-300 nsec
100 m - 300 km
…………………....
……
gradient
with further input
without input
filling
loading
accelerating field pulse:
C. Pagani - ISLC08 - Lecture 1
Oak Brook, October 20, 2008

## Slide 15: TESLA Collaboration: Origin and Mission
Develop SRF for a TeV Linear Collider
  Increase gradient by a factor of 5
  Reduce cost per MV by a factor 20 (New cryomodule concept and Industrialization)
  Make possible pulsed operation
Major advantages vs NC Technology
  Higher conversion efficiency: more beam power for less plug power consumption
  Lower RF frequency: relaxed tolerances and smaller emittance dilution

## Slide 16: TESLA Technical Design Report: March 2001
As in the TDR
Updated tunnel cross section

## Slide 17: Industrial Studies for TESLA TDR & E-XFEL

## Slide 18: TESLA/XFEL Accelerator Components
HOMs
coupler
RF
LLRF
cavities
TESLA Technology
Tuners
Cryomodule

## Slide 19: The TESLA SRF Cavity, 1.3 GHz, 9-cell
Large number of cells with minimum reasonable bore radius for FF and tuning Odd number of cells with sligthly different end groups for trap modes
Large wall angle and round equator for surface treatments and multipatoring
2 HOM coupler to extract dangerous modes excited by the beam (1% DF)
Stiffening rings for Lorentz Forces, mechanical rigidity and eigen modes
New fabrication strategy required

## Slide 20: Contents
SRF Concieved for CW Operation
TESLA Technology developped for Pulsing
What’s needed to go back to CW
CW interpretation of the TESLA Technology

## Slide 21: From Pulsed EuXFEL back to CW
Duty Factor, DF is goin from 1% to 100%
Dynamic Cryo-losses follow DF if cavity parameters stay unchanged
But dynamic cryo-losses are also:
  proportional to Eacc2
  inversely proportional to Q0
The reducttion of peak current and bunch charge require different RF sources but they are not affecting the cryo-power
    Beam current: from several mA peak to < 0.2 mA
    Buch charge, Ne : from several nC to < 0.2 nC
A new set of working parameters is needed for CW, but utilising as much as possible all the technology already developped and qualified in the framework of the TESLA Collaboration.

## Slide 22: Operating EuXFEL in CW
Just changing the pulsed Klystrons with CW RF Sources and adapting coupling and control electronics, the existing EuXFEL design, based on the TESLA pulsed machine, would be modest because of a few bottle neck:
    Limited installed cryo-power
    Cryo-strings of 12 cryomodules served by a JT valve (240 W limit)
    Insufficient HOM cooling
Eacc < 7 MV/m < 6 GeV with ca. 100 Cryomodules
Building a new machine with a larger cryo-plant, the TESLA design can perform much better thank to a few simple adjustment addressed to overcome the major bottle neck while mantaining all the key technologies.
Eacc > 16 MV/m > 8 GeV with ca. 70 Cryomodules

## Slide 23: Limitations of the actual XFEL Module - 1
The XFEL main linac consists out of 7 cryo strings,
every string includes 12 cryo modules,
every cryo module contains 8 cavities.
2.2 K forward
5 K forward
40 K forward
2-phase tube:
240 W (20 W/cryomodule) is the estimated limit for one cryo string.
2 K, Gas Return Tube
80 K, Return
8 K, Return
Heat load at 2K for each cryomodule must not exceed 20 W.
W.- D. Möller, J. Sekutowicz|

## Slide 24: Limitations of the actual XFEL Module - 2
Each cryomodule houses 8 cavities
  Cavity was designed for ca. 1% DF.
  End groups (FPC and HOM couplers) are cooled by means of heat conduction.
HOM coupler
HOM coupler
FPC
Dissipation on the HOM coupler antennas is the main sources of the heat for the end groups.
W.- D. Möller, J. Sekutowicz|

## Slide 25: Limitations of the actual XFEL Module - 3
Heating of the HOM couplers must not lead to quenching of the end-cells.
Experience with vertical tests (cavities immersed in the superfluid bath):
Without HOM antennae:
Eacc up to 45 MV/m in the CW mode
With HOM antennae:
Eacc up to 13 MV/m in the CW mode
W.- D. Möller, J. Sekutowicz|

## Slide 26: A few guidelines for TESLA based CW XFELs
Don’t tuch the cavity design and fabrication metodology
Improve surface treatment for higher Q0 (lower surface resisstance, Rs)
Mantain the ancillaries (power couipler, tuner, etc) whenever possiblle
Re-design cryogenic distribution to allow higher heat load at 2 K.
  1 JT valve per module, i.e. up to > 20 W/cavity
  Slightly increase the size of the 2 phase pipes accordingly
Implement touls needed for high Q0:
  Implement magnetic hygiene around the cavities
  Improuve 2 K distribution for fast cool-down
Suppress the lower part of the 5 K schield not needed for CW operation
Remember that a 50% marging is normally added in all cryogenic plants

## Slide 27: Contents
SRF Concieved for CW Operation
TESLA Technology developped for Pulsing
What’s needed to go back to CW
CW interpretation of the TESLA Technology

## Slide 28: TESLA / E-XFEL 1.3 GHz cavity
Pulsed RF up to 10 Hz repetition rate.
  1.4 ms RF pulse length
Longitudinal stiffness at about 3 kN/mm
Required coarse tuner sensitivity at 1 Hz/step level
Long piezo stacks required to provide LFD compensation.
  500-600 Hz detuning expected
  About 2 mm stroke at the cavity

## Slide 29: Dumb-bells & Stiffening Rings

## Slide 30: Cavity Fabrication Steps
Half cells are shaped by deep drawing.
Dumb bells are assemled by EB welding.
After proper cleaning eight dumb bells and two end group sections welded by EBW together

## Slide 31: Different EBW Strategies
E-beam
EBW: butt joint (e.g. JLab, PAVAC)
E-beam
E-beam
Vert. Pos. EBW: lap joint (recess) e.g. RI, CERCA, Sciaky
Horiz. Pos. EBW: lap joint (recess) DESY, AES, E.Zanon

## Slide 32: Test Pieces for PAD Qualification
Test piece (TP) is composed by 2 cell with helium vessel, representing all pressure bearing parts and welding seams. It is built using the same welding parameters that will be used in the series production. Two EBW machines/company. Consequently, two test pieces had been built per company.

## Slide 33: Intermediate Steps for Frequency and Length

## Slide 34: EDMS for Storing Data and Communication
EDMS
Cavity-DB
Inspection sheets for quality management
Fabrication structure. Subassembly parts related. Procedure related
Statistical analysis
Phys. Part
Files
All XFEL SC cavity documents (specifications, protocols, PED data etc.) recorded in EDMS. RI and E. Zanon have an access (to relevant data only)
Fabrication

## Slide 35: Sources of dynamic detuning, Pulsed & CW
The Lorentz force detuning, LFD
  Lorentz force on shielding currents on cavity walls induced by electromagnetic fields, equivalent to EM radiation pressure.
  mm level complex deformation of the cavity shape
  Detuning amplitude scales as Eacc2, forward power instead as Eacc4!
  Depends on both cavity stiffness and on external stiffness
  Time-varying for pulsed operations
  Repetitive, synchronous to RF pulses
Microphonics, MP – Crucial for CW
  Stochastic, strongly correlated to He bath pressure fluctuations
  Low amplitude, about 30 Hz rms
  Main harmonics coming from the cryomodule environment are contributing:, typically pumps and any other vibrating element

## Slide 36: E-XFEL Piezo assisted Tuner, OK for CW
Double asymmetric leverage
  lateral on the tank, on pick-up side
  Modified at DESY from the original CEA Saclay design
  Modified after TTF at DESY, now cavity is stretched by the tuner: cavity spring force is added to piezo preload
Cold stepper motor drive unit
  Harmonic Drive reduction gear
  Screw-nut coupling to generate the linear motion
Cold piezo actuators
  Two stacks in a single preloading frame, to gain redundancy and also to profit of the spare one as a mechanical sensor

## Slide 37: LLRF Based on Vector-sum not for CW
FPGA
mTCA system
A single RF sorce feeding multiple cavities is possible also for CW, but because of the moderate power of few kW required for each cavity, independent SSA sources are usually preferred
Conversely
The possible E-XFEL upgrade to CW would use the vector-sum scheme with one IOT per module

## Slide 38: Power Coupler is OK but can be simplified
TTF III Coupler has a robust and reliable design
Succesfully installed in the European XFEL
Pending problems
Long processing time: ~ 100 h
Excessive flexibility and High cost
Critical assembly procedure

## Slide 39: Very Robust Cryomodule Design

## Slide 40: TESLA →XFEL→ILC module design criteria
High filling factor
  maximize real estate gradient/cavity gradient
    long cryomodules/cryo-units, short connections
Moderate cost per unit length
  simple design, based on reliable technologies
  low static heat losses in operation
Effective cold mass alignment strategy
  room temperature alignment preserved at cold
Effective/reproducible assembling procedure
  clean room assembly just for the cavity string
  minimize time consuming operations (cost /reliability)
Module 1 & 2 in TTF I
Module 1, 2 & 3 in TTF II
Cry 1
1st Module in TTF I
Module 4 & 5 in TTF II
Cry 2
Cry 3

## Slide 41: Cryomodule & Assembly as Crucial as Cavity
Required plug power for static losses < 5 kW / (12 m module)
Reliable Alignment Strategy
Sliding Fixtures @ 2 K
“Finger Welded” Shields
Three cryomodule generations to:
improve simplicity and performances
ensure precise alignment
minimize the cost

## Slide 42: The INFN Cryomodule for XFEL & ILC

## Slide 43: TTF Cryomodule Performances

## Slide 44: EuXFEL Cross Section - Pulsed
Helium tank
Coupler port
Thermal shields
Sliding support
HeGRP & System backbone
Support Post
Two phase line
Pressurized He feeding
Shield cooling return pipes
WPM
Shield cooling pipes

## Slide 45: Some of the TESLA/XFEL specific features
Pulsed operation
  High field dominant wrt minimum losses
  Lorentz force detuning impact the cavity design
  Active fast tuner required for high field
  High peak power coupler for high current
CW operation for XFELs (low average current)
  High Q, low losses, dominant wrt maximum field
  Microphonics can be crucial
  Active fast tuner considered for low current
  High average power coupler for high current
Other TESLA/ILC dependent features
  Very high filling factor : interconnections, tuner, magnets, etc
  Very low static losses : long cryo-strings

## Slide 46: LCLS-II: TESLA Cryomodule adapted to CW
J.N. Galayda @ Linac2014

## Slide 47: LCLS-II Cavity in its titanum He Vessel
Marc Ross @ SRF 2015

## Slide 48: LCLS-II Cryomodule and TESLA/Eu-XFEL
T. Peterson et al. @ SRF 2015

## Slide 49: Cavity Beamline String and Supports
T. Peterson et al. @ SRF 2015

## Slide 50: Cryogenic Circuits in the Cryomodule
T. Peterson et al. @ SRF 2015

## Slide 51: LCLS-II Cryomodule Flow Scheme

## Slide 52: LCLS-II adapted for Fast Cooldown
Fast Cool Down Flow: Returns to GHRP
Fast Cool Down Flow: Bottom Inlet
G. Wu et al | SRF 2017

## Slide 53: LCLS-II Sensors on Prototypes
45-deg tilted fluxgate sensor
Transverse fluxgate sensor measuring transverse field
Cernox sensor
Cernox sensor
Cernox sensor
Cernox sensor
Helium Inlet
Helium Return
Four Cavities Fully Instrumented

## Slide 54: LCLS-II: Overall Cryomodule Performance
Dan Gonnella at TTC 2020
Successful demonstration of the first large scale nitrogen doped SRF cavity production by Industry
Demontration of the beneficial effect of fast cooldown for rising Q0 by flux expulsion

## Slide 55: Single Thermal Shield for large 2-Phase pipe
T. Peterson et al. @ SRF 2015

## Slide 56: Connection Details close to E-XFEL
T. Peterson et al. @ SRF 2015

## Slide 57: Power Coupler Design and Integration
Marc Ross @ SRF 2015

## Slide 58: New Split Quad Conduction Cooled
Marc Ross @ SRF 2015

## Slide 59: Reviewed Piezo.assisted Tuner
Marc Ross @ SRF 2015

## Slide 60: The LCLS-II Cryomodule – Tuner Ports
Marc Ross @ SRF 2015

## Slide 61
Thank you for your attention